UNITED STATES DEPARTMENT OF AGRICULTURE

Rural Electrification Administration

BULLETIN 1726A-125

SUBJECT:  Joint Use Agreement With CATV Companies

TO:  REA Electric Borrowers and REA Electric Staff

EFFECTIVE DATE:  Date of Approval

EXPIRATION DATE:  Seven years from effective date

OFFICE OF PRIMARY INTEREST:  Distribution Branch, Electric Staff Division

FILING INSTRUCTIONS:  This is a new bulletin.  File along with

7 CFR 1726 in the blue binders.

PURPOSE:  The purpose of this bulletin is to (1) furnish REA borrowers with a sample joint use agreement with CATV companies, (2) provide borrowers with guidance in executing such an agreement, and (3) provide borrowers with guidelines regarding construction practices on joint use poles.

James B. Huff, Sr.					  09/17/93

_______________________________           __________________

Administrator                           Date

Bulletin 1726A-125

Page 2

TABLE OF CONTENTS

1.  Introduction

2.  Purpose

3.  Application

4.  Execution

APPENDIX:  License Agreement

INDEX:  Joint Use Agreement With CATV Companies

ABBREVIATIONS

CATV   Cable Television (Company)

NESC   National Electrical Safety Code (Accredited Standards

Committee C2)

Bulletin 1726A-125

Page 3

1.  Introduction:  A sample agreement for the joint use of poles, between REA borrowers and cable television companies, has been developed.  A copy of this agreement, titled "License Agreement," is attached as an Appendix and a part of this bulletin.

2.  Purpose:  The purpose of this bulletin is to (1) furnish REA borrowers with a sample joint use agreement with CATV companies for the joint use of poles, (2) provide borrowers with guidance in executing such an agreement, and (3) provide borrowers with guidelines for construction and other related practices regarding joint use poles.

3.  Application:  The attached "License Agreement" is provided as a sample agreement which complies with all of the current, applicable REA requirements and recommendations.

3.1  The requirements for conformance to the NESC and other codes and regulations in Section 2, "Specifications," of the attached "License Agreement," are currently REA requirements and should remain essentially unchanged in the final executed agreement.  The remaining provisions of the attached agreement clearly define and document good construction, maintenance, notification, and billing practices.  Therefore, REA recommends, but does not require, that each one of these provisions be discussed and agreed upon by the parties, executed and enforced.

4.  Execution:  REA borrowers may execute the attached agreement without modifications, by filling in the appropriate information and securing the proper signatures.  Alternately, the borrowers may modify the sample agreement as may be appropriate or required before signing.  In either event, before executing the agreement, the borrower is advised to compare its provisions with the current requirements and guidelines of: (1) REA; (2) national, state, and local governing authorities having jurisdiction over contractual agreements and construction practices of the parties of the agreement; and (3) applicable national, state, and local safety and construction codes.  The borrower is advised to have the agreement reviewed by a corporate attorney for form and content before execution.

LICENSE AGREEMENT

(SAMPLE FORMAT)

PAGES 1-8

AVAILABLE IN HARD COPY ONLY

EXHIBIT "A"

LOCATION OF THE LICENSES DISTRIBUTION SYSTEM SERVICE AREA MAP

PAGE 9

AVAILABLE IN HARD COPY ONLY

EXHIBIT "B"

RULES AND PRACTICES FOR TELEVISION ATTACHMENTS

PAGES 10-11

AVAILABLE IN HARD COPY ONLY

EXHIBIT "C"

APPLICATION AND PERMIT FOR USE OF POLES

PAGE 12

AVAILABLE IN HARD COPY ONLY

EXHIBIT "C1"

ATTACHEMENTS TO BE INSTALLED

PAGE 13

AVAILABLE IN HARD COPY ONLY

EXHIBIT "D"

NOTIFICATION OF REMOVAL

PAGE 14

AVAILABLE IN HARD COPY ONLY

DRAWINGS NUMBERS 1-6

AVAILABLE IN HARD COPY ONLY