# GDE EDR WORK PACKAGE PROPOSAL DESCRIPTION - PHASE 1

### Part I: Work Package Definition

| Work Package categorization |
| --- |
| Technical Area (EDR Org Chart Level 2) | CFS & Global |
| Technical Group (EDR Org Chart Level 3) | Controls |
| Technical Group Work Package Number | 8 |
| Categories (up to 3 keywords) | Engineering Design, Test Facility |
| BCD, ACD, BOTH, or UNDEFINED | BCD |
| Time frame for major deliverables | EDR |
| Primary Target (one keyword) |  |
| Local WP dependencies |  |

| Work Package Details |
| --- |
| Work Package Title | Timing |
| Short keyword title | (For PMO use) |
| Abstract | The ILC controls system needs R&D on distribution techniques for the 1300 MHz timing distribution system. The specified phase stability requirement for timing across the 15 km accelerator complex pushes the state-of-the-art in stable RF signal distribution. The intent is to build on recent systems at SNS, DESY/TESLA and KEK and ongoing work at SLAC and ANL. |
| Major tasks and objectives | Implement a prototype phase reference stabilized fiber optic reference link, 15 km long operating at 1550 nm with 1.3 GHz modulation. This would serve as a test bed for different system control strategies and for testing and optimizing components such as phase shifters. The present design is based on the SNS local phase reference distribution. This scheme is very expensive at ~ $800/meter. Lower cost alternatives would be investigated. Investigate strategies for phase stabilizing long fiber optic links modulated at 1.3 GHz. Possible options include wavelength tuneable lasers, fiber frequency shifting with CW modulation, pulsed RF modulation. Implement a test bed version for likely candidates. Specify, develop and implement a prototype Event Generator and Event Receiver pair. Implementing this in parallel with the timing distribution studies can greatly simplify the event system with only a small impact on the timing system. Investigate feasibility for using a beam derived reference for locking a local phase reference. Investigate HOM phase detector scheme. Prototype a two-channel phase reference receiver with decision logic to auto switch to back-up reference upon detected failure of primary reference. |
| Deliverables from Work Package |  |
| Major Milestones (including key decision points) |  |  |
| Resources required (eg expertise, facilities, leader, …) |  |  |

### Part II: Proposed Institute Involvement Levels

The following information is to be considered strictly confidential until further notice.

If there are currently no known or proposed resources for a given WP, leave the tables blank.

| Ongoing or newly funded participation (List all know institutes who are currently participating in this work) |
| --- |
|  | Institution | Funding Source | Duration (begin/end) | Level of effort FTE / M&S |
| Coordinating Institution |  |  |  |  |  |
| Collaborating Institutions |  |  |  |  |  |

| Expressions of Interest (offered or submitted) |
| --- |
| Institution | Funding available? | Funding Source | Duration (begin/end) | Level of effort FTE / M&S | Comments (e.g. proposed coordinating role) |