WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10721 | In-Flight Anomaly Number -- | Contractor Report Number S-071-2 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title L02 FEEDLINE BOLTS DID NOT MEET THE TWO THREAD PROTRUSION ON LWT 35 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 80901010000 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE EXTERNAL TANK | PART# 80901010000 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE L02 FEEDLINE BOLTS | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U UC | Fail Mode UC - UNSAT | Cause MN - MFG-ISP |
| System PROPULSION | Defect MA - ME ADJ | Material L - FASTNR | Work Contact C. CAMPBELL | Fail Date 11/05/1986 |
| Received at MSFC 04/22/1987 | Date Isolated -- | FMEA Reference 2.X.X.X | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 01/10/1992 | CN RSLV SBMT 08/22/1987 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design J. WHITE | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design -- | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 09/24/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description DURING INSPECTION OF THE LWT 35, IT WAS OBSERVED THAT SOME OF THE L02 FEEDLINE BOLTS DID NOT MEET THE TWO THREAD PROTRUSION REQUIREMENT OF STP-2014. ALSO, DURING INSPECTION OF BIPOD STRUTS, IT WAS DETERMINED THAT THE NUTS ON THE 26L2 BOLTS WERE ENGAGING THE IMPERFECT THREAD REF. MARS: T-78994, T-90726 AND DC&R P-86-003, CAPS S-071C EFFECTIVITY: LWT 16, 20, 21, 22, 24 AND UP |
| Contractor Investigation/Resolution R/C: 1) PRODUCTION - MMC HAS REVISED STP 2014 TO PROVIDE SPECIFIC PROTRUSION REQUIREMENTS AND PLANNING HAS BEEN REVISED TO IMPLEMENT OD 453231. A PERSONNEL TRAINING COURSE WAS ALSO ESTABLSHED. 2) FLEET - RETROFIT MOD. KITS AND CHANGE SUMMARY BO 1777 HAS BEEN ISSUED. THIS PROBLEM IS NOT A LAUNCH CONTRAINTS. REQUIRED RETROFIT WILL BE ACCOMPLISHED BY CONTRACT MOD KIT (B0 1777). TASK I FAILURE/PROBLEM INVESTIGATION DURING INSPECTION OF LWTS 33 AND 35, IT WAS FOUND THAT THE LOX FEEDLINE BOLTS, WHICH MATE THE FEEDLINE TO THE LOX TANK, LACKED SUFFICIENT BOLT PROTRUSION THROUGH THE NUTS TO ASSURE LOCKING FEATURE ENGAGEMENT. AN ANALYSIS OF THE CONDITION REVEALED THAT THE BOLT GRIP LENGTH SPECIFIED PER DRAWING DID NOT ALLOW FOR MAXIMUM FLANGE THICKNESS (REFERENCE MARS T-90345 AND 78944). MPPS FOR THIS PARTICULAR INSTALLATION DID NOT REQUIRE QC TO VERIFY THE TWO THREAD PROTRUSION REQUIREMENT. A REVIEW OF MPPS, WHICH CONTAIN THROUGH BOLT INSTALLATION, REVEALED THREE PLANS WHERE THE TWO THREAD PROTRUSION REQUIREMENT WAS NOT SPECIFIED (REFERENCE INTEROFFICE MEMORANDUM 3743-86-129). DURING A SUBSEQUENT INVESTIGATION, IT WAS FOUND THAT THE FORWARD BIPOD FITTING BOLTS HAD EXCESSIVE PROTRUSION AND THE ASSOCIATED NUTS WERE ENGAGING THE IMPERFECT THREADS. IT WAS DETERMINED THAT THE ENGINEERING WAS CORRECT, BUT THAT AN INSUFFICIENT NUMBER OF WASHERS HAD BEEN INSTALLED TO AVOID SHANKING. A MEASURABLE REQUIREMENT DOES NOT EXIST IN STP/PI 2014 TO ASSURE LOCKING FEATURE ENGAGEMENT AND THE AVOIDANCE OF SHANKING. BASED ON THESE OBSERVATIONS, THE FOLLOWING ACTIONS ARE DEEMED NECESSARY: A. ENGINEERING IS TASKED TO PERFORM A TOLERANCE ANALYSIS ON ALL THROUGH BOLT INSTALLATIONS WITH AN UNTHREADED GRIP TO IDENTIFY ANY INSTALLATIONS WHICH ARE INCORRECT BY DESIGN. COMPLETED CLOSURE STATEMENT: DEFICIENCIES WERE FOUND. CHANGES ARE BEING IMPLEMENTED BY DCNS RELEASE (REFERENCE CORRECTIVE ACTIONS A AND CHANGE SUMMARY B0 1777). B. ENGINEERING IS TASKED TO PERFORM A TOLERANCE ANALYSIS ON ALL BLIND FASTENER INSTALLATIONS, TO IDENTIFY ANY APPLICATIONS WHICH ARE INCORRECT BY DESIGN. COMPLETED CLOSURE STATEMENT: DEFICIENCIES WERE FOUND CONSISTING OF APPROXIMATLEY 113 BOLT APPLICATIONS ON 22 DRAWINGS CHANGES ARE BEING IMPLEMENTED BY DCN RELEASE (REFERENCE CORRECTIVE ACTIONS A AND CHANGE SUMMARY B0 1777). C. DC&RS S-86-020 AND S-86-021 HAVE BEEN RELEASED TO INSPECT ALL ACCESSIBLE THROUGH BOLT INSTALLA- TIONS BUILT PRIOR TO IMPLEMENTATION OF THE REQUIREMENTS IN CORRECTIVE ACTIONS C. POST DD-250 VEHICLES ARE NOT INCLUDED IN THESE INSPECTIONS COMPLETED CLOSURE STATEMENT: INSPECTIONS COMPLETE AND DC&RS CLOSED DATA IS BEING ASSESSED UNDER TASK I.E. D. ENGINEERING WILL PERFORM TESTING TO DETERMINE THE EFFECTS OF SHANKING ON PRELOAD AND FASTENER STRENGTH. COMPLETED CLOSURE STATEMENT: TEST RESULTS ARE BEING ADDRESSED UNDER CORRECTIVE ACTIONS A (REFERENCE CHANGE B0 1777). E. CONSTRUCT A MATRIX TO IDENTIFY THE MEANS OF EXONERATING EVERY THROUGH BOLT INSTALLATION BY EFFECTIVITY. CLOSURE STATEMENT: MATRIX CONSTRUCTION IS COMPLETE. TASK II CORRECTIVE ACTIONS A. ENGINEERING ISSUED DCNS TO CORRECT DEFICIENCIES FOUND IN TASK I.A, I.B, AND I.D. (REFE- RENCE CHANGE SUMMARY B0 1777). B. BASED UPON INVESTIGATIONS, IT HAS BEEN DETERMINE THAT A SPECIFIC MEASURABLE REQUIRE- MENT IS NEEDED TO PRECLUDE BOLT SHANKING AND ASSURE ADEQUATE ENGAGEMENT OF THE LOCKING FEATURE. MATERIALS ENGINEERING IS TASKED TO PROVIDE MEASURABLE REQUIREMENTS AND IMPLEMENT BY REVISION OF STP-2014. COMPLETED CLOSURE STATEMENT: STP-2014 HAS BEEN REVISED TO PROVIDE SPECIFIC PROTRUSION REQUIREMENTS REFERENCE CHANGE SUMMARY J31020). C. A MANAGEMENT DECISION WAS MADE TO IMPLEMENT THE PROPOSED STP/PI CHANGES INTO CURRENT PRODUCTION. THIS ACTIVITY WAS DIRECTED BY OD 453231 ET/MGT-030-000 MANUFACTURING PLANNING IS TASKED TO IMPLEMENT THE OD REQUIREMENTS TO FUTURE BUILDS. COMPLETED CLOSURE STATEMENT: PLANNING HAS BEEN REVISED TO INCORPORATE THE OD REQUIREMENTS (REFERENCE INTEROFFICE MEMORANDUM 3614-86-381). D. CONTRACTS OBTAIN EO MSFC APPROVAL F0R RETROFIT MOD KITS AND CHANGE SUMMARY B01777. E. A PERSONNEL TRAINING COURSE IS REQUIRED TO ASSURE ADEQUATE UNDERSTANDING BY ALL PERSONNEL RE- GARDING CORRECT INSTALLATION OF FASTENERS. CLOSURE STATEMENT: COURSE X551 HAS BEEN ESTABLISHED AND IS SCHEDULED TO BEGIN AUGUST 17, 1987. TASK IV CAPS CLOSEOUT SUMMARY A REVIEW OF BOLT INSTALLATIONS REVEALED PROBLEMS WITH INCORRECT GRIP LENGTHS SPECIFIED ON ENGINEER- ING DRAWINGS, INADEQUATE INSPECTION REQUIREMENTS AND TRAINING OF PERSONNEL. AS A RESULT OF THESE FINDINGS, A COMPLETE TOLERANCE ANALYSIS WAS CONDUCTED BY ENGINEERING ON ALL BOLT INSTALLATIONS. DEFICIENCIES WERE CORRECTED THROUGH DCNS FOR THE APPROPRIATE DRAWINGS. INSTALLATIONS COMPLETED PRIOR TO DCN RELEASE WERE CORRECTED BY MOD KITS. A SPECIFIC MEASURABLE REQUIREMENT WAS ESTABLISHED TO VERIFY ALL BOLTS ENGAGE THE LOCKING FEATURE AND DO NOT SHANK. A PERSONNEL TRAINING COURSE WAS ALSO ESTABLISHED. THESE ACTIONS ARE DEEMED APPROPRIATE TO CLOSE THIS CAPS |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10721 | IFA# -- | Contractor RPT# S-071-2 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# N/A | Asmnt Part Name L02 FEEDLINE BOLTS | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 3 | CAUSE CD MAP - MFG-ASY-INST | FAIL MODE UC - UNSAT |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |