| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 19 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| common proposals for the work of the conference |
| Agenda item 1.19 |

1.19	to consider the results of the ITU-R studies regarding spectrum requirement for global broadband satellite systems in order to identify possible global harmonized fixed-satellite service frequency bands for the use of Internet applications, and consider the appropriate regulatory/technical provisions, taking also into account No. 5.516B

Introduction

At its fifth meeting of the Conference Preparatory Group for WRC-07, APT members considered the necessity for possible identification of global harmonized fixed-satellite service (FSS) frequency bands for Internet applications as well as the appropriate regulatory/technical provisions. The conclusion was that there is no need for the identification of specific FSS frequency bands for Internet applications.

ASP/41A19/321

No change to Article 5 of the Radio Regulations under Agenda item 1.19.

Reasons:	There are many existing and planned systems in a number of different FSS frequency bands fully capable of providing broadband/Internet applications on a global basis. Therefore, no changes to the Radio Regulations are necessary to accommodate such applications in the FSS. The responses to the studies requested in this agenda item have been provided in Recommendations ITU-R S.1782 and ITU-R S.1783. Administrations are encouraged to further contribute to ITU-R studies that would provide guidance, as appropriate, on technical and operational aspects of providing Internet applications over satellite systems.

______________