#### ORDER:	8400.10

APPENDIX:	3

BULLETIN TYPE:	Flight Standards Handbook Bulletin for Air Transportation (HBAT)

BULLETIN NUMBER:	HBAT 03-06

BULLETIN TITLE:	Reduced Vertical Separation Minimum (RVSM) Airspace

EFFECTIVE DATE:	09/08/03

TRACKING NUMBER:	N/A

-----------------------------------------------------------

1.  PURPOSE.  This document provides for the coordination of the guidance for Reduced Vertical Separation Minimum (RVSM) airspace and will be incorporated into Federal Aviation Administration (FAA) Order 8400.10, Air Transportation Inspector’s Handbook.

2.  BACKGROUND.  RVSM airspace is any airspace or route where aircraft are separated by 1,000 feet vertically between flight level (FL) 290 and FL 410, inclusive.  Generally, aircraft and operators that have not been authorized to conduct RVSM operations cannot operate at FLs where RVSM is applied.  Exceptions to this rule are published by individual Air Traffic Service Providers.  Air Traffic Service Providers have elected to implement RVSM as a means to provide more fuel/time-efficient altitudes and routes to operators, and to enhance en route airspace capacity. The attachment provides guidance for inspectors regarding RVSM authorization.

3.  CANCELLATION.  This bulletin cancels HBAT 99-11A, Approval of Aircraft and Operators for Flight in Airspace Above Flight Level (FL) 290 Where a 1,000 Foot Vertical Separation is Applied, dated September 21, 1999.

4.  INQUIRIES.  The Flight Technologies and Procedures Division, AFS-400, developed this HBAT. Questions or comments about this bulletin can be directed to Robert Swain, AFS-430, at

202-385-4576, or to AFS-200, at 202-267-8166.

5. LOCATION. The attachment will be incorporated in FAA Order 8400.10, volume 4, chapter 1, section 5.

/s/ Matthew Schack

Manager, Air Transportation Division

Attachment

ATTACHMENT

To be incorporated into Order 8400.10, Volume 4, Chapter 1, Section 5

220.  REDUCED VERTICAL SEPARATION MINIMUM (RVSM) AIRSPACE.  RVSM airspace is any airspace or route where aircraft are separated by 1,000 feet vertically between flight level (FL) 290 and FL 410, inclusive.  Generally, aircraft and operators that have not been authorized to conduct RVSM operations cannot operate at FLs where RVSM is applied.  Exceptions to this rule are published by individual Air Traffic Service Providers.  Air Traffic Service Providers have elected to implement RVSM as a means to provide more fuel/time efficient altitudes and routes to operators and to enhance en route airspace capacity.

A.  RVSM Areas of Operation.  The following table shows some examples of major areas where RVSM has been, or is planned to be, implemented.

| Area of Operations | Implementation Dates | Flight Levels |
| --- | --- | --- |
| North Atlantic MNPS Airspace | March 1997 October 1998 January 2002 | FL 330-370 FL 310-390 FL 290-410 |
| Pacific Oceanic Airspace | February 2000 | FL 290-390 |
| Australia | November 2001 | FL 290-410 |
| West Atlantic Route System | January 2002 | FL 290-410 |
| All European Airspace | January 2002 | FL 290-410 |
| Western Pacific/South China Sea | February 2002 | As published in ATS Documents |
| Northern Canada | April 2002 | FL 290-410 |
| Middle East and Asia South of the Himalayas | Planned for November 2003 | As published in ATS Documents |
| Domestic United States, Southern Canadian Domestic Airspace, Caribbean and South America | Planned for January 20, 2005 | FL 290-410 |

B.  RVSM Guidance.  Using the guidance provided in Interim Guidance (IG) 91-RVSM, Approval of Aircraft and Operators for Flight in Airspace Above Flight Level (FL) 290 Where a 1,000 Foot Vertical Separation Minimum is Applied (as amended), inspectors shall ensure that operators and aircraft meet the standards of Title 14 of the Code of Federal Regulations

(14 CFR) part 91, appendix G, Operations in RVSM Airspace.

C.  Sources of Information.   Sources of information on RVSM programs are:

(1)  Federal Aviation Administration (FAA) RVSM Homepage.  The RVSM homepage provides information on RVSM programs in various areas of the world.  It provides a link to the Domestic RVSM Web page where information is posted on plans and programs to implement RVSM in the domestic United States.  It also links to the RVSM Documentation page that provides specific information on aircraft and operator approval for RVSM operations.  The RVSM homepage can be accessed at:  www.faa.gov/ats/ato/rvsm1.htm.

(2)  RVSM Documentation Web page.  The RVSM Documentation Web page provides access to regulations, guidance, documents and contacts.  This Web page is maintained by the Flight Technologies and Procedures Division, AFS-400.  It can be accessed at:

(a)   www.faa.gov/ats/ato/rvsm1.htm, then clicking on “RVSM Documentation.”

(b)  In the Operations Specifications Subsystem (OPSS) in association with operations specifications (OpSpec) B046, Operations in RVSM Airspace.

(3)  Regulations.  Title 14 CFR part 91, section 91.706 applies to RVSM operations outside the United States.  Part 91, section 91.180, when published, will apply to RVSM operations within the U.S.   Both sections require that the operator and the operator’s aircraft comply with the standards of part 91, appendix G and that the operator obtain FAA authorization to conduct RVSM operations.  Part 91, appendix G provides basic RVSM standards for aircraft and operator programs.   The RVSM Documentation Web page provides a link to section 91.706 and appendix G.  It will be linked to section 91.180 when it is published.

(4)  Guidance.  FAA IG 91-RVSM, as amended, can be found on the RVSM Documentation Web page.  IG 91-RVSM provides an acceptable means to authorize operators and aircraft to conduct flight in RVSM airspace.  It provides detailed guidance for aircraft manufacturers, other engineering organizations, and operators to follow when developing programs intended to meet the standards of part 91, appendix G.

(a)  If an operator requests to deviate from the practices and procedures provided in

IG 91-RVSM, the inspector should forward a request for assistance through the Regional Flight Standards Division to AFS-400.  AFS-400 will respond after coordination with AFS-200, AFS-300, or AFS-800, as appropriate.

(b)  IG 91-RVSM was developed in national and international forums and is used by civil aviation authorities throughout the world.  International Civil Aviation Organization (ICAO) Document 9574, Edition 2 (Manual on Implementation of a 1,000 ft Vertical Separation Minimum Between FL 290 and FL 410 Inclusive) cites IG 91-RVSM as an acceptable means for RVSM approval.

D.  Overview of the Authorization Process.  The principal operations inspector (POI), principal avionics inspector (PAI), and principal maintenance inspector (PMI) should coordinate the issue of OpSpecs B046 and D092 to grant the operator authority to conduct RVSM operations for a specific aircraft type or group.  The FAA will issue the OpSpecs paragraphs if the following conditions exist:

(1)  The FAA determines that operator aircraft comply with RVSM standards.  For in-service aircraft, the FAA determines that inspections and/or aircraft system modifications are completed as required by the applicable Service Bulletin (SB), Service Letter, Supplemental Type Certificate (STC) or other Aircraft Certification Office approved document.   For aircraft manufactured RVSM compliant, the FAA determines that the Airplane Flight Manual (AFM) or Type Certificate Data Sheet (TCDS) contain a statement of RVSM eligibility.

(2)  The FAA approves the operator’s RVSM maintenance program.

(3)  The FAA approves the operator’s RVSM operations program.

(4)  The FAA accepts the operator’s plan to participate in monitoring programs.

(5)  If required by the POI in coordination with the PAI and PMI, the operator successfully completes a validation flight.

E.  RVSM Authorization Process and Policy.

(1)  Coordination Between Inspectors.  Before issuing RVSM authorizations B046 and D092, inspectors must coordinate with the responsible operations, maintenance and avionics inspectors.

(2)  Authorization Process Events.  Paragraph 11 of IG 91-RVSM is titled “Operational Approval.”  It provides guidance on the major events in the RVSM authorization process.  Also, the “Getting Started” section of the RVSM Documentation Web page contains an outline or checklist of the events or steps in the authorization process.  It includes references to applicable document paragraphs and sections.

(3)  OpSpecs Actions.  IG 91-RVSM, paragraph 11g(1) provides the following policy for part 121, 125, and 135 operators:  FAA will authorize initial operational approval for RVSM operations by issuing OpSpecs B046 and D092.  (Specific make/model/series and individual registration numbers are listed in D092).  Areas of RVSM operation that are new to the operator will be authorized by adding OpSpec B046 to the OpSpecs Part B (En route) paragraph B050: “Authorized Areas of En Route Operation.  Limitations and Provisions.”  (If you have any questions regarding these OpSpec paragraphs, please contact AFS-260 at 202-267-8166).

(4)  Relationship between RVSM Authorization and Horizontal Navigation Authorizations.  Currently, in designated oceanic airspaces, operators are required to obtain both RVSM authorization and certain horizontal navigation authorizations.   These are separate, specific authorization actions.   For example, to operate in North Atlantic Minimum Navigation Performance Specification (NAT MNPS) airspace, operators are required to obtain both RVSM and NAT MNPS authority.   In Pacific oceanic airspace, operators are required to obtain both RVSM and Required Navigation Performance 10 (RNP-10) authorization.

(5)  Traffic Alert and Collision Avoidance System (TCAS).  Information on TCAS as it relates to RVSM operations can be found on the RVSM Documentation Web page.  Part 91 appendix G does NOT require that aircraft be equipped with TCAS for RVSM operations.  Appendix G, section 2 does require, however, that if an aircraft is equipped with TCAS II and is used in RVSM operations, then it must be a TCAS II that meets Technical Standard Order (TSO)

C-119b (Version 7.0) or a later version.  TCAS equipage requirements can be found in parts 121, 125, 129, and 135 .

(6)  Determining Aircraft RVSM Compliance.  The phrases, “determining aircraft RVSM compliance,” and “initial RVSM airworthiness approval,” both appear in RVSM documents to indicate that the FAA has determined that the operator’s aircraft comply with appendix G, RVSM standards.

(a)  Inspector Guidance.   The Airworthiness Inspector’s Handbook (FAA Order 8300.10), volume 2, and IG 91-RVSM, paragraph 11d provide guidance on inspector determination that aircraft are RVSM compliant.   IG 91-RVSM Paragraph 11d(1) and (2) discuss the documents that the operator must submit to the FAA to show that in-service aircraft or aircraft manufactured RVSM-compliant are in compliance with the RVSM requirements of part 91, appendix G.

(b)  For most in-service aircraft, the RVSM airworthiness documents take the form of SBs, Service Letters or STCs.   These documents contain requirements that are specific to individual aircraft types or groups and generally require inspections and/or hardware or software modifications.  The operator must submit documents to the FAA to show that the required actions have been completed for each airframe that will operate in RVSM airspace.

(c)  For aircraft manufactured RVSM-compliant, the AFM or TCDS must contain statements that show the aircraft to be eligible for RVSM operations.

(7)  Program Tracking and Reporting Subsystem (PTRS) Codes.  When the inspector determines that individual operator airframes are RVSM compliant, the PTRS must be updated and the airframes listed in OpSpecs D092 or a Letter of Authorization (LOA), as appropriate.  See paragraph G below for PTRS action.

(8)  RVSM Maintenance Program Approval.   FAA Order 8300.10, volume 2 contains airworthiness inspector guidance for the evaluation and approval of an operator’s RVSM maintenance program.  Also, IG 91-RVSM paragraph 10 contains guidance on the content of maintenance programs.

(9)  Operations Program Approval.  Evaluation of operations programs should be completed in conjunction with the evaluation of maintenance programs.  IG 91-RVSM, paragraph 11d(3)(4) provides specific guidance on the process and policies to be followed for operations program approval.

(a)  Special Emphasis Items for Pilots.  IG 91-RVSM, appendix 4 provides operating practices and procedures applicable to all RVSM operations.  Appendix 4, paragraph 7 lists special emphasis items for pilot training.

(b)  Specific Procedures for Oceanic Airspace.   Appendix 5 provides specific practices and procedures for RVSM operations in oceanic airspace.

(c)  Domestic U.S. RVSM Operational Policy/Procedures.  Until operational policy and procedures for RVSM in the domestic United States are published, operators can use IG 91-RVSM, appendix 4 as the basis for their RVSM operations training and operating practices/procedures.  Operational procedures such as those for en route failure of RVSM systems in domestic U.S. airspace are planned to be published in the 4/Q 2003.  Guidance will be published in the Aeronautical Information Manual and, in addition, AFS-400 will publish and distribute a Sample Pilot Bulletin that can be incorporated into individual operator programs.  Operators will be responsible for incorporating this material into their programs prior to conducting RVSM operations in the United States.  The FAA anticipates that operational procedures unique to domestic U.S. airspace will not be extensive.

(10)  Validation Tests and Flights.

(a)  IG 91-RVSM, paragraph 11f provides guidance on the RVSM validation test.  In most cases, review of the operator’s RVSM application and program documents will suffice for validation test purposes.  However, as determined by the POIs, PMIs, and PAIs, the final step of the approval process may be the completion of a validation flight.  The FAA may accompany the operator on a flight to verify that RVSM operations and maintenance procedures and practices are used effectively.  The validation flight may be accomplished during a revenue flight, as determined by the principal inspectors on a case-by-case basis.

(b)  Validation flights are NOT required to be conducted in conjunction with the monitoring flights described below.  Also, the validation flight may be conducted before monitoring requirements are completed.

# F.  Monitoring Programs

(1)  Objective of Monitoring.  The primary goal of monitoring is to provide a quality control check on the altitude-keeping performance of the wide variety of operators and aircraft.  It has been determined that this may be accomplished by sampling a number of airframes of each aircraft type that an operator will operate in RVSM airspace.  Altitude-keeping performance data is analyzed to determine that the aircraft fleet, as well as individual operators, exhibits performance that is consistent with RVSM standards.

(2)  Operator Plan and Monitoring Requirements.  In its application for RVSM authority,

IG 91-RVSM paragraph 11d(8) calls for each operator to submit a plan to participate in monitoring programs.  It further notes that the current monitoring requirements for individual operators in specific RVSM areas of operation are published on the FAA RVSM Documentation Web site.

NOTE:  Operators are no longer required to complete monitoring prior to being granted operational approval.

(3)  Monitoring Procedures.  Monitoring procedures for ground-based and Global Positioning System (GPS)-based monitoring systems are published on the RVSM Documentation Web page.  Operator aircraft of a specific type or group are monitored after they have been determined to be RVSM compliant.  Currently, the operator can have its aircraft monitored by either the ground-based Height Monitoring Unit (HMU) or a portable GPS-based Monitoring Unit (GMU) that can be placed on the aircraft.  In the October 2003 timeframe, operators may have the option of over flying the FAA ground-based monitoring system called the Aircraft Geometric Height Measurement Element (AGHME).

(4)  Flight Standards district office (FSDO) or certificate management office (CMO) Notification.  When an operator has successfully completed monitoring requirements for the specific aircraft type or group, the FAA Technical Center Separation Standards Group

(ACB-310) will notify the POI and/or PAI.

G.  PTRS.

(1)  RVSM Approvals Database.  IT IS IMPERATIVE THAT THE PTRS BE UPDATED IN A TIMELY MANNER.  The FAA Technical Center (ACB-310) is retrieving PTRS information and compiling it into a database of RVSM aircraft and operator approvals.  It is also forwarding the information to the international bodies tasked with tracking RVSM aircraft/operator approval.  The approval information can also be faxed or e-mailed to ACB-310.  (See Appendix 2).

NOTE:  This information is being used to find and investigate aircraft that fly at RVSM FLs but are not RVSM-approved.  The database of RVSM approvals is not, however, used in real time to grant or deny clearance into RVSM airspace.

(2)  Separate PTRS entries must be made, as follows:

(a)  In-service Aircraft.  See IG 91-RVSM, paragraph 11d(1).  When the operator provides documentation that RVSM work is completed on individual airframes in accordance with appropriate airworthiness documents (e.g., SBs, STCs), the PTRS must be updated.

(b)  Aircraft Manufactured RVSM-compliant. A PTRS entry is also required for “Initial Airworthiness Approval” of aircraft that are RVSM compliant on delivery.  Since no specific work is required to be accomplished on such aircraft, the same date that is listed for the operations activity code when the OpSpecs or LOA is approved may be used for the airworthiness and avionics activity code.

(c)  OpSpecs or LOA Approval.  When OpSpecs or LOA authority is issued for each specific aircraft type or group, the PTRS must be updated.

(d)  Other Actions.  When “Other” actions, as described below are taken, the PTRS must be updated.

(3) The FSDO or CMO will update the system, at a minimum, with the specific items listed below:

|  | INITIAL AIRWORTHINESS APPROVAL# | LOA OR OPSPECS GRANTED | OTHER* |
| --- | --- | --- | --- |
| Operations Activity Code | None | 1411 | 1413 |
| Airworthiness Activity Code | 3411 | none | 3413 |
| Avionics Activity Code | 5411 | None | 5413 |

#  For in-service aircraft, approval means required SB, STC, or Aircraft Service Change work was accomplished.  For aircraft manufactured RVSM-compliant, AFM or other appropriate documents found to show RVSM compliance.

*  Other may include actions such as:  N-number change; withdrawing RVSM approval due to transfer of airframe to a different operator; biennial LOA renewal for part 91 operators; investigation of oceanic navigation error report, etc.

(4)  Specific PTRS Entries are as follows:

(a)  Section I—Transmittal.

CFR:  91, 121, 125, or 135

STATUS:  Closed

RESULTS:  Completed or Assisted

CLOSED DATE:  Date of Initial Airworthiness Approval or date OpSpecs were issued.

DESIGNATOR:  4-letter code for part 121, 125, and 135 operators; Optional for part 91 operators

NON-CERT. ACTIVITY NAME/COMPANY:  Prohibited for part 121, 125, and 135 operators; required for part 91 operators

TRACKING:  Used for all operators, the date RVSM approval was withdrawn

MISCELLANEOUS:  Manufacturer’s aircraft serial number

(b)  Section IV—Comments.

| PART 121, 125, and 135 OPERATORS | PRIMARY AREA | KEY WORD | OPINION CODE |
| --- | --- | --- | --- |
| Initial Airframe Acceptance | A or F | 643 | I |
| Full RVSM Approval | A or F | 643 | I |
| Other | A or F | 699 | I |
| PART 91 OPERATORS |  |  |  |
| Initial Airframe Acceptance | B or G | 643 | I |
| Full RVSM Approval | B or G | 643 | I |
| Other | B or G | 699 | I |

(c)  Additional Section IV Comments.

i.  For part 91 operators:  Date LOA expires.

ii.  For all operators:  Amplifying remarks why RVSM approval was withdrawn.

iii.  For all operators:  If available, Aircraft Mode-S Address Code.

H.  Inquiries.  Each Regional AFS Division has appointed RVSM Focal Points.  Each Field Office has appointed two RVSM Points of Contact.  A list of the focal points is published on the FAA RVSM Documentation Web page.  For general questions on RVSM, the appropriate Field Office Point of Contact should be contacted first.  Questions on this handbook material and specific questions on RVSM policy should be directed to (202) 385-4576 at the Flight Technologies and Procedures Division, AFS-400.