From Objective 2a:

H, He, O energy/pitch-angle spectra from 5-400 keV.@ 1/spin. Energy resolution of 50%with 20 degree pitch angel bins covering 0-180 degrees.

From Objective 2b:

H, He, O energy/pitch-angle spectra from 50-400 keV.@ 1/spin. Energy resolution of 50%with 20 degree pitch angel bins covering 60-120 degrees. Electron energy/pitch-angle spectra from 0.1-4 MeV @ 1/spin  Energy resolution of TBD (30%) with 20 degree pitch angel bins covering 60-120 degrees.

From Objective 2c:

H, He, O energy/pitch-angle spectra from 1-400 keV.@ 1/spin. Energy resolution of 50%with 20 degree pitch angel bins covering 60-120 degrees. Electron energy/pitch-angle spectra from 0.1-4 MeV @ 1/spin  Energy resolution of TBD (30%) with 20 degree pitch angel bins covering 60-120 degrees.

From Objective 3a:

Electrons (0.5 - 1000 keV); dE/E=20%; 30 second resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees; Protons, helium, oxygen (0.1 - 200 keV); dE/E=20%; 1 minute resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees; SEPs (5 - >500 MeV protons; >1 MeV/nuc heavy ions); 3 minutes resolution

From Objective 3b:

Energy and pitch angle resolved ion fluxes from 20 keV to 10 MeV. Required energy resolution varies from 20% dE/E at 20 keV to 100% dE/E at 10 MeV. Cadence 1 min.  Composition protons, helium, oxygen.  Pitch angle resolution TBD.

From Objective 4Q3:

Need ring current ion composition, energy, and pitch angles, <1 minute cadence, energy coverage from ~10 keV to 400 keV. (See Objectives 7 and 8 for details on measurement requirements.)

From Objective 5a:

Electrons (0.5 - 1000 keV); dE/E<40%; 1 minute resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees; Protons, helium, oxygen (0.1 - 200 keV); dE/E<40%; 1 minute resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees

From Objective 5d:

Electrons (0.5 - 1000 keV); dE/E<40%; 30 second resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees; Protons, helium, oxygen (0.1 - 200 keV); dE/E<40%; 1 minute resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees; SEPs (5 - >500 MeV protons; >1 MeV/nuc heavy ions); 3 minutes resolution

From Objective 6a:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 50%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 20 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 6c:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 20%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 10 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7a:

H, He, O energy spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 50%. Accuracy: 20%  Interspacecraft precision: 20%.

From Objective 7c:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 50%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 20 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7d:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 50%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 20 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7e:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 12 seconds.  Energy Resolution: 20%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 20 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7f:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 10%. Accuracy: 10%  Interspacecraft precision: 20%. Pitch angle resolution: 10 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 8a:

Energy and pitch-angle resolved particle fluxes at <0.02L spatial sampling. Required energy resoultion varies from 20% dE/E at 1 eV to 100% dE/E at 1 GeV. Electrons required from 1 eV to 10 MeV, protons from 1 eV to 1 GeV, Oxygen from 10 eV to 400 keV

From Objective 8b:

Energy and pitch-angle resolved particle fluxes at <0.02L spatial sampling. Required energy resoultion varies from 20% dE/E at 1 eV to 100% dE/E at 1 GeV. Electrons required from 1 eV to 10 MeV, protons from 1 eV to 1 GeV, Oxygen from 10 eV to 400 keV, Helium from ????-????. Particle data is the ground truth output and a minimum subset will be required as input.

Tightest Requirements:

Obj. 2a

H, He, O energy/pitch-angle spectra from 5-400 keV.@ 1/spin. Energy resolution of 50%with 20 degree pitch angel bins covering 0-180 degrees.

Obj. 3a

Protons, helium, oxygen (0.1 - 200 keV); dE/E=20%; 1 minute resolution; 2D pitch angle coverage; pitch angle resolution <40 degrees

From Objective 6c:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 20%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 10 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7e:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 12 seconds.  Energy Resolution: 20%. Accuracy: 20%  Interspacecraft precision: 20%. Pitch angle resolution: 20 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

From Objective 7f:

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 1 minute.  Energy Resolution: 10%. Accuracy: 10%  Interspacecraft precision: 20%. Pitch angle resolution: 10 degrees.  Pitch angle coverage: 0-90 or 90-180 degrees.

Combined, Driving Requirements, Ring Current (from 2a, 2b, 2c, 7e, 7f):

H, He, O energy/pitch-angle spectra from 5-400 keV.  Cadence: 12 seconds (1/spin).  Energy Resolution: 10%. Accuracy: 10%  Interspacecraft precision: 20%. Pitch angle resolution: 10 degrees.  Pitch angle coverage: 0-180 degrees.

RB-SPICE Capabilities:

H+:   10-1000 keV   (might get down to 5 keV; need HOPE to cover lower)

He+:   20-1000 keV    (need HOPE to cover lower)

O+:   40-1000 keV   (need HOPE to cover lower)

12-24 second resolution, high data rate; 48 second resolution, low data rate

Energy resolution: 	<10% for H > 30 keV, He > 45 keV, O > 80 keV

~20-40% below those energies.

Pitch angle coverage:  Either 0 -140 or 40 – 180.  Can’t get 0 – 180.

Pitch angle resolution:  Nominally ~ 22.5°;

for high data rate, good statistics, and using deconvolution, <10°

High data rate capabilities indicated in RED.

RB-SPICE Strawman Telemetry Products

|	Burst	| High Rate (~5 Days) | Low Rate|