## Chapter 10
Allowable Adaptations for Special Housing Adaptations (SHA), SHA Site Reviews, and SHA Bid/Proposal/Contract Reviews

#### Overview

| Introduction | This chapter contains information about allowable adaptations for Special Housing Adaptations (SHA), SHA site reviews, and SHA bid/proposal/contract reviews, including: allowable adaptations the existing home inspection interviews construction plans and bid/proposal/contract, and inspection schedules. |
| --- | --- |

| In this Chapter | This chapter includes the following sections: |
| --- | --- |

| Section | Section Name | See Page |
| --- | --- | --- |
| A | Allowable Adaptations for Special Housing Adaptations (SHA) Cases | 10-A-1 |
| B | Special Housing Adaptations (SHA) Existing Home Inspections | 10-B-1 |
| C | Interviews with the Architect and/or Contractor | 10-C-1 |
| D | Special Housing Adaptations (SHA) Bids/Proposals/Contracts | 10-D-1 |
| E | Special Housing Adaptations (SHA) Construction Plans | 10-E-1 |
| F | Special Housing Adaptations (SHA) Inspection Schedule and Assignment of a Department of Veterans Affairs (VA) Compliance Inspector | 10-F-1 |

## Section A
Allowable Adaptations for Special Housing Adaptations (SHA) Cases

#### Overview

| Introduction | This section contains information about allowable adaptations for Special Housing Adaptations (SHA) cases, including allowable adaptations for: blindness in both eyes with a 5/200 visual acuity or less loss of or loss of use of both hands, and secondary disabilities. |
| --- | --- |

| In this Section | This section includes the following topics: |
| --- | --- |

| Topic | Topic Name | See Page |
| --- | --- | --- |
| 1 | General Information About Allowable Adaptations for Special Housing Adaptations (SHA) Cases | 10-A-2 |
| 2 | Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less | 10-A-3 |
| 3 | Allowable Adaptations for Loss of or Loss of Use of Both Hands | 10-A-8 |
| 4 | Allowable Adaptations for Secondary Disabilities | 10-A-9 |

#### General Information About Allowable Adaptations for Special Housing Adaptations (SHA) Cases

| Introduction | This topic contains general information about allowable adaptations for Special Housing Adaptations (SHA) cases, including allowable adaptations based on disability type. |
| --- | --- |

| Statutory Reference | Title 38 United States Code (U.S.C.) Chapter 21 or sections 36.4401 through 35.4410 is the governing law that states SHA grants must be made available for adaptations determined to be reasonably necessary by the nature of the veteran’s disability. |
| --- | --- |

| Allowable Adaptations Based on Disability Type | The adaptations deemed allowable in SHA cases depend on the following types of disabilities: blindness in both eyes with a 5/200 visual acuity or less loss or loss of use of both hands, and secondary disabilities. |
| --- | --- |

#### Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less

| Introduction | This topic contains information about allowable adaptations for blindness in both eyes with a 5/200 visual acuity or less, including: the veteran’s freedom of choice special lighting sliding doors handrails/grab bars smoke, fire, and carbon monoxide detectors security items room additions covered porches concrete or asphalt walkways fencing electrical service swimming pools, and safety defect corrections. |
| --- | --- |

| Freedom of Choice | It is not required that the veteran adapt the home with every allowable adaptation item. The veteran has the freedom of choice as to which adaptations he/she will complete with the Special Housing Adaptations (SHA) Grant Program. If the veteran wants to add any additional adaptation items that are not included in the allowable adaptations list, approval must first be received from Central Office (CO). |
| --- | --- |

Continued on next page

Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less, Continued

| Special Lighting | Allowable adaptations for lighting include: florescent high intensity open, or indirect. |
| --- | --- |

| Sliding Doors | Allowable adaptations for doors include: sliding kitchen and bathroom cabinet doors pedestrian sliding doors, or pocket doors. Note: If it is not possible to adapt existing cabinets with sliding doors, new cabinets with sliding doors are acceptable. |
| --- | --- |

| Handrails/ Grab Bars | Allowable adaptations for handrails and grab bars include the installation of handrails or grab bars for stability and safety in the bathroom area or any area that presents an unsafe condition to the veteran when maneuvering. Typical locations include the: interior walls walkways/sidewalks decks/patios steps toilets tubs, and showers. |
| --- | --- |

Continued on next page

Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less, Continued

| Smoke, Fire, and Carbon Monoxide Detectors | Smoke detectors, fire detection systems, and carbon monoxide detectors are allowable adaptations to the veteran’s home. |
| --- | --- |

| Security Items | The following security items are allowable adaptations: security systems the replacement of exterior doors with solid core doors deadbolt locks storm shutters an emergency exit (for example, a level 5-foot by 5-foot platform with a stairway and railings) an exterior to interior intercom system without a radio unit, and an interior home intercom system without a radio unit. Note: If the veteran chooses an intercom system with a radio, the veteran must pay the difference in cost. |
| --- | --- |

| Room Additions | Room additions to an existing home are allowable for the purpose of storing sensory aids or exercise equipment. In addition, the following adaptations are allowed: installation of a permanent heating/cooling system, and storage shelving. Reference: For information about the proposed construction requirements, see Chapter 10, Section E, “Special Housing Adaptations (SHA) Construction Plans.” |
| --- | --- |

Continued on next page

Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less, Continued

| Covered Porches | The following adaptations regarding porches are allowable: awnings over the front and/or rear doors in moderate climate regions the covering of an existing porch in regions of severe inclement weather, or the construction of a covered porch in regions of severe inclement weather. Note: The maximum porch size is 6 feet by 8 feet. |
| --- | --- |

| Concrete or Asphalt Walkways | Concrete or asphalt walkways, but not driveways, are allowable if the design is a new design with a minimum width of 4 feet. The installation of new curbs for an existing walkway is allowable. Note: The replacement of an existing walkway with the same design is a maintenance item and is unacceptable. |
| --- | --- |

| Fencing | The installation of fencing to overcome a hazard or safety concern is allowable. Example: The installation of a fence at a steep drop or adjoining a busy street. |
| --- | --- |

| Additional Electrical Service | Additional electrical switches, outlets, and service capacity to accommodate sensory aids equipment are allowable adaptations. |
| --- | --- |

Continued on next page

Allowable Adaptations for Blindness in Both Eyes with a 5/200 Visual Acuity or Less, Continued

| Swimming Pools | Swimming pools are acceptable. Note: Grant funds cannot be used for spas, hot tubs, saunas, etc. Exception: The installation of spas or variations of swimming pools are acceptable if hydrotherapy is a prescribed treatment for the veteran, and medically required. |
| --- | --- |

| Correction of a Safety Defect | Corrections to safety defects are allowable. Examples: The replacement of a space heater with a gas forced air furnace system. The replacement of a gas range and oven with an electric range and oven. |
| --- | --- |

#### Allowable Adaptations for Loss of or Loss of Use of Both Hands

| Introduction | This topic contains information about allowable adaptations for loss of or loss of use of both hands, including: the veteran’s freedom of choice, and allowable adaptations. |
| --- | --- |

| Freedom of Choice | It is not required that a veteran adapt a home with every allowable adaptation item. The veteran has the freedom of choice as to which adaptations he/she will complete with the Special Housing Adaptations (SHA) Grant Program. If the veteran wants to add any additional adaptation items that are not included in the allowable adaptations list, approval must first be received from Central Office (CO). |
| --- | --- |

| Allowable Adaptations | The following items are allowable adaptations for loss of or loss of use of both hands: lever-type water faucet fixtures in the kitchen or bathroom quad-rubber doorknob covers or lever-type latches/locks for doors the lowering of cabinets, countertops, and sinks toggle or press type light switches tap plates to open and close interior doors keyless entry-lock systems for exterior doors automatic garage door openers circuit breaker electrical control panel smoke detectors, fire detectors, and carbon monoxide detection systems special plumbing fixtures the replacement of single or double hung windows with crank-type windows, and the correction of safety defects. |
| --- | --- |

#### Allowable Adaptations for Secondary Disabilities

| Introduction | This topic contains information about allowable adaptations for secondary disabilities, including: the veteran’s freedom of choice a definition of the term ‘secondary disability’, and a list of the allowable adaptations. |
| --- | --- |

| Freedom of Choice | It is not required that the veteran adapt the home with every allowable adaptation item. The veteran has the freedom of choice as to which adaptations he/she will complete with the Special Housing Adaptations (SHA) Grant Program. If the veteran wants to add any additional adaptation items that are not included in the allowable adaptations list, approval must first be received from Central Office (CO). |
| --- | --- |

| Secondary Disabilities | A secondary disability is a disability that does not entitle a veteran to the SHA grant, whether service-connected or non-service-connected. |
| --- | --- |

| Allowable Adaptations for Secondary Disabilities | Adaptations to address a secondary disability are allowable if the condition is documented: by a Department of Veterans Affairs (VA) physician, and in the veteran’s file. Example: Ramping for a blind/wheelchair-bound veteran is allowable when blindness is service-connected, but the wheelchair condition is non-service connected. |
| --- | --- |

## Section B
Special Housing Adaptations (SHA) Existing Home Inspections

#### Overview

| Introduction | This section contains information about the Special Housing Adaptations (SHA) existing home inspection. |
| --- | --- |

| In this Section | This section includes the topic “Inspecting the Existing Home.” |
| --- | --- |

#### Inspecting the Existing Home

| Introduction | This topic contains information about inspecting the existing home, including: the purpose when to perform considerations of the veteran’s present and future needs considerations for secondary disabilities documenting the findings of the home inspection, and tasks related to the inspection. |
| --- | --- |

| Purpose | The purpose of inspecting an existing home is to document and identify, based upon the veteran’s disability, the necessary adaptations that should be installed. |
| --- | --- |

| When to Perform | Perform the inspection of the existing home: at the time of the initial interview with the veteran, or upon the veteran’s request. Note: The existing home inspection must occur prior to grant approval. |
| --- | --- |

| Considerations of the Veteran’s Present and Future Needs | When conducting an inspection of an existing home, be aware of the veteran’s present needs, as well as adaptations that may be needed to meet future needs and abilities. Some thought should be given to how the home will accommodate the veteran should his/her condition deteriorate. |
| --- | --- |

| Considerations for Secondary Disabilities | When conducting the inspection of an existing home, consideration must be given to adaptations needed for secondary disabilities. Reference: For more information about secondary disabilities, see Chapter 10, Section A, “Allowable Adaptations for Secondary Disabilities.” |
| --- | --- |

Continued on next page

Inspecting the Existing Home, Continued

| Documenting the Findings of the Home Inspection | Document the findings and recommendations from the home inspection on the SHA Allowable Adaptations/Site Review or a similar document. A copy of the findings and recommendations may be provided to the veteran. IMPORTANT: Clearly explain all observations and recommendations to the veteran, so that he/she has a clear understanding of the adaptations that are needed for the home. |
| --- | --- |

| How to Inspect the Existing Home | Complete the tasks in the table below to inspect the exiting home. |
| --- | --- |

| Task | Description |
| --- | --- |
| 1 | Document the necessary adaptations for the home on the SHA Allowable Adaptations/Site Review or a similar document. |
| 2 | Notify the veteran (by phone or letter) of the adaptations that are needed for the existing home, and explain that he/she must provide bids/proposals/contracts for the adaptations. Note: Although the Department of Veterans Affairs (VA) may not recommend a contractor, the Specially Adapted Housing (SAH) agent may provide the veteran with a list of VA-approved builders in that area. Reference: For more information about bids/proposals/contracts, see Chapter 10, Section D, “Special Housing Adaptations (SHA) Bids/Proposals/Contracts.” |
| 3 | Document the grant file by: making a copy of the letter, or including a report of the telephone conversation with the veteran. |

## Section C
Interviews with the Architect and/or Contractor

#### Overview

| Introduction | This section contains information about interviews with the architect and/or contractor. |
| --- | --- |

| In this Section | This section includes the topic “Interviewing the Architect and/or Contractor.” |
| --- | --- |

#### Interviewing the Architect and/or Contractor

| Introduction | This topic contains information about interviewing the architect and/or contractor, including: when to perform, and a reference. |
| --- | --- |

| When to Perform | In most Special Housing Adaptations (SHA) cases, it is not necessary to interview the architect and/or contractor. However, an interview may be necessary when the veteran is including a room addition. |
| --- | --- |

| Reference | For more information about interviewing the architect and/or contractor, see Chapter 9, Section D, “Interviews with the Architect and/or Contractor.” |
| --- | --- |

## Section D
Special Housing Adaptations (SHA) Bids/Proposals/Contracts

#### Overview

| Introduction | This section contains information about Special Housing Adaptations (SHA) construction plans and bids/proposals/contracts. |
| --- | --- |

| In this Section | This section includes the following topics: |
| --- | --- |

| Topic | Topic Name | See Page |
| --- | --- | --- |
| 1 | General Information About the Special Housing Adaptations (SHA) Construction Plans and Bids/Proposals/Contracts | 10-D-2 |
| 2 | Components of SHA Construction Bids/Proposals/ Contracts | 10-D-4 |
| 3 | Handling Changes after Bid/Proposal/Contract Approval | 10-D-5 |

#### General Information About the Special Housing Adaptations (SHA) Construction Plans and Bids/Proposals/Contracts

| Introduction | This topic contains information about the Special Housing Adaptation (SHA) construction plans and bids/proposals/contracts, including: determining the items (bids/proposals/contracts and/or required plans) to review the purpose of bids/proposals/contracts components of the bids/proposals/contracts to review amendments, and filing the bid/proposal/contract. |
| --- | --- |

| Determining the Items to Review | Use the table to determine the appropriate items to review based on the type of adaptations required for the project. |
| --- | --- |

| If the project involves … | Then … |
| --- | --- |
| non-extensive adaptations (for example: handrails, sidewalks, fencing, etc.) | review the bids/proposals/contracts. |
| a room addition | review the: bid/proposal/contract specifications description of materials, and required plans. Reference: For information about the required plans for SHA cases, see Chapter 10, Section E “Special Housing Adaptations (SHA) Construction Plans.” Note: The requirements for plans in SHA cases are the same as the requirements in Specially Adapted Housing (SAH) cases. |

Continued on next page

General Information About the Special Housing Adaptations (SHA) Construction Plans and Bids/Proposals/Contracts, Continued

| Purpose of Bids/Proposals/Contracts | The purpose of fixed bids/proposals/contracts is to: clearly state the scope of the work and the total cost protect the veteran against increases in labor and material and other influences ensure that the contractor completes the project in a timely manner, and protect the veteran from incurring additional costs above and beyond the original bid/proposal/contract. |
| --- | --- |

| Components of the Bid/Proposal/ Contract to Review | Review the fixed bid/proposal/contract for the following components: parties to the bid/proposal/contract terms and cost of the project an escape clause, and signatures and dates from all parties. Reference: For more information about the required components of the contract, see “Components of SHA Construction Bids/Proposals/Contracts” later in this section. |
| --- | --- |

| Filing the Bid/Proposal/ Contract | A copy of all bids/proposals/contracts, signed by all parties, must be retained in the grant file. |
| --- | --- |

#### Components of SHA Construction Bids/Proposals/Contracts

| Introduction | This topic contains information about the components of Special Housing Adaptations (SHA) construction bids/proposals/contracts, including the: parties to the bid/proposal/contract terms and cost of the project an escape clause, and signatures and dates from all parties. |
| --- | --- |

| Terms and Cost | The bid/proposal/contract must define the terms and the cost of the project so that they cannot be changed without amendments signed by all parties. |
| --- | --- |

| Escape Clause | The bid/proposal/contract must include an escape clause with the following statement, exactly as shown below: “This contract is conditioned in its entirety upon the veteran receiving a grant under Title 38 U.S.C. Chapter 21 and if this veteran does not receive this grant, this contract is null and void and any and all monies will be returned without exception.” |
| --- | --- |

#### Handling Changes after Bid/Proposal/Contract Approval

| Introduction | This topic contains information about handling changes after a bid/proposal/contract approval in a Special Housing Adaptations (SHA) case, including: the purpose when to perform, and requirements for authorization. |
| --- | --- |

| Purpose | The purpose of handling changes after a bid/proposal/contract approval in a SHA case is to ensure that the changes are acceptable. |
| --- | --- |

| When to Perform | Handle the changes to an approved bid/proposal/contract upon notification of changes to the bid/proposal/contract. |
| --- | --- |

| Requirements for Authorization | When handling changes to a bid/proposal/contract for non-extensive adaptations or proposed construction cases, the revised bid/proposal/contract must: clearly identify changes and any adjustment in the bid/proposal/contract amount, and be signed by the veteran and the contractor. Note: Copies of the approved changes, signed by all parties, to the bid/proposal/contract or plans must be retained in the grant file. |
| --- | --- |

## Section E
Special Housing Adaptations (SHA) Construction Plans

#### Overview

| Introduction | This section contains information about Special Housing Adaptations (SHA) construction plans, including: general information about SHA construction plans obtaining the SHA construction plans and required certifications VA Form 26-1852, Description of Materials plot and foundations plans floor and wall plans exterior and interior elevation plans, and handling changes after construction plan approval. |
| --- | --- |

| In this Section | This section includes the following topics: |
| --- | --- |

| Topic | Topic Name | See Page |
| --- | --- | --- |
| 1 | General Information About Special Housing Adaptations (SHA) Construction Plans | 10-E-2 |
| 2 | Obtaining the SHA Construction Plans and Required Certifications | 10-E-5 |
| 3 | VA Form 26-1852, Description of Materials | 10-E-6 |
| 4 | Plot and Foundation Plans | 10-E-7 |
| 5 | Floor and Wall Plans | 10-E-8 |
| 6 | Exterior and Interior Elevation Plans | 10-E-9 |
| 7 | Handling Changes after Construction Plan Approval | 10-E-10 |

#### General Information About Special Housing Adaptations (SHA) Construction Plans

| Introduction | This topic contains information about Special Housing Adaptations (SHA) construction plan requirements, including: an important note when plans are drawn number of copies recipients, and components of the plans. |
| --- | --- |

| IMPORTANT | Never assume that all parties know what is to be built and included, regardless of any verbal assurances. Unless specified in writing, work is not required to be completed or installed. Documentation is critical. |
| --- | --- |

| When Plans Are Drawn | The architect and/or contractor draws up a set of construction plans after: the Specially Adapted Housing (SAH) agent and the architect and/or contractor have discussed: how the Minimum Property Requirements (MPRs) will be met, and other planning considerations, and architect and/or contractor have gathered all the needed information. |
| --- | --- |

| Number of Copies | For cases involving new construction or room additions, four plan sets are required. If the veteran has a Department of Veterans Affairs (VA) home loan, a fifth set is required for VA. Exception: The fifth set of plans is not required for veterans with conventional home loans. |
| --- | --- |

Continued on next page

General Information About Special Housing Adaptations (SHA) Construction Plans, Continued

| Recipients | The following individuals should receive a copy of the plans: SAH agent contractor veteran, and VA-assigned Compliance Inspector (CI). Note: The SAH agent’s set of plans is filed in the grant file. Reference: For more information about the requirement for filing one set of plans in the grant file, see M26-9: “Quality Control Procedures, Loan Guaranty Operations.” |
| --- | --- |

| Components of the Plans | The table below lists the components required for proposed construction that need to be included when the architect and/or contractor draws up a set of construction plans. |
| --- | --- |

| Component | Reference |
| --- | --- |
| VA Form 26-1852, Description of Materials | See “VA Form 26-1852, Description of Materials” later in this section. |
| Plot plan | See “Plot and Foundation Plans” later in this section. |
| Foundation plan | See “Plot and Foundation Plans” later in this section. |
| Floor levels/floor plans | See “Floor and Wall Plans” later in this section. |
| Wall detail | See “Floor and Wall Plans” later in this section. |
| Interior/exterior elevations | See “Exterior and Interior Elevation Plans” later in this section. |
| Builder’s Certification of Plans, Specifications, and Site | See “Other Required SAH Exhibits and Certifications” in section 9-F-13. |

Continued on next page

General Information About Special Housing Adaptations (SHA) Construction Plans, Continued

| Components of the Plans (continued) | Notes: For remodeling cases, with a proposed addition, all items listed in the table are required. If only remodeling is involved with no room addition, in many cases the builder’s work statement is acceptable provided all adaptations to be completed are clearly defined. However, in some instances a floor plan layout, with dimensions of all rooms of the existing house must be submitted, along with another set showing the adaptations that are to be completed. |
| --- | --- |

| Changes to Plans and Specifications | The SAH agent must inform the veteran and contractor that changes to plans and specifications cannot be made without prior approval of the SAH agent. Reference: For information on handling changes after plan approval, see “Handling Changes after Construction Plan Approval” later in this section. |
| --- | --- |

#### Obtaining the SHA Construction Plans and Required Certifications

| Introduction | This topic contains information about obtaining the construction plans and required certifications, including: the purpose when to perform, and how to obtain construction plans and required certifications. |
| --- | --- |

| Purpose | The purpose of obtaining the construction plans and required certifications is to define the project. |
| --- | --- |

| When to Perform | Review the construction plans and required certifications upon receipt. |
| --- | --- |

| How to Obtain Construction Plans and Required Certifications | The table below lists the plans and certifications that need to be requested from the contractor for both proposed construction and remodeling cases. |
| --- | --- |

| Plan/Certifications | Case Type | Reference |
| --- | --- | --- |
| VA Form 26-1852 | Proposed and Remodeling | See “VA Form 26-1852, Description of Materials” later in this section. |
| Plot and Foundation plans | Proposed and Remodeling | See “Plot and Foundation Plans” later in this section. |
| Floor levels/floor plans | Proposed and Remodeling | See “Floor and Wall Plans” later in this section. |
| Wall detail | Proposed and Remodeling | See “Floor and Wall Plans” later in this section. |
| Exterior/interior elevations | Proposed and Remodeling | See “Exterior and Interior Elevation Plans” later in this section. |

IMPORTANT: See “Other Required SAH Exhibits and Certifications” in Chapter 9, Section F.

#### VA Form 26-1852, Description of Materials

| Introduction | This topic contains information about VA Form 26-1852 formats. |
| --- | --- |

| Formats | Specially Adapted Housing (SAH) agents use VA Form 26-1852 (HUD Form 920005) to document the description of materials. VA Form 26-1852 must be fully completed and have the original signatures of the veteran and the contractor on the form filed in the grant folder. Other specification formats are acceptable, provided that they are signed and dated by the contractor and veteran as described above, and are specifically detailed for Special Housing Adaptations (SHA) appraisal, and compliance inspection purposes. |
| --- | --- |

#### Plot and Foundation Plans

| Introduction | This topic contains information about the plot and foundation plans, including: plot plan requirements sea level heights, and foundation plan requirements. |
| --- | --- |

| Plot Plan Requirements | A plot plan should illustrate where the following items will be located: the proposed house or addition setbacks, and easements (building and utility). |
| --- | --- |

| Sea Level Heights | It is preferable that the plot plan show the sea level heights of the finished grade at the: foundation top of the foundation, and four corners of the site. |
| --- | --- |

| Foundation Plan Requirements | Foundation plans should include the dimensions and materials used for: footings walls tie-in of existing walls and foundations to new walls and foundations, and support piers. |
| --- | --- |

#### Floor and Wall Plans

| Introduction | This topic contains information about the floor and wall plans. |
| --- | --- |

| Floor Plan Requirements | Floor plans must illustrate the design and layout. |
| --- | --- |

| Wall Plan Requirements | Sectional wall detail must show all components from the foundation footing upward to the roof ridge. |
| --- | --- |

#### Exterior and Interior Elevation Plans

| Introduction | This topic contains information about exterior and interior elevation. |
| --- | --- |

| Exterior Elevation Requirements | For proposed construction, exterior elevations on all four sides of the house should be shown. For a room addition, exterior elevations on the three new sides of a room addition should be shown. |
| --- | --- |

| Interior Elevation Requirements | Interior elevations must show the height of cabinets, grab bars, fixtures, and other features necessary to accommodate the veteran’s disability. |
| --- | --- |

#### Handling Changes after Construction Plan Approval

| Introduction | This topic contains information about handling changes after construction plan approval, including: the purpose when to perform requirements to authorize changes, and how to handle changes after plan approval. |
| --- | --- |

| Purpose | The purpose of this procedure is to ensure that the changes are acceptable. |
| --- | --- |

| When to Perform | Perform this procedure upon notification of changes to the construction plans and specifications. |
| --- | --- |

| Requirements to Authorize Changes | Changes can only be authorized: upon receipt of: VA Form 26-1844, Request for Acceptance of Changes in Approved Drawings and Specifications specifically itemizing the changes, cost of changes, and signed by the veteran, contractor, and lender (if applicable), or written notification specifically itemizing the changes, costs of changes, and signed by the veteran, contractor, and lender (if applicable), and if no Minimum Property Requirements (MPRs) are changed. Note: Copies of the changes, whether approved or denied, must be retained in the grant file. |
| --- | --- |

Continued on next page

Handling Changes after Construction Plan Approval, Continued

| How to Handle Changes after Plan Approval | To handle changes after plan approval: accept or deny the changes by signing: VA Form 26-1844 indicating the decision, or the change order request and indicating acceptance or denial, and notify the following individuals of the findings: contractor veteran lender (if applicable), and Department of Veterans Affairs (VA)-assigned Compliance Inspector (CI). IMPORTANT: Any adjustment in value of 5 percent or more requires a staff field review. The Specially Adapted Housing (SAH) agent can approve any adjustment up to 5 percent, otherwise the Valuation Officer, or designee, must countersign approval. |
| --- | --- |

## Section F
Special Housing Adaptations (SHA) Inspection Schedules and Assignment of a Department of Veterans Affairs (VA) Compliance Inspector

#### Overview

| Introduction | This section contains information about the inspection schedule and assignment of a Department of Veterans Affairs (VA) Compliance Inspector, including: general information about inspection schedules, and assigning the VA Compliance Inspector. |
| --- | --- |

| In this Section | This section includes the following topics: |
| --- | --- |

| Topic | Topic Name | See Page |
| --- | --- | --- |
| 1 | General Information About Inspection Schedules | 10-F-2 |
| 2 | Assigning the Department of Veterans Affairs (VA) Compliance Inspector | 10-F-4 |

#### General Information About Inspection Schedules

| Introduction | This topic contains information about creating the inspection schedule, including: the purpose when to perform a description of standard number of inspections, and how to determine the number of required inspections. |
| --- | --- |

| Purpose | The purpose of creating the inspection schedule is to notify the Department of Veterans Affairs (VA) Compliance Inspector (CI) of the number of inspections required for a project. |
| --- | --- |

| When to Perform | Create the inspection schedule before construction starts. |
| --- | --- |

| Description of the Minimum Number of Inspections | The minimum number of inspections for proposed construction, including room additions, is three. The three inspections are: first inspection where the foundations walls are complete and ready for backfill second inspection when the building is enclosed, including rough-ins (electrical, heating, and plumbing) third inspection when the building and landscape is complete. Note: The number of inspections may increase depending on the project. If more than five inspections are planned, consult Central Office (CO). |
| --- | --- |

Continued on next page

General Information About Inspection Schedules, Continued

| How to Determine the Number of Required Inspections | Use the table below to determine the number of required VA compliance inspections. |
| --- | --- |

| If the case involves … | Then the number of required VA compliance inspections is … |
| --- | --- |
| proposed construction | a minimum of 3. |
| remodeling job that includes an addition | a minimum of 3. |
| remodeling job that does not include an addition | 3 or less depending on the complexity of the project. |

#### Assigning the Department of Veterans Affairs (VA) Compliance Inspector

| Introduction | This topic contains information about assigning the Department of Veterans Affairs (VA) Compliance Inspector (CI), including: the selection of the VA CI the SAH/TAS Letter #16 (FL 26-638), Inspector Assignment Letter documents sent with the SAH/TAS Letter #16 (FL 26-638) when the assigned VA CI is unavailable areas without a VA CI, and payment vouchers. |
| --- | --- |

| Selection of the VA Compliance Inspector | Select the VA CI from Specially Adapted Housing (SAH)/The Appraisal System (TAS). |
| --- | --- |

| The SAH/TAS Letter #16 (FL 26-638), Inspector Assignment Letter | The SAH/TAS Letter #16 (FL 26-638), Inspector Assignment Letter): is used to assign the VA CI, and includes important information, such as the: amount to be paid for the inspections number of inspections location of the property name of the veteran, and voucher with an obligation number. Note: The obligation number is assigned in accordance with Regional Loan Center (RLC) procedures. |
| --- | --- |

| Documents Sent With SAH/TAS Letter #16 (FL 26-638) | The following documents are sent with SAH/TAS Letter #16 (FL 26-638) as applicable: the contract the approved plans, and the specifications. |
| --- | --- |

Continued on next page

Assigning the Department of Veterans Affairs (VA) Compliance Inspector, Continued

| When the Assigned VA Approved Compliance Inspector Is Unavailable | If a VA CI has been assigned, but is unavailable at the time of request for the inspection, the following individuals may conduct the inspection: another VA CI the SAH agent, or other qualified VA personnel. IMPORTANT: Compliance inspections must be performed by a designated fee compliance inspector. Compliance inspections may be made by qualified salaried personnel only when designated fee compliance inspectors are not immediately available. The LGO must approve each case where the SAH agent, or other qualified salaried personnel, is assigned to perform compliance inspections. The LGO must also notify, via e-mail, the Chief of Specially Adapted Housing, Central Office, for each such action. |
| --- | --- |

| Areas Without VA Compliance Inspectors | In areas without VA CIs, any qualified, salaried personnel may perform compliance inspections. Requirements: The Loan Guaranty Officer (LGO) must approve the use of a contracted inspector for a project. The SAH agent must document the grant file or obtain evidence documenting the need for assignment of the inspector on the project. |
| --- | --- |

| Payment Vouchers | Upon receipt of a completed voucher from the CI, the voucher is: certified by a LGO-designated individual, and processed for payment through finance activity. |
| --- | --- |