WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A13576 | In-Flight Anomaly Number -- | Contractor Report Number E-145 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title GO2 ULLAGE PRESSURE TRANSDUCER FAILED CALIBRATION TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE GO2 ULL PRES TRNSDCR | PART# PD7400098-079 | SER/LOT# 1869 | MANUFACTURER GULTON-SERV |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode UC - UNSAT | Cause D - DESIGN |
| System ELECTRICAL | Defect MW - MISWIR | Material A - CIRC T | Work Contact J. ADAMS | Fail Date 10/29/1990 |
| Received at MSFC 03/08/1991 | Date Isolated 03/04/1991 | FMEA Reference 3.2.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON-SER | Symptom EG - SIG HI OR LO | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary OCCASIONAL FAILURES EXPECTED; FAILURE RATE IS ACCEPTABLY LOW |
| Last MSFC Update 05/07/1992 | CN RSLV SBMT 03/04/1991 | Defer Date -- | Add Date 03/12/1991 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 03/21/1991 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID MARS T-34408 |
| Related Document Title MARTIN ANOMALY REPORTING SYSTEM |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CLOSED AT CONTRACTOR |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE PRESSURE TRANSDUCER FAILED A TEST OF CALIBRATION ACCURACY DURING VENDOR ACCEPTANCE TESTING CRITICALITY: THE TRANSDUCER IS CRIT. 1R; FMEA ITEM CODE 3.2.1.2; "FAILS WITH LOW READING." NOTE: THE TRANSDUCERS ARE LIMITED LIFE CONTROLLED GENERAL: THE TRANSDUCER FAILED TESTS OF THE ACCURACY OF THE OUTPUT VOLTAGE VERSUS THE APPLIED PRESSURE. AT BOTH +40 DEGREES F. AND +140 DEGREES F. THE OUTPUT VOLTAGE WAS LOWER THAN THE MINIMUM ACCEPTABLE VALUE. THE WORST CASE WAS AN OUTPUT OF 3.439 VDC AT 21 PSID AND +140 DEGREES F.; THE MINIMUM ACCEPTABLE VALUE IS 3.450 VDC. THE TEST REQUIREMENTS ARE CONTAINED IN GULTON ACCEPTANCE TEST PLAN 3061-0000-81, PARAGRAPH 5.5 |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence TASK I. FAILURE INVESTIGATION THE FAILURE WAS DOCUMENTED ON MARS T-34408. NO FAILURE ANALYSIS WAS WARRANTED. THE TRANSDUCER FAILED TO MEET THE ALLOWABLE ERROR BAND BY 11 MILLIVOLTS. THE 11 MILLIVOLTS IS EQUIVALENT TO 0.2% OF FULL SCALE. THE ALLOWABLE ERROR IS +/- 1% OF FULL SCALE. THE RESOLUTION OF THE TRANSDUCER IS APPROXIMATELY 10 MILLIVOLTS AS THE UNIT OPERATES AT 5 VOLTS INPUT AND THERE ARE APPROXIMATELY 500 TURNS IN THE WIREWOUND RESISTIVE ELEMENT OF THE POTENTIOMETER. THE 11 MILLIVOLTS ERROR IS EQUIVALENT TO A POSITIONAL ERROR OF THE TRANSDUCER INTERNAL ANEROID PRESSURE CAPSULES OF 100 MICROINCHES. NO ANALYSIS WAS POSSIBLE TASK CLOSED TASK II. CORRECTIVE ACTION A. NO CORRECTIVE ACTION IS REQUIRED. OCCASIONAL VENDOR ATP FAILURES DUE TO SMALL CALIBRATION ERRORS ARE EXPECTED DUE TO THE CHARACTERISTICS OF THE DESIGN. THE FAILURE RATE IS ACCEPTABLY LOW B. A DELAY OCCURRED IN THE INITIATION OF THIS CAPS DUE TO A COMMUNICATION BREAKDOWN BETWEEN MMC PROCUREMENT QUALITY, DEPT. 3977, AND MMC RELIABILITY ASSURANCE, DEPT. 3741. PROCUREMENT QUALITY OPERATING INSTRUCTION NO. 1.2 WAS REVISED FEBRUARY 14, 1991, TO PROVIDE MORE EFFECTIVE MEANS OF COMMUNICATION BETWEEN THE DEPARTMENTS INVOLVED TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ETS CLEARED. ALL INSTALLED TRANSDUCERS HAVE SUCCESSFULLY PASSED THE VENDOR ACCEPTANCE TEST TASK CLOSED TASK IV. CLOSURE SUMMARY THE TRANSDUCER FAILED TWO CALIBRATION TEST SEGMENTS OF THE VENDOR ACCEPTANCE TEST. THE ERROR WAS SMALL. OCCASIONAL FAILURES OF THIS TYPE ARE EXPECTED. THE FAILURE RATE IS ACCEPTABLY LOW. NO CORRECTIVE ACTION IS REQUIRED THE PROBLEM REPORTING METHOD BETWEEN MMC PROCUREMENT QUALITY AND MMC RELIABILITY ASSURANCE WAS REVISED SO AS TO PREVENT DELAYS IN THE FUTURE TASK CLOSED PAC NOTE: PROBLEM REPORT WAS CLOSED BY PRB ON 3/21/91 |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A13576 | IFA# -- | Contractor RPT# E-145 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-079 | Asmnt Part Name GO2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 1869 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD D - DESIGN | FAIL MODE UC - UNSAT |
| Asmnt FMEA 3.2.1.2 | Asmnt FM 2 | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |