THE DUE DATE FOR QUESTIONS TO THE SUBJECT RFQ IS EXTENDED FROM JUNE 24, 2002 TO JUNE 28, 2002.

# Questions 6/22/02 THRU 6/25/02

# REAL TIME DYNAMIC DATA ACQUISITION SYSTEM

# RFQ3-201356

Q1.  Are there any programming language preferences?

A1.	No.

Q2.  After acquisition do the displays need to be updated real time?

A2.	Yes.

Q3.  Can signal processing be done off-line or does it need to be done in real time?

A3.	Real time and post-processing are required.

Q4.  What format are you looking to store data?  Text, binary, or ASCII?

A4.	At least binary and ASCII.

Q5.  What is the meaning of an integral user interface? Please give an example of a non integral UI.

A5.	An integral user interface means the displays for monitoring the time history and processed data are an integral part of the host computer.  An example of a non-integral user interface: the data system acquisition hardware is separate from the GUI computer.

Q6.  What is meaning of system checkout? How will the system be validated?

A6.	System checkout is the process of verifying that the delivered hardware and software perform to the specifications.  The system will be checked out using signal generators.

Q7.	Will monitoring need any analog or digital outputs on DAQ board, say for control purpose?

A7.	No.

Q8.	Is it expected that each channel should be configurable for different signal inputs (on the fly?) without resetting the DAQ board? Normally during any given test run, a channel is dedicated for one type of input signal. Please explain.

A8.	Yes. Each channel should be software configurable for different input signals.

Q9.	Normally circular buffering caters for most requirements of real time data display - could you be more specific on event planning requirements

A9.	At times we need to capture a pre-trigger and a post-trigger history of events.

Q10.	Do all of the required Real-time Interactive plots need to run at the same time?

A10.	No, the user shall select the ones to run and only needs to interact with one interactive plot at a time.

Q11.  We are assuming that "IRIG code" is IRIG-B.  Is this correct?

A11. 	Yes, IRIG-B is correct..

Q12.	 Can you be more restrictive with the statement "Licensing of the software shall permit unlimited reproduction of the software for distribution with the data produced by the system to NASA personnel and others for post-test analysis".

A12.	The quoted sentence applies only to the software that is used to view the data.