DEPARTMENT OF HOUSING AND URBAN DEVELOPMENT 	STRUCTURAL ENGINEERING

## Housing - Federal Housing Commissioner 	BULLETIN NO.

# TO: 	DIRECTORS, SINGLE FAMILY HOCs 	ISSUE DATE

# DIRECTORS, MULTIFAMILY HUBs

#### REVIEW DATE

##### SUBJECT: 	1.	 Item Description

- Name and address

of Manufacturer

This Structural Engineering Bulletin (SEB) should be filed with other SEBs and related Bulletins on materials or products as required by prescribed procedures.

1.	General:

This Bulletin sets forth specific requirements under the Technical Suitability of Products Program for determining the eligibility of housing to be constructed under HUD mortgage insurance, or other HUD housing programs.

2.	Scope:

This Bulletin applies only to the structural features of this method of construction.  Final determination of eligibility is made by the appropriate HUD Field Office. Other factors considered will be valuation, location, architectural planning and appeal, mechanical equipment, thermal characteristics, and market acceptance.  Consideration is also necessary to determine whether a specific property will qualify under the specific HUD program, when constructed according to the method outlined in this Bulletin, and where the structure is to be located.

-2-

3.	Minimum Property Standards (MPS):

Compliance with HUD MPS will be determined by the HUD Field Office or Homeownership Center on the same basis as the submissions involving conventional construction, except for the special features described in this bulletin.

4.	Inspection:

Field compliance inspections covering conventional items of construction and any special features covered in this bulletin shall be made in accordance with prescribed procedures.

The appropriate HUD Field Office or Homeownership Center shall furnish a copy of a HUD field inspection report to Headquarters, Office of Manufactured Housing Programs, when there is:

a.  Evidence of non-compliance with any portion of the system of construction described in this bulletin.

b.	Faulty shop fabrication, including significant surface defects.

c.	Damage to shop fabricated items or materials due to improper transportation, storage, handling, or assembly.

d.	Unsatisfactory field workmanship or performance of the product or system.

e.	Any significant degradation or deterioration of the product or evidence of lack of durability or performance.

Periodic plant inspections will be made by HUD Field Office, Homeownership Center, or a HUD designated representative in accordance with their prescribed procedures.  Factory inspection reports shall be submitted to HUD Headquarters, upon request.

5.	Certification:

The manufacturer named in this bulletin shall furnish the builder with written certification that the product has been manufactured in compliance with the HUD Minimum Property Standards (MPS), except as modified by this bulletin.  The builder shall endorse the certification with a statement that the product has been installed in compliance with HUD MPS, except as modified by this bulletin, and that the manufacturer’s certification does not relieve the builder, in any way, of responsibility under the terms of the Builder’s Warranty required by the National Housing Act, or under any provisions applicable to any other housing program.  This certification shall be furnished to the HUD Field Office upon completion of the property.

-3-

OUTLINE DESCRIPTION, CATEGORY II CONSTRUCTION

GENERAL

This bulletin provides for the use of all TJI Prefabricated Wood I-Joists, manufactured by Trus Joist for floor and roof spans up to 46 feet.

PRODUCT DESCRIPTION

TJI joists are prefabricated wood I-joists having wood-based flanges and proprietary oriented strand board (OSB) webs.  Either the top and bottom flanges are parallel, forming a constant-depth joist; or the top flange has a single taper, forming a variable-depth joist.  The web panels have the face grain oriented vertically and the web-to-web connection is either butt jointed or serrated and glued to form a continuous web.  The web-to-flange connection is a proprietary tongue-and-groove joint.  Refer to Table 1 for TJI joist series and material descriptions.

Flange material is either MicrollamR laminated veneer lumber (LVL) or TimberStrandR laminated strand lumber (LSL), which has been qualified as flange stock material and meets the requirements noted in the approved quality control manual that contains Trus Joist manufacturing standards.  Table 1 specifies flange widths and depths. Flange material and grades are as specified in the approved quality control manual that contains Trus Joist manufacturing standards.

Web material is Performance PlusR OSB conforming to DOC Voluntary Product Standard PS 2-92, Exposure 1, along with further requirements set forth in the approved quality control manual that contains Trus Joist manufacturing standards. Web material thickness requirements are noted in Table 1.

Adhesives shall be of the types specified in the approved quality control manual that contains Trus Joist manufacturing standards.

TJI Joists are produced in a continuous fabrication process, and are cut to the desired length after fabrication.

DESIGN AND INSTALLATION

The design and installation of TJI joists shall comply with the requirements of this bulletin.  Design of TJI joists is governed by the applicable code and ANSI/AF&PA NDS-97 National Design Specification for Wood Construction (NDS).

-4-

ALLOWABLE CAPACITY

Table 2 specifies allowable moments, reactions, shears, and joist stiffness (EI).  Maximum allowable reactions are based on minimum and maximum bearing lengths of 1-3/4 inches, 2-1/2 inches and 3-1/2 inches at end supports; and 3-1/2, 5-1/4 and 7 inches at intermediate supports of continuous spans.  When joists are used as multiple span members, the calculated shear used for design at the intermediate support may be reduced by the percentage determined from the following formula and limited to the depths shown in the table that appears after the formula:

R =  W ÷ K ≤ 18%

where:

K	=	V12 ( 100.

R	=	The percent reduction.

V12	=	The allowable shear for a 12-inch or 11 7/8-inch deep joist (pounds).

W	=	The uniform load (plf).

| TJI JOIST SERIES | TJI JOIST DEPTH (inches) | V12 | K |
| --- | --- | --- | --- |
| TJI 110 | ≤ 14 | 1,560 | 15.60 |
| TJI 210, TJI 230 | ≤ 16 | 1,655 | 16.55 |
| TJI 360 | ≤ 16 | 1,705 | 17.05 |
| TJI 560 | ≤ 20 | 2,050 | 20.50 |
| TJI/L45 | ≤ 16 | 1,420 | 14.20 |
| TJI/L65, TJI/L90, TJI/H90 | ≤ 24 | 1,925 | 19.25 |
| TJI/HD90, TJI/HS90 | ≤ 24 | 2,320 | 23.20 |

For other joist depths, the design shear is the calculated shear at the interior face of support.

The allowable design shear at the interior supports of multiple-span-member TJI joists up to 12 inches deep, used in residential floor construction is permitted to be increased an additional 10 percent.  This increase of allowable design shear does not apply to the design shear at the ends of the joists.

FASTENERS

Allowable capacities and spacing of nails in MicrollamR LVL and TimberStrandR LSL flanges shall comply with this bulletin and the applicable code.  Nails installed perpendicular to the glue lines or strands on the wide face shall be installed in accordance with the applicable code.

The lateral nail capacity and nail withdrawal of nails installed on the wide face perpendicular to the glue lines of MicrollamR LVL or strands of TimberStrandR LSL flanges shall be as provided in the applicable code for Douglas fir-larch (minimum specific gravity SG = 0.50).

WEB STIFFENERS

Table 2 and Figure 1 show web stiffener requirements for reactions and concentrated loads.

-5-

LATERAL SUPPORT

TJI joist compression flanges with widths less than 2.30 inches require lateral support every 18 inches on center.  TJI joist compression flanges with widths equal to or greater than 2.30 inches require lateral support every 24 inches on center.  Each connection shall be capable of transmitting a 75-pound horizontal load.  All TJI joist ends require restraint to prevent rollover.  Code-approved methods of lateral restraint specified for sawn lumber are acceptable.  Bridging is not required for TJI joist floor and roof applications.

HOLES IN TJI JOIST WEB

The tables in Figures 2 and 3 specify allowable sizes and location of round, square, and rectangular holes in the TJI joist webs.

DURATION OF LOAD

Adjustments for duration of load, as permitted by the applicable code, apply to the TJI joists and their fastenings.

IN-SERVICE MOISTURE CONDITIONS

TJI joist properties and allowable loads in this bulletin are limited to covered installations with dry conditions of use.  Dry conditions of use are those environmental conditions represented by sawn lumber in which the moisture content is less than 16 percent.

REPETITIVE-MEMBER USE

The repetitive-member use factor applicable to the resistive moment capacities listed in Table 2 is 1.0.

MEMBER SPANS

The span of TJI joists shall be taken as distance from face to face of supports, plus one-half the required bearing length at each end, except that for cantilever and continuous spans, the span shall be taken as the distance between centers of bearings on supports over which the joist is continuous.

DEFLECTION

Deflection of simple span TJI joists with either uniform load or a concentrated load at midspan is determined using the formulas in the footnotes to Table 2.

-6-

BLOCKING PANELS

Bearing walls perpendicular to and supported by TJI joists at the end or intermediate supports, or both, require full-depth blocking.  TJI joists up to 16 inches in depth, when used as blocking panels, have a maximum vertical load transfer capacity of 2,100 plf. TJI joists over 16 inches and up to 20 inches in depth, when used as blocking panels, have a minimum vertical load transfer capacity of 1,550 plf.

TJI RIM JOISTS

TJI joists used as rim joists, having depths of up to 16 inches have a maximum vertical load transfer capacity of 2,100 plf.  TJI joists used as rim joists, having depths of up to 16 inches, are permitted to be used as boundary members of horizontal wood structural diaphragms.  The allowable shear values in pounds per foot specified in the code for horizontal wood structural panel diaphragms with framing of nominal 2-inch thick Douglas fir-larch or southern pine are applicable to TJI joists used as rim joists, in unblocked and blocked diaphragm applications.  The TJI joists used as rim joists shall be laterally supported at the top and continuously supported at the bottom, and the gravity loads shall be uniformly applied along the top.  Other loading or support conditions shall be investigated and approved by the design professional.

CANTILEVERED TJI JOISTS

TJI joists are permitted to be installed with cantilevers, provided the cantilevers have a maximum length equal to one-third of the adjacent span and support uniform loads only.  Otherwise cantilever applications require design by a design professional.

TABLE 1 –TJI JOIST DESCRIPTION

| TJI Joist Series | Flange Size Depth x Width (inches) | Web Thickness (inches) | Range of Joist Depths (inches) |
| --- | --- | --- | --- |
| TJI® 110 | 1.375 x 1.75 | 3/8 | 9 1/2 - 14 |
| TJI® 210 | 1.375 x 2.08 | 3/8 | 9 1/2 - 16 |
| TJI® 230 | 1.375 x 2.3 | 3/8 | 9 1/2 - 16 |
| TJI® 360 | 1.375 x 2.3 | 3/8 | 9 1/2 - 20 |
| TJI® 560 | 1.375 x 3.5 | 7/16 | 9 1/2 - 20 |
| TJI®/L45 | 1.5 x 1.75 | 3/8 | 8 - 20 Taper only |
| TJI®/L65 | 1.5 x 2.5 | 7/16 | 9 1/2 - 30 (9 1/2 - 30 Taper) |
| TJI®/L90 | 1.5 x 3.5 | 7/16 | 11 7/8 - 30 (9 1/2 – 30 Taper) |
| TJI®/H90 | 1.75 x 3.5 | 7/16 | 11 7/8 - 30 |
| TJI®/HD90 | 2.125 x 3.5 | 1/2 | 11 7//8 - 32 |
| TJI®/HS90 | 2.5 x 3.5 | 1/2 | 11 7/8 - 32 |

-7-

| TABLE 2 – PROPERTIES FOR TJI JOISTS |
| --- |
| BASIC PROPERTIES | REACTION PROPERTIES |
| Joist Depth (in.) | Joist Weight (plf) | Resistive Moment (ft.-lbs.) (10) | Vert. Shear (lbs.) | EI x 106 lbs.-in.2 | K | END REACTION (lbs.) | INTERMEDIATE REACTION (lbs.) |
|  |  |  |  |  |  | 1-3/4” | 3-1/2” | Nails Req’d. | 3-1/2” | 5-1/4” | Nails Req’d |
|  |  |  |  |  |  | 2-1/2” (9) |  |  | 5-1/4” (7) | 7” (7) |  |
|  |  |  |  |  |  | Bearing Length | Bearing Length |  | Bearing Length | Bearing Length |  |
|  |  |  |  |  |  | Web Stiffeners | Web Stiffeners |  | Web Stiffeners | Web Stiffeners |  |
|  |  |  |  |  |  | NO | YES | NO | YES |  | NO | YES | NO | YES |  |
| TJI 110 |
| 9-1/2 | 2.3 | 2380 | 1220 | 140 | 4.5 | 885 | NA | 1220 | NA | NA | 1935 | NA | 2350 | NA | NA |
| 11-7/8 | 2.5 | 3015 | 1560 | 238 | 4.5 | 885 | 1225 | 1350 | 1560 | 3-8d | 1935 | 2295 | 2350 | 2705 | 3-8d |
| 14 | 2.8 | 3565 | 1860 | 351 | 4.5 | 885 | 1225 | 1350 | 1705 | 3-8d | 1935 | 2295 | 2350 | 2705 | 3-8d |
| TJI 210 |
| 9-1/2 | 2.6 | 2860 | 1330 | 167 | 4.5 | 980 | NA | 1330 | NA | NA | 2145 | NA | 2565 | NA | NA |
| 11-7/8 | 2.8 | 3620 | 1655 | 283 | 4.5 | 980 | 1340 | 1435 | 1655 | 3-8d | 2145 | 2505 | 2565 | 2925 | 3-8d |
| 14 | 3.1 | 4280 | 1945 | 415 | 4.5 | 980 | 1340 | 1435 | 1790 | 3-8d | 2145 | 2505 | 2565 | 2925 | 3-8d |
| 16 | 3.3 | 4895 | 2190 | 566 | 4.5 | 980 | 1340 | 1435 | 1790 | 3-8d | 2145 | 2505 | 2565 | 2925 | 3-8d |
| TJI 230 |
| 9-1/2 | 2.7 | 3175 | 1330 | 183 | 4.5 | 1035 | NA | 1330 | NA | NA | 2410 | NA | 2790 | NA | NA |
| 11-7/8 | 3.0 | 4015 | 1655 | 310 | 4.5 | 1035 | 1395 | 1460 | 1655 | 3-8d | 2410 | 2765 | 2790 | 3150 | 3-8d |
| 14 | 3.3 | 4755 | 1945 | 454 | 4.5 | 1035 | 1395 | 1460 | 1815 | 3-8d | 2410 | 2765 | 2790 | 3150 | 3-8d |
| 16 | 3.5 | 5440 | 2190 | 618 | 4.5 | 1035 | 1395 | 1460 | 1815 | 3-8d | 2410 | 2765 | 2790 | 3150 | 3-8d |
| TJI 360 |
| 9-1/2 | 2.7 | 4790 | 1425 | 249 | 4.5 | 1080 | NA | 1425 | NA | NA | 2460 | NA | 3000 | NA | NA |
| 11-7/8 | 3.0 | 6180 | 1705 | 419 | 4.5 | 1080 | 1440 | 1505 | 1705 | 3-8d | 2460 | 2815 | 3000 | 3360 | 3-8d |
| 14 | 3.3 | 7335 | 1955 | 612 | 4.5 | 1080 | 1440 | 1505 | 1865 | 3-8d | 2460 | 2815 | 3000 | 3360 | 3-8d |
| 16 | 3.5 | 8405 | 2190 | 830 | 4.5 | 1080 | 1440 | 1505 | 1865 | 3-8d | 2460 | 2815 | 3000 | 3360 | 3-8d |
| 18 | 3.7 | 9465 | 2425 | 1085 | 4.5 | 1080 | 1440 | 1505 | 1865 | 3-8d | 2460 | 2815 | 3000 | 3360 | 3-8d |
| 20 | 4.0 | 10515 | 2660 | 1376 | 4.5 | 1080 | 1440 | 1505 | 1865 | 3-8d | 2460 | 2815 | 3000 | 3360 | 3-8d |
| TJI 560 |
| 9-1/2 | 3.6 | 7355 | 1670 | 378 | 5.3 | 1265 | NA | 1670 | NA | NA | 3000 | NA | 3455 | NA | NA |
| 11-7/8 | 4.0 | 9500 | 2050 | 636 | 5.3 | 1265 | 1740 | 1725 | 2050 | 3-16d | 3000 | 3475 | 3455 | 3930 | 3-16d |
| 14 | 4.2 | 11275 | 2390 | 926 | 5.3 | 1265 | 1740 | 1725 | 2200 | 3-16d | 3000 | 3475 | 3455 | 3930 | 3-16d |
| 16 | 4.5 | 12925 | 2710 | 1252 | 5.3 | 1265 | 1740 | 1725 | 2200 | 3-16d | 3000 | 3475 | 3455 | 3930 | 3-16d |
| 18 | 4.8 | 14550 | 3030 | 1631 | 5.3 | 1265 | 1740 | 1725 | 2200 | 3-16d | 3000 | 3475 | 3455 | 3930 | 3-16d |
| 20 | 5.1 | 16165 | 3345 | 2064 | 5.3 | 1265 | 1740 | 1725 | 2200 | 3-16d | 3000 | 3475 | 3455 | 3930 | 3-16d |
| TJI/L45 |
| 7-1/2 | 2.0 | 2720 | 860 | 103 | 4.5 | 860 | NA | 860 | NA | NA | 2025 | NA | 2025 | NA | NA |
| 9-1/2 | 2.2 | 3620 | 1120 | 185 | 4.5 | 1015 | NA | 1120 | NA | NA | 2025 | NA | 2575 | NA | NA |
| 11-7/8 | 2.5 | 4685 | 1420 | 319 | 4.5 | 1015 | 1225 | 1420 | 1420 | 3-8d | 2025 | 2385 | 2575 | 2930 | 3-8d |
| 14 | 2.8 | 5570 | 1710 | 474 | 4.5 | 1015 | 1225 | 1560 | 1710 | 3-8d | 2025 | 2385 | 2575 | 2930 | 3-8d |
| 16 | 3.0 | 6385 | 1970 | 653 | 4.5 | 1015 | 1225 | 1560 | 1915 | 3-8d | 2025 | 2385 | 2575 | 2930 | 3-8d |
| 18 | 3.2 | 7200 | 2155 | 865 | 4.5 | 1015 | 1225 | 1560 | 1915 | 3-8d | 2025 | 2385 | 2575 | 2930 | 3-8d |
| 20 | 3.5 | 8000 | 2165 | 1113 | 4.5 | 1015 | 1225 | 1560 | 1915 | 3-8d | 2025 | 2385 | 2575 | 2930 | 3-8d |

See notes at the end of the table.

-8-

| TABLE 2 – CONTINUED |
| --- |
| BASIC PROPERTIES | REACTION PROPERTIES |
| Joist Depth (in.) | Joist Weight (plf) | Resistive Moment (ft.-lbs.) (10) | Vert. Shear (lbs.) | EI x 106 lbs.-in.2 | K | END REACTION (lbs.) | INTERMEDIATE REACTION (lbs.) |
|  |  |  |  |  |  | 1-3/4” | 3-1/2” | Nails Req’d. | 3-1/2” | 5-1/4” | Nails Req’d |
|  |  |  |  |  |  | 2-1/2” (9) |  |  | 5-1/4” (7) | 7” (7) |  |
|  |  |  |  |  |  | Bearing Length | Bearing Length |  | Bearing Length | Bearing Length |  |
|  |  |  |  |  |  | Web Stiffeners | Web Stiffeners |  | Web Stiffeners | Web Stiffeners |  |
|  |  |  |  |  |  | NO | YES | NO | YES |  | NO | YES | NO | YES |  |
| TJI/L65 |
| 9-1/2 | 3.0 | 5215 | 1675 | 263 | 5.3 | 1375 | NA | 1675 | NA | NA | 2745 | NA | 3365 | NA | NA |
| 11-7/8 | 3.3 | 6750 | 1925 | 450 | 5.3 | 1375 | 1745 | 1885 | 1925 | 3-8d | 2745 | 3120 | 3365 | 3735 | 3-8d |
| 14 | 3.6 | 8030 | 2125 | 666 | 5.3 | 1375 | 1750 | 1885 | 2125 | 5-8d | 2745 | 3365 | 3365 | 3985 | 5-8d |
| 16 | 3.9 | 9210 | 2330 | 913 | 5.3 | 1375 | 1750 | 1885 | 2330 | 6-8d | 2745 | 3490 | 3365 | 4105 | 6-8d |
| 18 | 4.2 | 10380 | 2535 | 1205 | 5.3 | 1375 | 1750 | 1885 | 2535 | 7-8d | 2745 | 3615 | 3365 | 4230 | 7-8d |
| 20 | 4.4 | 11540 | 2740 | 1545 | 5.3 | NA | 1750 | NA | 2740 | 8-8d | NA | 3740 | NA | 4355 | 8-8d |
| 22 | 4.7 | 12690 | 2935 | 1934 | 5.3 | NA | 1750 | NA | 2935 | 9-8d | NA | 3860 | NA | 4480 | 9-8d |
| 24 | 5.0 | 13830 | 3060 | 2374 | 5.3 | NA | 1750 | NA | 3060 | 10-8d | NA | 3875 | NA | 4605 | 10-8d |
| 26 | 5.3 | 14960 | 2900 | 2868 | 5.3 | NA | 1750 | NA | 2900 | 11-8d | NA (7) | 4725(7) | NA (7) | 5345(7) | 11-8d |
| 28 | 5.5 | 16085 | 2900 | 3417 | 5.3 | NA | 1750 | NA | 2900 | 12-8d | NA (7) | 4850(7) | NA (7) | 5470(7) | 12-8d |
| 30 | 5.8 | 17205 | 2900 | 4025 | 5.3 | NA | 1750 | NA | 2900 | 13-8d | NA (7) | 4975(7) | NA (7) | 5590(7) | 13-8d |
| TJI/L90 |
| 9 1/2 | 3.8 | 7415 | 1675 | 365 | 5.3 | 1400 | NA | 1675 | NA | NA | 3350 | NA | 3965 | NA | NA |
| 11-7/8 | 4.2 | 9605 | 1925 | 621 | 5.3 | 1400 | 1715 | 1885 | 1925 | 2-16d | 3350 | 3665 | 3965 | 4285 | 2-16d |
| 14 | 4.5 | 11430 | 2125 | 913 | 5.3 | 1400 | 1875 | 1885 | 2125 | 3-16d | 3350 | 3825 | 3965 | 4440 | 3-16d |
| 16 | 4.7 | 13115 | 2330 | 1246 | 5.3 | 1400 | 2030 | 1885 | 2330 | 4-16d | 3350 | 3980 | 3965 | 4600 | 4-16d |
| 18 | 5.0 | 14785 | 2535 | 1635 | 5.3 | 1400 | 2030 | 1885 | 2515 | 4-16d | 3350 | 3980 | 3965 | 4600 | 4-16d |
| 20 | 5.3 | 16435 | 2740 | 2085 | 5.3 | NA | 2190 | NA | 2675 | 5-16d | NA | 4140 | NA | 4755 | 5-16d |
| 22 | 5.6 | 18075 | 2935 | 2597 | 5.3 | NA | 2345 | NA | 2830 | 6-16d | NA | 5090 | NA | 5705 | 11-16d |
| 24 | 5.8 | 19700 | 3060 | 3172 | 5.3 | NA | 2345 | NA | 2830 | 6-16d | NA | 5405 | NA | 6020 | 13-16d |
| 26 | 6.1 | 21315 | 2900 | 3814 | 5.3 | NA | 2450 | NA | 2900 | 7-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 14-16d |
| 28 | 6.4 | 22915 | 2900 | 4525 | 5.3 | NA | 2450 | NA | 2900 | 8-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 15-16d |
| 30 | 6.6 | 24510 | 2900 | 5306 | 5.3 | NA | 2450 | NA | 2900 | 8-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 17-16d |
| TJI/H90 |
| 11-7/8 | 4.6 | 10960 | 1925 | 687 | 5.3 | 1400 | 1715 | 1885 | 1925 | 2-16d | 3495 | 3810 | 4100 | 4420 | 2-16d |
| 14 | 4.9 | 13090 | 2125 | 1015 | 5.3 | 1400 | 1875 | 1885 | 2125 | 3-16d | 3495 | 3970 | 4100 | 4575 | 3-16d |
| 16 | 5.2 | 15065 | 2330 | 1389 | 5.3 | 1400 | 2030 | 1885 | 2330 | 4-16d | 3495 | 4130 | 4100 | 4735 | 4-16d |
| 18 | 5.4 | 17010 | 2535 | 1827 | 5.3 | 1400 | 2030 | 1885 | 2515 | 4-16d | 3495 | 4130 | 4100 | 4735 | 4-16d |
| 20 | 5.7 | 18945 | 2740 | 2331 | 5.3 | NA | 2190 | NA | 2675 | 5-16d | NA | 4285 | NA | 4890 | 5-16d |
| 22 | 6.0 | 20855 | 2935 | 2904 | 5.3 | NA | 2345 | NA | 2830 | 6-16d | NA | 5235 | NA | 5840 | 11-16d |
| 24 | 6.3 | 22755 | 3060 | 3549 | 5.3 | NA | 2345 | NA | 2830 | 6-16d | NA | 5425 | NA | 6155 | 13-16d |
| 26 | 6.5 | 24645 | 2900 | 4266 | 5.3 | NA | 2450 | NA | 2900 | 7-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 14-16d |
| 28 | 6.8 | 26520 | 2900 | 5059 | 5.3 | NA | 2450 | NA | 2900 | 8-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 15-16d |
| 30 | 7.1 | 28380 | 2900 | 5930 | 5.3 | NA | 2450 | NA | 2900 | 8-16d | NA (7) | 5800(7) | NA (7) | 5800(7) | 17-16d |

See notes at the end of the table.

-9-

TABLE 2 – CONTINUED

| BASIC PROPERTIES | REACTION PROPERTIES |
| --- | --- |
| Joist Depth (in.) | Joist Weight (plf) | Resistive Moment (ft.-lbs.) (10) | Vert. Shear (lbs.) | EI x 106 lbs.-in.2 | K | END REACTION (lbs.) | INTERMEDIATE REACTION (lbs.) |
|  |  |  |  |  |  | 1-3/4” | 3-1/2” | Nails Req’d. | 3-1/2” | 5-1/4” | Nails Req’d |
|  |  |  |  |  |  | 2-1/2” (9) |  |  | 5-1/4” (7) | 7” (7) |  |
|  |  |  |  |  |  | Bearing Length | Bearing Length |  | Bearing Length | Bearing Length |  |
|  |  |  |  |  |  | Web Stiffeners | Web Stiffeners |  | Web Stiffeners | Web Stiffeners |  |
|  |  |  |  |  |  | NO | YES | NO | YES |  | NO | YES | NO | YES |  |
| TJI/HD90 |
| 11-7/8 | 5.4 | 14075 | 2320 | 826 | 6.0 | 1835(9) | 2320(9) | 2150 | 2320 | 4-16d | 3995 | 4650 | 4690 | 5345 | 4-16d |
| 14 | 5.7 | 16920 | 2565 | 1232 | 6.0 | 1835(9) | 2565(9) | 2150 | 2565 | 6-16d | 3995 | 4980 | 4690 | 5670 | 6-16d |
| 16 | 6.0 | 19550 | 2790 | 1695 | 6.0 | 1835(9) | 2790(9) | 2150 | 2790 | 6-16d | 3995 | 4980 | 4690 | 5670 | 6-16d |
| 18 | 6.3 | 22150 | 3020 | 2239 | 6.0 | 1835(9) | 3020(9) | 2150 | 3020 | 8-16d | 3995 | 5310 | 4690 | 6000 | 8-16d |
| 20 | 6.7 | 24725 | 3250 | 2866 | 6.0 | NA(9) | 3250(9) | NA | 3250 | 10-16d | NA | 5425 | NA | 6330 | 10-16d |
| 22 | 7.0 | 27280 | 3480 | 3579 | 6.0 | NA(9) | 3475(9) | NA | 3480 | 10-16d | NA | 5425 | NA | 6330 | 10-16d |
| 24 | 7.3 | 29815 | 3710 | 4380 | 6.0 | NA(9) | 3500(9)(11) | NA | 3710 | 12-16d | NA | 5425 | NA | 6655 | 12-16d |
| 26 | 7.6 | 32330 | 3940 | 5272 | 6.0 | NA(9) | 3500(9)(11) | NA | 3940 | 14-16d | NA (7) | 6985(7) | NA (7) | 7675(7) | 14-16d |
| 28 | 7.9 | 34830 | 4165 | 6258 | 6.0 | NA(9) | 3500(9)(11) | NA | 4165 | 14-16d | NA (7) | 6985(7) | NA (7) | 7675(7) | 14-16d |
| 30 | 8.2 | 37310 | 4375 | 7339 | 6.0 | NA(9) | 3500(9)(11) | NA | 4375 | 16-16d | NA (7) | 7310(7) | NA (7) | 8005(7) | 16-16d |
| 32 | 8.5 | 39785 | 4375 | 8519 | 6.0 | NA(9) | 3500(9)(11) | NA | 4375 | 18-16d | NA (7) | 7640(7) | NA (7) | 8335(7) | 18-16d |
| TJI/HS90 |
| 11-7/8 | 6.0 | 16050 | 2320 | 900 | 6.0 | 1835(9) | 2320(9) | 2150 | 2320 | 4-16d | 3995 | 4650 | 4690 | 5345 | 4-16d |
| 14 | 6.3 | 19425 | 2565 | 1355 | 6.0 | 1835(9) | 2565(9) | 2150 | 2565 | 6-16d | 3995 | 4980 | 4690 | 5670 | 6-16d |
| 16 | 6.6 | 22550 | 2790 | 1876 | 6.0 | 1835(9) | 2790(9) | 2150 | 2790 | 6-16d | 3995 | 4980 | 4690 | 5670 | 6-16d |
| 18 | 7.0 | 25640 | 3020 | 2488 | 6.0 | 1835(9) | 3020(9) | 2150 | 3020 | 8-16d | 3995 | 5310 | 4690 | 6000 | 8-16d |
| 20 | 7.3 | 28695 | 3250 | 3195 | 6.0 | NA(9) | 3250(9) | NA | 3250 | 10-16d | NA | 5425 | NA | 6330 | 10-16d |
| 22 | 7.6 | 31725 | 3480 | 3998 | 6.0 | NA(9) | 3475(9) | NA | 3480 | 10-16d | NA | 5425 | NA | 6330 | 10-16d |
| 24 | 7.9 | 34730 | 3710 | 4901 | 6.0 | NA(9) | 3500(9)(11) | NA | 3710 | 12-16d | NA | 5425 | NA | 6655 | 12-16d |
| 26 | 8.2 | 37715 | 3940 | 5905 | 6.0 | NA(9) | 3500(9)(11) | NA | 3940 | 14-16d | NA (7) | 6985(7) | NA (7) | 7675(7) | 14-16d |
| 28 | 8.5 | 40680 | 4165 | 7014 | 6.0 | NA(9) | 3500(9)(11) | NA | 4165 | 14-16d | NA (7) | 6985(7) | NA (7) | 7675(7) | 14-16d |
| 30 | 8.8 | 43630 | 4375 | 8230 | 6.0 | NA(9) | 3500(9)(11) | NA | 4375 | 16-16d | NA (7) | 7310(7) | NA (7) | 8005(7) | 16-16d |
| 32 | 9.1 | 46560 | 4375 | 9555 | 6.0 | NA(9) | 3500(9)(11) | NA | 4375 | 18-16d | NA (7) | 7640(7) | NA (7) | 8335(7) | 18-16d |

FOOTNOTES FOR TABLE 2

1.	Refer to Figure 1 of this report for web stiffener details.

2.	Deflection is calculated as follows:

Where:

P = 	Concentrated load, pounds.	d = 	Out-to-out depth of joist, inches.

W = 	Uniform load in pounds per lineal foot.	EI = 	From table.

L = 	Clear span in feet.	K = 	From table.

-10-

FOOTNOTES FOR TABLE 2 – CONTINUED

3.	The stated allowable design properties are for loads of normal duration.  Adjustments to the allowable design values shall be in accordance with the applicable code, with the exception noted in footnote 10 below.

4.	Interpolation between bearing lengths and joist depths is permitted for allowable design reactions.

5.	The minimum bearing length is permitted to be reduced for joists supported by hangars if supplemental nail attachment is provided to the web stiffener.

6.	Allowable bearing lengths have been determined based on Trus Joist products.  Allowable bearing on supporting members shall be checked.

7.	Allowable bearing reactions for 5-1/4-inch and 7-inch bearing lengths at intermediate supports.

8.	Joist weights shown are calculated on a rational basis, are based on the heavier of eastern or western species products and are suitable for dead load calculation.  Contact the producing plant for shipping weight information if needed.

9.	Applicable to TJI/HD90 and TJI/HS90 joists only.  Areas indicate allowable bearing reactions of 1600 lbs. without web stiffeners for depths up to and including 18 inches; with web stiffeners the allowable reaction is 2255 lbs. for the 11-7/8 inch depth and 2450 lbs. for all other depths.

10.	The resistive moment capacities listed in Table 2 may not be increased by any code allowed repetitive-member use factor.

11.	Applicable to TJI/HD90 and TJI/HS90 joists only.  Reaction capacities at a 3-inch bearing length (interpolated as per note 4 above) may be increased 510 lbs. when supported by Simpson Strong-Tie Co. HWI or WPU joist hangers with a minimum of 4 10d common nails installed though the joist hanger stirrups and into the joist web stiffener and web.

-11-

FIGURE 1 – WEB STIFFENER NOTES AND DETAILS

1.	Web stiffeners shall be installed at bearing points as required in Table 2.

2.	Web stiffeners shall be installed at points of concentrated loads greater than 1500 pounds and are to be nailed in accordance with the intermediate reaction schedule in Table 2.

3.	Web stiffeners shall be installed on each side of the web as shown, with nails equally spaced vertically.

4.	A gap shall be left at the top of web stiffeners as shown at all bearing conditions.  In the case of concentrated loads, web stiffeners are required as shown and the gap shall be at the bottom.

5.	Web stiffener material shall be sheathing meeting the requirements of PS-1 or PS-2 with the face grain parallel to the long axis.

- Some hangers require web stiffeners to comply with nailing requirements through side plates.

- If web stiffeners are not used in hanger support, the side of the hanger shall extend up to laterally support the top flange.

Web stiffener specifications are as follows:

| TJI Joist Series | Minimum Dimensions | Grade |
| --- | --- | --- |
|  | “W” (Inches) | “T” (Inches) |  |
| TJI 110, TJI/L45 | 2 5/16 | 5/8 | See Note 5 |
| TJI 210 | 2 5/16 | 23/32 | See Note 5 |
| TJI 230, TJI 360, TJI/L65 | 2 5/16 | 7/8 | See Note 5 |
| TJI 560, TJI/L90, TJI/H90 | 3 1/2 | 1 ½ | Construction Grade 2x4 |
| TJI/HD90, TJI/HS90 | 3 1/2 | 1 ½ | 1.3E minimum grade TimberStrand LSL |

-12-

FIGURE 2.  Allowable Hole Size and Location for the TJI/L45, TJI/L65, TJI/L90, TJI/H90, TJI/HD90 and TJI/HS90 Joists ONLY.

Hole Factors and Locations Chart

| Round Hole Size (inches) | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rectangular Hole Size (inches) | 1¼ | 1¾ | 2¼ | 3 | 3½ | 4 | 4¾ | 5¼ | 6 | 6½ | 7 | 7¾ | 8¼ | 9 | 9½ | 10 | 10¾ | 11¼ | 12 |
| Joist depth (inches) | 11⅞ | A | A | B | C | E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 14 | A | A | B | C | C | D | E |  |  |  |  |  |  |  |  |  |  |  |  |
|  | 16 | A | A | A | B | C | C | D | E | E |  |  |  |  |  |  |  |  |  |  |
|  | 18 | 4” | 1’-3” | A | A | B | C | C | D | E | E |  |  |  |  |  |  |  |  |  |
|  | 20 | 4” | 1’-3” | A | A | B | B | C | C | D | D | E | E |  |  |  |  |  |  |  |
|  | 22 | 4” | 1’-3” | 1’-3” | A | A | B | B | C | C | D | D | E | E |  |  |  |  |  |  |
|  | 24 | 4” | 4” | 1’-3” | A | A | A | B | B | C | C | D | D | E | E | E |  |  |  |  |
|  | 26 | 4” | 4” | 1’-3” | A | A | A | B | B | B | C | C | D | D | D | E | E |  |  |  |
|  | 28 | 4” | 4” | 1’-3” | 1’-3” | A | A | A | B | B | B | C | C | D | D | D | E | E | E |  |
|  | 30 | 4” | 4” | 4” | 1’-3” | 1’-3” | A | A | A | B | B | B | C | C | C | D | D | E | E | E |

Hole Locations Chart

| Joist Span (center to center of support, feet) | Hole Factor |
| --- | --- |
|  | A | B | C | D | E |
| 14 | 1’-3” | 2’-0” | 2’-6” | 3’-9” | 5’-0” |
| 15 | 1’-3” | 2’-0” | 3’-0” | 4’-0” | 5’-3” |
| 16 | 1’-3” | 2’-3” | 3’-3” | 4’-6” | 5’-9” |
| 17 | 1’-6” | 2’-9” | 3’-9” | 5’-0” | 6’-3” |
| 18 | 1’-6” | 3’-0” | 4’-3” | 5’-6” | 6’-9” |
| 19 | 1’-9” | 3’-0” | 4’-3” | 5’-6” | 7’-0” |
| 20 | 1’-9” | 3’-0” | 4’-3” | 5’-6” | 7’-0” |
| 21 | 2’-0” | 3’-0” | 4’-3” | 5’-9” | 7’-3” |
| 22 | 2’-0” | 3’-0” | 4’-3” | 5’-9” | 7’-3” |
| 23 | 2’-0” | 3’-3” | 4’-3” | 5’-9” | 7’-6” |
| 24 | 2’-3” | 3’-3” | 4’-6” | 5’-9” | 7’-6” |
| 25 | 2’-3” | 3’-6” | 4’-9” | 5’-9” | 7’-9” |
| 26 | 2’-3” | 3’-9” | 4’-9” | 6’-0” | 7’-9” |
| 27 | 2’-6” | 3’-9” | 5’-0” | 6’-3” | 7’-9” |
| 28 | 2’-6” | 4’-0” | 5’-3” | 6’-6” | 8’-0” |
| 29 | 2’-6” | 4’-0” | 5’-6” | 6’-9” | 8’-3” |
| 30 | 2’-9” | 4’-3” | 5’-9” | 7’-0” | 8’-6” |
| 31 | 3’-0” | 4’-3” | 5’-9” | 7’-3” | 8’-9” |
| 32 | 3’-0” | 4’-6” | 6’-0” | 7’-6” | 9’-3” |
| 33 | 3’-0” | 4’-9” | 6’-3” | 7’-9” | 9’-6” |
| 34 | 3’-0” | 5’-0” | 6’-6” | 8’-0” | 9’-9” |
| 35 | 3’-3” | 5’-0” | 6’-6” | 8’-3” | 10’-0” |
| 36 | 3’-3” | 5’-0” | 6’-9” | 8’-6” | 10’-3” |

Notes to Figure 2:

- Charts are based on simple spans and uniform load applications or applicable building code provisions for concentrated loads (2000 lbs. Over 2.5 square feet) with 25 psf dead load and 20 psf partition load.

- For uniformly loaded multiple span applications holes shall be located 1.0 inch farther from the support for each foot of joist span, than the values indicated in the Charts.

- Holes are not allowed in cantilever areas unless specifically designed by a qualified design professional.

- Where more than one hole is to be cut in the web, the clear distance between holes shall be twice the length of the longest dimension of the largest adjacent hole.

- Hole sizes shown are hole sizes, not duct sizes.

- Rectangular hole sizes are based on measurement of the longest side.

-13-

FIGURE 3. ALLOWABLE HOLE SIZE AND LOCATION FOR THE TJI 110, TJI 210, TJI 230, TJI 360 AND TJI 560 JOISTS

Table A – End Support

Minimum Distance From Edge of Hole to Inside Face of Nearest End Support

| Joist Depth (inches) | TJI Joist Series | Round Hole Size (inches) | Square or Rectangular Hole Size (inches) |
| --- | --- | --- | --- |
|  |  | 2 | 3 | 4 | 6½ | 8⅞ | 11 | 13 | 2 | 3 | 4 | 6½ | 8⅞ | 11 | 13 |
| 9½ | TJI 110 | 1’-0” | 1’-6” | 2’-0” | 5’-0” |  |  |  | 1’-0” | 1’-6” | 2’-6” | 4’-6” |  |  |  |
|  | TJI 210 | 1’-0” | 1’-6” | 2’-0” | 5’-0” |  |  |  | 1’-0” | 2’-0” | 2’-6” | 5’-0” |  |  |  |
|  | TJI 230 | 1’-0” | 2’-0” | 2’-6” | 5’-6” |  |  |  | 1’-0” | 2’-0” | 3’-0” | 5’-0” |  |  |  |
| 11⅞ | TJI 110 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 5’-0” |  |  | 1’-0” | 1’-0” | 1’-6” | 4’-6” | 6’-0” |  |  |
|  | TJI 210 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 5’-6” |  |  | 1’-0” | 1’-0” | 2’-0” | 5’-0” | 6’-6” |  |  |
|  | TJI 230 | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 6’-0” |  |  | 1’-0” | 1’-0” | 2’-0” | 5’-6” | 7’-0” |  |  |
|  | TJI 360 | 1’-0” | 1’-0” | 1’-6” | 4’-6” | 7’-0” |  |  | 1’-0” | 1’-0” | 2’-6” | 6’-6” | 7’-6” |  |  |
|  | TJI 560 | 1’-0” | 1’-0” | 1’-6” | 5’-0” | 8’-0” |  |  | 1’-0” | 2’-0” | 3’-6” | 7’-0” | 8’-0” |  |  |
| 14 | TJI 110 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 5’-0” |  | 1’-0” | 1’-0” | 1’-0” | 3’-6” | 6’-0” | 8’-0” |  |
|  | TJI 210 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 6’-0” |  | 1’-0” | 1’-0” | 1’-0” | 4’-0” | 6’-6” | 8’-6” |  |
|  | TJI 230 | 1’-0” | 1’-0” | 1’-0” | 1’-6” | 3’-6” | 6’-6” |  | 1’-0” | 1’-0” | 1’-0” | 4’-0” | 7’-0” | 9’-0” |  |
|  | TJI 360 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 5’-6” | 8’-0” |  | 1’-0” | 1’-0” | 1’-0” | 5’-6” | 8’-0” | 9’-6” |  |
|  | TJI 560 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 6’-0” | 9’-0” |  | 1’-0” | 1’-0” | 1’-6” | 6’-6” | 9’-0” | 10’-0” |  |
| 16 | TJI 210 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 1’-6” | 3’-6” | 6’-0” | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 6’-6” | 8’-0” | 10’-6” |
|  | TJI 230 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 2’-0” | 4’-0” | 6’-6” | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 7’-0” | 9’-0” | 11’-0” |
|  | TJI 360 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 6’-0” | 9’-0” | 1’-0” | 1’-0” | 1’-0” | 4’-0” | 9’-0” | 10’-0” | 11’-6” |
|  | TJI 560 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 6’-6” | 10’-0” | 1’-0” | 1’-0” | 1’-0” | 5’-0” | 10’-0” | 11’-0” | 12’-0” |

See notes below Table B.

-14-

Table B – Intermediate or Cantilever Support

Minimum Distance from Edge of Hole to Inside Face of Nearest Intermediate or Cantilever Support

| Joist Depth (inches) | TJI Joist Series | Round Hole Size (inches) | Square or Rectangular Hole Size (inches) |
| --- | --- | --- | --- |
|  |  | 2 | 3 | 4 | 6½ | 8⅞ | 11 | 13 | 2 | 3 | 4 | 6½ | 8⅞ | 11 | 13 |
| 9½ | TJI 110 | 1’-6” | 2’-6” | 3’-0” | 7’-6” |  |  |  | 1’-6” | 2’-6” | 3’-6” | 6’-6” |  |  |  |
|  | TJI 210 | 2’-0” | 2’-6” | 3’-6” | 7’-6” |  |  |  | 2’-0” | 3’-0” | 4’-0” | 7’-0” |  |  |  |
|  | TJI 230 | 2’-6” | 3’-0” | 4’-0” | 8’-0” |  |  |  | 2’-6” | 3’-0” | 4’-6” | 7’-6” |  |  |  |
| 11⅞ | TJI 110 | 1’-0” | 1’-0” | 1’-6” | 4’-0” | 8’-0” |  |  | 1’-0” | 1’-6” | 2’-6” | 6’-6” | 9’-0” |  |  |
|  | TJI 210 | 1’-0” | 1’-0” | 2’-0” | 4’-6” | 9’-0” |  |  | 1’-0” | 2’-0” | 3’-0” | 7’-6” | 10’-0” |  |  |
|  | TJI 230 | 1’-0” | 2’-0” | 2’-6” | 5’-0” | 9’-6” |  |  | 1’-0” | 2’-6” | 3’-6” | 8’-0” | 10’-0” |  |  |
|  | TJI 360 | 2’-0” | 3’-0” | 4’-0” | 7’-0” | 11’-0” |  |  | 2’-0” | 3’-6” | 5’-0” | 9’-6” | 11’-0” |  |  |
|  | TJI 560 | 1’-6” | 3’-0” | 4’-6” | 8’-0” | 12’-0” |  |  | 3’-0” | 4’-6” | 6’-0” | 10’-6” | 12’-0” |  |  |
| 14 | TJI 110 | 1’-0” | 1’-0” | 1’-0” | 2’-0” | 4’-6” | 8’-0” |  | 1’-0” | 1’-0” | 1’-0” | 5’-0” | 9’-0” | 12’-0” |  |
|  | TJI 210 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 5’-0” | 9’-0” |  | 1’-0” | 1’-0” | 2’-0” | 6’-0” | 10’-0” | 12’-6” |  |
|  | TJI 230 | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 5’-6” | 10’-0” |  | 1’-0” | 1’-0” | 2’-6” | 6’-0” | 10’-6” | 13’-0” |  |
|  | TJI 360 | 1’-0” | 1’-0” | 2’-0” | 5’-6” | 8’-6” | 12’-6” |  | 1’-0” | 2’-0” | 4’-0” | 9’-0” | 12’-0” | 14’-0” |  |
|  | TJI 560 | 1’-0” | 1’-0” | 1’-6” | 5’-6” | 9’-6” | 13’-6” |  | 1’-0” | 3’-0” | 5’-0” | 10’-0” | 13’-6” | 15’-0” |  |
| 16 | TJI 210 | 1’-0” | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 5’-6” | 9’-6” | 1’-0” | 1’-0” | 1’-0” | 4’-6” | 9’-6” | 12’-6” | 15’-6” |
|  | TJI 230 | 1’-0” | 1’-0” | 1’-0” | 1’-6” | 4’-0” | 6’-6” | 10’-6” | 1’-0” | 1’-0” | 1’-0” | 5’-0” | 10’-6” | 13’-0” | 16’-0” |
|  | TJI 360 | 1’-0” | 1’-0” | 1’-0” | 3’-0” | 6’-6” | 10’0” | 13’6” | 1’-0” | 1’-0” | 2’-0” | 7’-6” | 13’0” | 14’6” | 17’0” |
|  | TJI 560 | 1’-0” | 1’-0” | 1’-0” | 2’-6” | 7’-0” | 11’0” | 15’0” | 1’-0” | 1’-0” | 3’-6” | 9’-0” | 14’6” | 16’0” | 18’0” |

1.	The clear distance between multiple holes shall be twice the longest dimension of the largest hole.

2.	Holes may be located vertically anywhere within the web.  Leave 1/8 inch of web minimum at top and bottom of hole.

3.	Tables A and B are based on uniform load applications, within the limitations of the applicable Trus Joist literature.

4.	TJI Joists are manufactured with 1 1/2 inch diameter perforated knockouts in the web at approximately 12 inches on center along the length of the joist.

5.	For simple span (5 foot minimum) uniformly loaded joists one maximum size hole may be located in the web at the center of the joist span provided no other holes occur in the joist.

MANUFACTURING PLANTS

TJI Joists covered by this bulletin shall be produced at the following locations:

Trus Joist

2345 Deschutes Drive

P. O. Box 60

Stayton, OR  97383

Trus Joist

162 N. Jackson Street.

Hwy 31 S

P. O. Box 368

Castleberry, AL  36432

Trus Joist

Hanger 5

Claresholm Industrial Airport

P. O. Box 1060

Claresholm, Alberta T0L0T0

Trus Joist

610 Trus Joist Lane

Chavies, KY  41727

Trus Joist

410 Clay Road

Valdosta, GA  31601

Trus Joist

195 N. Bertelsen Road

Eugene, OR  97402

Trus Joist

234 Industrial Avenue

Natchitoches, LA  71457

The appropriate HUD Field Office or Homeownership Center in whose jurisdiction the manufacturing plant is located, or HUD designated representative will inspect this plant in accordance with prescribed procedures.

-15-

QUALITY CONTROL

The appropriate HUD Field Office or HUD designated representative, or Homeownership Center in whose jurisdiction the manufacturing plant is located, shall review and approve plant fabrication procedures and quality control program, and shall report to Headquarters in accordance with outstanding instructions.

IDENTIFICATION

TJI Joists are identified by a stamp indicating the product designation, the number of this bulletin (HUD 689), manufacturer’s name (Trus Joist) or logo, plant number, and production date.

###### SAMPLE STAMP:

RECORD OF PROPERTIES

The manufacturer shall provide HUD a list of the first ten properties in which the component or system described in this bulletin is used.  The list shall include the complete address, or description of location, and the approximate date of installation or erection.  Failure of the manufacturer to provide HUD with the above information may result in cancellation of this bulletin.

NOTICE OF CHANGES:

The manufacturer shall inform HUD in advance of changes in production facilities, transportation, field erection procedures, design, or materials used in this product.  Further, the manufacturer shall inform HUD of revision to corporate structure, change of address or change in name or affiliation of the prime manufacturer.  Failure of the manufacturer to notify HUD of any of the above changes may result in cancellation of this bulletin.

EVALUATION:

This SEB shall be valid for a period of three years from the date of initial issuance or most recent renewal or revision, whichever is later.  The holder of this bulletin shall apply for renewal or revision 90 days prior to the review date printed on this bulletin.

-16-

Submittals for renewal or revision shall be sent to:

U. S. Department of Housing and Urban Development

FHA Standards, Office of Manufactured Housing Programs

451 Seventh Street, SW, Room 9168

Washington, DC  20410-8000

Appropriate User Fee shall be sent to:

U. S. Department of Housing and Urban Development

Miscellaneous Income - Technical Suitability of Products Fees

Bank of America

P. O. Box 198762

Atlanta, GA  30384-8762

The holder of this SEB may apply for revision at any time prior to the review date.  Minor revisions may be in the form of a supplement.

If the Department determines that a proposed renewal or supplement constitutes a revision, the appropriate User Fee for a revision will need to be submitted in accordance with Code of Federal Regulations 24 CFR 200.934, “User Fee System for the Technical Suitability of Products Program,” and current User Fee Schedule.

CANCELLATION:

Failure to apply for a renewal or revision shall constitute a basis for cancellation of the bulletin.  HUD will notify the manufacturer that the bulletin may be cancelled when:

- conditions under which the document was issued have changed so as to affect production of, or to compromise the integrity of the accepted material, product, or system,

- the manufacturer has changed its organizational form without notifying HUD, or

3.	the manufacturer has not complied with responsibilities it assumed as a condition of HUD’s acceptance.

-17-

However, before cancellation, HUD will give the manufacturer a written notice of the specific reasons for cancellation, and the opportunity to present views on why the SEB should not be cancelled.  No refund of fees will be made on a canceled document.

************************************************************************

This bulletin is issued solely for the captioned firm, and is not transferable to any person or successor entity.

************************************************************************

# Text boxes

Trus Joist

A Weyerhaeuser Business

PO Box 8449

Boise, ID  83707

TJI® Prefabricated Wood I-Joists

February 18, 2007

February 18, 2004

(Supersedes issue dated

February 13, 2002)

689 Rev. 9

The technical description, requirements and limitations expressed herein do not constitute an endorsement or approval by the Department of Housing and Urban Development (HUD) of the subject matter, and any statement or representation, however made, indicating approval or endorsement by HUD is unauthorized and false, and will be considered a violation of the United States Criminal Code, 18 U.S.C. 709.

NOTICE: THIS BULLETIN APPLIES TO DWELLING UNITS BUILT UNDER HUD HOUSING PROGRAMS. NON-HUD-INSURED UNITS MAY OR MAY NOT BE IN CONFORMINTY WITH THE REQUIREMENTS OF THE HUD MINIMUM PROPERTY STANDARDS.

Any reproduction of this Bulletin must be in its entirety and any use of all or any part of this Bulletin in sales promotion or advertising is prohibited.