# Milton G. Davies

Director, Board of Directors

Fallbrook Public Utility District

Testimony

Before the Committee on Energy and Natural Resources

United States Senate

Hearing on H.R. 29 (Issa) Santa Margarita River, California

April 24, 2008

Mr. Chairman, I am Milton Davies, Chairman of the Board of Directors of the Fallbrook Public Utility District (FPUD).  The people of Fallbrook appreciate this opportunity to discuss the need for the Santa Margarita River Conjunctive Use Project.  It appears there really may be a light at the end of the tunnel for this project after 80 years of water rights litigation, studies, hearings, re-restudies and much frustration.  The spirit of cooperation between the Bureau of Reclamation, the Navy Department, local Marine Corps officials and the District has never been better.  The time to move forward on this project is not only ripe, but has reached the point of absolute necessity.  Exhibit A is a vicinity map showing the general location of this project.  Exhibit B depicts the proposed Conjunctive Use Project.

Project History

This process started in 1930 when the state of California issued the first water appropriation permit on the Santa Margarita River to the Fallbrook Irrigation District (later to become FPUD) for a dam on the River.

In 1926, the Vail Ranch, a large land grant occupying almost the whole Temecula Valley was sued by the Rancho Santa Margarita (later to become Camp Pendleton), over water rights to the Santa Margarita River.  The Fallbrook Irrigation District was unsuccessful in trying to resolve the dispute amicably.  This litigation was settled in 1940 with a stipulated judgment dividing the water resources between the litigants but setting the stage for the present, unresolved dispute since it failed to account for the 1930 appropriative permit issued to Fallbrook. (include 2.5 cfs direct diversion at the sump)

Since 1941 numerous attempts have been made to develop a “physical solution” to the water rights issues between Camp Pendleton and FPUD.  From the 1940’s through the 1980’s these included a 2 dam project and a 1 dam project on the river.  There were many studies, starts and stops during those 4 decades but no project was completed.  High costs, and environmental concerns were the main deterrents to completing any dam project.

In 1990, a two-party agreement was signed by FPUD and Camp Pendleton which recognized that if upstream dischargers put recycled water into the Santa Margarita River, then these two parties would benefit from the water supply out of those discharges and that they would enter into a joint project to operate the groundwater basin and treatment facilities.  This was the birth of the Conjunctive Use Project.  At that point it was necessary to pursue feasibility and environmental work.  The Conjunctive Use Study was prepared in 1994 as a follow-up to the two-party agreement.  This study was the basis for the project that is being proposed today.

One of the two primary objectives of the project presented to you today is the resolution of eighty years of water rights disputes and litigation on the Santa Margarita River, over 60 years of which involve the federal government.  Secondly, this project will provide for an environmentally sound, financially feasible, water resource development where it is most needed, in coastal Southern California.

The availability of a supplemental local water source from the Santa Margarita River has become increasingly important to the District’s capability to meet all water demands at a reasonable price.  The long-term safe yield from this project will provide 100% of the needs of Camp Pendleton and 20 to 40% of the District’s total needs.

## Project Description

The proposed Santa Margarita Conjunctive Use Project provides for enhanced recharge and recovery through aggressive groundwater management strategies on Camp Pendleton to provide a water supply for both Camp Pendleton and Fallbrook to resolve a long-standing water rights dispute between the United States and Fallbrook.  In 1954, P.L. 83-547, the Santa Margarita Project Act, authorized the Bureau of Reclamation to construct a dam on the Santa Margarita River at a cost of $22 million (approximately $333 million in 2008 $) with a yield of 14-16,000 acre-feet.  The Conjunctive Use Project that this bill authorizes replaces that project and produces the same amount or possibly more water at a lower cost.

The project, as proposed, is financially feasible, environmentally beneficial and will result in the conservation and preservation of the entire Santa Margarita River riparian zone from Temecula to the Pacific Ocean, while at the same time providing 16,000 acre-feet per year (AF/yr) of vitally needed local supply in coastal Southern California.

## Project Facilities

The project facilities include:

Enhanced Recharge.  Groundwater recharge is enhanced by the construction of a new collapsible diversion weir and 46 acres of new recharge ponds.  The enhanced recharge potential is 14,000 AF/yr in addition to the naturally occurring recharge.  The collapsible weir will divert low flows and permit flood flows to pass, flushing the lower river and estuary as well as providing beach sand replenishment.

Enhanced Groundwater Recovery.  Groundwater recovery is enhanced by the construction of up to five new wells, predictive monitoring, monitoring, and a collection system to provide a total of 18,000 AF/yr of extraction capability.

Advanced Water Treatment.  Treatment will be provided to exceed all requirements of the Safe Drinking Water Act.  The construction of membrane filtration, disinfection, and brine disposal facilities at the Rattlesnake Canyon site on Camp Pendleton will allow treatment of 20 million gallons per day.

Distribution Facilities.  Project water will be distributed to the existing Camp Pendleton and Fallbrook distribution systems through construction of two pump stations and approximately nine miles of transmission pipeline.  This pipeline will also provide Camp Pendleton with a critically needed connection to San Diego County Water Authority’s imported water delivery system in case of emergency, thus ensuring uninterrupted water service at one of our country’s most important military establishments.

## Project Yield

Two independent groundwater models predict an average annual project yield of 16,000 acre-feet (AF/yr).  The current Camp Pendleton demand and use of the groundwater system is less than 8,000 AF/yr so the project results in 8,000 AF/yr of new water, reducing demand on diversions from imported supplies from Northern California and the Colorado River.

## Project Cost

The current project cost estimate is $120-$150 million resulting in a higher project yield than the 1954 project, then estimated at $22 million, an amount that equates to approximately  $333 million today.  Camp Pendleton’s share of the project cost will primarily come from already approved MILCON funds for facilities that will be needed by Camp Pendleton regardless of whether the Conjunctive Use Project proceeds.  These facilities, if used by the Conjunctive Use Project will provide a credit against the total project cost in Camp Pendleton’s favor.

# Current Project Status

The Conjunctive Use Project is in the forth year of management by the Bureau of Reclamation’s Southern California office in Temecula, California (located in the upper Santa Margarita River basin).  Project funding currently comes from several Federal sources, including Camp Pendleton, Military Construction, and Reclamation Planning , as well as local funds contributed by FPUD.  At the direction of Congress, the Bureau is conducting this feasibility analysis.

The major current activity is the Bureau’s in-house feasibility assessment as well as management of the EIS/EIR outside contract.  This work involves the Bureau’s project team completing the preliminary design of the necessary facilities and alternatives in order to complete a jointly managed EIR/EIS/FA.  The Bureau and Camp Pendleton are joint Federal leads and FPUD is the state lead agency on the environmental documentation.  An agreement  has been reached to codify this effort to produce an environmental ROD/NOD and completion of the Feasibility Assessment.

Reclamation staff is conducting these planning operations and administering the EIR/EIS contract by outside contract funded by Camp Pendleton and FPUD.  This effort is overseen and directed by an Executive Management Team comprised of Reclamation, Camp Pendleton, and FPUD.

# Project Benefits

The Santa Margarita Project is somewhat unique among water resources projects in that the benefits are vast and project liabilities are almost non-existent.  The project has failed to proceed over the preceding eighty years because of institutional, political, and legal disagreements among and between the basin’s stakeholders.  At this point, these issues are largely resolved and the success of H.R. 29 will provide for the final settlement of the case of U.S. v. Fallbrook, .  In identifying project benefits, this settlement should not be overlooked--it is the action from which all other project-related benefits flow.

Other benefits include:

Water Supply.  The project develops a new supply of 8,000 AF/yr from local resources in San Diego at a cost that is competitive with today’s cost for imported water.  San Diego, like much of coastal Southern California, is largely dependent upon water imported great distances from the Colorado River and Northern California.  The recent drought in the Colorado River Upper Basin and the emergence of the Quantification Settlement Agreement, along with the recent cutback in Delta deliveries due to endangered species protection, have demonstrated the limits and risks attendant to this imported supply.

In addition to the new component of supply, the total project yield of 16,000 AF/yr will receive advanced water treatment prior to distribution.  Water quality in the Camp Pendleton distribution system will be dramatically improved and the operational costs related to water hardness will be eliminated.

Project Cost.  The current preliminary studies indicate this new supply can be developed for roughly one-third to one-half the cost of the project Congress authorized in 1954 (P.L. 547, Chapter 593) for the same project yield, making it one of the most cost-effective new water supply projects that you will be asked to consider.

Environmental Benefits.  The proposed project has no opposition from environmental interests and is generally supported by them because, aside from localized, construction-related impacts, the project is environmentally beneficial.  These benefits include:

- Preserving the entire riparian length of the Santa Margarita River from Temecula to the ocean in public ownership.

- Providing 1400 acres of mitigation lands for this and future military construction projects on Camp Pendleton.

- Operating the groundwater basins on Camp Pendleton to preserve critical habitat for the largest population of Least Bell’s Vireos in the United States.

- Permitting periodic high storm flows of the Santa Margarita River to flow unimpeded across Camp Pendleton, scouring the lower river valley, opening and flushing the estuary, and nourishing the beaches.

- Over time, the project will improve groundwater quality on Camp Pendleton, assist in removing the estuary from the listing of impaired waters, and preserve the endangered nesting habitat for the Least Tern on the estuary bar.

- The Fallbrook portion of the Santa Margarita River, including the Sandia and Rainbow Creek tributaries, will provide an extensive network of hiking and riding trails, as well as education and open-space benefits.

In summary, the need for the Project facilities to provide a supplemental local water source has become particularly important due to dwindling imported water supplies.  In addition, the economics of the Project are as good, or better, than future imported water costs.

I am confident that the current effort underway by the Bureau of Reclamation to update the economic and environmental aspects of the feasibility study will show the benefit-cost ratio to be extremely positive and that the extra study time that has been required to achieve a superior solution will prove to be very beneficial to the stakeholders.

I urge your speedy favorable action on HR 29 so that final planning and design can begin on this project that is so vital to the well being of our District and the Marine Corps.

Thank you very much for this opportunity to appear before you today and offer this testimony in support of H.R. 29.

SANTA MARGARITA WATER RESOUCES

Historical Timeline 1922-Present

1922	Fallbrook Public Utility District established to provide potable water to downtown Fallbrook (500 acres).

1925		Fallbrook Irrigation District established to provide

agricultural water from both San Luis Rey and Santa Margarita Rivers.  Initial studies began for diversion and storage on Santa Margarita River.  Fallbrook dam site

selected.

1926		Vail Ranch sued by Santa Margarita Ranch over Santa

Margarita water rights.  Fallbrook Irrigation District tried to

resolve issue unsuccessfully.

1928		Fallbrook Irrigation District filed condemnation suit for

unused riparian rights on Santa Margarita River.

1930		Fallbrook Irrigation District issued permit to appropriate

35,000 AF for Santa Margarita River storage and 15,000 AF

for annual use.

1930-1940	Legal entanglements and financial constraints prevented Fallbrook Irrigation District from proceeding with construction.  Vail/Santa Margarita Ranch litigation proceeded without Fallbrook Irrigation District as an interested party.

1937	Fallbrook Irrigation District dissolved.  Consolidated with Fallbrook Public Utility District.

1940		Vail/Santa Margarita Ranch lawsuit settled; 67% to Santa

Margarita and 33% to Vail Ranch.

1941		Navy Department buys Santa Margarita Ranch for Camp

Pendleton.

1944		San Diego County Water Authority formed to bring

Colorado River water to San Diego City.  Fallbrook Public Utility District a charter member, and the Navy a senior rights holder to imported water (15,000 AF/yr.)

1946		Fallbrook Public Utility District diversion and storage

permits on Santa Margarita River refiled.  Storage permits for 30,000 AF granted in 1948.

1948		Imported water arrives in Fallbrook.

1948	Navy Department applied to State Engineering to build DeLuz dam at Camp Pendleton.

1949		Tentative agreement reached to build multi-purpose dam at

DeLuz site to serve both Camp Pendleton and Fallbrook

Public Utility District.

1951		Federal government sues Fallbrook Public Utility District

and all its citizens over water rights on Santa Margarita

River.

1954		Congress authorized Santa Margarita Project (PL 83-547)

for single dam at DeLuz site with 60-40 water rights

between Navy Department and Fallbrook Public Utility District of original Santa Margarita Ranch 67% share.  U.S. Justice Department fails to agree with split of water.  The project authorization was for $22 million (1954).

1955-1958	Fallbrook Public Utility District buys river valley lands for the Fallbrook Reservoir.

1961		Each agency pursuing separate projects while litigation

proceeds.   Fallbrook Public Utility District files for PL-984

Small Reclamation Projects loan of $4.5 million for

Fallbrook dam.

1966	Lawsuit on water rights results in Stipulated Judgment between the Navy, Justice, Interior, and Fallbrook.

1968		Memorandum of Understanding and Agreement signed by

U.S. Attorney General, Secretary of the Navy, Secretary of

the Interior, Fallbrook Public Utility District Board of

Directors.  Interior directed to prepare feasibility

report for project to satisfy needs and rights, both of

Fallbrook Public Utility District and Camp Pendleton with

Bureau of Reclamation to operate project.  Two dam project

declared most economic with 36,500 AF Fallbrook reservoir

and 143,000 AF DeLuz reservoir.  Total cost in 1968 dollars

estimated at $48,675,000 with Fallbrook Public Utility

District share at $13,254,000.

1969		Bureau of Reclamation completed preliminary draft of

Feasibility Report.  Environmental Policy Act of 1969

required preparation of environmental impact assessment.

1971		Draft EI assessment completed and distributed for

comments.

1972		HR 13299 introduced by Congressman Schmitz.

1973		HR 3023 introduced by Congressman Veysey.  No hearings

scheduled as Feasibility Report and EIR not referred to

committee by Interior or Office of Management & Budget

(OMB).  No specific support from Navy Department.

1976		Final EIR published.

1978		Severe flood damage at Camp Pendleton.

1979		HR 6014 introduced by Congressman Burgener.  Bill died in

committee.

1980		Severe flood damage at Camp Pendleton; 205,000 AF lost to

the ocean.

1981		HR 1527 introduced by Congressman Burgener.  Referred to

House Interior and Insular Affairs Committee.

1982		S 2684 introduced by Senator S.I. Hayakawa.  Referred to

Energy and 	Natural Resources Committee.  Hearings held

on July 20, 1982 in both House and Senate.  BUREC starts

updating old studies.

1983		HR 1581 introduced by Congressman Packard.  S 805

introduced by Senator Wilson; passed Committee and

Senate floor by unanimous vote.  Authorization for two-dam

plan at $218,670,000.

1983-1984	House hearings held on HR 1581 and S 805.  Both bills died

in House and sub-committee.

1984		Bureau of Reclamation released draft supplemental

environmental impact statement and planning report for

Santa Margarita Project.  Rancho California Water District

releases facilities Master Plan to expand well field in upper

basin.

1985		House Armed Services Committee directed Secretary of

Navy to conduct independent study of Camp Pendleton’s

water supply and flood control requirements.

1985-1986	Bureau of Reclamation formulated an alternative project

consisting of a 65,000 AF structure (50,000 AF of storage

and 15,000 AF of flood control) at Fallbrook site with levees

on Camp Pendleton.  Cost estimate for the smaller project

$118,750,000 with a water supply yield of 11,900 AF.  U.S.

Fish & Wildlife Service announces intent to list least Bell’s

Vireo as an endangered species and designates proposed critical habitat.

1986		In April, Bureau of Reclamation indicated they were unable

to continue further studies due to budget constraints.  U.S. Fish & Wild	life lists least Bell’s vireo as endangered; critical habitat designation deferred for more public input.  In September, Department of the Navy awards contract for Camp Pendleton water study.  FPUD awards Phase I contract for development of mitigation plan for smaller project.  Navy determines that federal real estate not available for least Bell’s vireo 	mitigation.  USMC signs MOU with U.S. Fish & Wildlife Service to maintain 1200 acres riparian lands for Least Bell’s vireo.

1987		In January, FPUD awards Phases II, III & IV of environmental

Study contract for small project.  FPUD considers non-federal financing.  Camp Pendleton puts Rancho California Water District on notice regarding over pumping of groundwater basin.

1988		FPUD/Rancho California WD/Camp Pendleton agree to

Reestablish Watermaster.  Camp Pendleton Water Supply

Study (Leedshill-Herkenhoff) completed.  Recommends

Base obtain additional water from MWD in lieu of local dam and reservoir project.

1989		U.S. District court appoints Watermaster; also establishes

Steering Committee with initial membership from Camp

Pendleton, FPUD, and Rancho California WD.  Rancho

California WD and Eastern MWD consider live stream discharge of tertiary treated wastewater to Santa Margarita River as least cost disposal option.

1990		BUREC gets State Water Resources Control Board approval

to extend water rights permits (3 for FPUD, 1 for Camp

Pendleton) to 1994.  Rancho California WD/Eastern

MWD/FPUD/Camp Pendleton sign Four-Party Agreement

permitting live stream discharge, with dischargers 			obligated to mitigate water quality impacts on Camp

Pendleton’s wells, and providing for year round releases.

FPUD/Camp Pendleton sign Two-Party Agreement for

conjunctive use of Camp Pendleton’s groundwater basin as

an alternative to the 2-dam project.

1994		FPUD/Camp Pendleton complete comprehensive study of

conjunctive use of Camp Pendleton’s groundwater basin.

BUREC gets another 2-year extension of the 4 water rights

permits.

2001		Navy publishes the enhanced recovery program report and

Camp Pendleton concludes negotiations with Rancho

California Water District to provide replacement riverine

flows.

2002	FPUD, Navy, Reclamation undertake Joint EIR/EIS development for proposed project.

2003	Reclamation funding for pre-feasibility established.

2004	Reclamation and Navy become Joint Federal Lead Agencies; Fallbrook becomes State Lead Agency, and the Project Management Team is established in the Temecula Field Office to proceed with the EIR/EIS/FA.