Project Name: Project Number: CFLHD Project Manager: A/E or Hwy Design Mgr: Lead Designer: Date:

Capitalized text represents significant changes or additions from the 15% requirements.  However, all requirements are applicable.

| 30% DEVELOPMENT CHECKLIST 4R Projects Only Lead Designer: “INITIAL” in block to indicate those elements completed, including incorporation of data. Place an “I” in the block to indicate those elements that are incomplete, or write “N/A” to indicate those elements not applicable to the project. No initials are necessary in shaded areas. Document additional information in the Comments section at the end. | LEAD DESIGNER (Initials) |
| --- | --- |
| GENERAL |  |
| Comments from 15% review incorporated – 15% PS&E Comment & Response Tracking Form submitted, if applicable |  |
| Documents are in compliance with established CFLHD format standards – Match agreed to format, PDDM, CADD Standards Manuals, and Sample Plan Sheets. |  |
| Sheet numbers may be hand written |  |
| Project footprint checked against project mapping to determine need for additional surveys. Obscured areas in mapping are also reviewed. |  |
| Planimetric features shown in the project files are compared with the actual site and the need for additional surveys to tie in the features are determined (i.e. new access roads, cattleguards, utilities, and wetlands) |  |
| Insert design file path on all sheets (Place in lower left corner – outside of border) |  |
| All remaining alternatives are updated to reflect information obtained during development |  |
| TITLE SHEET |  |
| Use the Title Sheet Template at http://www.cflhd.gov/design/TemplateFiles/ |  |
| Location Map shows: |  |
| Proposed Begin & End Stations of Project |  |
| Distances to Nearest Large Destinations |  |
| Design Designations included for all major roadways (not only mainline). |  |
| CONVENTIONAL PLAN SYMBOLS AND ABBREVIATIONS |  |
| All Symbols and Abbreviations used in the plans match the Conventional Plan Symbols and Abbreviations Template at http://www.cflhd.gov/design/TemplateFiles/ |  |
| SITE PLAN |  |
| Preliminary section lines, property boundaries, and ownership; land marks (significant planimetric features); horizontal alignment; north arrow; and graphic scale |  |
| Previous CFLHD project boundaries and dates of construction, including projects under construction. Include all projects constructed during the previous 10 years. |  |
| TYPICAL SECTION(S) |  |
| Refine the typical sections |  |
| Use the Typical Section Sheet Template at http://www.cflhd.gov/design/TemplateFiles/ |  |
| Structural Section in Conformance with Geotechnical recommendations. All structural lifts shown. Future pavement, number of pavement lifts, item descriptions, prime, tack, and seal coats shown. |  |
| Show typical sections for guardrail, paved ditches, curb, subexcavation, and miscellaneous typical sections necessary to define the work. |  |
| Show typical transition details between different typical section types (address width and structural section depths) |  |
| Existing roadway typical section (widths, surfacing, and etc.) superimposed – dashed line. This may require a separate detail if too complicated (i.e., for clarity) |  |
| SUMMARY OF QUANTITIES |  |
| Use the Summary of Quantities Template at http://www.cflhd.gov/design/TemplateFiles/ |  |
| Quantities for all known bid items are computed (includes earthwork, surfacing quantities, drainage items, retaining walls, guardrail, curbs, revegetation, etc.) |  |
| Summary also includes: Item Numbers, Item Descriptions, and Pay Units (plan and bid) |  |
| show preliminary bridge items based on conceptual layout |  |
| DRAINAGE SUMMARY |  |
| Use the Drainage Summary Template at http://www.cflhd.gov/design/TemplateFiles/ |  |
| Develop preliminary drainage summary – Show all new culverts for all natural drainage areas. Showing ditch relief culverts is optional. |  |
| Show stationing, length, diameter, end treatments, and permanent erosion control devices (standard outlet protection; and special outlet protection for 1200 mm/48” or larger) |  |
| EARTHWORK SUMMARY |  |
| Preliminary Grading Summary and Mass Haul Diagram developed. Grading summary does not need to be broken down into station ranges. Only show total earthwork volumes. |  |
| Adjustments to horizontal and vertical alignments made to achieve an overall earthwork balance. If an overall balance CANNOT be ACHIEVED, identify borrow or waste needs. |  |
| Earthwork summary columns in accordance with Earthwork Representation Guidelines at http://www.cflhd.gov/design/_documents/technical_guides/earthwork_representation.pdf |  |
| Major earthwork volume adjustments listed in the summary (shrink/swell, topsoil stripping, subexcavation, approach roads, conserved materials, and retaining wall backfill and excavation). |  |
| HIGHWAY DESIGN STANDARDS |  |
| Project design standards determined using CFLHD and AASHTO guidelines (Green Book & Roadside Design Guide). Preliminary design incorporates: design speed, lane width, shoulder width, bridge width, structural design live load, grade, stopping sight distance, cross slope, superelevation, horizontal and vertical clearances, clear zone, roadside barriers, end treatments, and curve widenings. |  |
| Confirm design vehicle |  |
| AASHTO Roadside Design Guide reviewed for determination of roadside barriers, and end treatments. |  |
| Rollover is less than or equal to 8% between traveled way and shoulder (pullouts, adjacent parking areas, parking lanes, passing lanes, etc.) |  |
| Pedestrian and bicycle safety considered: separation between traveled way and bicycle/pedestrian facilities, width of facility, and vertical clearance determined. |  |
| Interactive Highway Safety Design Model used to evaluate the design and report generated submitted. |  |
| GEOMETRY |  |
| Horizontal Alignment – Refer to AASHTO Policy |  |
| Horizontal alignment revised based on reviews, environmental work, and comments |  |
| Horizontal alignment adjusted to best fit topography, minimize environmental and visual impacts, and to minimize overall project construction costs |  |
| Horizontal alignment uses curvilinear alignment concepts, the use of minimum curvature is avoided wherever possible, and flatter curves are generally used. |  |
| Horizontal alignment adjusted to facilitate construction and traffic (major structures, retaining walls) |  |
| The alignment follows the natural contours instead of having long tangents slashing though the terrain. |  |
| Alignment consistent with driver expectations |  |
| No sharp curves introduced at the ends of long tangents and no sudden changes from flat curves to sharp curves |  |
| Flatter curves or long tangents are transitioned to sharper curves through a succession of ever increasing curves. The curve radius and superelevation of adjacent curves limit the difference in design speed. |  |
| attempt to use very flat curvature on Long high fills |  |
| Small deflection angles have long curves |  |
| Sufficient distance is provided between curves for superelevation runoff (sum of the runoff lengths) or for spirals. |  |
| Broken-back or compound curves are not used, unless unavoidable situations justify use. Reasoning for use of such curves is documented. |  |
| Compound curves, the degree of the sharper curve is not more than 1.5 times that of the flatter curve |  |
| The minimum radius of curvature meets the requirements for the design speed and emax. Minimum radius for curvature should be avoided where practical. |  |
| Curve widening is included for sharper curves and the widening is correctly located with respect to the curve. |  |
| Adequate stopping sight distance is provided for all horizontal curves and it has been adjusted according to grade. The distance is documented. |  |
| Adequate passing sight distance is provided where required. The distance is documented. |  |
| Alignment adjusted for tie in with approach roads, parking areas, etc. |  |
| All coordinate geometry checked for tangency (no non-tangent curves), angle points are unacceptable. Curve parameters reviewed. |  |
| Avoid reverse curves, spirals, and changes to horizontal alignment on structures. |  |
| Vertical Alignment – Refer to AASHTO Policy |  |
| Vertical alignment revised based on reviews, environmental work, and comments |  |
| Vertical alignment adjusted to best fit topography, minimizes environmental and visual impacts, and minimizes overall project construction costs. |  |
| The grade line is rolled to take advantage of the topography and to reduce cut and fill heights where possible. Roller coaster or hidden dips are avoided |  |
| Vertical alignment adjusted for culvert cover requirements. |  |
| Maximum gradient not exceeded. |  |
| Minimum ditch grade of 0.5 percent is used, 1.0 percent preferred |  |
| Adequate passing opportunities have been provided if required (passing lanes, pullouts, shoulders) |  |
| Crest curves meet stopping sight distance requirements |  |
| Crest curves meet passing sight distance, if required. |  |
| Substantial lengths of momentum grades have been evaluated for their effect on traffic operations |  |
| On long grades an attempt has been made to place the steepest grades at the bottom and flatten the grades near the top. |  |
| Sag curves meet the headlight sight distance requirements. |  |
| Broken back or flat curves are avoided |  |
| Vertical alignment adjusted for tie in with approach roads, parking areas, etc. |  |
| Avoid sag vertical curves and changes to vertical alignment on structures. |  |
| Horizontal And Vertical Alignment Relationships |  |
| The horizontal curvature and grades are balanced (i.e. flatter curves used with flatter grades and sharper curves with steeper grades). On two-lane roads, the need for safe passing sections often supersedes the desirability for a well-coordinated line and grade. |  |
| Tangent grade superimposed on tangent line, and vertical curves on horizontal curves. |  |
| Horizontal curves lead vertical curves when they are superimposed. The length of the vertical curve should preferably approach that of the horizontal curve. Horizontal curves are not hidden behind crest vertical curves. |  |
| Sharp horizontal curvature and profile grade is as flat as possible at intersections where sight distance is important. |  |
| Sharp horizontal curvature not introduced near the bottom of a steep grade approaching or near the low point of a sag vertical curve. |  |
| Minimum radius horizontal curves are not superimposed on pronounced crest or sag vertical curves. |  |
| The alignment enhances scenic views, whether natural or manmade. The highway should head toward those views that are outstanding, it should descend toward those features of interest at a low elevation, and it should ascend toward those features best seen from below or in silhouette against the sky. |  |
| Superelevation |  |
| The maximum superelevation rate (emax) meets the guidelines for the specific roadway taking into consideration climate, urban or rural, design speed, etc. |  |
| The superelevations, superelevation runoffs, and tangent runout lengths meet the guidelines for emax design speed and radii. |  |
| The rotation point of superelevation shown and consistent with CFLHD guidelines. |  |
| The superelevation runout relative gradient matches those of the runoffs. |  |
| The superelevation runoff lengths located correctly with respect to the end of curve. |  |
| Superelevation at structures is consistent where possible |  |
| PLAN AND PROFILE PLAN SHEETS |  |
| Plan |  |
| Plan updated to include all comments and observations from the 15% field review |  |
| Information shown is clear and concise. Symbology is not cluttered. |  |
| Beginning and end of proposed construction shown |  |
| Identified and referenced to profile with arrow |  |
| Stations of terminus points shown |  |
| North Arrow (each sheet) |  |
| Township, Range, and Section No.’s (only on projects with Right-of-Way) |  |
| Updated preliminary horizontal alignment |  |
| Curve Data – curve name, PI station, delta, radius, tangent length, curve length, spiral lengths, and superelevation shown for each curve |  |
| Edge of Existing Roadway Shown |  |
| Limits of Disturbance shown (includes Cut & Fill Slope Stake, Rounding, & Clearing, Drainage Structures, Approach Roads, Obliteration, and Temporary traffic diversions) |  |
| Preliminary right-of-way limits shown – existing R/W and ownerships |  |
| Control Points – Point number and symbology (elevations not shown) |  |
| New and Existing Culverts |  |
| All new culverts for all natural drainage areas are to be shown. Showing ditch relief culverts is optional. |  |
| Identify boundaries of historic, cultural, and natural resources that require protection or special treatment. Add note to plans stating that references to historic, cultural, and natural resources will be removed from the plans at the 70% submittal and replaced with construction notes for the protection of site. |  |
| Planimetric features shown |  |
| Existing Creeks and Rivers shown w/correct names |  |
| Pullout/Parking Area |  |
| Show conceptual layout design details |  |
| Road Approaches |  |
| Major public road intersections have preliminary design |  |
| Show location of minor roads with standard symbol (type and class) |  |
| Review approach road grade and connection with mainline roadway to help determine adjustments to approach road location and mainline horizontal and vertical adjustments |  |
| Show preliminary guardrail, retaining wall, and paved ditch locations with linestyles, no text. |  |
| Existing Utilities (power, phone, & buildings). Show all utilities mapped during the S1, S2, and U1 activities. |  |
| Index contour lines show elevations (elevations are readable) |  |
| Profile |  |
| Profile updated to include all comments and observations from the 15% field review |  |
| Existing ground line shown and labeled |  |
| Proposed profile grade shown and labeled – maximum gradient not exceeded. |  |
| Length of Vertical Curves, K-Values, and stopping sight distance shown |  |
| Grid elevations |  |
| Profile grade agrees with Typical Section grade point location |  |
| VPI’s Stations and Elevations |  |
| Culvert locations agree with plan sheets and drainage summary |  |
| Culvert symbol(s) shown |  |
| Text shows station, culvert diameter and number of barrels. Showing length is optional |  |
| Correct culvert symbol and scale is used |  |
| Hydraulic Information for Large Culverts, 1200mm (48”) and above (design flow, drainage basin area, etc.) shown |  |
| Show retaining wall face outline |  |
| Show structure layout shape |  |
| Show preliminary low water crossing locations |  |
| HYDRAULICS |  |
| review and Incorporate all preliminary Hydraulics recommendations (from H2 activities) |  |
| GEOTECHNICAL |  |
| review and Incorporate all preliminary Geotech recommendations (from G2 activities) |  |
| ENVIRONMENT |  |
| Review the current environmental documents for the project. Become familiar with the environmental policy, impacts, and issues associated with the project. Support the environmental process as necessary |  |
| Environmental mitigation measures and commitments identified in the environmental document are incorporated into the design. |  |
| TEMPORARY TRAFFIC CONTROL |  |
| Identify areas where detours may need to be constructed (major structures), where part width construction is not possible without traffic delays/closures and/or costly mitigation (retaining walls), and alternate routes for traffic |  |
| ROAD APPROACHES |  |
| Update and refine preliminary horizontal and vertical alignments of major intersections. |  |
| PARKING AREAS |  |
| Update and refine preliminary layout of parking areas (include striping for large parking areas) |  |
| Turning and back-up movement, stall and aisle widths are reviewed for sufficiency |  |
| EROSION CONTROL |  |
| Research and prepare a list of CFLHD and local best management practices for construction activities for use on erosion control and revegetation plans |  |
| Incorporate erosion control standard and detail sheets showing the typical materials, installation, and dimensions of the erosion control devices proposed. Identify additional erosion control detail sheets and begin development. |  |
| Identify locations for sediment basins, including size requirements for the basins. |  |
| MAJOR STRUCTURES |  |
| Review and incorporate all preliminary Structural recommendations (from B2 activity) |  |
| Other large structures |  |
| Provide separate plan sheets for major culverts, culverts greater than 1.75 meter/72” diameter |  |
| Develop Preliminary Temporary shoring to accommodate traffic and facilitate construction |  |
| UTILITIES |  |
| Support utility locate activities |  |
| SURVEY |  |
| Review and incorporate Supplemental Survey Data (from S2 activity) |  |
| STANDARD DRAWINGS |  |
| Applicable FLH Standard Drawings included, current version |  |
| Applicable CFLHD Detail Drawings included, current version |  |
| ROADWAY CROSS-SECTIONS |  |
| Cut and fill slopes in accordance with the Geotechnical Memorandum |  |
| Cross-sections match Typical Section |  |
| intermediate stations are incorporated into the cross-sections at changes in subgrade width (i.e. guardrail terminal locations, culvert inlets, curve widening, pullouts, etc.). Locate changes in template width on 10 or 20 meter (25’ or 50’) stations where possible. Provide cross-sections on 10 meter (25’) intervals through retaining walls and on centerline curves with a radius of 75 meters (250’) or less. |  |
| Existing ground |  |
| Proposed cross-section showing all structural section layers |  |
| Curve widening, paved ditches, curbs, retaining walls, guardrail, etc. is incorporated |  |
| Slope ratios for all slopes outside of subgrade shoulder |  |
| Superelevation rates (m/m or ft/ft) between subgrade shoulders |  |
| Station, design grade, subgrade, and original ground elevations |  |
| Centerline symbol |  |
| Horizontal location of existing and proposed Right-of-Way limits |  |
| Horizontal and vertical location of utilities |  |
| Grid elevations and offset distances |  |
| CULVERT CROSS-SECTIONS |  |
| Cross-sections match Typical Section |  |
| Cross-sections show end treatments, including riprap and inlet and outlet ditches. |  |
| Culvert is located to match the natural stream gradient and proper cover is achieved |  |
| Culverts station and skew agree with plan and profile sheet |  |
| Text shows station. Culvert Slope shown on culvert cross-section with an arrow indicating direction of flow. |  |
| Culvert is drawn proportional to grid |  |
| Existing ground |  |
| Proposed cross-section (drawn along alignment of culvert) |  |
| Slope ratios shown for all slopes outside of subgrade shoulder |  |
| Superelevation rates (m/m or ft/ft) between subgrade shoulders |  |
| Horizontal location of existing and proposed Right-of-Way limits shown |  |
| Horizontal and vertical location of utilities shown |  |
| Show guardrail, retaining walls, and paved ditches symbols/shapes |  |
| Grid elevations and offset distances |  |
| RIGHT-OF-WAY |  |
| Review and incorporate preliminary right-of-way information |  |
| PLANS CONTAIN THE FOLLOWING SHEETS |  |
| Title sheet |  |
| Conventional Plan Symbols and Abbreviations |  |
| Site map |  |
| Typical sections |  |
| Miscellaneous typical section details |  |
| Summary of Quantities |  |
| Drainage summary |  |
| Grading Summary and Mass Haul Diagram |  |
| Mainline Plan and Profile |  |
| Major public intersecting road plan and profile |  |
| Preliminary TS&L sketch(s) |  |
| Erosion Control Standards & Details |  |
| Embankment benching detail |  |
| Placed riprap details |  |
| Pipe culvert Standards |  |
| Drop inlet specials |  |
| Underdrain details |  |
| Guardrail Standards |  |
| Fence and Gate Details |  |
| Cattleguard Standards |  |
| Widening for Cattleguard and Gate Detail |  |
| temporary traffic control Standards |  |
| Mainline cross-sections |  |
| Culvert pipe cross-sections |  |
| ESTIMATE |  |
| 30% Cost Estimate |  |
| Estimate to include all identified pay items, including: earthwork, surfacing quantities, bridges, drainage items, retaining walls, guardrail, curbs, revegetation, etc. |  |
| Preliminary Unit Price Analysis for all identified pay items |  |
| Traffic control, erosion control, etc, can be combined and a percentage of the total project used to compute cost as a lump sum for each category. |  |
| Preliminary cost estimate for bridges is on a square area basis |  |
| Cost estimate may be provided in a spreadsheet format or Engineer’s Estimate program |  |
| DELIVERABLES |  |
| 30% Plans |  |
| 30% Cost Estimate |  |
| Preliminary unit price analysis for identified bid items |  |
| 30% development checklist |  |
| 15% Comment and Response Tracking form |  |
| Update Preliminary Highway Design Standards form |  |
| Interactive Highway Safety Design Model report, including narrative explaining results |  |
| Draft Construction Schedule |  |
| Update Design Technical memorandum – Continue the documentation of the issues and concerns for the project |  |
| Recommendations for field work (i.e. Right-of-way boundaries, topographical surveys, planimetrics, etc.) |  |
| FIELD REVIEW |  |
| SC30 activity - Alignment Staking For 30% Field Review |  |
| Alignment staked on 40 meter (100 foot) stations for tangents and 50 foot (20 meters) for curves. As a minimum stake the beginning, end. and center point on short curves |  |
| Topography on mapping and DTM is ground truthed by visual observation, hand level, and cloth tape by designer at critical locations to confirm that the terrain is representative or not. |  |
| Prepare agenda for field review |  |
| Prepare a list of discussion topics for the field review |  |
| Check utilities – visible, crossing, approaches, etc. |  |
| Determine all proposed ditch relief culvert locations |  |
| Review proposed design at all natural drainages |  |
| Review Geotechnical recommendations |  |
| Review overall footprint (impacts) |  |
| Review intersections, mailbox areas, wall areas, etc. |  |
| Produce a master redlined plan set with field review comments for inclusion in the 50% design |  |
| Prepare trip report |  |

# COMMENTS