NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 11/21/2003, 12/20/2006

LOCATION: Fayetteville

STREAM: Elk River

BASIN: Elk                              HSA: HUN

REFERENCES:

USGS description of gaging station, TVA hydrologic branch.

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: FYTT1

NWS INDEX NUMBER: 244227796

USGS NUMBER:

MAP OF GAGE LOCATION

LATITUDE: 35 08 04  		SOURCE:

LONGITUDE: 86 32 23

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  650.580         VERTICAL DATUM:

LEVELING AGENCY AND DATE:                        CHECKBAR:

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------     -------

RM1           A standard USGS reference tablet set in solid rock 12 feet downstream from       21.400     671.980

the walkway to the gage house.

RM3           A bolt set in concrete block at the end of the upstream walkway.                 28.170     678.750

RM4           A chiseled square in the downstream shoreward corner of the old concrete         19.180     669.760

walkway support...10 feet from the gage.

RM5           A chiseled square in the top of the concrete outside gage support 6 feet          4.340     654.920

landward from the gage.

RP1           A 3/8 inch lag screw in the top of a 2 X 6 outside gage backing board.           27.180     677.760

RP2           A chiseled square on the landward side of the cleanout door still.                9.540     660.120

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID:                         TYPE OF TELEMETRY:

OWNER:                                     OWNER:

REPORT TIME:                              PHONE NUMBER:

INTERVAL:                                  INTERVAL:

PAYOR/COST OF LINE:  / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- ------------------------------------------------------

float       USGS        USGS        10/01/1925 09/01/1934

float       USGS        USGS        09/01/1934 01/01/1982

wireweight  TVA         TVA         10/16/1968            Upstream side of Hwy 231 bridge in Fayetteville. 									  Bankfull stage is near 665.0 ft on this wire weight.

float       TVA         TVA         01/01/1982            Eldad Road Bridge near the water treatment plant.							                 Just upstream (east) of the city of Fayetteville.

tape        TVA         TVA         01/01/1997            Highway 64 bridge near the Frito-Lay Plant.  This is								  the Local Warning Gage that activates the automatic            	   	                                               calling system.  Bankfull stage is near 12.7 feet.

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

float                     USGS        10/01/1925       09/01/1934

float                     USGS        09/01/1934       01/01/1982

wireweight                TVA         10/16/1968

float                     TVA         01/01/1982

tape                      TVA         01/01/1997

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 17.50    ACTION STAGE: 14.00     BANKFULL STAGE:

FLOOD FLOW:           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ----------------------------------------------

03/13/1842 UNDEF   27.50  37000

03/23/1929 UNDEF   27.20  36000

01/05/1949 UNDEF   27.20

02/03/1957 UNDEF   26.70

03/12/1963 UNDEF   27.20  36500

03/16/1973 UNDEF   28.60  41600     X

03/21/1980 UNDEF   22.85  22200

12/23/1990 UNDEF   29.52  45200                                FLOOD OF RECORD

02/20/1991 UNDEF   24.00

12/02/1991 UNDEF   20.74

12/01/1996 UNDEF   18.40  13400

03/03/1997 UNDEF   18.40  13400

06/09/1997 UNDEF   17.51  12100

01/08/1998 UNDEF   23.60  24400

02/06/2004 14:00   21.99

12/07/2004 22:45   20.26                                       Inserted from the FloodTS table via Hydrobase

12/10/2004 11:45   20.22                                       Inserted from the FloodTS table via Hydrobase

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

12/09/1970     0.75      67

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 93.9       DRAINAGE AREA: 827.0      POOL STAGE:

STREAM BED: gravel and silt

REACH: Fayetteville

REGULATION: Flow is affected by releases from Tims Ford Dam and Woods

Reservoir.  Fayetteville Water Plant can divert water

through the plant.

DIVERSION: None.

WINTER: Some ice during extreme winters.

TOPOGRAPHY: The right bank is steep and does not normally overflow. The

left bank overflows at around 16 feet.  Both banks are

tree-lined.

REMARKS: Area to flood lies from Highway 65 to the mouth of Norris

Creek.  Backwater starts at 660 feet MSL.

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  -------------------------------------------------------------------------------------------------

17.50  Flood Stage. Bottomland along the river begins to flood.

20.70  Moderate Flooding. Flood waters reach the city pumping station.

21.00  Flood waters reach residential areas in low-lying areas of town.

23.50  Flood water covers Highway 273 at several locations in and around Fayetteville.

26.00  Major flooding. Several businesses and homes are flooded.

29.52  Record flood.

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  33-|

|-----|

|-----|

|-----|

|-----|

|  31-|

|-----|

|-----|

|-----|

29.52 - Record flood.                                                                           |-----|   29.52  12/23/1990

|  29-|

|-----|

|-----|   28.60  03/16/1973

|-----|

|-----|   27.50  03/13/1842

|  27-|   27.20  03/23/1929

|-----|   26.70  02/03/1957

|-----|

26.00 - Major flooding. Several businesses and homes are flooded.                               |-----|

|-----|

|  25-|

|-----|

|-----|

|-----|   24.00  02/20/1991

23.50 - Flood water covers Highway 273 at several locations in and around Fayetteville.         |-----|   23.60  01/08/1998

|  23-|

|-----|   22.85  03/21/1980

|-----|

|-----|   21.99  02/06/2004

|-----|

|  21-|

21.00 - Flood waters reach residential areas in low-lying areas of town.                        |-----|   20.74  12/02/1991

20.70 - Moderate Flooding. Flood waters reach the city pumping station.                         |-----|   20.26  12/07/2004

|-----|

|-----|

|  19-|

|-----|

|-----|   18.40  12/01/1996

|-----|

17.50 - Flood Stage. Bottomland along the river begins to flood.                                |-----|   17.51  06/09/1997

|  17-|

|-----|

|-----|

|-----|

|-----|

|  15-|

|-----|

|-----|

|-----|

|-----|

|  13-|

REACH: Fayetteville                                                                    	ELEVATION ZERO:  650.58

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

0  Fayetteville PD                                    931-438-4522

0  Highway Department                                 931-433-2585

0  Lincoln County EMA                                 931-438-1575

They read the river gages at Kelso and Hwy 231.

We CANNOT request that they read the Hwy 231

gage as it does not meet OSHA regulations.

LOCATION: Elk River NEAR Fayetteville, TN                           Revised, Printed Dates: 11/21/2003, 12/20/2006

ID: FYTT1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

Backwater floods the “new park” in Fayetteville (Stone Bridge Memorial Park)