NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 12/20/2006, 12/20/2006

LOCATION: Whitesburg

STREAM: Tennessee River

BASIN: Tennessee                        HSA: HUN

REFERENCES:

DATED 5/8/89

USGS DESCRIPTION OF GAGE STATION...WATER RESOURCES DATA

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level	TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: WHIA1

NWS INDEX NUMBER: 03575500

USGS NUMBER: 03575500

MAP OF GAGE LOCATION

LATITUDE: 34 34 18  		SOURCE: USGS

LONGITUDE: 86 33 29

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  549.000         VERTICAL DATUM: NGVD OF 1929

LEVELING AGENCY AND DATE: Level                  CHECKBAR:   56.130

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------     -------

CSG           TOP OF BOTTOM CAP ON 2 INCH PIPE OF CREST STREAM GAGE.                           24.500     573.500

RM1           IS A STANDARD BRONZE DISK MARKED WSR-63R, SET IN A STANDARD POST ON RIGHT        18.630     567.630

BANK OF TN RIVER, .3 MILE UPSTREAM FROM HIGHWAY BRIDGE, 10 FT NORTH OF

OLD GRAVEL ROAD ALONG RIVER.

RM10          (ABANDONED) A CHISELED SQUARE ON THE NORTHEAST CORNER OF THE GUARDRAIL OF        25.730     574.730

THE STATE DOCKS WHARF, 80 FT UPSTREAM FROM THE PIPE WELL, AND 100 FT

STREAMWARD FROM THE BUBBLE GAGE.

RM11          (ABANDONED) IS A CHISELED SQUARE ON THE TOP OF THE NORTHWEST CORNER OF THE       29.140     578.140

LOADING PLATFORM OF THE STATE WAREHOUSE, 95 FT UPSTREAM FROM BUBBLE GAGE,

AND 10 FT STREAMWARD FROM THE BUBBLE GAGE.

RM12          (ABANDONED) THE HEAD OF A 1/2 INCH LAG BOLT DRIVEN HORIZONTALLY IN THE           16.400     565.400

SHOREWARD SIDE OF THE NORTHWEST CORNER AND ABOUT A HALF FOOT FROM THE TOP

OF CRIBBING BUNKER, 20 FT DOWNSTREAM FROM THE BUBBLE GAGE.

RM13          (ABANDONED) THE HEAD OF A 1/2 INCH LAG BOLT DRIVEN HORIZONTALLY IN THE DS        15.150     564.150

SIDE, ABOUT 1.5 FT FROM THE TOP, AND 4 FT FROM THE NW CORNER OF A

CRIBBING BUNKER LOCATED 20 FEET FROM THE BUBBLE GAGE, 811 FT US FROM THE

PIPE WELL.

RM14          A CHISELED SQUARE 40 FT RIVERWARD FROM RM15 IN TOP OF SOME CONCRETE               8.260     557.260

CURBING AT DOWNSTREAM, RIVERWARD CORNER OF CONCRETE DOCK 2 FT LANDWARD

FROM STEEL LIGHT POLE.

RM15          CHISELED SQUARE ON THE CONCRETE CURB 40 FT LANDWARD FROM RM14, IN THE            25.713     574.713

VICINITY OF THE ORIFICE LINES AND NEAR THE CORNER OF THE CURBING.

RM16          USGS/TVA BRASS DISC ON THE STEPS UP TO THE LOADING DOCK OF THE WAREHOUSE         26.110     575.110

RM17          CHISELED SQUARE ON THE PLATFORM LEVEL OF THE LOADING DOCK OF THE OLD             29.102     578.102

WAREHOUSE.

RM3           A STANDARD USGS BENCHMARK TABLET, STAMPED 41, SET IN THE TOP OF THE DS END       34.090     583.090

OF THE RIGHT BANK PIER OF THE HIGHWAY BRIDGE, 1/2 MILE BELOW GAGE.

RM8           (ABANDONED) THE HEAD OF A 1/2 INCH LAG BOLT DRIVEN HORIZONTALLY IN THE TOP       17.450     566.450

OF THE UPSTREAM ROOT OF A 20 INCH SWEETGUM TREE. THE TREE IS 15 FT UP

FROM THE PIPE-WELL GAGE AND 10 FT STREAMWARD FROM THE TOP OF THE BANK.

RM9           (ABANDONED) THE HEAD OF A 1/2 INCH LAG BOLT DRIVEN HORIZONTALLY IN THE           18.380     567.380

DOWNSTREAM SIDE OF A 20 INCH SWEETGUM TREE. (SAME TREE AS RM 8)

RP1           ARROW ON WIRE-WEIGHT GAGE.                                                       25.245     574.245

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID: 17B6B162                TYPE OF TELEMETRY: telemark

OWNER: USGS                                OWNER: TVA

REPORT TIME: 01:42                        PHONE NUMBER: 256-881-0970

INTERVAL: 240                              INTERVAL: UNK

CRITERIA: NONE

PAYOR/COST OF LINE: TVA / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- --------------------------------------------------------

pres trans  TVA         USGS        03/04/1937 11/24/1959 DIGITAL RECORDER. RECORDER WAS LOCATED IN 48 INCH 	 	                                                     CORRUGATED STEEL PIPE WELL 800 FT DOWNSTREAM.

wireweight  USGS        USGS        03/04/1937            THE OUTSIDE GAGE IS A WIRE-WEIGHT GAGE ATTACHED TO THE

DOWNSTREAM SIDE OF THE STATE DOCKS LOADING PLATFORM AND

VERY NEAR THE ORIFICE.

pres trans  TVA         USGS        11/24/1959 04/14/1965 BUBBLE GAGE. A BALANCE BEAM MANOMETER.

pres trans  TVA         USGS        04/14/1965 06/07/1989 DIGITAL RECORDER AND MERCURY MANOMETER, MODEL 4A. SERVO	                                                     WAS THE PROPERTY OF TVA.

pres trans  TVA         USGS        06/07/1989            CR-19 DATALOGGER WITH SM1922 OPERATED BY A PS-2 PRESSURE

TRANSDUCER. THE RECORDING EQUIPMENT IS HOUSED IN A ARMCO

STEEL SHELTER 5'4" X 5'4" X 8' OVER A CONCRETE SLAB. THE

SHELTER IS LOCATED ABOUT 150 FT FROM TOP OF RT BANK AND	                                                     100 FT DS OF STATE DOCKS.

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

USGS MEM                              03/04/1937

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

pres trans                TVA         03/04/1937       11/24/1959

wireweight                USGS        03/04/1937

pres trans                TVA         11/24/1959       04/14/1965

pres trans                TVA         04/14/1965       06/07/1989

pres trans                TVA         06/07/1989

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

549.000                              03/04/1937

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 17.00    ACTION STAGE: 15.00     BANKFULL STAGE: 11.00

FLOOD FLOW: 0           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- -----------------------------------------------

04/11/1938 UNDEF   15.40

02/18/1939 UNDEF   20.30

12/31/1942 UNDEF   21.60

03/30/1944 UNDEF   20.50

02/20/1945 UNDEF   14.20

01/09/1946 UNDEF   23.10

01/22/1947 UNDEF   21.00

02/15/1948 UNDEF   23.00

01/06/1949 UNDEF   22.90

03/15/1950 UNDEF   19.40

03/30/1951 UNDEF   21.50

03/13/1952 UNDEF   16.30

02/24/1953 UNDEF   14.80

01/23/1954 UNDEF   22.00

03/24/1955 UNDEF   16.60

02/06/1956 UNDEF   19.80

02/02/1957 UNDEF   23.93 293000

12/21/1959 UNDEF   13.00

02/25/1961 UNDEF   20.53 234000

02/27/1962 UNDEF   21.64 252000

03/14/1963 UNDEF   23.40 285000

03/16/1964 UNDEF   18.00 199000

03/30/1965 UNDEF   21.51 244000

02/17/1966 UNDEF   14.60 152000

03/15/1967 UNDEF   31.40            X                          PRIOR TO PERIOD OF RECORD

07/09/1967 UNDEF   13.86 128000

12/23/1967 UNDEF   18.00 191000

02/04/1969 UNDEF   19.20 213000

01/02/1970 UNDEF   20.30 227000

02/28/1971 UNDEF   13.10 128000

03/19/1973 UNDEF   26.10 323000                                FLOOD OF RECORD

12/28/1973 UNDEF   19.75 216000

03/15/1975 UNDEF   20.90 230000

01/04/1976 UNDEF    9.56  91400

04/07/1977 UNDEF   20.40 222000

11/30/1977 UNDEF   14.70 141000

03/06/1979 UNDEF   19.75 217000

03/22/1980 UNDEF   22.01 250000

04/05/1981 UNDEF    8.74  51400

01/05/1982 UNDEF   17.92 189000

04/07/1983 UNDEF   16.80 168000

05/10/1984 UNDEF   21.65 245000

02/02/1985 UNDEF   11.30 113000

03/01/1987 UNDEF   15.32 156000

01/22/1988 UNDEF   13.24 121000

06/23/1989 UNDEF   16.80 183000

02/17/1990 UNDEF   22.00 260000

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- -----------------------------------------------

12/25/1990 UNDEF   24.80 304000

12/04/1991 UNDEF   20.09 217000

03/25/1993 UNDEF   17.35 176000

03/30/1994 UNDEF   22.40 268000

03/05/1997 UNDEF   17.30

03/05/1998 UNDEF   17.30

04/22/1998 UNDEF   19.50

01/25/1999 UNDEF   13.33

04/05/2000 UNDEF   18.17 193000

02/18/2003 UNDEF   19.80

02/24/2003 UNDEF   17.40

05/09/2003 20:15   24.67

02/08/2004 08:00   16.65

09/19/2004 17:45   18.48                                       Inserted from the FloodTS table via Hydrobase

12/11/2004 06:45   22.00                                       Inserted from the FloodTS table via Hydrobase

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-2: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

08/19/1925    -0.40

07/16/1937     0.06

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 333.9      DRAINAGE AREA: 25610.0     POOL STAGE: 0.0

STREAM BED: ROCK AND GRAVEL

REACH: MOUTH OF PAINT ROCK RIVER (MI 343.2) TO MOUTH OF INDIAN

CREEK (MI 320.9)

REGULATION: REGULATED BY GUNTERSVILLE AND WHEELER DAMS.

DIVERSION: UNKNOWN.

WINTER: NO EFFECT

TOPOGRAPHY: BOTH BANKS EXCEEDINGLY LOW, A LOW RIDGE RISES STEEPLY

ELEVATIONS ABOVE 740 FT NEXT TO RIGHT BANK.

REMARKS:

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  -------------------------------------------------------------------------------------------------

11.00  THE RIVER BACKS UP INTO SOME SLOUGHS AND APPEARS TO BE FLOODING BUT IT ACTUALLY IS NOT.

14.00  THE RIVER STARTS TO COVER RAMPS AT THE MADISON COUNTY BOAT HARBOR AT DITTO LANDING...AS WELL AS

PASTURELAND NEAR THE RIVER. BACKWATER FROM ALDRIDGE CREEK COVERS PART OF THE DITTO LANDING WALKING

TRAIL.

17.00  FLOOD STAGE. LOWLAND FLOODING BEGINS. SOME ACCESS ROADS IN THE AREA BECOME FLOODED.

19.00  THE ENTRANCE TO THE DITTO LANDING AREA IS UNDERWATER...ALONG WITH MUCH OF THE BOAT HARBOR. SEVERAL

ROADS IN NORTHEASTERN MORGAN COUNTY ARE UNDERWATER...AND WATER IS BEGINNING TO APPROACH HOMES ON

RIVER LOOP ROAD IN THE LACEYS SPRING COMMUNITY.

20.00  MODERATE FLOODING.

23.00  MAJOR FLOODING. HOBBS ISLAND IS FLOODED.

24.00  ACCESS ROADS TO REDSTONE ARSENAL FROM THE EAST ARE CLOSED.

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  29-|

|-----|

|-----|

|-----|

|-----|

|  27-|

|-----|

|-----|

|-----|   26.10  03/19/1973

|-----|

|  25-|

|-----|   24.80  12/25/1990

|-----|

24.00 - ACCESS ROADS TO REDSTONE ARSENAL FROM THE EAST ARE CLOSED.                              |-----|   23.93  02/02/1957

|-----|

|  23-|   23.40  03/14/1963

23.00 - MAJOR FLOODING. HOBBS ISLAND IS FLOODED.                                                |-----|   23.00  02/15/1948

|-----|   22.40  03/30/1994

|-----|   22.00  01/23/1954

|-----|   21.65  05/10/1984

|  21-|

|-----|   20.90  03/15/1975

|-----|

20.00 - MODERATE FLOODING.                                                                      |-----|   20.09  12/04/1991

|-----|   19.80  02/18/2003

|  19-|

19.00 - THE ENTRANCE TO THE DITTO LANDING AREA IS UNDERWATER...ALONG WITH MUCH OF THE BOAT      |-----|

HARBOR. SEVERAL ROADS IN NORTHEASTERN MORGAN COUNTY ARE UNDERWATER...AND WATER IS       |-----|   18.48  09/19/2004

BEGINNING TO APPROACH HOMES ON RIVER LOOP ROAD IN THE LACEYS SPRING COMMUNITY.          |-----|

|-----|

|  17-|   17.40  02/24/2003

17.00 - FLOOD STAGE. LOWLAND FLOODING BEGINS. SOME ACCESS ROADS IN THE AREA BECOME FLOODED.     |-----|   16.80  06/23/1989

|-----|

|-----|

|-----|

|  15-|   15.32  03/01/1987

|-----|   14.70  11/30/1977

|-----|

14.00 - THE RIVER STARTS TO COVER RAMPS AT THE MADISON COUNTY BOAT HARBOR AT DITTO              |-----|

LANDING...AS WELL AS PASTURELAND NEAR THE RIVER. BACKWATER FROM ALDRIDGE CREEK          |-----|

COVERS PART OF THE DITTO LANDING WALKING TRAIL.                                         |  13-|   13.24  01/22/1988

|-----|

|-----|

|-----|

|-----|

|  11-|

11.00 - THE RIVER BACKS UP INTO SOME SLOUGHS AND APPEARS TO BE FLOODING BUT IT ACTUALLY IS      |-----|

NOT.                                                                                    |-----|

|-----|

|-----|

REACH: MOUTH OF PAINT ROCK RIVER (MI 343.2) TO MOUTH OF INDIAN CREEK (MI 320.9)        	ELEVATION ZERO:  549.00

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Madison County EMA                                 256-427-5130

Director: John Rusty Russell

2  Ditto Landing Marina                               256-883-9420

3  Redstone Arsenal                                   256-876-4105

In very extreme events...may need to contact due

to road closures.

LOCATION: Tennessee River AT Whitesburg, AL                         Revised, Printed Dates: 12/20/2006, 12/20/2006

ID: WHIA1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

View of the gage house.

Flooding of the Aldridge Creek Greenway at Ditto Landing.