NWS FORM E-19 (COVER)

U.S. DEPARTMENT OF COMMERCE

NATIONAL OCEANIC AND ATMOSPHERIC ADMINISTRATION

NATIONAL WEATHER SERVICE

REPORT ON RIVER GAGE STATION

REVISED, PRINTED DATES: 11/20/2003, 12/20/2006

LOCATION: Florence

STREAM: Tennessee River

BASIN: Tennessee                        HSA: HUN

REFERENCES:

UPDATED 03/23/2000

USGS DESCRIPTION OF GAGING STATION DATED 2/14/1978

ABBREVIATIONS:

BM  - bench mark		EPA   - Environmental Protection Agency

DS  - downstream		IBWC  - International Boundary and Water Comm.

US  - upstream		MSRC  - Mississippi River Commission

HW  - high water		MORC  - Missouri River Commission

LW  - low water		NOAA  - National Oceanic and Atmospheric Admin.

RB  - right bank		NOS   - National Ocean Survey

LB  - left bank		NWS   - National Weather Service

MGL - mean gulf level		TVA   - Tennessee Valley Authority

MLW - mean low water		USACE - U.S. Army Corps of Engineers

MSL - mean sea level		USBR  - U.S. Bureau of Reclamation

MLT - mean low tide		USGS  - U.S. Geological Survey

MT  - mean tide		USWB  - U.S. Weather Bureau

WQ  - water quality		NGVD  - National Geodetic Vertical Datum

RM  - reference mark		NAD   - North American Datum

RP  - reference point

LOCATION IDENTIFICATION: FLOA1

NWS INDEX NUMBER: 03589500

USGS NUMBER: 03589500

MAP OF GAGE LOCATION

LATITUDE: 34 47 13  		SOURCE: USGS

LONGITUDE: 87 40 12

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 1: GAGE MAP

BENCHMARKS

ELEVATION OF GAGE ZERO:  401.120         VERTICAL DATUM: NGVD OF 1992

LEVELING AGENCY AND DATE: Level                  CHECKBAR:    0.000

RATING AGENCY:

BENCHMARK     DESCRIPTION                                                                   GAGE ZERO      DATUM

----------------------------------------------------------------------------------------    ---------      ------

RM10          (TVA) TOP OF 1 INCH TIEDOWN BOLT IN THE NORTHWEST CORNER OF FOOT PLATE ON        30.500     431.620

SECOND UPSTREAM FOOTING, NORTH OF SOUTH WATER STREET, OF THE SOUTHERN

RAILROAD BRIDGE.

RM11          A CHISELED SQUARE ON UPSTREAM STREAMWARD EDGE OF SECOND STEP LEADING TO          29.392     430.512

GAGE HOUSE.

RM12          TOP OF 1/2 INCH LAG BOLT IN TELEPHONE POLE 20 FT DOWNSTREAM OF STEPS TO          30.494     431.614

GAGE HOUSE.

RM13          TOP OF NUT ON 1/2 INCH ANCHOR 1/2 FOOT DOWNSTREAM OF GAGE DOOR SILL IN           32.600     433.720

WELL WALL.

RM7           (PBM 73 USE) IS A STANDARD USE BENCHMARK TABLET, STAMPED "73" SET IN THE         21.507     422.627

TOP OF THE LOWER END OF  THE RIGHT CONCRETE LOCK WALL AT LOCK AND DAM

1,600 FT. UPSTREAM FROM THE GAGE.

RM8           (ABANDONED) A 2 INCH CHISELED SQUARE CUT INTO THE STEEL DOOR SILL AT THE         32.500     433.620

UPSTREAM STREAMWARD CORNER OF THE DOOR TO THE GAGE HOUSE.

RM9            A BRONZE TABLET SET IN TOP OF THE NORTH SIDE OF THE SECOND UPSTREAM              30.320     431.440

FOOTING, NORTH OF SOUTH WATER STREET, OF THE SOUTHERN RAILROAD BRIDGE.

RP10          (ABANDONED) A CHISELED ARROW CUT INTO THE CENTER OF THE STREAMWARD EDGE OF       16.880     418.000

THE STREAMWARD VALVE HANDLE BRACE INSIDE THE CLEANOUT DOOR.

RP11          (ABANDONED) AN ARROW CUT INTO SHOREWARD SIDE OF TRAP DOOR IN GAGE HOUSE.         32.508     433.628

RP12          (ABANDONED) AN ARROW CUT INTO FIRST ANGLE HANDRAIL BRACE FROM GAGE ON            31.522     432.642

BOTTOM OF WALKWAY.

RP13          (ABANDONED) AN ARROW CUT INTO TOP OF DOWNSTREAM SHOREWARD CORNER OF I-BEAM       14.906     416.026

SUPPORTING LOWER STAFF SECTION.

RP14          BETWEEN CUT MARKS ON ANGLE AT BOTTOM OF DOOR BELOW GAGE ITSELF.                  32.692     433.812

RP15          CUT MARK ON UPSTREAM SIDE OF LOWER STAFF SECTION AND STREAMWARD CORNER OF        14.914     416.034

I BEAM.

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 2: BENCHMARKS

GAGES

DCP                                        TELEM

NESS ID: 16F473F6                TYPE OF TELEMETRY: telemark

OWNER: USGS                                OWNER: USGS

REPORT TIME: 01:11                        PHONE NUMBER: 256-767-7521

INTERVAL: 240                              INTERVAL: UNK

CRITERIA: NONE

PAYOR/COST OF LINE: USGS / $

GAGE TYPE   OWNER       MAINTENANCE BEGAN      ENDED      GAGE LOCATION/REMARKS

----------- ----------- ----------- ---------- ---------- -------------------------------------------------------

float       USGS        USGS        04/03/1926 05/17/1934 WATER-STAGE RECORDER ON LEFT BANK AT LOWER END OF OLD LOCK

AND DAM, 1400FT.

float       USGS        USGS        05/17/1934 07/07/1939 AU CONTINUOUS RECORDER.

float       TVA         USGS        07/07/1939 01/31/1958 FRIEZ RECORDER.

Unk         TVA         Unk         02/01/1958 03/11/1958 TVA TEMPORARY GAGE USED.

float       USGS        USGS        03/11/1958            PRESENT GAGE AT MILE 256.7, 137 FEET UPSTREAM FROM 					                            RAILROAD BRIDGE AND 2.7 MILES DOWNSTREAM FROM WILSON DAM.

float       USGS        USGS        03/11/1965 08/26/1999 DIGITAL RECORDER.

crest       USGS        USGS        09/26/1996            CREST STAGE GAGE IS A 2" GALVANIZED PIPE ATTACHED TO THE

SHOREWARD SIDE OF THE GAGE HOUSE AT THE DOWNSTREAM CORNER.

pres trans  USGS        USGS        08/26/1999            CR10 DATA LOGGER WITH MODEM, SM192 MODULE AND PRESSURE

SENSOR IN A 5' BY 5' CONCRETE HOUSE. RECORDER IS REFERRED

TO A STAFF GAGE IN 3 SECTIONS. ORIFICE LINE FOR PRESSURE

SENSOR ATTACHED TO STAFF PLATE I-BEAM AND CONCRETE BLOCK	                                                  IN STREAM.

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 3: GAGES

HISTORY

PUBLICATION/LOCATION OF RECORDS       STARTING DATE    ENDING DATE

-------------------------------       -------------    -----------

USGS                                  11/06/1971

TYPE OF GAGE              OWNER       STARTING DATE    ENDING DATE

------------              -----       -------------    -----------

float                     USGS        04/03/1926       05/17/1934

float                     USGS        05/17/1934       07/07/1939

float                     TVA         07/07/1939       01/31/1958

Unk                       TVA         02/01/1958       03/11/1958

float                     USGS        03/11/1958

float                     USGS        03/11/1965       08/26/1999

crest                     USGS        09/26/1996

pres trans                USGS        08/26/1999

ZERO ELEVATION                        STARTING DATE

--------------                        -------------

401.120                              11/06/1971

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 4: HISTORY

CRESTS

FLOOD STAGE: 18.00    ACTION STAGE: 16.00     BANKFULL STAGE: 18.00

FLOOD FLOW:           ACTION FLOW:

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ----------------------------------------------

03/19/1897 UNDEF   32.50 444000                                FLOOD OF RECORD

04/20/1900 UNDEF   19.20

08/22/1901 UNDEF   18.90

03/08/1902 UNDEF   20.90

03/06/1903 UNDEF   18.90

03/15/1909 UNDEF   19.60

04/10/1911 UNDEF   22.00

04/13/1912 UNDEF   19.60

03/21/1913 UNDEF   18.50

12/31/1914 UNDEF   19.20

07/12/1916 UNDEF   20.50

03/12/1917 UNDEF   24.70

02/06/1918 UNDEF   22.00

05/09/1919 UNDEF   19.50

04/10/1920 UNDEF   23.50

02/13/1921 UNDEF   18.70

03/11/1922 UNDEF   21.50

02/11/1923 UNDEF   18.20

12/29/1926 UNDEF   26.50

04/24/1928 UNDEF   18.40

03/25/1929 UNDEF   22.90

02/04/1932 UNDEF   19.70

02/20/1933 UNDEF   21.20

03/05/1934 UNDEF   21.20

04/06/1936 UNDEF   24.40

01/04/1937 UNDEF   20.30

04/12/1938 UNDEF   21.10

02/17/1939 UNDEF   25.00

03/22/1942 UNDEF   18.10

01/02/1943 UNDEF   23.20

03/30/1944 UNDEF   25.60

02/22/1945 UNDEF   21.50

01/11/1946 UNDEF   25.10

01/20/1947 UNDEF   23.70

02/13/1948 UNDEF   28.00

01/08/1949 UNDEF   25.80

02/14/1950 UNDEF   22.50

03/29/1951 UNDEF   24.10

02/23/1953 UNDEF   18.20

01/23/1954 UNDEF   23.30

03/22/1955 UNDEF   25.70

02/05/1956 UNDEF   22.30

02/04/1957 UNDEF   26.20

03/08/1961 UNDEF   21.22 240000

02/28/1962 UNDEF   24.60 300000

03/14/1963 UNDEF   24.50 339000

03/15/1964 UNDEF   21.93 282000

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 5: CRESTS

DATE OF    TIME   CREST  FLOW   FROM HIGH  BASED ON  CAUSED BY

CREST      LST    (ft)   (CFS)  WATERMARKS OLD DATUM ICE JAM   REMARKS

---------- ------ ------ ------ ---------- --------- --------- ----------------------------------------------

03/30/1965 UNDEF   24.60 341000

02/18/1966 UNDEF   16.30 171000

03/07/1967 UNDEF   15.49 164000

01/10/1968 UNDEF   20.82 260000

02/02/1969 UNDEF   21.00 267000

01/02/1970 UNDEF   21.01 250000

02/22/1971 UNDEF   18.80 196000

01/11/1972 UNDEF   18.31 171000

03/17/1973 UNDEF   30.03 530000

01/11/1974 UNDEF   25.03 327000

03/14/1975 UNDEF   25.00 341000

10/17/1975 UNDEF   18.54 185000

04/08/1977 UNDEF   21.81 252000

05/09/1978 UNDEF   21.74 226000

03/06/1979 UNDEF   20.21 237000

03/22/1980 UNDEF   24.83 336000

01/05/1982 UNDEF   20.06 234000

05/22/1983 UNDEF   23.06 273000

05/04/1984 UNDEF   23.81 339000

02/05/1985 UNDEF   15.42 159000

03/01/1987 UNDEF   20.92 243000

01/22/1988 UNDEF   14.46 142000

06/22/1989 UNDEF   21.71

11/02/1989 UNDEF   21.91 318000

12/23/1990 UNDEF   27.58 440000

12/03/1991 UNDEF   25.12 332000

03/27/1993 UNDEF   20.83 222000

03/28/1994 UNDEF   25.53 364000

03/03/1997 UNDEF   21.50

05/05/1997 UNDEF   19.50

06/18/1997 UNDEF   20.10

03/03/1998 UNDEF   21.50

04/22/1998 UNDEF   20.40

01/24/1999 UNDEF   20.10

02/19/2001 12:00   19.16

02/18/2003 23:15   21.94

05/07/2003 05:15   25.53

02/09/2004 13:30   20.44                                      gage was inoperative for several hours...crest						                        was estimated

09/19/2004 06:15   20.01

09/19/2004 12:45   20.53                                      Inserted from the FloodTS table via Hydrobase

09/20/2004 13:45   20.75

09/22/2004 13:15   18.80

11/26/2004 21:15   19.07                                      Inserted from the FloodTS table via Hydrobase

12/01/2004 22:30   20.58                                      Inserted from the FloodTS table via Hydrobase

12/10/2004 09:00   25.98                                      Inserted from the FloodTS table via Hydrobase

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                   NWS FORM E-19 PAGE 5-2: CRESTS

LOW WATER RECORDS

DATE OF     STAGE    FLOW

LOW WATER   (ft)     (CFS)   REMARKS

----------  -------  ------  ---------------------------------------------

10/08/1925    -0.30          caused by filling of wilson lake

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 6: LOW WATER

CONDITIONS AFFECTING FLOW

MILES ABOVE MOUTH: 256.7      DRAINAGE AREA: 30810.0     POOL STAGE: 0.0

STREAM BED: gravel and sill

REACH: levees protect an area in the vicinity of the gage (RB) to

above 431.15 ft MSL.

REGULATION: Flow regulated by power plants and storage at numerous dams

upstream. Power operation at Wilson Dam 2-3/4 miles

upstream.

DIVERSION: none

WINTER: very little ice effect occurs.

TOPOGRAPHY: The RB is fairly high and will overflow only at extremely

high stages; however from below the highway bridge for

about half a mile, overflow begins above 18 feet stage.

Left bank is a high vertical rock bluff and is not subject

to overflow.

REMARKS:

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 7: CONDITIONS

DAMAGE

STAGE    AREAS AFFECTED

-------  ----------------------------------------------------------------------------------------------------

18.00  McFarland Park floods extensively at flood stage, however no structure damages are incurred.

20.00  Alabama State Highway 20 is covered by water at the underpass below US highway 43 and 72. The

underpass will likely be closed.

21.50  Water covers the parking lots of the marina at McFarland Park...with extensive flooding occurring at

the soccer fields and golf course within the park. Water is also beginning to cover the road that

goes underneath U.S. Highways 43 and 72 at the new playground.

27.00  Moderate flooding. Flooding of industries near the river begins.  There are a few buildings below a

stage of 27 feet upstream of the railroad, but they are protected by a dike that was not topped in

1973 (stage of 30.3 ft).

30.00  Widespread flooding of industries near the river is occurring.

32.00  MAJOR FLOODING.

32.50  RECORD FLOOD - 3/19/1897

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 8: DAMAGE

RIVER STAGE DATA

|  35-|

|-----|

|-----|

|-----|

|-----|

|  33-|

|-----|

32.50 - RECORD FLOOD - 3/19/1897                                                                |-----|   32.50  03/19/1897

32.00 - MAJOR FLOODING.                                                                         |-----|

|-----|

|  31-|

|-----|

|-----|

30.00 - Widespread flooding of industries near the river is occurring.                          |-----|   30.03  03/17/1973

|-----|

|  29-|

|-----|

|-----|

|-----|   28.00  02/13/1948

|-----|   27.58  12/23/1990

27.00 - Moderate flooding. Flooding of industries near the river begins.  There are a few       |  27-|

buildings below a stage of 27 feet upstream of the railroad, but they are protected     |-----|

by a dike that was not topped in 1973 (stage of 30.3 ft).                               |-----|

|-----|   25.98  12/10/2004

|-----|   25.53  03/28/1994

|  25-|   25.12  12/03/1991

|-----|   24.83  03/22/1980

|-----|

|-----|   23.81  05/04/1984

|-----|

|  23-|

|-----|

|-----|

|-----|   21.94  02/18/2003

21.50 - Water covers the parking lots of the marina at McFarland Park...with extensive          |-----|   21.50  03/03/1998

flooding occurring at the soccer fields and golf course within the park. Water is       |  21-|

also beginning to cover the road that goes underneath U.S. Highways 43 and 72 at the    |-----|   20.83  03/27/1993

new playground.                                                                         |-----|   20.58  12/01/2004

20.00 - Alabama State Highway 20 is covered by water at the underpass below US highway 43 and   |-----|   20.01  09/19/2004

72. The underpass will likely be closed.                                                |-----|

|  19-|   19.16  02/19/2001

|-----|   18.80  09/22/2004

|-----|

18.00 - McFarland Park floods extensively at flood stage, however no structure damages are      |-----|

incurred.                                                                               |-----|

|  17-|

|-----|

|-----|

|-----|

|-----|

REACH: levees protect an area in the vicinity of the gage (RB) to above 431.15 ft MSL. 	ELEVATION ZERO:  401.12

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                     NWS FORM E-19 PAGE 9: STAFF

CONTACTS

SQ  CONTACT/REMARKS                                    PHONE

--  -------------------------------------------------- ------------------

1  Lauderdale County EMA                              256-766-4201

Director:  George Grabryan

2  McFarland Golf Course                              256-760-6428

3  Florence PD                                        256-760-6610

LOCATION: Tennessee River AT Florence, AL                           Revised, Printed Dates: 11/20/2003, 12/20/2006

ID: FLOA1                          HSA: HUN                    NWS FORM E-19 PAGE 10: CONTACTS

Flooding near the gage site.

Section of staff gage.