| PAYLOAD FLIGHT HAZARD REPORT | a. NO: | AMS-02-F20 |
| --- | --- | --- |
| b. PAYLOAD | Alpha Magnetic Spectrometer-02 (AMS-02) | c. PHASE: | II |
| d. SUBSYSTEM: | Tracker Alignment System | e. HAZARD GROUP: | Injury/Illness | f. DATE: | May 25, 2007 |
| g. HAZARD TITLE: | Crew Exposure to Coherent Light | i. HAZARD | CATASTROPHIC | X |
|  |  | CATEGORY: | CRITICAL |  |
| h. APPLICABLE SAFETY REQUIREMENTS: | NSTS 1700.7B and ISS Addendum, 200.1b, 212.3 |
| j. DESCRIPTION OF HAZARD: | Operation of the Laser for the Tracker Alignment System makes use of coherent light pulses. Should these irradiate the Crew, there is a potential for ocular damage. |
| k. CAUSES | 1. Laser Power Output Exceeds Design Capability 2. Loss of Beam Path Containment and Integrity |
| (list) |  |
| o. APPROVAL | PAYLOAD ORGANIZATION | SSP/ISS |
| PHASE I |  |  |
| PHASE II |  |  |
| PHASE III |  |  |
| l. HAZARD CONTROL (CONTROL), m. SAFETY VERIFICATION METHODS (SVM), n. STATUS OF VERIFICATIONS (STATUS) | OPS CONTROL |
| 1. CAUSE: Laser Power Output Exceeds Design Capability |  |
| 1.1 CONTROL: The Tracker Alignment System (TAS) generates laser energy from ten independent laser diodes, pairs of the diodes contained within five Laser Fiber Coupler (LFCR) boxes. This energy is generated by Eagleyard EYP-RWL-1083 infrared (1083 nm) laser diodes with a maximum power output of 80 mW. Each laser diode will emit at a maximum 1 kHz interval with a maximum of 8 μs pulse duration when operating. Each laser diode’s emissions are split into four output fibers, each with approximately one quarter of the total power output. The operation of the TAS consists of less than 1% of the AMS-02 operational time. The LFCR boxes are light tight and can not release any laser emissions with the exception of the fiber ports where laser emission are nominal design features. 1.1.1 SVM: Review of design. 1.1.2 SVM: Inspection of as-built hardware. 1.1.1 STATUS: Open 1.1.2 STATUS: Open |  |
| 1.2 CONTROL: The laser energy is carried from the LFCR boxes by fibers that interface with the LFCR by way of FC-type connectors. These fibers are routed from the M-structure mounted LFCR boxes to the rim of the outer tracker plate where there are subminiature fiber-fiber connectors. From these connectors the fibers are routed to the beam port boxes (positioned within the tracker at the “top” and “bottom” of the tracker. The connectors are securely held in place and should there be a release of a fiber, either through connector failure or fiber breakage, the NOHD for the laser energy has been established to be just under 2 inches. The fibers are routed under the MLI of the AMS-02 and are not exposed to the exterior environment. 1.2.1 SVM: Review of design. 1.2.2 SVM: Inspection of as-built hardware. 1.2.3 SVM: Laser Safety Analysis 1.2.1 STATUS: Open 1.2.2 STATUS: Open 1.2.3 STATUS: Open |  |
| 2. CAUSE: Loss of Beam Path Containment and Integrity |  |
| 2.1 CONTROL: The connectors used by the TAS at the LFCR are FC-type and will not inadvertently release. The fiber optics cables are restrained. 2.1.1 SVM: Review of design. 2.1.2 SVM: Inspection of as built hardware. 2.1.1 STATUS: Open 2.1.2 STATUS: Open |  |
| 2.2 CONTROL: The connectors to make fiber to fiber connections are clamped subminiature fiber connectors. The connectors are attached to Patch Panels at the rim of the tracker plate, restraining the fibers and connectors. 2.2.1 SVM: Review of Design 2.2.2 SVM: Inspection of as built hardware 2.2.1 STATUS: Open 2.2.2 STATUS: Open |  |
| 2.3 CONTROL: Fibers are fixed within the beamport boxes by use of standard fiber connectors to provide careful alignment with the optics of the beamport boxes. 2.3.1 SVM: Review of Design 2.3.2 SVM: Inspection of as built hardware 2.3.1 STATUS: Open 2.3.2 STATUS: Open |  |
| 2.4 CONTROL: Fibers that interconnect the LFCR, patch panels and beamport boxes are Corning HI 1060RC type with cladding (0.08mm diameter) and jacket (diameter 0.165 mm). In addition the fibers are “armored” with Nylon (diameter 0.9 mm). Routed fibers are bundled in standard braided installation sleeves and fixed with tie wraps to cable fixation points. Cable routing considers the minimum bending radius of the individual fibers and bundled fibers, 20 mm and 40 mm respectively. 2.4.1 SVM: Review of Design 2.4.2 SVM: Inspection of as built hardware 2.4.1 STATUS: Open 2.4.2 STATUS: Open |  |
| 2.5 CONTROL: Laser beams are emitted across the interior of the Tracker. The Tracker is designed to be light tight, and vent ports are specifically designed to preclude the entry and exit of light. 2.5.1 SVM: Review of Design 2.5.2 SVM: Inspection of As Built Hardware 2.5.1 STATUS: Open 2.5.2 STATUS: Open |  |
| NOTES: |  |

| ACRONYMS |
| --- |
| AMS-02 – Alpha Magnetic Spectrometer | MLI – Multilayer Insulation |
| ANSI – American National Standards Institute | mm – millimeter |
| CFC – Carbon Fiber Composite | mW – milliWatt |
| CW – Continuous Wave | nm – nanometer |
| Hz – Hertz | NOHD – Nominal Ocular Hazard Distance |
| LASER – Light Amplification by Stimulated Emission of Radiation | OD – Outer Diameter |
| LBBX – Laser Beamport Boxes | Si – Silicon |
| LDDR – Laser Diode DriveR | TAS – Tracker Alignment System |
| LFCR – Laser Fiber (Fibre) Coupler | TRD – Transition Radiation Detector |
| LFIB – Laser Fibers (Fibres) |  |

| System Feature | Control Type | Verification method |
| --- | --- | --- |
| Laser light sources generated within five light tight boxes exterior to the Tracker, mounted to the M-Frame. Each box contains two lasers diodes that operate at: 1043 nm 1 kiloHertz pulse frequency 8 microsecond maximum pulse duration. 80mW continuous operation power (not an operations mode supported on AMS-02) | DESIGN | Review of Design Inspection of As Built Hardware |
| Software control of the laser diodes allows only two diodes to be firing simultaneously | Not Directly Relevant to Safety Controls | Safety Controls provide for control of continuosly powered lasers without threat, an operational mode that can not occur in the AMS-02 TAS Design |
| Within each laser source box, the emissions from the two laser diodes are split into four beams, each with approximately 20mW of power if the lasers were to be continuously powered. Each of these split beams is guided by a single fiber matched and bundled and taken to a FC-type connector. Internal optics misalignment or fault results in no laser emission through fiber and contained beam. | CONTAINMENT | Review of Design Inspection of As Built Hardware |
| Outside of the box fiber optics cables connected with a FC-type Connectors contain and direct the laser energy, with a single fiber per split beam. All fibers are routed the laser energy from each box to the interior of the Tracker. The fibers are split between the top and bottom of the Tracker and terminate at five beam ports. Each beam port takes the energy from four fibers and directs it along the central axis of the Tracker to illuminate the silicon sensors. | CONTAINMENT | Review of Design Inspection of As Built Hardware |
| Tracker volume is design to be light tight, including shielded vents that preclude exterior light from entering, or interior laser sources from exiting. Tracker Structure acts as beam stop if misalignment occurs. | CONTAINMENT | Review of Design |
| Rupture/breakage of fiber path. System is design to minimize the potential for breakage (clad, jacketed and armored fibers that are bundled within a sleeve). Routed under the MLI of the AMS-02. Should a broken fiber be exposed and allowed to emit, the NOHD has been established to be just under 2 inches. | DESIGN | Review of Design Inspection of As Built Hardware Laser Safety Analysis |

Laser Diode Specifications

Laser Diode Output Classification (CW and AMS-02 Operational)

GRAPHIC OF VENTING PATHS AND LIGHT TRAP OF AMS-02 Tracker Volume

Tracker Volume vents designed to preclude light passage (Laser path down center of Silicon Sensor Planes, Filter mesh not shown in Tracker Vent Trap)

|  | Figures not republished with new assessment to ANSI Z 136.1 (2000) Previously published figures referenced. Those figures are provided in the following pages |
| --- | --- |