Distributed Hydrogen Production from Wind

Wind power is currently utilized as a renewable power technology for generating electricity.  Combining this electricity with water electrolysis, wind can provide hydrogen with few emissions and with very low consumption of petroleum.  Wind-generated electricity can be sent to distributed electrolyzers via the electric grid.  The petroleum energy use and resultant CO2 emissions from this process are associated with hydrogen compression at the forecourt, as well as the use of grid electricity.  Grid electricity supplements the electricity from wind in order to increase the capacity factor on the electrolyzer.

| Well-to-Wheels Energy and Greenhouse Gas Emissions Data |
| --- |
|  | Current (2005) Gasoline ICE Vehicle | Current (2005) Gasoline Hybrid Electric Vehicle | Current (2005) Distributed Electrolysis Using Wind/Grid - FCV | Future (2015) Distributed Electrolysis Using Wind/Grid - FCV |
| Well-to-Wheels Total Energy Use (Btu/mile) | 5,900 | 4,200 | 6,200 | 4,500 |
| Well-to-Wheels Petroleum Energy Use (Btu/mile) | 5,300 | 3,800 | 130 | 100 |
| Well-to-Wheels Greenhouse Gas Emissions (g/mile) | 470 | 340 | 490 | 310 |
| Cost of Hydrogen ($/gge, Delivered) |  |  | 5.70 | 3.10 |

Notes: Distributed Hydrogen Production from Wind

- Source: Well-to-wheels energy, petroleum and greenhouse gas emissions information from the Argonne National Laboratory GREET model, Version 1.7.  Well-to-wheels values represent primary fuel production, electricity production, hydrogen production, hydrogen compression, and hydrogen dispensing.  Fossil resource exploration and equipment manufacture is not included.

- Source: Cost, resource requirements, energy requirements, all fuel and feedstock energy contents, and efficiency values for the Current (2005) case is from the National Renewable Energy Laboratory and the H2A model, Version 1.0.9 for a forecourt electrolysis facility.  Capacity of plant represented here is 1,500 kg/day.

- Source: Cost, resource requirements, energy requirements, all fuel and feedstock energy contents, and efficiency values for the Future (2015) case is from the H2A advanced forecourt case modified to include a $250/kW installed capital cost for the electrolyzer, and $0.038/kWh electricity price.

- Basis is 1 kg of hydrogen, dispensed from filling station for 5,000 psi fills.  A kg of hydrogen contains approximately the same amount of energy as one gallon of gasoline, or one gallon of gasoline equivalent (gge).

- Diagram is for future (2015) case, showing feedstock and energy consumption levels required to meet technology cost goals.  Flows in diagram represent direct energy and emissions between production and dispensing, and are not based on well-to-wheels calculations.

- The petroleum use and resultant GHG emissions are associated with the grid electricity for compression, and to supplement the wind based electricity for electrolysis.

- Energy from incoming wind was not included in the overall energy balance, although the wind-generated electricity is.  Grid efficiency loss = 7.3% as per assumption in ANL GREET model.

- Diagram is for Future (2015) case.  Cost of Future (2015) case assumes electricity assistance provided by grid to maintain capacity factor at 70%; the electricity to the electrolyzer is assumed to be 50% wind, 50% grid.  Cost of Current (2005) case also assumes electricity assistance provided by grid to maintain capacity factor at 70%; the electricity to the electrolyzer is assumed to be 30% wind, 70% grid.  Wind energy is assumed to be transported via the electrical grid to the distributed electrolyzer.

- Current (2005) electrolyzer uses 53.4 kWh of electricity per kg of hydrogen generated.  Future (2015) electrolyzer uses 44.5 kWh/kg.  The LHV electrolyzer efficiencies for the Current (2005) and Future (2015) cases are 64% and 76%, respectively.

- Installed electrolyzer capital cost for 2005 and 2015 cases is $730/kW and $250/kW, respectively.

- Efficiency results are presented in terms of lower heating value (LHV) of hydrogen.

- The efficiency of the electric forecourt compressor, which raises pressure of the gaseous hydrogen for 5,000 psi fills, is 94%.

- The operating capacity factor of the production unit is 70%.

- Electricity is consumed by the process for compression and electrolyser operations.  Electricity prices for the Current (2005) case is based on the 2015 projection for industrial-rate electricity by the Department of Energy’s Energy Information Administration Annual Energy Outlook 2005 High A case.  Electricity price for the Future (2015) case is $0.038/kWh.  Prices shown in table are in 2005 $.  Electricity is inflated at 1.9%/year for the 20 year operating life of the plant.  It is assumed that both grid electricity and wind electricity is available at the same price.

- Cost of hydrogen is the minimum required to obtain a 10% internal rate of return after taxes on the capital investment.

- The data relevant to the Distributed Hydrogen Production from Wind technology diagram above is provided in the table below.

|  | Current (2005) Distributed Electrolysis Using Wind/Grid - FCV | Future (2015) Distributed Electrolysis Using Wind/Grid - FCV |
| --- | --- | --- |
| Feedstock Price ($/million Btu) | N/A - Wind Energy | N/A - Wind Energy |
| Energy in Feedstock (Btu) | N/A - Wind Energy | N/A - Wind Energy |
| Grid Electricity Consumed (kWh) | 40 | 24 |
| Electricity Price ($/kWh) | 0.052 | 0.038 |
| Electricity to Process (Btu) | 182,000 | 152,000 |
| Energy Losses from Process (Btu) | 66,000 | 36,000 |
| Pressure of Hydrogen from Production (psi) | 300 | 300 |
| Energy Use for Delivery at the Forecourt (Btu) | 7,200 | 7,200 |
| Energy Use for Delivery Transport (Btu) | N/A - Forecourt Production | N/A - Forecourt Production |
| Hydrogen Dispensing Fill Pressure (psi) | 5,000 | 5,000 |
| Plant Gate Energy Use Including Feedstock (Btu) | 182,000 | 152,000 |
| Production Process Efficiency | 64% | 76% |
| Pathway Efficiency | 61% | 73% |

# Text boxes

This analysis is based on the best available technology in the laboratory.  Currently, it has not been validated through demonstration.