UNITED STATES ENVIRONMENTAL PROTECTION AGENCYREGION III

1650 Arch Street
Philadelphia, Pennsylvania  19103-2029

| SUBJECT: | Technical Support Document-Commonwealth of Virginia-Norfolk Southern Corporation RACT Permit EPA-R03-OAR-2008-0333 |  |
| --- | --- | --- |
| FROM: | Ellen Wentworth /s/ |
| TO: | File |
| THRU: | Cristina Fernandez, Branch Chief /s/ Air Quality Planning Branch |

Date:		     April 30, 2008

I.  Background

Prior to the final establishment of the 8-hour ozone nonattainment areas, the Environmental Protection Agency (EPA) developed a program to allow potential nonattainment areas to voluntarily adopt local emission control programs to avoid air quality violations and mandated nonattainment area controls.  Areas with air quality meeting the 1-hour ozone standard were eligible to participate.  In order to participate, state and local governments and EPA developed and signed a memorandum of agreement that described the local control measures the state or local communities intended to adopt and implement in order to reduce ozone emissions in advance of air quality violations.  In this agreement, also known as an Early Action Compact (EAC), the state or local community agreed to prepare emission inventories and conduct air quality modeling and monitoring to support is selection of emission controls.  Areas that participated in the EAC program had the flexibility to institute their own approach in maintaining clean air and protecting public health.

Several localities in the Winchester and Roanoke, VA areas elected to participate in the EAC program.  The areas that signed an EAC are the City of Winchester and Frederick County, which comprise the Northern Shenandoah Valley EAC, and the Cities of Roanoke and Salem, and the Counties of Roanoke and Botetourt, which comprise the Roanoke EAC.  Virginia’s strategy for enabling these localities to participate in the EAC program was to have them be subject to volatile organic compound (VOC) and nitrogen oxide (NOx) control measures from which they had previously been exempt.  In order to enable the affected localities to implement these VOC and NOx controls, the Regulations for the Control and Abatement of Air Pollution were revised to include these affected localities.  As a result, the list of VOC and NOx emissions control areas (9 VAC 5-20-206) was expanded to include the EAC areas as the Western Virginia Emissions Control Area (70 FR 21625).  By doing so, the VOC and NOx control regulations of Chapter 40 became applicable in these areas.  In order to implement the NOx control measures, the Virginia Department of Environmental Quality (VADEQ) adopted a regulation (Rule 4-4)  which provides that VADEQ must, on a case-by-case basis, determine whether there is Reasonably Available Control Technology (RACT) to reduce NOx emissions from major sources for which EPA has not issued a control technique guideline (CTG).  A major source in the Western Virginia Emissions Control Area emits or has the potential to emit 100 tons per year of NOx.  CTGs are documents issued to define RACT for a particular source category.  RACT is the lowest emission limit that a particular source is capable of meeting by the application of control technology that is reasonably available considering technological and economic feasibility.

The following sources in the Western Virginia Emissions Control Area have been identified as sources subject to the RACT requirements:  (1) Roanoke Electric Steel Corporation Steel Mill located in the City of Roanoke, (2) Roanoke Cement Company Portland Manufacturing Plant, located in Troutville, County of Botetourt, (3) Norfolk Southern Railway Company-East End Shops, located in the City of Roanoke, and (4) Global Stone Chemstone Corporation located in Frederick County.

On April 27, 2005 (70 FR 21621), EPA issued a direct final rulemaking establishing and requiring NOx RACT via permits for the above four major sources.

II.  Summary of SIP Revision

On February 11, 2008, the Commonwealth of Virginia submitted a revision to its SIP stating that since the time of EPA’s approval of the NOx RACT requirements for the Norfolk Southern Railway Company rail car and locomotive maintenance facility, located in Roanoke, Virginia, many of the units at the facility were permanently shut down, including those that were previously subject to the NOx RACT requirements of permit No. 20468.  VADEQ is requesting that EPA remove permit no. 20468 from the Commonwealth of Virginia SIP, since these sources are no longer in operation and have permanently shut down.

The sources previously subject to NOx RACT according to permit no. 20468 include the following:  Unit ID # 8-01-B & W Stirling coal-fired spreader stoker boiler; Unit ID # 8-02-B & W Stirling coal-fired spreader stoker boiler; Unit ID # 8-03-B & W Stirling coal-fired spreader stoker boiler; Unit ID #8-04-Zurn Energy coal-fired spreader stoker boiler; Unit ID # 43-03-15 open-front oil-fired metal heating furnances; and Unit ID # 51-13/14-one 13-ton capacity electric arc furnace.

The February 11, 2008 SIP revision consists of mutual agreements between the VADEQ and Norfolk Southern Corporation for permanent shutdowns for these RACT-subject sources in accordance with 9 VAC 5-20-220, Shutdown of a Stationary Source:  Unit ID # 8-01 through 8-03 B&W coal-fired boilers were permanently shutdown as per the permanent shutdown agreement between VADEQ and the Northern Southern Corporation, dated August 20, 2007 (see attached agreement); Unit ID # 8-04 B&W coal-fired boiler, Unit ID # 43-03, 15 open-front oil-fired metal heating furnaces, and Unit # 15-13/14-one 13-ton capacity electric arc furnace were permanently shutdown as per the permanent shutdown agreement between VADEQ and the Northern Southern Corporation, dated June 22, 2005. (see attached agreement).

III.  EPA’s Analysis of the Commonwealth Request

VADEQ’s regulation 9 VAC 5-20-220 gives the Commonwealth of Virginia authority, upon determination that a stationary source or emissions unit is shutdown permanently, to revoke any permits by written notification to the owner and removing the stationary source or emissions unit from the emission inventory or consider its emissions to be zero in any air quality analysis conducted.  In addition, the stationary source or emissions unit cannot commence operation without a permit being issued under the applicable provisions of 9 VAC 5-80-10, et seq. (Permits for Stationary Sources).  The mutual shutdown agreements of September 9, 2005 and August 20, 2007 comply with the requirements of 9 VAC 5-20-220 and 9 VAC 5-80-10.  The Commonwealth’s state operating permit regulations also require, in accordance with subsection L of 9 VAC 5-80-1210 (Permit Invalidation, Suspension, Revocation and Enforcement), that “nothing in the regulations of the board shall be construed to prevent the board and the owner from making a mutual determination that a permit is rescinded because all of the statutory or regulatory requirements (i) upon which the permit is based or (ii) that necessitated issuance of the permit are no longer applicable.” The RACT permit No. 20468, provision 15 under General Conditions, grants the Virginia State Air Pollution Control Board (“Board”) the authority to modify, rewrite or amend the permit in accordance with the regulations of the Board and the Administrative Process Act (§2.2-4000 et seq).  However, a repeal of the NOx RACT permit for Norfolk Southern Railway Company would not be effective until the revision or repeal is approved by EPA.

Because the above emission units have permanently shutdown as demonstrated by the attached mutual shutdown agreements, EPA recommends that the RACT requirements for the above named units be removed from the Virginia SIP.

# Footnotes

The non-CTG RACT determination requirements have since been removed from Rule 4-4 and relocated to a new Rule 4-51.