Voluntary Report - public distribution

Date: 8/1/2006

GAIN Report Number: CH6058

CH6058

China, Peoples Republic of

Solid Wood Products

Revised MB Treatment Requirements for Entry/Exit Wood Packaging Material

2006

Approved by:

Maurice House

U.S. Embassy

Prepared by:

James Butterworth & Zhang Lei

Report Highlights:

On July 31, 2006, the General Administration of Quality Supervision, Inspection, and Quarantine (AQSIQ) released the revised methyl bromide (MB) fumigation requirements for entry/exit wood packing material.   This report is a free UNOFFICIAL translation provided for the benefit of U.S. exporters by the USDA FAS Agricultural Affairs Office in Beijing.

Includes PSD Changes: No

Includes Trade Matrix: No

Unscheduled Report

Beijing [CH1]

[CH]

# Background

On July 31, 2006, the General Administration of Quality Supervision, Inspection, and Quarantine (AQSIQ) published its Announcement 2006 No. 105 on the revised methyl bromide (MB) fumigation requirements for entry/exit wood packing. The original document is available in Chinese at:

http://www.aqsiq.gov.cn/cms/template/item.html?did=8&cid=2038\20182

The new regulation mandated a longer fumigation period and a higher dosage.  See below tables for comparison. The new requirements are scheduled to enter into force on October 1, 2006.  The U.S. exporters are encouraged to follow the new requirements to avoid entry delays.

The new requirements:

| Temperature | Dosage rate (g/m3) | Minimum concentration (g/m3) at |
| --- | --- | --- |
|  |  | 2 hour | 4 hours | 12 hours | 24 hours |
| ≥21°C | 48 | 36 | 31 | 28 | 24 |
| ≥16°C | 56 | 42 | 36 | 32 | 28 |
| ≥11°C | 64 | 48 | 42 | 36 | 32 |

The old requirements:

| Temperature | Dosage rate (g/m3) | Minimum concentration (g/m3) at |
| --- | --- | --- |
|  |  | 0.5 hour | 2 hours | 4 hours | 16 hours |
| ≥21°C | 48 | 36 | 24 | 17 | 14 |
| ≥16°C | 56 | 42 | 28 | 20 | 17 |
| ≥11°C | 64 | 48 | 32 | 22 | 19 |

For more information about China’s quarantine requirements for imported wood packing material, please see GAIN CH5052.

# Disclaimer

Information in this translated report may not be completely accurate either because policies may change when the regulation is adopted, or because clear and consistent information about these policies was not available.  Therefore, U.S. exporters should try to verify all import requirements with their foreign customers, who are normally best informed, before any goods are shipped.  Final import approval of any product is subject to the importing country’s rules and regulations as interpreted by border officials at the time of product entry.  In the event of any errors or omissions in this translation, the original Chinese version shall prevail.

(BEGIN TRANSLATION)

2006 No. 105 Announcement

By The General Administration of Quality Supervision, Inspection and Quarantine

The technical requirements for MB fumigation treatment stated in AQSIQ’s Announcement 2005 No. 32 and 69 are revised, in accordance with the MB fumigation requirements of the International Standards for Phytosanitary Measures (ISPM) Publication No. 15 of “Guidelines for Regulating Wood Packing Material in International Trade”, which was revised by the International Plant Protection Convention (IPPC) in April 2006.

Methyl Bromide (MB) Fumigating Treatment

- The wood packing material shall be treated as per the below criteria at normal atmospheric pressure:

| Temperature | Dosage rate (g/m3) | Minimum concentration (g/m3) at |
| --- | --- | --- |
|  |  | 2 hour | 4 hours | 12 hours | 24 hours |
| ≥21°C | 48 | 36 | 31 | 28 | 24 |
| ≥16°C | 56 | 42 | 36 | 32 | 28 |
| ≥11°C | 64 | 48 | 42 | 36 | 32 |

- The fumigating temperature should be no lower than 10°C, and fumigating time should be no less than 24 hours.  Dosage rate should be tested at least at the 2nd, 4th and 24th hours.

Before the Announcement comes into effect, the already treated and mark-issued wood packaging in accordance with the previous technical requirements for MB fumigation treatment is not required to be re-treated and re-marked based on new requirement.

The Announcement will be effective on October 1, 2006.  (END TRANSLATION)

# Text boxes

Global Agriculture Information Network

USDA Foreign Agricultural Service

GAIN Report

Template Version 2.09