Precipitation Processing System (PPS) Product Format Description

User Selectable Storm Total Precipitation (USP)

This product shall provide a rainfall accumulation map displayed as an image, for

user selected accumulation period.  The product format and content shall be the

same as the Surface Rainfall Accumulation and Storm Total Rainfall Accumulation

products, except the accumulation period shall be of variable duration (in whole

clock hours), ranging from a beginning to an ending time specified by the user.

The product will usually be generated by request, but may also be generated

routinely for limited, designated periods.  One of these periods shall be the Default

Period, which will span a 24 hour period from 1200z of the previous day to 1200z of

the present day.  The default version of the product may be generated any time

following the completion of the first volume scan to start after 1200z each day,

up to 6 hours later.  The period of accumulation shall be defined by the operator

via two parameters: the Ending Hour (ranging from 0 to 23z), and the Time Span

(ranging form 1 to 24 whole clock hours prior to the Ending Hour.)  No more than

30 hours of rainfall data prior to the most recent clock-hour will be required to generate this product. If a requested product cannot be generated due to an error condition, a message will be displayed explaining why, and the available hours of precipitation accumulation in the precipitation data base will be listed. "This product shall include annotations for product name, radar ID, maximum data value detected, radar position, times and dates of the beginning and end (clock hour) of the rainfall rate integration, radar position, radar elevation above MSL, radar operational mode, the bias in the radar estimate of the precipitation rate, and the error variance of the bias estimate."

Data Levels

The User Selectable Rainfall Accumulation is displayed in 16 data levels on one of two possible scales, based on the maximum data value detected: one scale corresponding to that presently in use for the Surface Rainfall Accumulation products (OHP & THP); the other scale corresponding to that presently in use for the Storm Total Rainfall Accumulation product (STP).  The scale used for the User Selectable product will switch automatically between the two, with the OHP & THP scale in effect unless the product maximum data value exceeds the lower limit of the maximum data level (e.g. 8 inches), in which case the STP scale will be invoked.  Each data level code may vary with operational mode and with NEXRAD (or agency) system adaptation data.

Color Level Code Tables

See sections 28.2.2 and 29.2.2.

Range/Data Resolution

The resolution of this graphic product is 1.1 nmi (range) by 1 deg (azimuth) out to

a range of 124 nmi.

Alphanumeric Display Graphic Screen

A tabular format (Appendix B, Format III, Configuration 6) will be displayable on the graphic display screens.  The tabular format will include:

(a)	Gage Bias Flag

(b)	Number of Hours in product

(c)	End Times

(d)	Bias

(e)	Hours Included Flag

Standard Annotations

Beginning/ending Date and Time of Rainfall Rate Integration

Maximum Data Value

Radar Rate Bias Estimate

Error Variance of Bias Estimate

Gage Adjustment Bias Flag

Product Interaction

The following overlay products are displayable on this product:

 Hail Index

 Mesocyclone

 Severe Weather Probability

 Storm Tracking Information

 Tornado Vortex Signatures.

USP is a 16 data level product, formatted as a radial image, with 1.1 Nmi x 1 Degree resolution and a range of 124. The product is not compressed.

Highlighted areas indicate fields which are specific to this product (or might be)

[Note: a Halfword is 16 bits]

MESSAGE HEADER

References

2620001F (Class I User ICD):

Fig 3-3 “Message Header”

| HALFWORD | FIELDNAME | TYPE | UNITS | VALUE | PRECISION/ ACCURACY | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| 01 | Message Code | INT*2 | N/A | 31 | N/A | From Fig 3-3 |
| 02 | Date of Message | INT*2 | Julian Date | 1 to 32,767 | 1 | From Fig 3-3 |
| 03-04 | Time of Message | INT*4 | Seconds | 0 to 86,399 | 1 | From Fig 3-3 |
| 05-06 | Length of Message | INT*4 | N/A | 18 to 409856 | 1 | From Fig 3-3 |
| 07 | Source ID | INT*2 | N/A | 0 to 999 | 1 | From Fig 3-3 |
| 08 | Destination ID | INT*2 | N/A | 0 to 999 | 1 | From Fig 3-3 |
| 09 | Number of Blocks | INT*2 | N/A | 3 | 1 | From Fig 3-3 |

PRODUCT DESCRIPTION BLOCK

References

2620001F (Class I Users ICD):

Fig 3-6 “Graphic Product Message” Sheet 2, Sheet 6, Sheet 7

Table III “Message Codes for Products”

Table V “Product Dependent Halfword Definition for Product Description Block”

2620003F (Product Spec ICD):

Section 28.2.2 “Color Level Code Table”

| HALFWORD | FIELDNAME | TYPE | UNITS | VALUE | PRECISION/ ACCURACY | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| 10 | Block Divider | INT*2 | NA | -1 | N/A | From Fig 3-6 Sheet 6 |
| 11-12 | Latitude of Radar | INT*4 | Degrees | -90 to +90 | 0.001 | From Fig 3-6 Sheet 6 |
| 13-14 | Longitude of Radar | INT*4 | Degrees | -180 to +180 | 0.001 | From Fig 3-6 Sheet 6 |
| 15 | Height of Radar | INT*2 | Feet | -100 to +11000 | 1 | From Fig 3-6 Sheet 6 |
| 16 | Product Code | INT*2 | N/A | 31 |  | From Table III |
| 17 | Operational Mode | INT*2 | N/A | 0 to 2 | N/A | From Fig 3-6 Sheet 6 |
| 18 | Volume Coverage Pattern | INT*2 | N/A | 1 to 767 | N/A | From Fig 3-6 Sheet 6 |
| 19 | Sequence Number | INT*2 | N/A | -13, 0 to 32767 | 1 | From Fig 3-6 Sheet 6 |
| 20 | Volume Scan Number | INT*2 | N/A | 1 to 80 | 1 | From Fig 3-6 Sheet 6 |
| 21 | Volume Scan Date | INT*2 | Julian Date | 1 to 32767 | 1 | From Fig 3-6 Sheet 6 |
| 22-23 | Volume Scan Start Time | INT*4 | Seconds GMT | 0 to 86399 | 1 | From Fig 3-6 Sheet 6 |
| 24 | Product Generation Date | INT*2 | Julian Date | 1 to 32767 | 1 | From Fig 3-6 Sheet 6 |
| 25-26 | Product Generation Time | INT*4 | Seconds | 0 to 86399 | 1 | From Fig 3-6 Sheet 6 |
| 27 | End Hour | INT*2 | Hours | 0 to 23 | 1 | From Table V |
| 28 | Time Span | INT*2 | Hours | 1 to 24 | 1 | From Table V |
| 29 | Elevation Number | INT*2 | N/A | 0 to 20 | 1 | From Fig 3-6 Sheet 6 |
| 30 | Null Product Flag | INT*2 | N/A | 0 to 1 | N/A | From Table V |
| 31 | Data Level 1 Threshold | INT*2 | Inches | OHP/THP Code for ND (i.e. 0); STP Code for ND (i.e. 0) | 1 | From 32.2.2 |
| 32 | Data Level 2 Threshold | INT*2 | Inches | OHP/THP Code for > 0.00; STP Code for > 0.0 | 1 | From 32.2.2 |
| 33 | Data Level 3 Threshold | INT*2 | Inches | OHP/THP Code for > 0.10; STP Code for > 0.3 | 1 | From 32.2.2 |
| 34 | Data Level 4 Threshold | INT*2 | Inches | OHP/THP Code for > 0.25; STP Code for > 0.6 | 1 | From 32.2.2 |
| 35 | Data Level 5 Threshold | INT*2 | Inches | OHP/THP Code for > 0.50; STP Code for 1.0 | 1 | From 32.2.2 |
| 36 | Data Level 6 Threshold | INT*2 | Inches | OHP/THP Code for > 0.75; STP Code for 1.5 | 1 | From 32.2.2 |
| 37 | Data Level 7 Threshold | INT*2 | Inches | OHP/THP Code for > 1.00; STP Code for 2.0 | 1 | From 32.2.2 |
| 38 | Data Level 8 Threshold | INT*2 | Inches | OHP/THP Code for > 1.25; STP Code for 2.5 | 1 | From 32.2.2 |
| 39 | Data Level 9 Threshold | INT*2 | Inches | OHP/THP Code for > 1.50; STP Code for 3.0 | 1 | From 32.2.2 |
| 40 | Data Level 10 Threshold | INT*2 | Inches | OHP/THP Code for > 1.75; STP Code for 4.0 | 1 | From 32.2.2 |
| 41 | Data Level 11 Threshold | INT*2 | Inches | OHP/THP Code for > 2.00; STP Code for 5.0 | 1 | From 32.2.2 |
| 42 | Data Level 12 Threshold | INT*2 | Inches | OHP/THP Code for > 2.50; STP Code for 6.0 | 1 | From 32.2.2 |
| 43 | Data Level 13 Threshold | INT*2 | Inches | OHP/THP Code for > 3.00; STP Code for 8.0 | 1 | From 32.2.2 |
| 44 | Data Level 14 Threshold | INT*2 | Inches | OHP/THP Code for > 4.00; STP Code for 10.0 | 1 | From 32.2.2 |
| 45 | Data Level 15 Threshold | INT*2 | Inches | OHP/THP Code for > 6.00; STP Code for 12.0 | 1 | From 32.2.2 |
| 46 | Data Level 16 Threshold | INT*2 | Inches | OHP/THP Code for > 8.00; STP Code for 15.0 | 1 | From 32.2.2 |
| 47 | Max rainfall | INT*2 | Inches | 0.0 to 327.6 | 0.1 | From Table V |
| 48 | Begin Date Rainfall | INT*2 | Julian Date | 1 to 32767 | 1 | From Table V |
| 49 | Begin Time Rainfall | INT*2 | Minutes | 1 to 1439 | 1 | From Table V |
| 50 | End Date Rainfall | INT*2 | Julian Date | 1 to 32767 | 1 | From Table V |
| 51 | End Time Rainfall | INT*2 | Minutes | 0 to 1439 | 1 | From Table V. NOTE: Fig 3-6 Sheet 7 Note 3 says this field should be compression method |
| 52 | Average Mean-field Bias | INT*2 | N/A | 0.01 to 99.99 | 0.01 | From Table V |
| 53 | Average Effective No. G-R Pairs (Sample Size) | INT*2 | N/A | 0.00 to 9999.99 | 0.01 | From Table V |
| 54 | Version | INT*1 | N/A | 0 | 1 | Not listed on Sheet 7, Note 2 |
| 54 | Spot Blank | INT*1 | N/A | 0 to 1 | 1 | From Fig 3-6 Sheet 6 |
| 55-56 | Offset to Symbology | INT*4 | Halfwords | 60 | 1 | From Fig 3-6 Sheet 6. Is this known/fixed for USP? |
| 57-58 | Offset to Graphic | INT*4 | Halfwords | 0 to 400000 | 1 | From Sheet 6 |
| 59-60 | Offset to Tabular | INT*4 | Halfwords | 0 | 1 | From Fig 3-6 Sheet 6. Varies, depending on size of Symbology |

PRODUCT SYMBOLOGY BLOCK

References

2620001F (Class I User ICD):

Section 3.2.1.2 “Product Symbology Block”

Fig 3-6 “Graphic Product Message” Sheet 3 and Sheet 8

Fig 3-10 “Radial Data Packet”

| HALFWORD | FIELDNAME | TYPE | UNITS | VALUE | PRECISION/ ACCURACY | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
| 61 | Block Divider | INT*2 | N/A | -1 | N/A | From Fig 3-6 Sheet 8 |
| 62 | Block ID | INT*2 | N/A | 1 | N/A | From Fig 3-6 Sheet 8 |
| 63-64 | Length of Block | INT*4 | Bytes | 1 to 400000 | 1 | From Fig 3-6 Sheet 8 |
| 65 | Number of Layers | INT*2 | N/A | 1 | 1 | From 3.2.1.2 |
| 66 | Layer Divider | INT*2 | N/A | -1 | N/A | From Fig 3-6 Sheet 8 |
| 67-68 | Length of Data Layer | INT*4 | N/A | 1 to 400000 | 1 | From Fig 3-6 Sheet 8 |
| 69 | Packet Code | INT*2 | N/A | AF1F (Hex) | N/A | From Figure 3-10 |
| 70 | Index of First Range Bin | INT*2 | N/A | 0 | 1 | From Figure 3-10 |
| 71 | Number of Range Bins | INT*2 | N/A | 115 | 1 | From Figure 3-10 |
| 72 | I Center of Sweep | INT*2 | Km/4 | 256 | 1 | From Figure 3-10 |
| 73 | J Center of Sweep | INT*2 | Km/4 | 280 | 1 | From Figure 3-10 |
| 74 | Scale Factor | Scaled Integer | Pixels | 2.0 | 0.001 | From Figure 3-10 |
| 75 | Number of Radials | INT*2 | N/A | 360 | 1 | From Dennis’s notes |
| 76 | Number of RLE Halfwords in Radial | INT*2 | Halfword | 1 to 116 | 1 | } } |
| 77 | Radial Start Angle | Scaled Integer (INT*2?) | Degrees | 0.0 to 359.9 | 0.1 | } for } } |
| 78 | Radial Angle Delta | Scaled Integer (INT*2?) | Degrees | 1.0 to 2.0 | 0.1 | } each } } |
| 79 | Run (0) | 4 Bit INT | N/A | 0 to 15 | 1 | } } of |
| 79 | Color Code (0) | 4 Bit INT | N/A | 0 to 15 | 1 | } for each } 360 |
| 79 | Run (1) | 4 Bit INT | N/A | 0 to 15 | 1 | } “run” } radials |
| 79 | Color Code (1) | 4 Bit INT | N/A | 0 to 15 | 1 | } } |
| … | … | … | … | … | … | } |
| … | … | … | … | … | … | } |
| … | … | … | … | … | … | } |
|  | Run (N) | 4 Bit INT | N/A | 0 to 15 | 1 | [N is even] } |
|  | Color Code (N) | 4 Bit INT | N/A | 0 to 15 | 1 | } |
|  | End of Block | 4 Bit INT | N/A | 0000 | N/A | End of } block } marker } |
|  | End of Block | 4 Bit INT | N/A | 0000 | N/A | End of } block } marker } |

GRAPHIC ALPHANUMERIC BLOCK

References:

2620001F (Class I User ICD):

Figure 3-6 “Graphic Product Message” Sheet 4, Sheet 9 and Sheet 11

Section 3.2.1.3 “Graphic Alphanumeric Block”

Packet Code 8 (Text and Special Symbol Packets), shown in Figure 3-8b

Packet Code 10 (Unlinked Vector Packet), shown in Figure 3-8

Table VII. Product Dependent Definition for Graphic Alphanumeric Block: Fig 3-62

2620003F (Product Spec ICD):

Appendix B “Graphic Display Formats” Format III “Attribute Area”

| HALFWORD | FIELDNAME | TYPE | UNITS | VALUE | PRECISION/ ACCURACY | NOTES |
| --- | --- | --- | --- | --- | --- | --- |
|  | Block Divider | INT*2 | N/A | -1 | N/A | From Fig 3-6 Sheet 9 |
|  | Block ID | INT*2 | N/A | 2 | N/A | From Fig 3-6 Sheet 9 |
|  | Length of Block | INT*4 | Bytes | 604 | 1 | From CVG display |
|  | Number of Pages | INT*2 | N/A | 1 to 3 from the source inference | 1 | From the source code inference |
|  | Page Number | INT*2 | N/A | 1 | 1 | From Fig 3-6 Sheet 9 |
|  | Length of Page | INT*2 | Bytes | 590 | 1 | From CVG display |
|  | Text Packet | INT*2 | N/A | 8 | N/A | From Fig 3-6 Sheet 11 |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 86 | 1 | From source code inference and CVG display |
|  | Value of Text String | INT*2 | N/A | 0 | 1 | Color Level of text; From Fig. 3-8b and CVG display |
|  | I Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | J Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | Message to follow | Char*80 | 8 bit ASCII | Gage Bias – XXXX (range from Applied/Not Applied) | N/A | From Fig. 3-8b and Fig. 3-62 |
|  | Text Packet | INT*2 | N/A | 8 | N/A | From Fig 3-6 Sheet 11 |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 86 | 1 | From source code inference and CVG display |
|  | Value of Text String | INT*2 | N/A | 0 | 1 | Color Level of text; From Fig. 3-8b and CVG display |
|  | I Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | J Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | Message to follow | Char*80 | 8 bit ASCII | XX OF XX HOURS IN PRODUCT (range from 1 to 24) | 0/1 | From Fig. 3-8b |
|  | Text Packet | INT*2 | N/A | 8 | N/A | From Fig 3-6 Sheet 11 |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 86 | 1 | From source code inference and CVG display |
|  | Value of Text String | INT*2 | N/A | 0 | 1 | Color Level of text; From Fig. 3-8b |
|  | I Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | J Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | Message to Follow | Char*80 | 8 bit ASCII | END TIMES xxZ xxZ xxZ (end time range from 00 to 23) | 0/1 | From Appendix B Format III and Fig. 3-62 |
|  | Text Packet | INT*2 | N/A | 8 | N/A |  |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 86 | 1 | From source code inference and CVG display |
|  | Value of Text String | INT*2 | N/A | 0 | 1 | Color Level of text; From Fig. 3-8b |
|  | I Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | J Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | Fig. 3-8b |
|  | Message to Follow | Char*80 | 8 bit ASCII | Bias x.xx x.xx x.xx… (bias value range from 0.00 to 99.9) | 0.01 | From Appendix B Format III and Fig. 3-62 |
|  | Text Packet | INT*2 | N/A | 8 | N/A | From Fig. 3-8b |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 86 | 1 | From source code inference and CVG display |
|  | Value of Text String | INT*2 | N/A | 0 | 1 | Color Level of text; From Fig. 3-8b |
|  | I Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | J Start | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8b |
|  | Message to Follow | Char*80 | 8 bit ASCII | HOURS INCLUDED? XX XX XX… (value range from YES to NO) | N/A | From Appendix B Format III |
|  | Text Packet | INT*2 | N/A | 10 | N/A | From Fig. 3-8 |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 50 | 1 | From source code infererce and CVG display |
|  | Value (level) of vector | INT*2 | N/A | 5 | 1 | From CVG display |
|  | Begin I Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Text Packet | INT*2 | N/A | 10 | N/A | From Fig. 3-8 |
|  | Length of Data Block (Bytes) | INT*2 | Bytes | 82 | 1 | From CVG display |
|  | Value (level) of vector | INT*2 | N/A | 5 | 1 | From CVG display |
|  | Begin I Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 1 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 2 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 3 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 4 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 5 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 6 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 7 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 7 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 7 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 7 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 8 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 8 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 8 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 8 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 9 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 9 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 9 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 9 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin I Vector 10 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | Begin J Vector 10 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End I Vector 10 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |
|  | End J Vector 10 | INT*2 | Km/4 or Pixels | -2048 to +2047 | 1 | From Fig. 3-8 |

[TABULAR ALPHANUMERIC BLOCK NOT APPLICABLE FOR USP]

The following is the octal dump of USP Graphical Alphanumerical Block abstracted from

The linear buffer

0026420  \0  \0 002   \  \0 001  \0 001 002   N  \0  \b  \0   V  \0  \0

00  00  02  5c  00  01  00  01  02  4e  00  08  00  56  00  00

0026440  \0  \0  \0 001           G   A   G   E       B   I   A   S

00  00  00  01  20  20  47  41  47  45  20  42  49  41  53  20

0026460   -       N   O   T       A   P   P   L   I   E   D

2d  20  4e  4f  54  20  41  50  50  4c  49  45  44  20  20  20

0026500

20  20  20  20  20  20  20  20  20  20  20  20  20  20  20  20

*

0026560                  \0  \b  \0   V  \0  \0  \0  \0  \0  \v

20  20  20  20  00  08  00  56  00  00  00  00  00  0b  20  20

0026600       4       O   F           4       H   O   U   R   S       I

20  34  20  4f  46  20  20  34  20  48  4f  55  52  53  20  49

0026620   N       P   R   O   D   U   C   T

4e  20  50  52  4f  44  55  43  54  20  20  20  20  20  20  20

0026640

20  20  20  20  20  20  20  20  20  20  20  20  20  20  20  20

*

0026700                                                          \0  \b

20  20  20  20  20  20  20  20  20  20  20  20  20  20  00  08

0026720  \0   V  \0  \0  \0  \0  \0 025           E   N   D       T   I

00  56  00  00  00  00  00  15  20  20  45  4e  44  20  54  49

0026740   M   E   S                                   1   3   Z

4d  45  53  20  20  20  20  20  20  20  20  31  33  5a  20  20

0026760       1   4   Z               1   5   Z               1   6   Z

20  31  34  5a  20  20  20  31  35  5a  20  20  20  31  36  5a

0027000

20  20  20  20  20  20  20  20  20  20  20  20  20  20  20  20

*

0027040                                  \0  \b  \0   V  \0  \0  \0  \0

20  20  20  20  20  20  20  20  00  08  00  56  00  00  00  00

0027060  \0 037           B   I   A   S

00  1f  20  20  42  49  41  53  20  20  20  20  20  20  20  20

0027100                       1   .   2   5           1   .   2   5

20  20  20  20  20  31  2e  32  35  20  20  31  2e  32  35  20

0027120       1   .   2   5           1   .   2   5

20  31  2e  32  35  20  20  31  2e  32  35  20  20  20  20  20

0027140

20  20  20  20  20  20  20  20  20  20  20  20  20  20  20  20

*

0027200          \0  \b  \0   V  \0  \0  \0  \0  \0   )           H   O

20  20  00  08  00  56  00  00  00  00  00  29  20  20  48  4f

0027220   U   R   S       I   N   C   L   U   D   E   D   ?           Y

55  52  53  20  49  4e  43  4c  55  44  45  44  3f  20  20  59

0027240   E   S               Y   E   S               Y   E   S

45  53  20  20  20  59  45  53  20  20  20  59  45  53  20  20

0027260       Y   E   S

20  59  45  53  20  20  20  20  20  20  20  20  20  20  20  20

0027300

20  20  20  20  20  20  20  20  20  20  20  20  20  20  20  20

0027320                                                  \0  \n  \0   2

20  20  20  20  20  20  20  20  20  20  20  20  00  0a  00  32

0027340  \0 005  \0 004  \0  \0 001   Ò  \0  \0  \0 004  \0  \n 001   Ò

0027540 001   Ò  \0  \0 001   Ò  \0   2

01  d2  00  00  01  d2  00  32