About this resource:

EPA is providing this resource solely for informational purposes. The agency can not attest to the accuracy, effectiveness, legality or usefulness of the information provided, nor does the inclusion or reference of such language constitute an endorsement by EPA.

Document Name:

CDOT Particulate Filter Spec

Organization/Agency Responsible:

Connecticut Dept. of Transportation (CDOT)

Contact:  	Jim Kocaba

Connecticut Dept. of Transportation

860-594-2082

james.kocaba@po.state.ct.us

Description:  	Connecticut DOT's I-95 New Haven Harbor Crossing Project

Connecticut DOT’s I-95 New Haven Harbor Crossing (I-95 NHHC) project is a 12-year bridge and highway upgrade that will reconstruct and widen Interstate 95 along the state’s coastline.  CDOT’s focus is on reducing diesel chemical and particulate emissions.  Under the Connecticut Clean Air Initiative (CCAI), all contractors and subcontractors are required to adhere to idling specifications and to reduce hazardous diesel emissions using control devices, such as alternate fuels, diesel oxidation catalysts (DOCs), diesel particulate filters (DPFs), and truck staging zones.

ITEM #0110xxxA – Diesel particulate filter

Description: Work under this item shall consist of furnishing and installing diesel particulate filter(s) (DFP) on two (2) diesel powered non-road construction equipment with engine horsepower (HP) ratings of 100 HP and above, or as directed by the Engineer. It is the intent of this specification to select, analyze, and use DFP on diesel powered non-road construction equipment in real world operations, experiencing typical work duty cycles typical of construction activities on ConnDOT construction projects.

The work shall also include all necessary research, evaluation, pre-testing and testing required to ensure that the appropriate device is selected and utilized in accordance with this specification and the manufacturer’s recommended instructions.

Materials: The Diesel Particulate Filter shall be (1) included on the Environmental Protection Agency (EPA) Verified Retrofit Technology List and/or California Air Research Board (CARB) Verification List and (2) is verified by EPA, CARB or certified by the manufacturer to provide a minimum emissions reduction of 50% PM10, 40% CO, and 50% HC. On-road EPA/CARB technologies are acceptable for usage to meet the requirements of this specification.

Construction Methods:

General: The requirements of the “Notice to Contractor – Diesel Vehicle Emissions Controls” are to be adhered to by the Contractor for the selected test equipment, with the exceptions required under this specification, notably the evaluation, selection and installation of Diesel Particulate Filters. If a conflict exists between the Notice and this specification, the more restrictive shall apply.

Evaluation and Selection of Diesel Particulate Filter (DPF): The Contractor shall have the selected diesel powered non-road construction equipment and its associated project duty cycle evaluated by qualified technical representative(s) from the manufacturer of the DPF, or their designee. The evaluation shall include a top-down technology review beginning with diesel particulate filters (DPFs), or similar emissions control technology that offers the highest reductions technically achievable and verified by EPA or CARB to provide emission reductions greater than 50% for PM10, 40% for CO, and 50% for HC. It may be necessary to evaluate more than one piece of equipment to determine the qualifying construction equipment that has the appropriate duty cycle and operating temperature profile.

In the event that the evaluation does not support the utilization of a DPF to achieve the noted emissions reductions, then the evaluation report must indicate alternate technologies in a top-down order of emissions reductions that would be suitable for the indicated work duty cycle. The minimum device allowed would be the oxidation catalysts specified in the “Notice to Contractor – Diesel Vehicle Emissions Controls”.

An evaluation report shall be prepared by the technical representative performing the evaluation. The report shall be submitted to the Engineer for review prior to ordering any DPF or alternate technology for use on the test equipment. The report shall include at a minimum the following information:

- Description of the evaluated diesel powered non-road construction equipment, including make, model, horsepower rating, model year, and equipment number;

- Description of work duty cycle evaluated and expected of the tested equipment;

- Operating temperature profile of the test equipment;

- Tests performed and methods employed to perform said tests;

- DPFs and alternate technologies considered for utilization on the test equipment, including reasons for qualifying or rejecting each technology in accordance with the manufacturer’s recommended specifications and/or the EPA/CARB guidelines;

- Any special requirements for utilizing the recommended device (i.e. ultra low sulfur diesel fuel, engine or equipment modifications, etc.);

- EPA/CARB verifications or manufacturer’s certifications; and

- Schedule of manufacture and installation.

The evaluation report, certifications and catalog cuts shall be submitted to the Engineer for review prior to ordering the DPF or other device, unless approved by the Engineer in writing.

Installation and Use of Diesel Particulate Filter (DPF): After approval of the selected DPF or other device, the Contractor shall install the device in accordance with manufacturer’s recommendations. A Technical Representative of the manufacturer must be present during the installation and be available during any maintenance of the device.

Close-out Report: A close-out report summarizing the selection, installation and utilization of the device must be prepared and submitted to the Engineer within 30 days of the last day the tested equipment is no longer utilized on this project.

The report shall include at a minimum the following information:

- Description of the evaluated diesel powered non-road construction equipment, including make, model, horsepower rating, model year, and equipment number;

- Description of work duty cycle observed on the tested equipment with the device installed;

- Operating temperature profile of the test equipment with the device installed;

- Tests performed, if any, and methods employed to perform said tests;

- Maintenance required and performed on the equipment and device;

- Any special requirements utilized on the equipment (i.e. ultra low sulfur diesel fuel, engine or equipment modifications, etc.);

- Timeline indicating operations and usage of the test equipment and associated operating conditions.

There shall be no time granted to the contractor for compliance with this specification.  The contractor’s compliance with this specification and any associated regulations shall not be grounds for claims as outlined in Section 1.11 – “Claims”.

Method of Measurement:  The following work will be measured for payment and paid in accordance with Article 1.09.04 – “Extra and Cost-Plus Work”:

- Evaluation and Selection of Diesel Particulate Filter (DPF): The evaluation, testing, selection of the construction equipment, the evaluation by qualified technical representative(s) from the manufacturer of the DPF, or their designee, evaluation report, selection of device and all associated submittals will be measured.

- Installation and Use of Diesel Particulate Filter (DPF): The cost of the Diesel Particulate Filter will be measured for payment. Receipted invoices documenting the purchase of the DPF are required.

- Close-out Report: The close-out report shall be measured.

The following work will not be measured for payment:

- Installation and Use of Diesel Particulate Filter (DPF): The installation and use of the Diesel Particulate Filter will not be measured for payment, but shall be included in the general cost of the contract.

- Equipment and Labor:  All use and maintenance of the tested construction equipment, including all labor, fuel, parts, tools, and other associated equipment and costs will not be measured for payment, but shall be included in the general cost of the contract.

Basis of Payment:  The sum of money shown on the Estimate and in the itemized proposal as “Estimated Cost” for this work will be considered the bid price even though payment will be made as described below.  The estimated cost figure is not to be altered in any manner by the bidder.

Should the bidder alter the amount shown, the altered figures will be disregarded and the original price will be used to determine the total amount for the contract.  The basis of payment for this work shall be as follows:

Evaluation and Selection of Diesel Particulate Filter (DPF): The evaluation, testing, selection of the construction equipment, the evaluation by qualified technical representative(s) from the manufacturer of the DPF, or their designee, evaluation report, selection of device and all associated submittals shall be paid in accordance with Article 1.09.04 – “Extra and Cost-Plus Work”.

Installation and Use of Diesel Particulate Filter (DPF): The cost of the Diesel Particulate Filter shall be paid in accordance with Article 1.09.04 – “Extra and Cost-Plus Work”. Receipted invoices documenting the purchase of the DPF are required. The installation and use of the Diesel Particulate Filter will not be measured for payment, but shall be included in the general cost of the contract.

Close-out Report: The close-out report shall be paid in accordance with Article 1.09.04 – “Extra and Cost-Plus Work”.

Equipment and Labor:  All use and maintenance of the tested construction equipment, including all labor, fuel, parts, tools, and other associated equipment and costs shall be included in the general cost of the contract.

All materials, equipment, labor, submittals, tools, labor, and services of the technical advisor not identified shall be included in the general cost of the contract.

Pay Item	Pay Unit

Diesel Particulate Filter	Est’d