Landsat Beta surface reflectance product - April, 2005

1. Algorithm Description

The Landsat surface reflectance product is derived from Top of the Atmopshere (TOA) reflectance by applying an atmospheric correction scheme that assumes that: (a) the target is lambertian and infinite and (b) the gaseous absorption and particle scattering in the atmosphere can be decoupled. The TOA reflectance can be expressed as:

TOA = Tg(O3,O2,CO2,NO2,CH4) [ R+A + TR+A Tg(H2O) s / (1 - SR+A s) ]

Where s is the surface reflectance, Tg is the gaseous transmission due to the gases listed between parentheses, TR+A is Rayleigh and aerosol transmission, R+A is the Rayleigh and aerosols atmospheric intrinsic reflectance, and SR+A is the Rayleigh and aerosols spherical albedo. The transmission, intrinsic reflectance and spherical albedo terms are computed using the 6S radiative transfer code (Vermote et al., 1997). The surface pressure, ozone concentration and water vapor content needed in these computations are determined from the NCEP reanalysis data.

Most available radiative transfer methods for Landsat atmospheric correction (Vermote et al., 1997; Ouaidrari and Vermote, 1999; Liang et al., 1997) make use of the dark dense vegetation (DDV) method of Kaufman et al. (1997) in order to extract aerosol optical thickness from the imagery. Based on the physical correlation between chlorophyll absorption and bound water absorption, the DDV method suggests a linear relation between shortwave-infrared (SWIR) surface reflectance (nearly unaffected by the atmosphere) and surface reflectance in the blue and red bands. Using this relation to calculate surface reflectance for the visible bands, and comparing the result to the TOA reflectance, we

may estimate aerosol optical depth.

Specifically, the aerosol optical thickness used in the LEDAPS atmospheric correction process is retrieved from Landsat data using simulated reflectance Look up tables (LUTs) and an estimate of the surface reflectance in the blue band. A continental aerosol model is then applied through the blue AOT retrieval. The LUTs are computed for each scene using the 6S code, the scene geometry and NCEP ancillary data. The estimate of the blue band reflectance is determined for a 1km x 1km grid cell as a function of the reflectance in the2.2 m band (band 7) using the Kaufman et al (1997) approach. Figure 1 illustrates the high correlation the surface reflectance in the blue band and the SWIR reflectance. The blue band was corrected for atmospheric effects using the aerosol optical thickness measured by AERONET.

Fig.1: Relation between the ETM+ blue and SWIR reflectances.

2. Validation

Four approaches are being used to validate Landsat surface reflectance (SR) products:

- comparison with near-simultaneous (15 minutes apart) MODIS 500m single-swath surface reflectance data.

- comparison of Landsat aerosol optical thickness with that obtained by simultaneous AERONET sun photometer network observations.

- comparison of Landsat surface reflectance with independent surface reflectance retrievals using helicopter or ultralight based radiometers, within10 days of Landsat acquisition (e.g. BOREAS, SNF helicopter MMR data).

- examination of temporal stability of invariant targets across multiple acquisitions.

For the Beta release of the Landsat surface reflectance product, only the first two

validation tasks have been attempted, on a limited geographic basis.

2.1. Comparison with Aeronet Aerosol Optical Thickness

Aerosol Robotic Network (AERONET) sites record aerosol properties throughout the world, and several of these records extend back to the early 1990’s (Holben et al., 1998). The Beta SR dataset includes several AERONET sites, and observations from 21 of these sites were compared with simultaneous aerosol optical thickness obtained using the image-based approach discussed above (Table 1, Fig. 2).

All AOT values reported are for the blue wavelengths. Results suggest reasonable agreement with AERONET observations. Spatial patterns for the sites suggest that land cover type may influence the aerosol retrievals (Fig. 3), although this effect is suppressed compared to earlier versions of the product.

For comparison, uncertainties in MODIS land AOT retrievals is (0.05 + 0.2*AOT), which have also been plotted on Fig. 2.

| AERONET Site | TM Scene | Date | AOT blue Aeronet | AOT blue ETM |
| --- | --- | --- | --- | --- |
| Howland | p011r029 | 2002253 | 0.4 | 0.1767 |
| GSFC | p015r033 | 2001278 | 0.25 | 0.257 |
| MD_Science_Center | p015r033 | 2001278 | 0.29 | 0.414 |
| SERC | p015r033 | 2001278 | 0.25 | 0.294 |
| BSRN_BAO_Boulder | p033r032 | 2000261 | 0.05 | 0.024 |
| Sevilleta | p034r036 | 2000130 | 0.12 | 0.135 |
| Bratts_Lake | p035r025 | 2000208 | 0.2 | 0.161 |
| Bratts_Lake | p036r025 | 2001217 | 0.08 | 0.026 |
| Maricopa | p036r037 | 2000167 | 0.09 | 0.1889 |
| Tucson | p036r037 | 2000167 | 0.11 | 0.056 |
| UCLA | p041r036 | 2000122 | 0.2 | 0.275 |
| Shirahama | p109r037 | 2001105 | 0.3 | 0.344 |
| Anmyon | p116r035 | 2001266 | 0.11 | 0.156 |
| Moscow_MSU_MO | p179r021 | 2002150 | 0.17 | 0.059 |
| Rome_Tor_Vergata | p191r031 | 2001215 | 0.49 | 0.384 |
| Ilorin | p191r054 | 2000037 | 1.05 | 0.921 |
| Ouagadougou | p195r051 | 2001195 | 0.275 | 0.346 |
| Lille | p199r025 | 2000237 | 0.29 | 0.38 |
| Palaiseau | p199r026 | 2000237 | 0.22 | 0.156 |
| Thompson | p033r021 | 2001260 | 0.06 | 0.033 |
| HJAndrews | p045r029 | 1999275 | 0.08 | 0.033 |

Table 1: AERONET and ETM+ AOT comparisons

Fig. 2: ETM+ AOT values regressed against simultaneous AERONET AOT values for the blue band. Solid red line is the one-to-one line, dashed lines represent MODIS AOT uncertainties of (0.05+0.2*AOT).

Fig. 3. TOA reflectance, atmospherically corrected surface reflectance, and AOT (blue wavelengths) for the AERONET sites used in the study.

2.2. Comparisons with MODIS

MODIS 500m Surface Reflectance (SR) products were processed from individual swaths,and registered with Landsat-7 ETM+ SR products from images acquired within 15 minutes. The Landsat SR products were aggregated to 500m resolution by averaging blocks of pixels. For one scene in Canada (BOREAS study region), three sub-windows from each dataset were extracted and compared (Fig. 4).

Plotting histograms before and after correction for each sub-window suggests that, for most spectral bands, differences between MODIS and ETM+ SR values are negligible (Figs. 5,6,7). One exception is the blue band, where ETM+ SR  values trend ~1% higher than the comparable MODIS band.

For two sub-windows, some differences also exist for the shortwave infrared (1.m) band, although the spread of the data distribution makes it difficult to detect a consistent trend.

3. Evaluation and Known Issues

As noted elsewhere, Beta products are intended primarily for users to become familiar with data formats and general product characteristics, and to feed further validation efforts. Without further validation, it is not recommended to use Beta products for scientific use. Nevertheless, the initial results presented here suggest that the atmospheric correction approach is producing reasonably accurate surface reflectance values, and is certainly improving the radiometric accuracy and stability of the data compared to top-of-atmosphere products.

Known issues to emerge from our analyses (to be corrected in future releases) include:

- Cloud/snow/ice mask is prone to errors. For the Beta release the snow/ice bits in the QA mask have been zeroed.

- Landsat AOT retrievals are prone to adjacency effects (scattered radiance into dark target locations from surrounding bright targets).

- Landsat blue band SR too high (undercorrected)

- The calibration of bands 1 and 2 of Landsat 5 is suboptimal.

Fig. 4. BOREAS ETM+ scene (top-of-atmosphere Œ TOA and SR) with locations of sub-windows for comparison with MODIS surface reflectance.

Fig. 5: Histograms of Landsat TOA reflectance (red), MODIS surface reflectance (blue) and Landsat surface reflectance (green) for the following bands: blue (upper-left), green (upper-center), red (upper-right), near-infrared (lower-left), mid-infrared (lower-right)

Fig. 6: Same as Fig 5, for Subwindow 2

Fig. 7: Same as Fig. 5, for Subwindow 3

4. References

Kaufman, Y.J., Wald, A.E., Remer, L.A. et al., 1997, The MODIS 2.1-micron channel Œ correlation with visible reflectance for use in remote sensing of aerosol, IEEE Trans. Geosci. Remote Sens., 35, 1286-1296.

Liang, S., Fallahdal, H., Kalluri, S., et al., 1997, An operational atmospheric correction algorithm for Landsat Thematic Mapper imagery over the land, J. Geophys. Res., 102, 17,173-17,186.

Ouaidrari, H., and Vermote, E.F., 1999, Operational atmospheric correction of Landsat TM data, Remote Sens. Environ., 70, 4-15.

Vermote, E.F., et al., 1997, Atmospheric correction of visible to middle-infrared EOS-MODIS data over land surfaces: Background, operational algorithm, and validation, J. Geophys. Res., 102, 17131- 17141.

# Text boxes

Sci. Center

SERC

Thompson

GSFC

0.5

AOT

Blue

Surface

0.375

0.25

0.125

0.0

TOA

Surface

TOA

Scene: p033r021

Date: 09/17/2001

MODIS surface

TM surface

TM TOA

TM surface

MODIS surface

TM TOA

TM TOA

MODIS surface

TM surface