WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11125 | In-Flight Anomaly Number -- | Contractor Report Number E-110 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title GH2 PRESSURE TRANSDUCER FAILED DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1 | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE PRESSURE TRAN | PART# PD7400098-089 | SER/LOT# 2132 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 PRES TRN | PART# PD7400098-089 | SER/LOT# 2132 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EV - NOT-TO-SPEC | Cause ETE - EI-TEST-ENVR |
| System ELECTRICAL | Defect CX - VOID | Material C - EEE | Work Contact J. ADAMS | Fail Date 12/08/1987 |
| Received at MSFC 12/10/1987 | Date Isolated -- | FMEA Reference 3.4.X.X | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EE - RANDOM | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/13/1995 | CN RSLV SBMT 05/23/1988 | Defer Date -- | Add Date -- | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 06/03/1988 | Status E - CLOSED-E | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE ULLAGE TRANSDUCER FAILED THE VENDOR ATP REQUIREMENTS FOR ACCURACY OF THE OUTPUT VOLTAGE VERSUS THE APPLIED PRESSURE. THE TRANSDUCER OUTPUT VOLTAGE WAS 4.3% OF FULL SCALE BELOW THE NOMINAL VALUE AT 33 PSIA, ON PRESSURE RISE. MAXIMUM ALLOWED IS 1% |
| Contractor Investigation/Resolution CAUSE: THE TRANSDUCER CASE HAD AN AIR LEAK, PROBABLY AT THE SEAL-OFF WELD OR ELECTRICAL FEED THROUGH HERMETIC SEALS R/C: NONE REQUIRED 12/10/87 - THIS REPORT IS NOT A LAUNCH CONSTRAINT: THE FAILURE WAS DETECTED DURING VENDOR ACCEPTANCE TEST WHICH IS DESIGNED TO DETECT DEFECTIVE HARDWARE. THIS STATEMENT HAS BEEN COORDINATED WITH THE ET PROJECT MANAGER, MR. G.P. BRIDWELL _________________________________ 5/3/88 - THIS REPORT HAS BEEN DEFERRED FOR STS-26, PER NSTS 07700, VOLUME XI AND NSTS 08126 PARAGRAPH 3.4.1, ITEM C WHICH STATES "PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE AND IS CLEARLY SCREENED BY ACCEPTANCE TEST, PREFLIGHT CHECKOUT, OR SPECIAL TEST." THE DEFERRAL STATUS HAS BEEN APPROVED BY THE ET PROJECT MANAGER, MR. G.P. BRIDWELL ____G.P. BRIDWELL (SIGNED) 5/13/88______ 5/23/88 GENERAL - THE TRANSDUCER FAILED TO MEET THE ACCURACY REQUIREMENTS FOR OUTPUT VOLTAGE VERSUS APPLIED PRESSURE AT 73 DEGREES-F DURING VENDOR ACCEPTANCE TESTING (ATP). THE VENDOR ATP CONTAINS MULTIPLE TESTS OF ACCURACY, BOTH BEFORE AND AFTER VIBRATION AND PROOF PRESSURE TESTING, AND AT SEVERAL DIFFERENT OPERATING TEMPERATURES. PREVIOUS CAPS: E-082, E-091, E-101, E-106 TASK I. FAILURE INVESTIGATION FAILURE ANALYSIS T-34365 WILL BE PERFORMED AT THE VENDOR'S FACILITY, UNDER THE OBSERVATION OF THE MMC SOURCE REPRESENTATIVE CLOSURE STATEMENT THE VENDOR PERFORMED THE FAILURE ANALYSIS ACCORDING TO A JOINTLY APPROVED FAILURE ANALYSIS PLAN. THE TRANSDUCER CASE WAS FOUND TO HAVE AN AIR LEAK, PROBABLY AT THE CASE SEAL-OFF HOLE WELD OR AT ONE OF THE ELECTRICAL FEEDTHROUGH HERMETIC SEALS. THE TIME BETWEEN THE VENDOR'S IN-PROCESS TEST, WHICH HAD LESS THAN 1% ERROR, AND THE ACCEPTANCE TEST PLAN FAILURE WAS 266 DAYS. ASSUMING A CONSTANT LEAK RATE, THE TRANSDUCER LEAKED AT APPROXIMATELY 4.2 X 10(TO THE NEGATIVE EIGTH) CC/SEC OF AIR, AT NORMAL TEMPERATURE AND PRESSURE THE VENDOR TESTS THE COMPLETED TRANSDUCER, LESS THE CASE SEAL-OFF WELD AND OUTPUT WIRE ATTACHMENT, TO A LEAK RATE OF LESS THAN 1.0 X 10(TO THE NEGATIVE 10TH) CC/SEC OF AIR, AT NORMAL TEMPERATURE AND PRESSURE TASK II. CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. THIS IS THE FIRST OCCURRENCE OF SUCH A FAILURE IN THE ET PROGRAM TASK III. CLEARANCE OF EFFECTIVITIES THERE ARE NO CONSTRAINTS. THERE ARE NUMEROUS CHECKS OF TRANSDUCER ACCURACY BETWEEN MANUFACTURE AND FLIGHT. THE TESTS APPLY TO BOTH LOX AND LH2 ULLAGE PRESSURE TRANSDUCERS O THE VENDOR ACCEPTANCE TEST PLAN PROVIDES HIGHLY ACCURATE CALIBRATION CHECKS ACROSS THE ENTIRE TRANSDUCER OPERATING BAND AT THREE DIFFERENT TEMPERATURES O TRANSDUCER ACCURACY IS VERIFIED DURING FINAL TEST AND CHECK-OUT OF THE ET PER THE "ET FLIGHT ACCEPTANCE REQUIREMENT, TM04K-B" THE TEST RESULTS ARE REQUIRED TO BE EVALUATED BY MMC ELECTRICAL ENGINEERING O THE "OPERATIONS AND MAINTENANCE REQUIREMENTS AND SPECIFICATIONS DOCUMENT, FILE IV", CHECKS THE TRANSDUCERS FOR ACCURACY AT THE STORAGE PRESSURE OF THE ET (I.E. APPROXIMATELY 6 PSIG) O THE "OPERATIONS AND MAINTENANCE REQUIREMENTS AND SPECIFICATIONS DOCUMENT, FILE II," CHECKS THE TRANSDUCERS FOR ACCURACY, ONE AGAINST THE OTHER, AT THE STORAGE PRESSURE OF THE ET. THE CHECKS ARE REQUIRED AFTER ET/ORBITER MATE AND DURING THE LAUNCH COUNTDOWN TASK IV. CAPS CLOSURE SUMMARY THE TRANSDUCER FAILED THE VENDOR ATP FOR ACCURACY DUE TO AN AIR LEAK IN THE CASE. THIS WAS THE FIRST SUCH FAILURE IN THE ET PROGRAM. THERE ARE SUFFICIENT TESTS OF TRANSDUCER PERFORMANCE IN THE BUILD/FLIGHT PREPARATION CYCLE TO DETECT ANY SUCH FAILURES THIS PROBLEM IS SUBMITTED TO MSFC FOR REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11125 | IFA# -- | Contractor RPT# E-110 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-089 | Asmnt Part Name LH2 PRES TRANSDUCER | Asmnt Serial/Lot# 2132 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE MV - EXT LEAK |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 4 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |