MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A05946 | In-Flight Anomaly Number -- | Contractor Report Number E-068 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title WIRE SHORT TO SHIELD HARNESS 303W10 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B (X) C D E (X) F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-1 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE WIRE | PART# E6590081 | SER/LOT# N/A | MANUFACTURER N/A |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause MAW - MFG-ASY-WORK |
| System ELECTRICAL | Defect DA - ROUGH | Material F - INSUL | Work Contact S. BRAGG | Fail Date 12/13/1982 |
| Received at MSFC 01/04/1983 | Date Isolated -- | FMEA Reference 3.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 02/24/1983 | Defer Date -- | Add Date -- | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project P. DICKERSON | Project MGR -- |
| Approval |
| Design L. GUZINSKY | Chief Engineer -- | S & MA D. NEWMAN | Project P. DICKERSON | Project MGR -- |
| PAC Assignee M. GLASS | PAC Review Complete MG | MSFC Closure Date 04/07/1983 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: DURING PRE-FRF CHECKOUT OF ST-6 AT KSC A SHORT TO SHIELD WAS IDENTIFIED ON A SRB POWER CIRCUIT. SUBSEQUENT TO FRF THE SHORT WAS ISOLATED TO CABLE HARNESS 303W10, PIN B' ON LWT-1 |
| Contractor Investigation/Resolution CAUSE - A DEFECT IN THE KAPTON INSULATION OF THE WIRE RESULTED IN A SHORT CIRCUIT OF THE WIRE'S CONDUCTOR TO THE OVERALL SHIELD WHEN THE CABLE TRAY FILLED WITH RAIN WATER. THE CAUSE OF THE DEFECTIN KAPTON INSULATION COULD NOT BE DETERMINED DUE TO THE EXTENSIVE ARCING DAMAGE HOWEVER MFR'G DAMAGE AT MAF IS THE MOST PROBABLE REASON. 1/7/83 - LWT-1 CONSTRAINT IS LIFTED BASED ON THE FOLLOWING RATIONALE: - SHORTED WIRE WAS REPAIRED & RETESTED (REF AR M2663, SUPA). - ECP B01575 WILL ADD DRAIN HOLES TO CABLE TRAY TO ASSURE NO WATER BUILDUP. THIS CHANGE HAS BEEN COORDINATED WITH THE ET PROJ OFFICE - ____JAMES B. ODOM____ 2/25/83 RESOLUTION - FAILURE ANALY REVEALED THE CAUSE TO BE A DEFECT IN THE KAPTON INSULATION WHICH BROKE DOWN WHEN THE CABLE TRAY COLLECTED RAIN WATER. LWT-1 WAS CLEARED FOR LAUNCH BY REPAIR AT KSC.ALSO, DRAIN HOLES WERE ADDED TO THE CABLE TRAYS. HWT-6 & LWT-2 & SUBS WILL BE MODIFIED TO INCLUDE CABLE TRAY DRAIN HOLES. A REVIEW OF MFR'G INSPECTION & TEST REQMNTS (BOTH VENDOR & MAF) WAS CON- DUCTED & PROVED THEM ADEQUATE. THIS FAILURE IS, THEREFORE, CONSIDERED TO BE AN ISOLATED FAILURE. MAF QUALITY & PRODUCTION PERSONNEL HAVE BEEN ADVISED OF THIS DISCREPANCY. R/C: NONE REQ'D, ISOLATEDINCIDENCE. 2/28/83 - CLOSURE DISTRIBUTED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A05946 | IFA# -- | Contractor RPT# E-068 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# E6590081 | Asmnt Part Name WIRE | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.12.10.2 | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# HARNESS 303W10 | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# N/A | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |