A Briefing Paper on

Fiber Reinforced Polymer Composite Bridge Technology

For the AASHTO Subcommittee on Construction

August 2001, Wichita, Kansas

Steven E. Toillion

The Federal Highway Administration (FHWA), in partnership with State Departments of Transportations (DOTs), has researched and demonstrated the use of fiber reinforced polymer (FRP) composite, space age technology for bridge construction. New breeds of these high performance and innovative materials developed in the last 70 years are making headway into the civil and bridge infrastructures. Structural components for hybrid bridge construction such as FRP reinforcing elements, cable and tendon systems, and laminates have been successfully used in highway bridges. Currently, there are more vehicular bridge projects using FRP composite materials in the United States than in any other country. Many of these projects are funded through FHWA's Innovative Bridge Research and Construction program (IBRCP). The current focus for the FHWA is to advance the FRP composite technology to rebuild the American transportation infrastructure in new bridge construction, as well as the rehabilitation and maintenance of the existing bridge inventory. The use of the FRP materials for repair and strengthening of structural concrete members is increasing, and when properly designed and applied, it can be effective and efficient.

The IBRCP was established under TEA-21. IBRCP is a 6-year program that provides direction and funding to help local and country road agencies, as well as State DOTs, defray the cost of incorporating innovative materials and materials technologies in bridge repair, rehabilitation, replacement, and new construction. The legislation establishes program goals to emphasize the role of these high-performance materials and construction techniques in reducing maintenance and life cycle costs. Authorized funding levels for the program are:

|  | FY 1998 | FY 1999 | FY 2000 | FY 2001 | FY 2002 | FY 2003 |
| --- | --- | --- | --- | --- | --- | --- |
| Research | $ 1 M | $ 1 M | $ 1 M | $ 1 M | $ 1 M | $ 1 M |
| Construction | $ 10 M | $ 15 M | $ 17 M | $ 20 M | $ 20 M | $ 20 M |

Bridges on all public roads, including State and locally funded projects, are eligible for IBRCP funding. During FY 1998-2001, the IBRCP funded 84 FRP projects. Shown below is a breakdown of the projects by application:

- 35%	Decks

- 26%	Bonded Reinforcement

- 17%	Other (Includes Superstructure Beams, Piles, Railings, Etc.)

- 11%	Rebar

- 6%	Prestressing

- 5%	FRP/Glulam

FRP PROJECTS IN KANSAS

The first vehicular FRP bridge in the United States was installed in Russell County, KS in 1996. This bridge is a single span, slab bridge. In 1999, two bridge decks were replaced using FRP deck panels. The panels were placed on existing steel beams. These two bridges are on K 126 in Crawford County, KS. There are currently three projects underway. The first project is looking at bridge rails. We have taken two, one concrete and one steel, crash tested bridge rail systems and are testing them on FRP deck panels. Static testing has been completed and the actual crash testing will be done later this year. The second project is to build a temporary bridge to use during construction projects. The temporary bridge will use FRP deck panels on steel beams. The third project is using FRP to strengthen existing girders. Six concrete ‘T’ beams are being strengthened or repaired and tested to failure.

FRP VIRTUAL TEAM

The FHWA created a FRP Virtual Team (V-Team). The objective of the team is to:

1) Accelerate the delivery of technical expertise on FRP composites bridge technology

2) Develop and lead a national agenda on FRP composites bridge technology

3) Serve as a reliable and creditable information source to the public

The V-Team is made up of individuals from the FHWA, State DOTs, academia, and industry. The team has had two face-to-face meetings and a number of teleconferences. A database of FRP projects is being created and will be available to the public soon. The database and other FRP information can be accessed through the FHWA’s bridge web site, http://www.fhwa.dot.gov/bridge/index.htm. The products of the team will include the following:

1) Develop a customer-oriented virtual team

2) Develop a community for continuous learning

3) Develop and maintain a homepage and network

4) Develop and maintain a national knowledge management resource

5) Maintain a database on FRP bridge projects

If you have any FRP related questions of any kind please submit them on the web site or call one of the V-Team members directly.

FHWA 		STATE DOT

Milo Cress, NE	(402) 437-5977	Pat Hipley, CALTRANS	(916) 227-8608

John Hooks, HQ	(202) 366-6712	Paul Liles, Jr., GA DOT	(404) 656-5280

Gary Jakovich, EFLHD	(703) 404-6236	Jerry O'Connor, NY DOT	(607) 324-8456

Eric Munley, TFHRC	(202) 493-3046

Roland Nimis, WRC	(415) 744-2653 	OTHER

Tom Saad, MRC	(708) 283-3521 	Gregg Blaszak, BG Intrnl	(410) 337-9779

Jeff Smith, SRC	(404) 562-3905 	Nabil Grace, Lawrence Tech	(248) 204-2556

Benjamin Tang, HQ	(202) 366-4592 	Mark Henderson, LJB Engrs	(937) 259-5090

Lou Triandafilou, ERC	(410) 962-3648 	Sami H. Rizkalla, NC State	(919) 513-4336

Steve Toillion, KS	(785) 267-7281