|  | Forest Service Manual national headquarters (wo) Washington, DC |
| --- | --- |

fsM 6700 - safety and health program

chapteR 6740 - hazardous materials

Amendment No.:  6700-2001-1

Effective Date:  October 23, 2001

Duration:  This amendment is effective until superseded or removed.

| Approved: clyde thompson Deputy Chief for Business Operations | Date Approved: 10/07/2001 |
| --- | --- |

Posting Instructions:  Amendments are numbered consecutively by title and calendar year.  Post by document; remove the entire document and replace it with this amendment.  Retain this transmittal as the first page(s) of this document.  The last amendment to this title was 6700-99-1 to 6740 Contents.

| New Document | 6740 | 33 Pages |
| --- | --- | --- |
| Superseded Document(s) (Amendment Number and Effective Date) | 6740 Contents (amendment 6700-99-1, 11/16/99) 6740 (amendment 6700-97-2, 5/6/97) | 3 Pages 3 Pages |

Digest:

6741 to 6741.4	 - Incorporates with only minor editorial changes the direction on radiation protection previously contained in interim directive (ID) 6740-99-1.  This amendment revises direction on authorities, objectives, policies, and responsibilities; revises position titles; and sets out requirements and procedures for obtaining a radiation source permit from the USDA Radiation Safety Staff.  An individual needing to apply for a permit to use, handle, store, and transport radioactive materials and radiation-emitting equipment and devices, including x-ray,

Digest--Continued:

must complete Form RSS-10, Radiation Worker Registration, and Form RSS-20, Application To

Use Radiation Producing Sources, to the USDA Radiation Safety Staff, along with the appropriate permit application within the five general categories of radioactive materials:  general radioactive material (Form RSS-21); moisture/density gauges (Form RSS-22); electron capture detectors (Form RSS-23); self-shielded irradiators (Form RSS-24); and x-ray producing equipment (Form RSS-25).

6745 to 6745.3	 - Incorporates with only minor content and editorial changes the direction on authorities, objectives, policies, and responsibilities regarding explosives and blasting materials (including avalanche ammunition) previously contained in ID 6740-99-2.  This amendment contains requirements on training and certification for Forest Service blasters, including the use of Form FS-6700-24, Application for Explosives and Blasting Certification, and Form 
FS-6700-27, Explosives and Blasting Certificate.

This amendment retains the requirements formerly in ID 6740-99-2 that a Level I Blaster-in-Training does not need a commercial driver’s license (CDL) to meet the explosives and blasting certification requirements (FSM 6745.1, ex. 01; FSM 6745.12, ex. 01).  The CDL is required for blaster certification only when transporting explosives (FSM 6745.11).

This amendment does not incorporate the responsibilities for the National Explosives and Blasting Steering Committee previously set out in ID 6740-99-2.  This amendment clarifies that   the National Safety and Health Council is responsible for collaborating with affected staffs on all safety matters, to include explosives safety.

Table of Contents

6741 - RADIATION PROTECTION	5

6741.01 - Authority	5

6741.02 - Objective	6

6741.03 - Policy	6

6741.04 - Responsibility	6

6741.04a - Chief	6

6741.04b - Regional Foresters, Station Directors, Area Director, and Institute Director	6

6741.04c - Field Location Managers	7

6741.04d - Director, Human Resources Management, Washington Office	7

6741.04e - National Radiation Protection Program Manager	7

6741.04f - Radiation Technical Advisor	8

6741.04g - Radiation Protection Coordinators	8

6741.04h - Location Radiation Protection Officers	9

6741.04i - Radiation Source Users	10

6741.05 - Definitions	11

6741.06 - Role of U.S. Department of Agriculture in Radiation Safety	11

6741.1 - Procurement, Use, and Disposal of Radiation Sources	12

6741.2 - USDA Radiation Source Use Permits	13

6741.3 - Transportation of Radiation Sources	13

6741.4 - Protection of Ancillary Staff from Occupational Radiation Exposure	13

6742 - HAZARDOUS CHEMICALS	14

6742.01 - Authority	14

6742.04 - Responsibility	15

6742.04a - Regional Foresters, Station Directors, Area Director, and Institute Director	15

6742.04b - Hazardous Materials Management Coordinators	15

6742.1 - Procurement	15

6742.2 - Labeling	15

6742.3 - Transportation	16

6742.4 - Storage	16

6742.5 - Disposal	16

6742.6 - Pesticides	16

6743 - ASBESTOS	16

6743.1 - Purchase and Use	16

6743.2 - Removal	16

6743.3 - Sealing	17

6743.4 - Reporting	17

6744 - TRAINING	17

6745 – EXPLOSIVES AND BLASTING MATERIALS	17

6745.01 - Authority	17

6745.01a - Use	17

6745.01b - Storage	18

6745.01c - Transportation	18

6745.01d - Disposal	19

6745.02 - Objectives	19

6745.03 - Policy	19

6745.04 - Responsibility	21

6745.04a – Chief	21

6745.04b - Deputy Chief for Business Operations	21

6745.04c - National Explosives and Blasting Technical Advisory Group	21

6745.04d – National Explosives Safety Program Manager	21

6745.04e - Managers of Technology and Development Centers and Director of National Avalanche Center	22

6745.04f - Regional Foresters	22

6745.04g - Regional Blaster Coordinators	23

6745.04h - Regional Blaster Examiners	23

6745.04i - Forest Supervisors and Unit Managers	24

6745.04j - Contracting Officers	24

6745.04k - Lead Blasters	25

6745.04l - Blasters - General/Fireline/Avalanche	26

6745.05 - Definitions	26

6745.06 - Reference	26

6745.1 - Certification	27

6745.11 - Steps in Certification Process	30

6745.12 - Certificate	31

6745.2 - General Standards	33

6745.3 - Contractor Requirements	33

# 6741 - RADIATION PROTECTION

See FSM 2160 and FSH 6709.11 for further direction on radioactive materials and radiation-emitting equipment and devices (radiation sources).  All Forest Service employees using radiation sources must hold a current radiation source permit issued by the USDA Radiation Safety Staff.  Procedures for permit application and renewal are in FSM 6741.2.  Application forms include:

1.  Form RSS-10, Radiation Worker Registration.

2.  Form RSS-20, Application To Use Radiation Producing Sources.

3.  Form RSS-21, Application for Radioactive Materials Use.

4.  Form RSS-22, Application To Use Nuclear Gauges.

5.  Form RSS-23, Application To Use Electron Capture Detectors.

6.  Form RSS-24, Application To Use Self-Shielded Irradiators.

7.  Form RSS-25, Application To Use X-Ray Producing Equipment.

8.  Form RSS-29, X-Ray Producing Equipment Inventory Record.

9.  Form RSS-70, Personnel Dosimetry Request.

### 6741.01 - Authority

1.  Title 10, Code of Federal Regulations, parts 20 and 30 (10 CFR 20 and 30).  U.S. Nuclear Regulatory Commission regulations in part 20 establish standards for protection against radiation; part 30 covers domestic licensing of by-product material.

2.  Title 29, Code of Federal Regulations, sections 1910.96 and 1926.53 (29 CFR 1910.96 and 1926.53).  U.S. Department of Labor Occupational Safety and Health Administration regulations establish standards for employee protection from overexposure to ionizing radiation within general industry and construction activities.

3.  Title 40, Code of Federal Regulations, parts 171-178 (40 CFR 171-178).  U.S. Department of Transportation regulations in these parts establish requirements for transport and handling of hazardous materials.

4.  U.S. Department of Agriculture, Safety and Health Manual.  This manual, issued by the Office of Human Resources Management, Safety and Health Management Division, establishes safety and health requirements at the Departmental and agency level throughout USDA.

5.  U.S. Department of Agriculture, Radiation Safety Handbook.  This handbook, issued by the Office of Human Resources Management, Safety and Health Management Division, Radiation Safety Staff, establishes requirements for Radiation Safety Programs at the Departmental and agency level throughout USDA.

### 6741.02 - Objective

To achieve safe, accident-free use, handling, storage, and transportation of radiation sources in the Forest Service for satisfactorily accomplishing research, engineering applications, and other uses, thereby preventing exposure of employees, the public, visitors, facilities, and the environment to radiation contamination.

### 6741.03 - Policy

1.  Comply with all applicable Federal, State, and local laws and regulations governing the use, handling, storage, and transportation of radiation sources.

2.  Protect employees, the public, visitors, facilities, and the environment from the risk of radiation hazards that could result from the use, handling, storage, and transportation of radiation sources under the control of the Forest Service.

### 6741.04 - Responsibility

### 6741.04a - Chief

The Chief is responsible for:

1.  Ensuring agency compliance with radiation-related laws and regulations and with USDA Radiation Safety Program policies, procedures, and practices.

2.  Nominating qualified individuals to serve as members and alternates on the USDA Radiation Safety Committee.

### 6741.04b - Regional Foresters, Station Directors, Area Director, and Institute Director

Regional Foresters, Station Directors, the Area Director, and the Institute Director are responsible for:

1.  Appointing a Radiation Protection Coordinator at the Region, Station, Area, and Institute headquarters level.

2.  Ensuring that managers at each location using radiation sources designate a Location Radiation Protection Officer.

3.  Terminating any activity or practice involving the unsafe use of radiation sources, or as recommended by the USDA Radiation Safety Committee or Director of USDA Radiation Safety Staff based on results of field inspections and program audits.

4.  Ensuring that employees who are occupationally exposed to radiation sources receive appropriate training and information on the associated hazards, risks, and safeguards of ionizing radiation.

### 6741.04c - Field Location Managers

Field Location Managers are responsible for:

1.  Reviewing and concurring on initial and renewal requests for radiation source permit applications submitted by Radiation Source Users at the unit.

2.  Appointing a Location Radiation Protection Officer to coordinate the location radiation protection program.

3.  Ensuring that all individuals who are permit holders have appropriate safety elements in their performance plans and that job descriptions clearly define actual duties and responsibilities involving radiation sources.

4.  Supporting the location radiation protection program.

5.  Ensuring prompt abatement of identified hazardous conditions.

### 6741.04d - Director, Human Resources Management, Washington Office

The Director of Human Resources Management, Washington Office, is responsible for:

1.  Ensuring that managers, supervisors, and Location Radiation Protection Officers at locations using radiation sources that emit ionizing radiation are evaluated on their compliance with the USDA Radiation Safety Program and the Forest Service Radiation Protection Program.

2.  Appointing the National Radiation Protection Program Manager from within the Safety, Health, and Uniforms Branch.

3.  Appointing the Radiation Technical Advisor.

### 6741.04e - National Radiation Protection Program Manager

The National Radiation Protection Program Manager, Human Resources Management Staff, Safety, Health, and Uniforms Branch, Washington Office, is responsible for administering radiation safety oversight of the Forest Service Radiation Protection Program, to include:

1.  Serving as liaison with the USDA Radiation Safety Committee, USDA Radiation Safety Staff, and Forest Service Radiation Protection Coordinators to resolve Forest Service radiation safety issues affecting compliance with Nuclear Regulatory Commission regulations and other applicable requirements.

2.  Representing the Forest Service as the primary member on the USDA Radiation Safety Committee.

3.  Reviewing permit applications and other radiation safety issues at the request of Radiation Protection Coordinators.

4.  Reviewing and updating annually the Forest Service Location Radiation Protection Officer - Radiation Source User list at the beginning of each fiscal year.

5.  Evaluating and monitoring the Forest Service Radiation Protection Program annually to ensure compliance with Nuclear Regulatory Commission regulations and USDA Radiation Safety Program requirements.

6.  Requesting the services of the Forest Service Radiation Technical Advisor, as necessary, to resolve Forest Service radiation safety issues.

7.  Recommending a Radiation Technical Advisor to the Director of Human Resources Management, Washington Office, for appointment from the Research and Development Deputy Area.

8.  Reporting all incidents of radiation exposure/leakage to the USDA Radiation Safety Staff upon notification from a Radiation Protection Coordinator, Location Radiation Protection Officer, or Radiation Source User.

### 6741.04f - Radiation Technical Advisor

The Radiation Technical Advisor, Research and Development Deputy Area, is responsible for:

1.  Advising the National Radiation Protection Program Manager on technical issues, problems, regulatory interpretations, and other radiation matters, as requested.

2.  Assisting with special projects that promote radiation protection, as necessary, when requested or authorized by the National Radiation Protection Program Manager.

### 6741.04g - Radiation Protection Coordinators

Radiation Protection Coordinators at the Region, Station, Area, and Institute headquarters offices are responsible for:

1.  Informing the USDA Radiation Safety Staff of changes to individual location radiation sources.

2.  Coordinating Region, Station, Area, and Institute radiation activities in accordance with Federal, State, and local laws and regulations, and USDA Radiation Safety Program and Forest Service Radiation Protection Program requirements.

3.  Ensuring that Location Radiation Protection Officers are aware of Department and Forest Service requirements and other communications related to the USDA Radiation Safety Program and Forest Service Radiation Protection Program requirements.

4.  Processing initial and renewal applications for radiation source permits received from Location Radiation Protection Officers, to include other administrative actions regarding the use, handling, storage, and transportation of radiation sources, as required.

5.  Coordinating training programs for Location Radiation Protection Officers.

6.  Submitting updated lists of Location Radiation Protection Officers and radiation source inventories to the National Radiation Protection Program Manager upon request.

7.  Reporting all incidents of radiation exposure/leakage to the National Radiation Protection Program Manager within six hours.

### 6741.04h - Location Radiation Protection Officers

Location Radiation Protection Officers at field unit locations in the Regions, Stations, Area, and Institute are responsible for:

1.  Maintaining an inventory of all radiation sources and users in the unit and reporting all changes to the Radiation Protection Coordinator.

2.  Maintaining radiation source inventories and reporting all changes to the Radiation Protection Coordinator.

3.  Ensuring that the unit takes adequate steps to protect Forest Service personnel, the public, visitors, facilities, and the environment from unacceptable levels of radiation exposure from radiation sources under Forest Service control.

4.  Reporting all incidents of radiation exposure/leakage from radiation sources under Forest Service control to the Radiation Protection Coordinator within 24 hours.

5.  Ensuring that all radiation sources on the unit are purchased, used, handled, stored, transported, and disposed of according to applicable Federal, State, and local laws and regulations; USDA Radiation Safety Program requirements; and Forest Service Radiation Protection Program requirements.

6.  Reporting all unsafe practices and conditions related to radiation sources to the field location manager and Radiation Protection Coordinator.

7.  Complying with the requirements contained in the USDA Radiation Safety Handbook (FSM 6741.01).

8.  Providing appropriate training, notification, and protective measures to prevent occupational exposure to radiation of visitors and ancillary staff (see FSM 6741.4).  This responsibility may be delegated to Radiation Source Users.

### 6741.04i - Radiation Source Users

Radiation Source Users are responsible for:

1.  Using, handling, storing, transporting, and disposing of radiation sources in accordance with Federal, State, and local laws and regulations; USDA Radiation Safety Program requirements; and Forest Service Radiation Protection Program requirements.

2.  Meeting minimum standards for permit issuance by the USDA Radiation Safety Staff.  See FSM 6741.2 for permit requirements.

3.  Providing the Location Radiation Protection Officer and Radiation Protection Coordinator copies of all administrative actions taken regarding radiation sources and users.

4.  Forwarding initial and renewal applications for radiation source permits to the Location Radiation Protection Officer for processing through the Radiation Protection Coordinator.

5.  Reporting within two hours to the Location Radiation Protection Officer all incidents of radiation source exposure, leakage, and spills, and providing information on actions taken to correct and decontaminate the workplace.

6.  Discontinuing all operational and administrative radiation source use in a responsible and timely manner before the effective dates of any retirement, transfer, termination, or other personnel action that affects the status and responsibilities of Radiation Source Users.

7.  Maintaining currency in technical use, health physics, and administration of radiation sources by meeting training or refresher course requirements in compliance with the USDA Radiation Safety Program and Forest Service Radiation Protection Program requirements.

8.  Complying with the requirements contained in the USDA Radiation Safety Handbook (FSM 6741.01).

9.  Providing appropriate training, notification, and protective measures to prevent occupational exposure to radiation of visitors and ancillary staff (see FSM 6741.4) when delegate the Location Radiation Protection Officer or when local conditions dictate.

### 6741.05 - Definitions

Ancillary Staff.  Auxiliary or support staff personnel (for example, administrative, janitorial, maintenance, academic, and research personnel).

Health Physics.  The application of radiation safety techniques to recognizing, evaluating, and controlling the effects of ionizing radiation and the use of its sources and generating equipment and devices.

Location.  A building, facility, research center, area, region, or State that has been designated as a single entity for purposes of radiation protection.

Location Radiation Protection Officer.  An individual who has been designated to provide advice and assistance regarding the USDA Radiation Safety Program and the Forest Service Radiation Protection Program requirements at a specific location where radioactive materials and/or radiation-emitting devices and equipment are used.

Radiation-Emitting Equipment and Devices.  Equipment and devices capable of producing or emitting ionizing radiation; for example, x-ray machines, electron microscopes, and x-ray diffraction units.

Radiation Sources.  Radioactive materials and/or radiation-emitting equipment and devices.

Radioactive Materials.  Substances containing an element that emits ionizing radiation upon decay.

### 6741.06 - Role of U.S. Department of Agriculture in Radiation Safety

1.  The Assistant Secretary for Administration has overall responsibility for the USDA Radiation Safety Program.  Routine operational aspects of the USDA Radiation Safety Program have been delegated to the Director of the USDA Radiation Safety Staff, Safety and Health Management Division, Office of Human Resources Management.  The USDA Radiation Safety Staff manages the daily functional operations for the safe use and control of radiation sources.

2.  The USDA Radiation Safety Committee establishes general policies regarding the USDA Radiation Safety Program and conducts periodic inspections and program audits of field locations and an annual audit of the USDA Radiation Safety Staff.  The committee includes representatives from the USDA Office of Human Resources Management, Safety and Health 
Management Division; Agricultural Marketing Service; Animal and Plant Health Inspection Service; Agricultural Research Service; Food Safety and Inspection Service; Forest Service; Grain Inspection, Packers, and Stockyard Administration; and Natural Resources Conservation Service.

## 6741.1 - Procurement, Use, and Disposal of Radiation Sources

1.  Radiation Source Users shall coordinate purchase, use, and disposal of all radiation sources through the Location Radiation Protection Officer.

2.  All Forest Service Radiation Source Users must hold a current and valid radiation source permit issued by the USDA Radiation Safety Staff before engaging in any activity requiring the purchase, use, handling, storage, transfer, transportation and/or disposal of radiation sources.  See FSM 6741.2 for detailed direction on the permit application process.

3.  Radiation Source Users are subject to permit review, field inspections, and program audits at the discretion of the Director of USDA Radiation Safety Staff, USDA Radiation Safety Committee, and Forest Service National Radiation Protection Program Manager.

4.  Disposal of radiation sources, including transferring and recycling, shall be fully documented by contractual agreement or other equivalent instrument.  To ensure proper disposal of radiation sources:

a.  Identify all radiation sources for disposal in the contract.

b.  Verify Nuclear Regulatory Commission or State licensing of the contractor to receive identified radiation sources.

c.  Assess the contractor's ability to perform by contacting Federal, State, and local nuclear regulatory agencies and former clients of the contractor.

d.  Include a contractual requirement for the contractor to certify that proper disposal of identified sources has been effected.

## 6741.2 - USDA Radiation Source Use Permits

1.  All uses of radiation sources require the issuance of a USDA radiation source permit.  Since USDA has been issued a specific license that regulates the use of by-product material by the Nuclear Regulatory Commission, the control of all radioactive materials and radiation-emitting equipment and devices, including x-ray, is required.

2.  Radiation Source Users must apply for radiation source permits issued by the USDA Radiation Safety Staff in order to use radioactive or radiation producing sources.  Complete Form RSS-10, Radiation Worker Registration, and Form RSS-20, Application To Use Radiation Producing Sources, along with the appropriate form for the specific radiation source needed, and forward these forms to the Location Radiation Protection Officer after concurrence by the appropriate Field Location Manager.

3.  The USDA Radiation Safety Staff issues permits in five general categories.  Applications for permits can include more than one category or may address a specific research or program requirement that is outside of the categories listed.  The five general categories are:

a.  General radioactive material (Form RSS-21).

b.  Moisture/density gauges (Form RSS-22).

c.  Electron capture devices (Form RSS-23).

d.  Self-shielded irradiators (Form RSS-24).

e.  X-ray producing equipment (Form RSS-25).

4.  Refer to chapter 5 of the USDA Safety and Health Manual (FSM 6741.01) for application requirements for specific radiation sources.

## 6741.3 - Transportation of Radiation Sources

Comply with the U.S. Department of Transportation requirements in 49 CFR parts 171-178 regarding transportation of radiation sources (FSM 6741.01).

## 6741.4 - Protection of Ancillary Staff from Occupational Radiation Exposure

1.  Ensure that appropriate training and notification are provided and protection measures are taken to prevent occupational exposure to radiation of visitors and ancillary staff (FSM 6741.05) who do not hold radiation source permits issued by the USDA Radiation Safety Staff as required by the USDA Safety and Health Manual.  For example, protection measures including timing/scheduling, distance, and shielding may be supplemented with a health physics presentation to all persons in the vicinity of radiation sources (FSM 6741.01).

2.  Post placards and labels in restricted areas regarding the presence of radiation sources in accordance with USDA Radiation Safety Staff requirements and 10 CFR 20.

3.  Post the following information in such a manner that individuals can read the information on their way into or out of restricted areas:

a.  Nuclear Regulatory Commission Form-3, Notice to Employees.

b.  10 CFR 19 and 20.

c.  Section 206 of the Atomic Energy Act of 1974, as amended.

d.  USDA license and license application.

e.  Results of Nuclear Regulatory Commission inspections and Notice of Violations and Department responses.

4.  Notify local emergency response units (police, fire department, and emergency medical services) of the presence of any radiation sources that may be a potential exposure when responding to an emergency.

5.  Ensure that clerical personnel responsible for purchasing, shipping, and receiving radiation sources are properly trained in their role in handling materials labeled as radiation sources.

# 6742 - HAZARDOUS CHEMICALS

For further direction on hazardous materials, see FSM 2160.

### 6742.01 - Authority

1.  Title 49, Code of Federal Regulations, parts 100-199 (49 CFR 100-199).  U.S. Department of Transportation regulations in these parts establish requirements for transportation of hazardous materials by rail, aircraft, vessel, and highway.

2.  Title 40, Code of Federal Regulations, parts 152-186 (40 CFR 152-186).  U.S. Environmental Protection Agency regulations in these parts establish requirements for implementing the Federal Insecticide, Fungicide, and Rodenticide Act.

3.  National Fire Protection Association 49, Hazardous Chemicals Data (NFPA 49).  National Fire Protection Association consensus standards list data on the health, flammability, and instability of approximately 325 chemicals.

4.  National Fire Protection Association 704 (NFPA 704).  National Fire Protection Association consensus standards establish requirements for the identification of the fire hazards of materials for emergency response.

5.  State and Local Requirements.  States and local jurisdictions may issue additional requirements that may apply to the agency’s hazardous chemicals procurement, use, labeling, transportation, storage, and disposal.

### 6742.04 - Responsibility

### 6742.04a - Regional Foresters, Station Directors, Area Director, and Institute Director

Regional Foresters, Station Directors, the Area Director, and the Institute Director have the responsibility to appoint a Hazardous Materials Management Coordinator who is responsible for technical information concerning hazardous materials.

### 6742.04b - Hazardous Materials Management Coordinators

For responsibilities of Hazardous Materials Management Coordinators, see FSM 2160.43a to 2160.43e.

## 6742.1 - Procurement

1.  Obtain a Material Safety Data Sheet from the manufacturer when purchasing chemicals other than common household chemicals.  All chemical manufacturers must provide these information sheets on request, but it is the responsibility of the purchaser to initiate the request.

2.  Order the smallest amount of chemicals feasible to prevent accumulation of unused chemicals.

## 6742.2 - Labeling

1.  During transportation, chemicals must be labeled in accordance with 49 CFR 172.400, General Labeling Requirements.

2.  Pesticides must be labeled in accordance with 40 CFR 156, Labeling Requirements for Pesticides and Devices.

3.  Chemicals identified as hazardous wastes that are being stored until disposal must be labeled in accordance with 40 CFR 262, Standards Applicable to Generators of Hazardous Waste.

4.  Additional requirements and guidance on chemical labeling are in the National Fire Protection Administration 325M, Guide to Fire Hazard Properties of Flammable Liquids, Gases, and Volatile Solids (NFPA 325) and FSH 6709.11, chapter 60, Hazardous Materials.

## 6742.3 - Transportation

See 49 CFR subchapter C, Hazardous Materials Regulation, and FSH 6709.11, Health and Safety Code Handbook, chapter 61.17, for transportation requirements.

## 6742.4 - Storage

For requirements on the storage of hazardous chemicals, see the following:

1.  NFPA 30, Flammable and Combustible Liquids Code.

2.  NFPA 45, Standards on Fire Protection for Laboratories Using Chemicals.

3.  FSH 6709.11, Health and Safety Code Handbook, section 61.71.

## 6742.5 - Disposal

See FSM 7460 for direction on the proper disposal of hazardous chemicals.  Where State and Federal disposal regulations differ, follow the more stringent regulation.

## 6742.6 - Pesticides

See FSM 2150 and FSH 2109.13 for direction on the use, storage, and disposal of pesticides.

# 6743 - ASBESTOS

## 6743.1 - Purchase and Use

1.  Forest Service employees shall not purchase or use asbestos in any form that may disperse fibers into the air (friable asbestos).

2.  Employees shall not be exposed to levels of airborne asbestos above permissible exposure limits established by the Department of Labor, Occupational Safety and Health Administration (OSHA).

## 6743.2 - Removal

No Forest Service employee shall remove friable asbestos products.  A qualified contractor shall perform all necessary removal operations (FSH 6709.11, sec. 61.8).

## 6743.3 - Sealing

Encapsulating or sealing asbestos in place rather than disturbing it by removal is more advantageous in many cases.  Qualified individuals who are trained and certified in asbestos control must make this determination.

## 6743.4 - Reporting

Report all discoveries of suspected asbestos to the appropriate Hazardous Materials Management Coordinator (FSM 6742.04).

# 6744 - TRAINING

Employees handling or supervising the use, storage, or transportation of hazardous materials shall receive appropriate training.  Training resources are available through the National Technical Information Service.

# 6745 – EXPLOSIVES AND BLASTING MATERIALS

Direction in this section applies to Forest Service operations and activities involving explosives and blasting materials to accomplish project works, avalanche control, and fire suppression activities.  Related direction is in FSM 2160 and 7103.5 and in FSH 6709.11.  Forest Service operations and activities related to the use, storage, and transportation of explosives and blasting materials must also comply with requirements in the most recent edition of the Guide for Using, Storing, and Transporting Explosives and Blasting Materials, published by the Missoula Technology and Development Program.

The term "blaster" used in this section applies to Forest Service employees who are currently certified blasters or blasters-in-training.  Requirements governing contractor blaster operations and activities are specifically identified in FSM 6745.3.

### 6745.01 - Authority

### 6745.01a - Use

Requirements and constraints on the use of explosives and blasting materials are in:

1.  Title 29, Code of Federal Regulations:

a.  Section 1910.109, Explosives and Blasting Agents (29 CFR 1910.109).

b.  Part 1926, subpart U, Blasting and the Use of Explosives (29 CFR 1926, 
subpart U).

2.  Title 30, Code of Federal Regulations:

a.  Part 56, subpart E, Explosives (30 CFR 56, subpart E).

b.  Part 57, subpart E, Explosives (30 CFR 57, subpart E).

### 6745.01b - Storage

Requirements for storage of explosives and blasting materials are in Title 27, Code of Federal Regulations, part 55, Storage (27 CFR part 55).

### 6745.01c - Transportation

Requirements for the transportation of explosives and blasting materials are in:

1.  Title 33, Code of Federal Regulations:

a.  Part 125, Identification Credential for Persons Requiring Access to Waterfront Facilities or Vessels (33 CFR 125).

b.  Part 126, Handling of Class 1 (Explosive) Materials or Other Dangerous Cargoes Within or Contiguous to Waterfront Facilities (33 CFR 126).

2.  Title 49, Code of Federal Regulations:

a.  Part 172, Hazardous Materials Table, Special Provisions, Hazardous Materials Communications, Emergency Response Information, and Training Requirements 
(49 CFR 172).

b.  Part 173, Shippers-General Requirements for Shipments and Packaging 
(49 CFR 173).

c.  Part 174, Carriage by Rail (49 CFR 174).

d.  Part 175, Carriage by Aircraft (49 CFR 175).

e.  Part 176, Carriage by Vessel (49 CFR 176).

f.  Part 177, Carriage by Public Highway (49 CFR 177).

g.  Part 390, Federal Motor Carrier Safety Regulations; General (49 CFR 390).

h.  Part 391, Qualifications of Drivers (49 CFR 391).

i.  Part 392, Driving of Commercial Motor Vehicles (49 CFR 392).

j.  Part 393, Parts and Accessories Necessary for Safe Operation (49 CFR 393).

k.  Part 395, Hours of Service of Drivers (49 CFR 395).

l.  Part 396, Inspection, Repair, and Maintenance (49 CFR 396).

m.  Part 397, Transportation of Hazardous Materials; Driving and Parking Rules 
(49 CFR 397).

3.  Department of Transportation (DOT), Research and Special Programs Administration, Exemption Number DOT-E 9198, which authorizes the U.S. Department of the Interior and U.S Department of Agriculture Forest Service to transport hazardous materials in aircraft under their exclusive direction and control (FSM 5714.2).

### 6745.01d - Disposal

1.  Requirements for disposal of explosives and excess blasting materials declared as hazardous waste are in Title 40, Code of Federal Regulations, part 264, Standards for Owners and Operators of Hazardous Waste Treatment, Storage, and Disposal Facilities (40 CFR 264).

2.  Special policies and procedures governing the utilization, donation, sale, exchange, or other disposition of hazardous materials, dangerous property, and other categories of property with special utilization and disposal requirements are in Title 41, Code of Federal Regulations, part 101-42, Utilization and Disposal of Hazardous Materials and Certain Categories of Property (41 CFR 101-42).

### 6745.02 - Objectives

1.  To ensure safe and secure storage, transportation, and use of explosives and blasting materials.

2.  To use explosives and blasting materials in the safest manner possible as cost-effective tools to accomplish project work.

### 6745.03 - Policy

(See FSM 7103.5 for additional policies related to explosives and blasting materials; see FSM 6745.2 for general standards applicable to blasting operations and activities.)  To ensure that employees and the public are protected from injury:

1.  Comply with applicable Federal, State, and local laws and regulations for all work connected with explosives and blasting materials.  Follow the most stringent requirements where a difference appears.

2.  Ensure that all Forest Service blasters take and pass a regional written test, oral examination, and field exercise to attain blaster certification.  The certification shall specify the type of blasting qualifications (FSM 6745.1).

3.  Ensure that all Forest Service blasters involved in the transportation of explosives and avalanche ammunition comply with requirements to hold a State-issued Commercial Driver's License (CDL) with Hazardous Materials Endorsement and a current Medical Examiner's Certificate.

4.  Ensure that all personnel responsible for monitoring or inspecting blasting operations and activities are trained to recognize unsafe or unlawful practices and procedures.

5.  Use only explosives and blasting materials on the approved Forest Service list (FSM 6745.04f).  Ensure that a Material Safety Data Sheet (MSDS) for explosives and blasting materials is available at the workplace or job site, and that a job hazard analysis is conducted in accordance with FSH 6709.11.

6.  Use exploding bridgewire or non-electric detonators as the detonation system of choice in all Forest Service blasting operations and activities, unless contraindicated by a particular blasting application.

7.  Prohibit the use of cap and fuse in general blasting operations and activities for both force account and contract.

8.  Require special training for use of cap and fuse in avalanche control.

9.  Ensure that all force account blasting operations and activities (including transportation, use, mixing of component explosives, storage, magazine inspection, and disposal) are conducted by or under the direct supervision of a certified Forest Service blaster in accordance with FSM 6745.1.

10.  Designate one certified Forest Service blaster as the Blaster-in-Charge when two or more blasters are working together.  Either the respective supervisor or the blasters themselves may designate the Blaster-in-Charge.

11.  Use contractors for blasting operations and activities when it is the most cost-effective and efficient alternative for the Government.  Ensure that blasting contracts comply with the same standards, laws, and regulations that are applicable to Forest Service blasting operations and activities (FSM 6745.3).

### 6745.04 - Responsibility

### 6745.04a – Chief

The Chief is responsible for ensuring agency compliance with explosives and blasting materials policies, procedures, and practices.

### 6745.04b - Deputy Chief for Business Operations

The Deputy Chief for Business Operations, as the Designated Agency Safety and Health Official, has the responsibility to consider recommendations from the National Explosives and Blasting Technical Advisory Group and other officials, and to resolve national issues, concerns, and policies related to explosives and blasting materials that affect the work environment and safety of employees.

### 6745.04c - National Explosives and Blasting Technical Advisory Group

The National Explosives and Blasting Technical Advisory Group, composed of all Regional Blaster Examiners and Blaster Coordinators, the Director of the National Avalanche Center (or designee), and a Technology and Development Center representative, is responsible for:

1.  Developing standardized national training programs on all categories of blasting operations and activities.

2.  Developing certification criteria for blasters (general, avalanche, and fireline).

3.  Establishing accepted practices and procedures for the safe use, handling, storage, and transportation of explosives and blasting materials in compliance with applicable laws and regulations.

4.  Addressing national issues at the annual National Blaster Examiners' and Coordinators' Workshop that affect the Forest Service explosives and blasting materials program.

5.  Providing information on newly developed explosives and blasting materials and associated technology to the Technology and Development Centers and the National Avalanche Center for development of the approved explosives and blasting materials list.

### 6745.04d – National Explosives Safety Program Manager

The National Explosives Safety Program Manager, Safety, Health and Uniforms Branch, Human Resources Management Staff, Washington Office, is responsible for:

1.  Providing overall program leadership and safety oversight for the National Explosives Safety Program.

2.  Ensuring that the list of explosives, blasting materials, and avalanche ammunition for use, including all explosives, blasting equipment, and avalanche ammunition approved by the Technology and Development Centers and the National Avalanche Center is updated and issued on an annual basis when new items are approved for Forest Service use.

3.  Reviewing the most current edition of the Guide for Using, Storing, and Transporting Explosives and Blasting Materials on an annual basis, and updating as appropriate (FSM 6745.06).

4.  Ensuring distribution of the latest revision of the Department of Transportation (DOT), Research and Special Programs Administration, Exemption Number DOT-E 9198, which authorizes the U.S. Department of the Interior and U.S Department of Agriculture Forest Service to transport hazardous materials in aircraft under their exclusive direction and control.

### 6745.04e - Managers of Technology and Development Centers and Director of National Avalanche Center

The Managers of the Technology and Development Centers at Missoula, Montana, and San Dimas, California, and the Director of the National Avalanche Center, Ketchum, Idaho are responsible for:

1.  Serving as technical advisors to the National Explosives Safety Program manager.

2.  Providing technical support to Regional Blaster Examiners and Coordinators on the use, acquisition, transport, and storage of explosives and blasting materials.

3.  Suspending and/or removing from Service-wide use any explosive or blasting material that is considered an immediate threat to the safety and health of employees and the public.

4.  Developing and issuing the approved explosives and blasting materials list with input from the Regional Blaster Examiners and Coordinators.

### 6745.04f - Regional Foresters

Regional Foresters are responsible for:

1.  Authorizing all explosives and blasting materials to be used by properly certified blasters within the Region from the approved explosives and blasting materials developed by the Technology and Development Centers and the National Avalanche Center (FSM 6745.04e).

2.  Appointing a Regional Blaster Coordinator and Regional Blaster Examiner (FSM 6745.04j and 6745.04k).

3.  Providing workshops and training to keep certifications current for blasters.

### 6745.04g - Regional Blaster Coordinators

Regional Blaster Coordinators are responsible for:

1.  Recommending to Regional Foresters those blasting operations and activities that may be accomplished through force account or contract.

2.  Determining Regional training needs and coordinating and monitoring Regional training programs that cover contracting and force account use of explosives and blasting materials.

3.  Coordinating and monitoring all categories of explosives and blasting certification.

4.  Developing and maintaining a tracking system for pertinent information on all respective blasters.  This system should include:  name; location; telephone number; electronic mail address; certification and re-certification date(s); type(s) of blasting certification; skill level; and special blasting skills.

5.  Recommending appointment of Regional Blaster Examiners (FSM 6745.04k).

6.  Coordinating the development of Regional supplements to the Manual and Handbooks related to explosives and blasting materials.

7.  Coordinating with affected staffs to secure sufficient funding levels and support for the administration of the Regional blasting program (FSM 6745.04k).

### 6745.04h - Regional Blaster Examiners

Regional Blaster Examiners are responsible for:

1.  Developing training programs for all categories of explosives and blasting certification (FSM 6745.1) for force account use of explosives and blasting materials.

2.  Providing training for inspection of contracted blasting operations and activities.

3.  Keeping explosives and blasting certification references and training materials up-to-date with Federal laws and regulations for the safe transportation, storage, use, and disposal of explosives and blasting materials.

4.  Conducting or supervising certification classes (written, practical field exercises, and oral examination programs) for blasters.

5.  Being available to assist with all blasting training, as needed.

6.  Recommending for approval by Forest Supervisors/Unit Managers the issuance of Explosives and Blasting Certificates (Form FS-6700-27) to applicants who satisfactorily complete blaster-in-training and blaster certification requirements (FSM 6745.12).

7.  Recommending to Forest Supervisors/Unit Managers revocation or suspension of certificates when such action is justified (FSM 6745.1).

8.  Making periodic monitoring trips and assistance visits to field units.

9.  Assisting in the investigation and documentation of all accidents and infractions of security and safety requirements related to blasting operations and activities.

10.  Ensuring permanent storage facilities and locations for explosives and blasting materials comply with 27 CFR 55 (FSM 6745.01b).

11.  Assisting or advising with large or more difficult blasting projects.

12.  Maintaining explosives and blasting certification (FSM 6745.1).

### 6745.04i - Forest Supervisors and Unit Managers

Forest Supervisors and Unit Managers are responsible for:

1.  Issuing Explosives and Blasting Certificates (Form FS-6700-27) on Regional Blaster Examiners' recommendations to blasters-in-training and blasters.

2.  Designating certified Lead Blasters based on the Regional Blaster Examiners' recommendations.

3.  Suspending or revoking certificates when such action is justified (FSM 6745.11).

4.  Ensuring that all blasting operations and activities, including special uses and projects under contract or agreement, are monitored for compliance with all Federal, State, and local laws and regulations and applicable Forest Service requirements for explosives and blasting materials.

### 6745.04j - Contracting Officers

Contracting Officers are responsible for:

1.  Incorporating contractor requirements listed in FSM 6745.3 into contracts for blasting operations and activities conducted within National Forest System boundaries or other land and properties under the control of the Forest Service.

2.  Ensuring that all blasting contracts are reviewed by a certified blaster or qualified Engineering Representative/Contracting Officer Representative for safety and resource protection issues before they are released for solicitation.

### 6745.04k - Lead Blasters

Lead Blasters are responsible for:

1.  Directing or providing on-the-job training for blasters.

2.  Keeping individual files on each blaster (including themselves), with records containing, at a minimum, the following information:

a.  Copy of application from last certification class attended.

b.  Current list of activities.

c.  Copy of blast record for each shot made.

3.  Maintaining sufficient copies of the most current edition of the Guide for Using, Storing, and Transporting Explosives and Blasting Materials so that they are readily available to blasters in the field (FSM 6745.06).

4.  Reviewing current qualifications of blasters and making recommendations to Regional Blaster Examiners on certification and re-certification of current blasters, and estimating personnel, training, and certification needs for future activities.

5.  Securing and maintaining State and local licenses or certificates required for the purchase, use, storage, and disposal of explosives and blasting materials.

6.  Distributing a list of blasters approved to purchase explosives and blasting materials with their certificates or State license numbers to appropriate distributors and officials.

7.  Annually inspecting explosives and blasting materials storage facilities and records.

8.  Monitoring performance of blasters.

9.  Assisting in or conducting training sessions to qualify blasters.

10.  Reviewing plans for or conducting major force account blasting projects.

11.  Destroying or supervising the destruction of all explosives and excess blasting materials designated as hazardous waste (if properly certified).

12.  Assisting in the investigation of blasting accidents and incidents or infractions of safety and security requirements.

13.  Maintaining explosives and blasting certification (FSM 6745.1).

### 6745.04l - Blasters - General/Fireline/Avalanche

Blasters - General/Fireline/Avalanche are responsible for:

1.  Completing appropriate blast plans in accordance with the most current edition of the Guide for Using, Storing, and Transporting Explosives and Blasting Materials (FSM 6745.06).

2.  Complying with general standards listed in FSM 6745.2 when conducting blasting operations and activities.

3.  Meeting certification requirements in accordance with FSM 6745.1.

### 6745.05 - Definitions

Avalanche Ammunition.  All ammunition and propellant that is designated by the military for use in 75-mm, 105-mm, and 106-mm recoilless rifles; 75-mm pack howitzers; and 105-mm howitzers; or commercially available device made specifically for avalanche control (such as the avalauncher) that is officially recognized by the National Avalanche Center as acceptable and safe for avalanche control.

Explosives and Blasting Materials.  All ammunition, munitions fillers, demolition material, solid rocket motors, liquid propellants, cartridges, pyrotechnics, and bombs, including associated explosives and blasting equipment and avalanche ammunition.

General Blasting.  All explosives and blasting operations and activities exclusive of fireline, avalanche, and specialty blasting.

Level 1 Blaster-in-Training.  The entry level for general blasters and blasters designated to use fireline explosives for wildfire suppression and prescribed burns.

### 6745.06 - Reference

Guide for Using, Storing, and Transporting Explosives and Blasting Materials, Missoula Technology and Development Program, Technical Service-Explosives (current edition).  Copies of this guide are available from Lead Blasters in field units and from the Missoula Technology and Development Center.

## 6745.1 - Certification

The basis for certification is eligibility, knowledge, experience, and testing.  Use Form 
FS-6700-24, Application for Explosives and Blasting Certification, Part I, Part II, and Part III, respectively, to apply for an explosives and blasting certificate.  Minimum certification requirements are:

1.  Demonstrating knowledge of and compliance with safety and security requirements.

2.  Exercising reasonable and prudent judgment in all situations.

3.  Possessing knowledge of current Federal, State, and local laws and regulations applicable to blasting operations and activities (FSM 6745.2).

4.  Maintaining certification as specified for the levels indicated in exhibit 01.

6745.1 - Exhibit 01

| Explosives and Blasting Certification Requirements |
| --- |
|  | CERTIFICATION LEVELS |
| REQUIREMENTS To certify or recertify, possess the following certificates and licenses, and meet the indicated requirements for each certification level | 1,2Blaster-in -Training Level 1 | 2General Blaster Level 2 | 2General Blaster Level 3 | 2Lead Blaster | 2Blaster Examiner | 2Avalanche | 2Fireline (Prescribed) | 2Fireline (Wildfire) |
| Prerequisites |  |  |  |  |  |  |  |  |
| Hazard Communication Standard (Employee Right-to-Know) | **** | **** | **** | **** | **** | **** | **** | **** |
| First Aid | **** | **** | **** | **** | **** | **** | **** | **** |
| Hazardous Materials Course (49 CFR 172)3 | **** | **** | **** | **** | **** | **** | **** | **** |
| Endorsements and Licensing |  |  |  |  |  |  |  |  |
| Commercial Driver's License (CDL) | **** | **** | **** | **** | **** | **** | **** | **** |
| Hazardous Materials Endorsement | **** | **** | **** | **** | **** | **** | **** | **** |
| Medical Examiner's Certificate | **** | **** | **** | **** | **** | **** | **** | **** |
| General Requirements |  |  |  |  |  |  |  |  |
| Every 3 years attend a 16-hour minimum classroom training on using, storing, and transporting explosives and blasting materials Pass 8-hour field practical exercise/test Pass written examination Pass oral examination | **** | **** | **** |  |  | **** |  |  |
| Complete 1-year minimum field work with a minimum of 3 shots and have the recommendation of lead blaster |  | **** | **** |  |  |  |  |  |
| Present shot records since last certification | **** | **** | **** | **** | **** | **** | **** | **** |
| Shoot a minimum of 3 shots per year | **** | **** | **** | **** | **** | **** | **** | **** |
| Attend a yearly lead blaster's workshop |  |  |  | **** |  |  |  |  |
| Participate in Blaster's Workshops (Certification) |  |  |  | **** |  |  |  |  |
| Additional Avalanche and FLE Requirements |  |  |  |  |  |  |  |  |
| Every 3 years attend a 4-hour minimum classroom training on using cap and fuse, and avalanche blasting materials Pass 4-hour field practical exercise/test |  |  |  |  |  | **** |  |  |
| Pass avalanche school |  |  |  |  |  | **** |  |  |
| Pass military weapons training |  |  |  |  |  | **** |  |  |
| Pass yearly military weapons 8-hour refresher |  |  |  |  |  | **** |  |  |
| Pass national fireline explosives training |  |  |  |  |  |  | **** | **** |
| Pass yearly fireline explosives refresher |  |  |  |  |  |  | **** | **** |

6745.1 - Exhibit 01--Continued

| Explosives and Blasting Certification Requirements |
| --- |
|  | CERTIFICATION LEVELS |
| REQUIREMENTS To certify or recertify, possess the following certificates and licenses, and meet the indicated requirements for each certification level | 1,2Blaster-in -Training Level 1 | 2General Blaster Level 2 | 2General Blaster Level 3 | 2Lead Blaster | 2Blaster Examiner | 2Avalanche | 2Fireline (Prescribed) | 2Fireline (Wildfire) |
| Specialty and Other Blasting Authorizations4 |  |  |  |  |  |  |  |  |
| Stumps |  | **** |  |  |  |  |  |  |
| Ditches |  | **** |  |  |  |  |  |  |
| Misfires |  | **** |  |  |  |  |  |  |
| Delays |  | **** |  |  |  |  |  |  |
| 40+ Hole Shots |  |  | **** |  |  |  |  |  |
| Quarries |  |  | **** |  |  |  |  |  |
| Wildlife Ponds/Beaver Dams |  |  | **** |  |  |  |  |  |
| Hazard Tree Blasting |  | **** | **** |  |  |  | **** | **** |
| Seismic |  |  | **** |  |  |  |  |  |
| Other (Specify) |  | **** | **** |  |  |  |  |  |
| **** INDICATES REQUIREMENTS FOR EACH CERTIFICATION LEVEL 1Level 1-Blaster-in-Training requirements apply to general, fireline (FLE), and avalanche certifications 2CDL only required when transporting explosives 3Hazardous materials may be taught as part of the blaster’s training course 4Work with and be recommended by master performer/lead blaster |

### 6745.11 - Steps in Certification Process

1.  Certified Blaster-in-Training Requirements.  To become a certified blaster-in-training, an applicant must:

a.  Possess a current multi-media first aid card.

b.  Attend current hazardous materials general awareness training.

c.  Attend 16-hours classroom training session at a minimum and pass an examination demonstrating applicant proficiency in the blasting level for which the applicant applies.

2.  Certified Blaster Requirements.  To become a certified blaster, a certified blaster-in-training must:

a.  Work under the direct supervision of a certified blaster for a minimum of one year to develop the necessary knowledge, skills, and experience required to perform safely and effectively.

b.  Attend and successfully complete a blaster's training course.

c.  Provide current shot records indicating proficiency at the level applied for (exhibit 01).

d.  Have a commercial driver's license (CDL) with hazardous materials endorsement and a current medical examiner's card (ICC) when transporting explosives and avalanche ammunition.

3.  Maintaining Certification.  To maintain certification, a blaster must:

a.  Conduct a minimum of three shots per year.

b.  Maintain shot records of each shot.

c.  Attend a recertification class every three years and pass an examination demonstrating blaster proficiency at the level of blasting currently certified.

d.  Maintain the required licenses, certifications, and training required by Federal, State, and local governing agencies.

### 6745.12 - Certificate

As evidence of certification, issue Form FS-6700-27, Explosives and Blasting Certificate 
(ex. 01) to applicants.  Exhibit 01 displays an electronic facsimile of Form FS-6700-27, which is available only in a paper copy format.  Certificates are valid for three years from the date of issue, unless temporarily suspended or revoked by the issuing Forest Supervisor/unit manager at any time during that period.  Certificate renewal or reissue is the same as for original certificates.  Reasons for temporary suspension or revocation include, but are not limited to, the following:

1.  Conviction for violating any law or regulation relating to explosives and blasting materials.

2.  Lax security or unsafe procedures and practices relating to explosives and blasting materials.

3.  Lack of proficiency, as demonstrated by the following:

a.  Involvement in an accident or incident related to explosives and/or blasting materials.  The blaster may be reinstated only after an investigation warrants such action.

b.  Unsatisfactory performance or less than three shots per year.

6745.12 - Exhibit 01

FS-6700-27 (7/99)

| EXPLOSIVES AND BLASTING CERTIFICATE |
| --- |
| Agency: USDA Forest Service Issue Date: 6/7/96 |
| Name: Gerry P. Everyone |
| SSN: 555-55-5555 Birth Date: 6/28/44 |
| State License # AR 5679 |
| Height: 5'4" Weight: 160 |  |
| Level/Class: 2 |  |
|  | PHOTO |
| Issued by S.T. Truly . |  |
| Blaster Examiner/Officer |  |
| Approved by W.E. Marshall . |  |
| Supervisor |

| WORK AUTHORIZATION LEVELS |
| --- |
| GENERAL |  | INTLS |  |
| LEVEL 1 - GENERAL/FIRELINE BLASTER-IN-TRAINING |  |  |  |
| Store/Inspect/Transport |  |  |  |
| LEVEL 2 - GENERAL/FIRELINE-PRESCRIBED |  |  |  |
| Store/Transport/Inspect |  | STT |  |
| Rocks/Stumps/Ditches |  | STT |  |
| 10 Holes/Clear Misfires |  | STT |  |
| Fireline-Prescribed |  |  |  |
| Other___________________________________________ |  |  |  |
| LEVEL 3 - GENERAL/DEMOLITION |  |  |  |
| Store/Transport/Inspect |  |  |  |
| Quarries/40+ Holes |  |  |  |
| Wildlife Ponds/Beaver Dams |  |  |  |
| Other___________________________________________ |  |  |  |
| FIRELINE-WILDFIRE |  |  |  |
| Store/Transport/Inspect |  |  |  |
| FLEI (Initial Attack) |  |  |  |
| FLEB (Blaster-in-Charge) |  |  |  |
| FLEA (Advisor) |  |  |  |
| FLEC (Crewmember) |  |  |  |
| AVALANCHE/GUNNER OPERATIONS |  |  |  |
| Store/Transport/Inspect |  |  |  |
| Blaster-in-Training |  |  |  |
| Avalanche Gunner |  |  |  |
| Avalanche Hand Charges |  |  |  |
| Other___________________________________________ |  |  |  |
| SPECIALTY BLASTING |  |  |  |
| Tree Topping |  |  |  |
| Hazard Trees |  |  |  |
| Other___________________________________________ |  |  |  |

## 6745.2 - General Standards

Conduct all blasting operations and activities in accordance with the policies in FSM 6745.03 and 7103.5, and the requirements in the following:

1.  Warnings and instructions adopted by the Institute of Makers of Explosives (IME), which are contained in every box of explosives and blasting caps.

2.  Federal, State, and local laws and regulations (see FSM 6745.01 - 6745.01d for applicable Federal regulations and FSM 6745.01c, para. 3 for the Department of Transportation exemption).

3.  Current edition of the Forest Service Guide for Using, Storing and Transporting Explosives and Blasting Materials (FSM 6745.06).

## 6745.3 - Contractor Requirements

Contracting officers shall ensure that the following requirements are included in contracts for blasting operations and activities conducted within National Forest System lands or on other lands and properties administered by the Forest Service (FSM 6745.04m):

1.  Contractors are to prepare blast plans in accordance with the most current edition of the Guide for Using, Storing, and Transporting Explosives and Blasting Materials (FSM 6745.06) before commencing any contracted blasting operations and activities within National Forest System boundaries or on other lands and properties administered by the Forest Service.  Such blast plans shall include, but are not limited to:

a.  Precautions necessary to maximize safety and protect the contractor's employees, Forest Service employees, and the general public during blasting operations and activities.

b.  Methods proposed to prevent damage to resources outside the immediate blast area by minimizing earth vibrations, air blast, and thrown fragments.

2.  The contractor is to provide the contracting officer copies of magazine records and shot logs to account for all explosives items and components and blasting materials brought onto, used, and removed from the contract area.

3.  The contractor must conduct all blasting operations and activities in accordance with warnings and instructions adopted by the Institute of Makers of Explosives (IME) contained in every box of explosives and blasting caps, and in compliance with applicable Federal, State, and local laws and regulations.