WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11272 | In-Flight Anomaly Number -- | Contractor Report Number E-112 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title ULLAGE PRESSURE TRANSDUCER FAILED THE SIGNAL DROPOUTS CRITERIA DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1R | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ULL. PRESSURE TRN | PART# PD7400098-089 | SER/LOT# 2164 | MANUFACTURER GULTON-SERV |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 ULL PRESSURE TRN | PART# PD7400098-089 | SER/LOT# 2164 | MANUFACTURER GULTON-SERV |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EG - SIG HI OR LO | Cause U - UNKNOWN |
| System ELECTRICAL | Defect -- | Material C - EEE | Work Contact J. ADAMS | Fail Date 02/25/1988 |
| Received at MSFC 03/03/1988 | Date Isolated -- | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EE - RANDOM | Time Cycle N/A |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUB |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/09/1995 | CN RSLV SBMT 05/16/1988 | Defer Date -- | Add Date 03/07/1988 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR G. BRIDWELL |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR G. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 06/03/1988 | Status E - CLOSED-E | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A PRESSURE TRANSDUCER FAILED DURING ATP. THE TRANSDUCER HAD A LOSS OF SIGNAL (DROPOUT) AT APPROXIMATLEY 19 PSIA, ON BOTH PRESSURE RISE AND FALL, DURING THE HIGH ACCURACY TEST. NO SIGNAL DROPOUTS ARE ALLOWED. REF. MARS T-34371 PREVIOUS CAPS: E-082, E-091, E-101, E-106, E-110, E-111 |
| Contractor Investigation/Resolution R/C: TBD CAUSE - THE ROOT CAUSE COULD NOT BE DETERMINED. A POSSIBLE CAUSE BASED ON PREVIOUS EXPERIENCE, IS FOREIGN PARTICLE CONTAMINATION OF THE INTERNAL POTENTIOMETER GENERAL - THE TRANSDUCER FAILED THE SIGNAL DROPOUT CRITERIA DURING VENDOR ACCEPTANCE TESTING (ATP). OCCASIONAL ATP FAILURES OF THIS TYPE ARE EXPECTED AS PART OF NORMAL PRODUCTION FALLOUT. INVESTIGATION OF PREVIOUS SIMILAR FAILURES HAS FOUND THAT MICROSCOPIC PARTICULATE CONTAMINATION OF THE INTERNAL RESISTIVE ELEMENT AND WIPER IS THE MOST PROBABLE CAUSE. REFERENCE: CAPS E-082 THE FAILURE WAS DETECTED DURING VENDOR ACCEPTANCE TEST WHICH IS DESIGNED TO SCREEN DEFECTIVE HARDWARE 5/3/88 - THIS REPORT HAS BEEN DEFERRED FOR STS-26, PER NSTS 07700, VOLUME XI AND NSTS 08126 PARAGRAPH 3.4.1, ITEM C WHICH STATES "PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE AND IS CLEARLY SCREENED BY ACCEPTANCE TEST, PREFLIGHT CHECKOUT, OR SPECIAL TEST." THE DEFERRAL STATUS HAS BEEN APPROVED BY THE ET PROJECT MANAGER, MR. G.P. BRIDWELL __ G.P. BRIDWELL (SIGNED) 5/13/88__ 5/13/88 TASK I. FAILURE INVESTIGATION A FAILURE ANALYSIS OF THE TRANSDUCER WAS PERFORMED AT MAF. THE VENDOR ACCEPTANCE TESTS HAD EXPERIENCED ONLY THE SINGLE DROPOUT, ON PRESSURE RISE, DURING THE HIGH ACCURACY CALIBRATION TEST. THE DROPOUT AFFECTED A VERY NARROW PRESSURE RANGE EQUIVALENT TO ONE OR TWO TURNS OF THE TRANSDUCER'S INTERNAL WIREWOUND POTENTIOMETER. THE DROPOUT HAD NOT RECURRED ON PRESSURE FALL. THE TRANSDUCER OPERATING MECHANISM WAS REMOVED FROM ITS CASE AND EXAMINED USING OPTICAL MICROSCOPE AT 70 DIAMETERS MAGNIFICATION. THE MECHANISM WAS FREE OF ANY FORM OF VISIBLE CONTAMINATION. THE POTENTIOMETER WIPER TENSION MET THE MANUFACTURERS SPECIFICATIONS. SCANNING ELECTRON MICROSCOPE EXAMINATION OF THE WIPER AND THE RESISTIVE ELEMENT COULD FIND NO CONTAMINATION OR OTHER CONDITIONS WHICH COULD HAVE CAUSED THE FAILURE TASK CLOSED TASK II. CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING TASK CLOSED TASK IV. CAPS CLOSURE SUMMARY THE TRANSDUCER FAILED DURING VENDOR ACCEPTANCE TEST. THE FAILURE WAS OF A TYPE CONSIDERED NORMAL PRODUCTION FALLOUT. NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED THIS PROBLEM CLOSURE IS SUBMITTED FOR MSFC REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11272 | IFA# -- | Contractor RPT# E-112 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-089 | Asmnt Part Name LH2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 2164 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD UU - UNK-UND | FAIL MODE EG - SIG HI OR LO |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |