MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10060 | In-Flight Anomaly Number -- | Contractor Report Number P-054 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title GH2 GROUND STRAPS PLATING PEELING - LWT'S 16, 20, 21, 22, AND 24 THRU 33/ASSY-INSP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (4) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ET | PART# 80901000000 | SER/LOT# NOTED | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE PRESS LINE | PART# 80911001319 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE GROUND STRAPS | PART# 80921021036 | SER/LOT# N/A | MANUFACTURER UNK |
| Test/Operation L - FLD | Prevailing Condtion N - INSPECTION | F / U F | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System PROPULSION | Defect DD - DETACH | Material L - FASTNR | Work Contact C. CAMPBELL | Fail Date 01/03/1986 |
| Received at MSFC 05/28/1986 | Date Isolated -- | FMEA Reference N/A | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 05/31/1988 | CN RSLV SBMT 11/25/1986 | Defer Date -- | Add Date -- | R/C Codes A - PURG -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer -- | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer -- | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee L. CUNNINGHM | PAC Review Complete LC | MSFC Closure Date 01/08/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description MARS T-82758 IDENTIFIED SIX GROUND STRAPS WITH PLATING PEELING. THESE WERE EXAMINED AND FOUND TO HAVE FINGERPRINTS ON THE COPPER SUBSTRATE AND NICKEL PLATE FAYING SURFACES. THIS EVIDENCE IS INDICATIVE OF INCOMPLETE CLEANING OF THE COPPER SUBSTRATE PRIOR TO PLATING. SUCH CONTAMINATION CAUSES INSUFFICIENT BONDING OF PLATING TO SUBSTRATE CONSULTATION WITH PRODUCTION PERSONNEL REVEALED THAT DELAMINATION OF THE PLATING IS NORMALLY FOUND WHEN THE STRAPS ARE SLIGHTLY FLEXED TO ACCOMPLISH INSTALLATION ON THE PRESSLINE FLANGES. PEELING NICKEL PLATING IS CONSIDERED SIGNIFICANT IN TERMS OF DEBRIS GENERATION DURING FLIGHT NICKEL PLATE DEBRIS 0.75 X 1.5 INCHES WITH RAZOR SHARP EDGES HAS BEEN OBSERVED. LWT'S AFFECTED ARE 16, 20, 21, 22 AND 24 THROUGH 33 |
| Contractor Investigation/Resolution R/A - ALL GROUND STRAPS ARE TO BE REMOVED FROM ALL ET'S AND REPLACED WITH AN UPDATED CONFIGURATION. 6/19/86 PRB STATUS - PROBLEM CAUSED BY INADEQUATE CLEANING PRIOR TO PLATING. A DC&R HAS BEEN GENERATED TO INSPECT COMPLETED AND DELIVERED TANKS. DESIGN REVIEW IS LOOKING AT EITHER MODIFYING OR DELETING GROUND STRAPS. ECD IS 11-7-86 AT MMC 7/15/86 PRB STATUS - PARTS IN STOCK HAVE BEEN FOUND TO HAVE RANDOM FAILURES. WILL REQUIRE 60 DAYS TO RECEIVE GOOD PARTS. VENDORS ARE USING SAME PLATING COMPANY. INCONSISTENCY BETWEEN GH2 AND GO2 INSTALLATION REDESIGN CONSIDERATIONS INCLUDE DELETING THE PLATING FROM GROUND STRAPS OR DELETING GROUND STRAPS COMPLETELY. 7/31/86 - RECEIVED REVISION "A", DATED 7-23-86. ADDITIONAL INVESTIGATIONS BY PROCUREMENT QUALITY REVEALED THAT ALL PARTS WERE PLATED BY THE SAME VENDOR. ALL PARTS AT MAF WERE DOCUMENTED AS DISCREPANT BY MARS ACTION. SUBSEQUENT DESTRUCTIVE TESTS REVEALED FAILURES ON PARTS PREVIOUSLY INSPECTED BY THE STOCK CHECK. NO NONDESTRUCTIVE TESTS EXIST TO DETECT DEFECTIVE HARDWARE. THEREFORE, ALL EXISTING STRAPS ARE CONSIDERED DEFECTIVE. MARS T-91701 AND T-95591 REJECTED ALL STOCK AT MAF. THEREFORE, LWT'S 37 AND UP WILL BE EQUIPPED WITH REPAIRED OR REWORKED STRAPS. THE EFFECTIVITY HAS BEEN CHANGED TO INCLUDE LWT'S 34 THROUGH 36. EFFECTIVITY IS NOW LWT'S 16, 20, 21, 22, AND 24 THROUGH 36. 8/21/86 PRB STATUS - LACK OF VENDOR CONTROL. REP SENT TO VENDOR. MOD ON STRAPS ON VEHICLE IN FIELD 9/18/86 PRB STATUS - FLEET TO BE RETROFITTED WITH GOOD STRAPS. B01771 HAS BEEN REVISED TO CHANGE STRAP MATERIAL TO 2169 STAINLESS. 10/16/86 PRB STATUS - THE 2169 STAINLESS STEEL HAS BEEN APPROVED BY MSFC AND IMPLEMENTATION IS AWAITING LEVEL II APPROVAL. MR. J. NICHOLS/EE31 ASKED THAT MMC ENGINEERING SEND HIM THE ELECTRICAL CONDUCTIVITY NUMBERS FOR THE CURRENT STRAP MATERIAL AND THE 2169 STAINLESS. ECD AT MMC IS 11-24-86.12/3/86 - CHANGE SUMMARY B01771-002 HAS BEEN ISSUED TO REPLACE ALL BOND JUMPERS WITH STAINLESS STEEL. ALL PLATED GROUND STRAPS ARE TO BE REMOVED FROM ALL ET'S AND REPLACED WITH THE UPDATED CONFIGURATION THIS PROBLEM IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10060 | IFA# -- | Contractor RPT# P-054 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80921021036 | Asmnt Part Name GROUND STRAPS | Asmnt Serial/Lot# N/A |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |