July 22, 1994

Contract #TW0592

SPECIAL STANDARD SPECIFICATION

SECTION 06100-S

ROUGH CARPENTRY

Page

PART 1 - GENERAL

1.01	Description Of Work	2

1.02	Submittals	2

1.03	Quality Assurance	2

1.04	Delivery And Storage	3

PART 2 - PRODUCTS

2.01	Lumber Standards	3

2.02	Miscellaneous Lumber	4

2.03	Construction Panels	4

2.04	Miscellaneous Materials	5

PART 3 - EXECUTION

3.01	Installation, General	5

3.02	Wood Grounds, Nailers, Blocking, And Sleepers	5

3.03	Wood Furring	6

3.04	Wood Framing	6

3.05	Floor Joist Framing	6

3.06	Rafter And Ceiling Joist Framing	7

3.07	Stair Framing	7

3.08	Installation Of Construction Panels	87

3.09	Cleaning	8

SPECIAL STANDARD SPECIFICATION

SECTION 06100-S

ROUGH CARPENTRY

PART 1 - GENERAL

1.01	DESCRIPTION OF WORK

A.	The extent and locations of rough carpentry are indicated on the drawings.  Furnish and install, complete, all rough carpentry work as shown on the drawings and specified herein, including all necessary connectors, hangers, and anchors.

B.	Included in this specification are the following:

1.	Wood framing.

2.	Posts and beams.

3.	Fascias.

4.	Soffits.

5.	Wood grounds, nailers and blocking.

6.	Wood furring.

7.	Sheathing.

8.	Subflooring.

9.	Underlayment.

1.02	SUBMITTALS

A.	Product Data:  Submit manufacturer's catalog data, specifications, and installation instructions for underlayment, sheathing, and subflooring.

B.	Material Certificates:  Where dimensional lumber is provided to comply with minimum allowable unit stresses, submit listing of species and grade selected for each use, and submit evidence of compliance with specified requirements. Compliance may be in form of a signed copy of applicable portion of lumber producer's grading rules showing design values for selected species and grade.  Design values shall be as approved by the Board of Review of American Lumber Standards Committee (ALSC).

1.03	QUALITY ASSURANCE

A.	Each construction and/or industrial wood or wood product panel shall be identified with the appropriate trademark of the American Plywood Association (APA), and shall meet the requirements of the latest edition of U.S. Product Standard PS 1 or APA PRP-108 Performance Standards.  All panels which have any edge or surface permanently exposed to the weather shall be classed Exterior Grade.  Panel thickness, grade, and group number or span rating shall be at least equal to that shown on the drawings.  Application shall be in accordance with recommendations of the APA.

B.	Manufactured lumber is to comply with "Product Standard PS 20-70" developed by the National Bureau of Standards and with applicable grading rules of inspection agencies certified by the ALSC Board of Review.  Lumber design values are to comply with ASTM D 2555, "Standard Methods for Establishing Clear Wood Strength Values", and ASTM D 245, "Standard Methods for Establishing Structural Grades and Related Allowable Properties for Visually Graded Lumber".

C.	Grade Marks:  Lumber shall bear the grade and trademark of an inspection agency certified by Board of Review of the ALSC evidencing compliance with grading rule requirements and identifying grading agency, grade, species, moisture content and a mark of mill identification.

1.04	DELIVERY AND STORAGE

A.	Deliver all wood products bundled or crated to provide adequate protection during transit and job storage with required grade marks clearly identifiable.  Inspect all wood products for damage upon delivery.  Remove and replace any damaged materials.

B.	Store materials on a level surface (min. 6 inches above grade), well ventilated, protected from sunlight, under cover and keep dry.  Protect against exposure to weather and damp or wet surfaces.  Stack lumber, plywood, and other panels, according to manufacturer's instruction.  Provide for air circulation within and around stacks and under temporary coverings, including polyethylene and similar materials, but avoid creating a humidity chamber.

PART 2 - PRODUCTS

2.01	LUMBER STANDARDS

A.	Nominal sizes are indicated, except as shown by detail dimensions.  Provide actual sizes as required by PS 20-70, for moisture content specified for each use.

1.	Provide dressed lumber, S4S (surfaced four sides), unless otherwise indicated.

2.	Dimension Lumber:

a.	For light framing (2 to 4 inches thick, 2 to 4 inches wide), provide standard grade or better.  Any species of specified grade under WWPA rules.

b.	For structural light framing (2 to 4 inches thick, 2 to 4 inches wide), provide select structural grade or No. 1 grade of any species of specified grade.

c.	For structural framing (2 to 4 inches thick, 5 inches and wider, posts and beams), provide select structural grade or No. 1 grade of any species of specified grade.

3.	Species and grades must meet or exceed the following values, unless indicated otherwise on drawings.

a.	Fb (minimum extreme fiber stress in bending), 1250 psi.

b.	E (minimum modules of elasticity), 1,000,000 psi.

B.	Exposed Framing Lumber:  Exposed framing refers to dimension lumber which is not concealed by other work and is indicated to receive a stained, painted, or natural finish.

Grading:  Hand select material of species and grade indicated for structural framing for compliance with "Appearance" grade requirements of ALSC National Grading Rule.

2.02	MISCELLANEOUS LUMBER

Provide wood for support or attachment of other work including bucks, nailers, blocking, furring, grounds, stripping and similar members.  Provide lumber of sizes indicated, worked into shapes shown, and meeting the following requirements:

Grade:  Standard grade light framing size lumber of any species or board size lumber as required, No. 3 Common or Standard grade boards per WWPA rules.

2.03	CONSTRUCTION PANELS

A.	Construction Panel Standards:  Panel thickness, grade, veneer qualities, and group number or span rating shall be shown on the drawings and in accordance with recommendations of the APA.  Comply with PS 1 "U.S. Product Standard for Construction and Industrial Plywood" for plywood panels and, for products not manufactured under PS 1 provisions, with APA Performance Standard PRP-108.

B.	Trademark:  Factory-mark each construction panel with APA trademark evidencing compliance with grade requirements.

C.	Where construction panels will be used for the following concealed types of applications, provide APA Performance Rated Panels complying with requirements indicated for grade designation, span rating, exposure durability classification, edge detail (where applicable), and thickness.  Provide panel clips for edge support as recommended by panel manufacturer or where required by the latest edition of the UBC.

Roof and Wall Sheathing:  Provide APA rated sheathing with Exposure Durability Classification of "Exposure 1", except where sheathing is permanently exposed to the weather on any side, it shall be Exposure Durability Classification "Exterior".  Span Rating shall be as required by manufacturer to suit rafter or stud spacing indicated.  Thickness shall be as shown on drawings.

D.	Where construction panels are to be used for soffits and fascias, provide APA A-C grade plywood, thickness as indicated on the drawings, Exposure Durability Classification "Exterior".

E.	Particleboards and Waferboards:

1.	Manufacture and factory-mark each particleboard panel to comply with ANSI A208.1 "Mat-Formed Manufactured Panels" for grade indicated.

2.	Underlayment:  Provide particleboard grade 1-M-1 in thickness indicated.  All underlayment must conform to the performance standards of APA-Sturd-I-Floor, or approved equal.

3.	Subflooring:  Provide waferboard grade 2-M-W in thickness indicated.  All subflooring must conform to performance standards of APA Sturd-I-Floor, or approved equal.

4.	Sheathing:  Provide waferboard grade 2-M-W in thickness indicated on drawings and as recommended by manufacturer.

5.	Provide tongue and grooved edges or panel clips on all edges as recommended by manufacturer and where required by the latest edition of UBC.

2.04	MISCELLANEOUS MATERIALS

A.	General:  All structural wood to wood, wood to steel, and wood to concrete connections shall be accomplished with industry standard metal connectors and hangers, unless indicated otherwise.

B.	Fasteners and Anchorages:  Provide size, type, material and finish as indicated and per applicable standards, complying with Federal Specifications and UBC for nails, staples, screws, bolts, nuts, washers, and anchoring devices.

C.	Where rough carpentry work is exposed to weather, in ground contact, or in areas of high relative humidity, provide fasteners and anchorages with a hot-dip zinc coating (ASTM A153).

PART 3 - EXECUTION

3.01	INSTALLATION

Set carpentry work to required levels and lines, with members plumb and true to line and cut and fitted.  Securely attach carpentry work to substrate by anchoring and fastening per latest edition of UBC and as shown on drawings.  Countersink nail heads on exposed carpentry work and fill holes.

3.02	WOOD GROUNDS, NAILERS, BLOCKING, AND SLEEPERS

A.	Install wood grounds, nailers, blocking, and sleepers wherever shown and, if not shown, where required for screeding or attachment of other work.  Form to shapes as shown, and cut as required for true line and level of work to be attached.  Coordinate location with other work involved.

B.	Attach to surfaces as required to support applied loading.

3.03	WOOD FURRING

Install all wood furring plumb and level, with closure strips at edges and openings.  Shim with wood as required for tolerance of finished work.  Firestop furred spaces on walls sat each floor level, at ceiling line of top story, and as required by applicable codes, with wood blocking or noncombustible materials, accurately fitted to close furred spaces.

3.04	WOOD FRAMING

A.	Install framing members as shown.

B.	Anchor and nail as shown, and to comply with latest edition of UBC and "National Design Specifications for Wood Construction" published by NFPA.  Install anchors where detailed, at ends of each plate, and elsewhere as required to secure carpentry, casework, or millwork to masonry concrete or steel.

C.	Firestop concealed spaces of wood framed walls and partitions at each floor level, at the ceiling line of the top story, and as required by applicable codes.  Where firestops are not automatically provided by the framing system used, use closely fitted wood blocks of nominal 2 inches thick lumber of the same width as framing members.

D.	Install stud framing of size and spacing indicated.  Arrange studs so that wide face of stud is perpendicular to direction of wall or partition and narrow face is parallel.  Provide single bottom plate and double top plates using 2 inches thick members with widths equaling that of studs.  Nail and/or anchor plates to supporting construction.

E.	Frame openings with multiple studs and headers.  Provide header members of thickness equal to width of studs and of depth indicated on the drawings.  Set headers on edge and support on jamb studs.

F.	Install diagonal bracing in stud framing of exterior walls, at corners.  Brace both walls at each external corner, full story height, at a 45 degree angle, using a let-in 1 x 4 or metal diagonal bracing.  Contractor may omit bracing where wood sheathing (4 foot wide panels vertically) are indicated.

3.05	FLOOR JOIST FRAMING

A.	General:  Install framing of sizes and spacings shown.  Install with crown edge up and support ends of each member with not less than 1-1/2 inches of bearing on wood or metal, or 3 inches on masonry.  Attach to wood bearing members by metal connectors; frame to wood supporting members with wood ledgers as shown, or if not shown, with metal connectors.  Fire-cut members built into masonry (if any).  Frame openings with headers and trimmers supported by metal joist hangers; double headers and trimmers where span of header exceeds 4feet, or where indicated on drawings.  Do not notch in middle third of joist span; limit notches to 1/6 depth of joist.  Do not bore holes larger than 1/4 depth of joist or locate closer than 2 inches from top or bottom.  Provide solid blocking (2 inches thick by depth of joist) at ends of joists unless nailed to header or bearing member.

B.	Lap members framing from opposite sides of beams, girders, or partitions not less than 4 inches or securely tie opposing members together.  Provide solid blocking (2 inches thick by depth of joist) over supports.

C.	Under jamb studs at openings, provide solid blocking between joists.

D.	Under non-load-bearing partitions, provide double joists separated by solid blocking equal to depth of studs above.

Provide triple-joists, similar to above, under partitions receiving ceramic tile and similar heavy finishes of fixtures, unless otherwise indicated.

E.	Provide bridging between joists at 8'-0" O.C. maximum.  Use solid wood bridging 2 inches thick by depth of joist with ends nailed to joist, or use metal X bridging.

3.06	RAFTER AND CEILING JOIST FRAMING

A.	Ceiling Joists:  Install member size and spacing shown, and as previously specified for floor joist framing.

B.	Rafters:  Install member size and spacing shown.  Notch to fit exterior wall plates and toe nail or use metal framing anchors.  Install double rafters to form headers and trimmers at openings in roof framing (if any), and support with metal hangers.  Where rafters abut at ridge, place directly opposite each other and nail to ridge member or use metal ridge hangers.

C.	Install collar beams (ties) as shown, or if not shown, provide 1" x 6" boards between every third pair of rafters.  Locate below ridge member, one-third of distance to ceiling joists.  Cut ends to fit slope and nail to rafters.

D.	Install special framing as shown for eaves, overhangs, and similar conditions, if any.

3.07	STAIR FRAMING

Install stair framing members of size, space, and configuration indicated or, if not otherwise indicated, to comply with the following requirements:

A.	Stringer size:  2" x 12" minimum.

B.	Notching:  Notch stringers to receive treads, risers and supports; leave at least 3 1/2 inches of effective depth.

C.	Stringer Spacing:  Not less than 3 stringers for each 3'-0" clear width of stair.

3.08	INSTALLATION OF CONSTRUCTION PANELS

A.	General:  Comply with applicable recommendations contained in Form No. E 30K, "APA Design/Construction Guide" for types of construction panels and applications indicated.  Allow 1/8 inch spacing at panel ends and edges, provide clips as required by latest edition of UBC or as recommended by panel manufacturer.

B.	Fastening Methods:  Fasten panels as indicated below and per latest edition of UBC.

1.	Combination of Subflooring-Underlayment:  Glue and nail to framing.

2.	Subflooring:  Glue and nail to framing.

3.	Sheathing:  Glue and nail to framing.

4.	Underlayment:  Nail or staple to subflooring.  Fill and sand edge joints of underlayment receiving resilient flooring.

3.09	CLEANING

At the end of each work day and the end of the subcontractor's work, clean all work areas of trash.  Neatly stack all materials and tools left on job site.

END OF SECTION