RECREATIONAL BOATING COMMUNICATIONS

## Digital Selective Calling (DSC)

Digital Selective Calling (DSC) is a feature of some VHF radios that provides, upon activation, a digital distress signal. During a distress alert DSC provides identification, nature of distress, and an exact position when connected to a GPS. It also provides an excellent means of making a routine individual call to another DSC equipped boater using their 9-digit Maritime Mobile Service Identity (MMSI). A valid MMSI can be obtained from the Federal Communications Commission, BoatUS, and SeaTow. The Coast Guard shore network also maintains a voice guard on channel 16 VHF and 2182 kHz.

TESTING YOUR VHF DSC RADIO

Exchange routine calls on CH70 with another suitably equipped vessel. It is illegal to send a false distress to test your radio.

RESPONDING TO A DISTRESS ALERT

If you receive a DSC distress alert, do not answer immediately. Allow a USCG station to contact the distress vessel. If no contact is heard, call the distress vessel on VHF CH16. Once you have made contact, call the USCG on VHF CH16 or by any available means and tell them you are relaying a distress. Give them the vessel’s position, identification, nature of distress, and vessel description.

MARITIME SAFETY INFORMATION  (MSI)            _

NAVTEX is an international automated medium frequency (518 kHz) direct-printing service for delivery of navigational and meteorological warnings and forecasts, as well as urgent marine safety information to ships. It was developed to provide a low-cost, simple, and automated means of receiving this information within approximately 200 nautical miles of shore. The U.S. Coast Guard operates NAVTEX stations in the U.S. There are no user fees associated with receiving NAVTEX broadcasts. A NAVTEX receiver provides important information and is a useful radio to have on your boat.

NOAA weather radio network provides voice broadcasts of local and coastal marine forecasts on a continuous cycle.

SATELLITE EPIRB’S

The most useful system for automated distress alerts is the 406 MHz Electronic Position Indicating Radio Beacon (EPIRB). It provides rapid alerting, identification (if properly registered), and accurate location to search and rescue authorities. The EPIRB has a built in homing beacon on 121.5 MHz. USCG aircraft have the ability to home on this signal. This is an important safety device and can be purchased or rented.

CELLULAR PHONES ARE NOT RECOMMENDED

Cellular phones generally cannot provide ship-to-ship safety communications or communications with rescue vessels.  If you make a distress call on a cellular phone only the one party you call will be able to hear you and none of the boats in your immediate vicinity will know you are in trouble. Locating a cellular caller is hard to do.  If you don't know precisely where you are, the Coast Guard will have difficulty finding your location on the water. Use your DSC VHF radio.

EMERGENCY DSC DISTRESS PROCEDURES

Always follow your radio manufacturer’s recommendations

HAVE ALL PERSONS PUT ON LIFE JACKETS

IF YOU HAVE AN EPIRB TURN IT ON

- MAKE SURE RADIO IS ON

- LIFT PLASTIC COVER AND PRESS DISTRESS BUTTON FOR 5 SECONDS AND RELEASE

- ONCE CALL IS ANSWERED, VERIFY RADIO IS SET ON CHANNEL 16

- IF CALL IS NOT ANSWERED, CHANGE TO CHANNEL 16

- PRESS MICROPHONE TRANSMIT BUTTON AND CLEARLY SAY:  MAYDAY, MAYDAY, MAYDAY

GIVE YOUR:

  - VESSEL NAME AND DESCRIPTION

  - POSITION AND/OR LOCATION

  - NATURE OF EMERGENCY

  - NUMBER OF PEOPLE ON BOARD

- RELEASE TRANMSIT BUTTON

- WAIT FOR 10 SECONDS – IF NO RESPONSE

REPEAT “MAYDAY” CALL

- ONCE CALL IS ANSWERED DO NOT CHANGE FROM CHANNEL 16 UNLESS INSTRUCTED TO DO SO. IF CONTACT IS LOST, CALL AGAIN ON CHANNEL 16

*Intentional hoax calls are an offense subject to prosecution

- Make certain your DSC radio is connected to your GPS to automatically give your position

- Use only an MMSI obtained from an officially authorized source

- Learn how to use your VHF DSC radio. Your USCG Auxiliary can show you how. http://www.cgaux.org/

For more information, please contact:

Commandant (CG-622)

United States Coast Guard

2100 Second Street S.W.

Washington, DC 20593

(202) 267-2860 / Fax: (202) 267-4106

E-mail: cgcomms@comdt.uscg.mil

Web site:

http://www.navcen.uscg.gov/marcomms/