WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11943 | In-Flight Anomaly Number -- | Contractor Report Number E-122 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LH2 PRESSURE TRANSDUCER FAILED DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1R | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LH2 PRESS TRANSDUCER | PART# PD7400098-089 | SER/LOT# 2193 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LH2 PRESS TRANSDUCER | PART# PD7400098-089 | SER/LOT# 2193 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EVP - ELEC TOLRNCE | Cause ETE - EI-TEST-ENVR |
| System ELECTRICAL | Defect CN - CONTAM | Material C - EEE | Work Contact J. ADAMS | Fail Date 12/22/1988 |
| Received at MSFC 01/05/1989 | Date Isolated -- | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom ET - MEAS ANOMALY | Time Cycle N/A |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/14/1995 | CN RSLV SBMT 01/13/1989 | Defer Date -- | Add Date 01/06/1989 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer A. JACKMAN | S & MA R. JACKSON | Project M. PESSIN | Project MGR J. SMELSER |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project C. BRAMON | Project MGR J. SMELSER |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 01/18/1989 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE PRESSURE TRANSDUCER FAILED ATP. THE UNIT HAD TWO LOSSES OF SIGNAL (DROPOUTS) DURING THE HIGH CALIBRATION RESOLUTION TESTING AT APPROXIMATELY 50 PSIA. NO SIGNAL DROPOUTS ARE ALLOWED REF. MARS T34393 PREVIOUS CAPS: E-082, E-091, E-101, E-106, E-110, E-111, E-112, E-115, E-119, E-120, E-121 |
| Contractor Investigation/Resolution CAUSE: CONTAMINATION OF THE INTERNAL POTENTIOMETER R/C: NONE GENERAL A PRESSURE TRANSDUCER FAILED DURING VENDOR ACCEPTANCE TESTING. THE TRANSDUCER HAD TWO LOSSES OF SIGNAL (DROPOUTS) AT APPROXIMATELY 50 PSIA DURING THE HIGH RESOLUTION CALIBRATION TEST. NO DROPOUTS ARE ALLOWED. MARS T-34393, SERIAL NUMBER 2193 OCCASIONAL ATP FAILURES OF THIS TYPE ARE EXPECTED AS PART OF NORMAL PRODUCTION FALLOUT. INVESTIGATION OF PREVIOUS SIMILAR FAILURES HAS FOUND THAT MICROSCOPIC PARTICULATE CONTAMINATION OF THE INTERNAL RESISTIVE ELEMENT AND WIPER IS THE MOST PROBABLE CAUSE. REFERENCE: CAPS E-082 TASK I FAILURE INVESTIGATION FAILURE ANALYSIS OF THE TRANSDUCER IS NOT WARRANTED. NUMEROUS PREVIOUS FAILURES OF THIS TYPE HAVE OCCURRED AND THE HARDWARE WAS ANALYZED. NO FAILURE CAUSE OTHER THAN CONTAMINATION HAS BEEN FOUND OR POSTULATED. THIS TYPE OF FAILURE MEETS ALL OF THE REQUIRMENTS OF "B80862 SPACE SHUTTLE EXTERNAL TANK CRITICALITY 1, 1R, 2 AND 2R PROBLEM REPORTING REQUIREMENTS PLAN; PARAGRAPH 2.3.4 CLOSURE REPORT" AND NEITHER ANALYSIS NOR CORRECTIVE ACTION IS REQUIRED TASK CLOSED TASK II CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED TRANSDUCERS HAS SUCCESSFULLY PASSED THE ACCEPTANCE TEST TASK CLOSED TASK IV CAPS CLOSURE SUMMARY TRANSDUCER FAILED DURING VENDOR ACCEPTANCE TEST. THE FAILURE WAS OF A TYPE THAT IS CONSIDERED NORMAL PRODUCTION FALLOUT. NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED THIS PROBLEM IS CONSIDERED CLOSED |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11943 | IFA# -- | Contractor RPT# E-122 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-089 | Asmnt Part Name LH2 PRES TRANSDUCER | Asmnt Serial/Lot# 2193 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD EIC - EI-CONTAM | FAIL MODE EVP - ELEC TOLRNCE |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE G | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |