MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A16677 | In-Flight Anomaly Number -- | Contractor Report Number E-161 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER FAILURE DURING SUPER LIGHTWEIGHT QUAL TEST AT MSFC |
| EICN# -- | ELEMENT ET | Contractor LMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LH2 ULLAGE PRESSURE | PART# PD7400098-089 | SER/LOT# 1700 | MANUFACTURER GULTON |
| Test/Operation Q - QAL | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EG - SIG HI OR LO | Cause EIC - EI-CONTAM |
| System ELECTRICAL | Defect DA - ROUGH | Material CA - DEVICE | Work Contact * MCKEOUGH/A | Fail Date 10/16/1995 |
| Received at MSFC 10/18/1995 | Date Isolated 10/17/1995 | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MSFC | Symptom EG - SIG HI OR LO | Time Cycle -- |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 04/19/1996 | Contractor Req Defer Until Date 11/07/1995 | LVL 3 Close -- | Remark / Action 11/07/1995 |
| Investigation / Resolution Summary |
| Last MSFC Update 01/24/2001 | CN RSLV SBMT 11/08/1995 | Defer Date -- | Add Date 10/18/1995 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design J. RATLEY | Chief Engineer M. PESSIN | S & MA M. SMILES | Project -- | Project MGR P. COUNTS |
| Approval |
| Design J. RATLEY | Chief Engineer M. PESSIN | S & MA M.D. SMILES | Project -- | Project MGR P. COUNTS |
| PAC Assignee J. NELSON | PAC Review Complete JMN | MSFC Closure Date 11/22/1995 | Status E - CLOSED-E | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID N012814 |
| Related Document Title E082 |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A TRANSDUCER FAILED A TEST OF APPLIED PRESSURE VERSUS OUTPUT VOLTAGE ACCURACY DURING A SUPER LIGHTWEIGHT QUALIFICATION TEST AT MSFC THE TRANSDUCER INDICATED A LOWER VOLTAGE THAN THAT REQUIRED WITH AN INPUT PRESSURE OF BETWEEN 32 TO 34 PSIA CRITICALITY: THE TRANSDUCER IS LISTED AS CRIT. 1R: FMEA ITEM CODE 3.4.1.2; "FAILS WITH LOW READING." NOTE: THE TRANSDUCER IS LIMITED LIFE CONTROLLED * REVISION "A" CLOSES ALL TASKS. SEE ASTERISKS |
| Contractor Investigation/Resolution * GENERAL: A QUALIFICATION TEST WAS BEING PERFORMED ON THE GULTON LH2 ULLAGE PRESSURE MEASUREMENT INSTALLATION TO CERTIFY IT FOR USE ON THE SUPER LIGHTWEIGHT EXTERNAL TANK (SLWT). THE INSTALLATION INCLUDES THE GULTON PD7400098 TRANSDUCERS, SHOCK MOUNT, AND THE FLEXIBLE HOSES. THE OUTPUT VOLTAGE OF ONE OF THE FOUR TRANSDUCERS READ LOWER THAN THE ACCEPTABLE VALUE DURING THE SIMULATED DETANKING SECTION OF THE QUALIFICATION TEST. SEE TABLE 1 FOR RESULTS THIS TEST ANOMALY IS INDICATIVE OF SHORTED TURNS ON THE WIRE WOUND RESISTIVE ELEMENT OF THE TRANSDUCER TABLE 1 APPLIED PRESSURE ACTUAL OUTPUT VOLTAGE MINIMUM ACCEPTABLE (PSIA) ASCENDING DESCENDING OUTPUT VOLTAGE 32 2.412 2.418 2.450 33 2.509 2.541 2.575 34 2.649 2.666 2.700 THE TRANSDUCER IS USED TO MEASURE THE ULLAGE PRESSURE IN THE LIQUID HYDROGEN PROPELLANT TANK DURING BOTH GROUND PROPELLANT LOADING AND IN FLIGHT. THE TRANSDUCER IS ATTACHED TO A SHOCK MOUNT ON THE FORWARD DOME OF THE HYDROGEN TANK, WITHIN THE INTERTANK. THE TRANSDUCER COVERS THE RANGE OF 12 TO 52 PSIA. THE ORBITER PROVIDES 5 VDC TO THE TRANSDUCER AND RECEIVES A VOLTAGE FROM THE TRANSDUCER PROPORTIONAL TO THE ULLAGE PRESSURE. THE PRESSURE MEASUREMENT IS USED TO CONTROL THE SPACE SHUTTLE MAIN ENGINE (SSME) GASEOUS HYDROGEN FLOW CONTROL VALVE TASK I. FAILURE INVESTIGATION THE TRANSDUCER FAILURE WAS DOCUMENTED ON NCD N012814. THE NCD WILL BE DISPOSITIONED FOR FAILURE ANALYSIS TO BE PERFORMED AT MAF AFTER COMPLETION OF QUAL TESTING RESPONSIBILITY: J. ADAMS/3741 - D. WESTPHAL/3740 L. COLON/4120 - Z. KIRKLAND/4100 COMPLETED: NOVEMBER 6, 1995 * CLOSURE STATEMENT THE TRANSDUCER HAD APPROXIMATELY 23 TO 27 SHORTED TURNS ON THE RESISTIVE ELEMENT AT THE RESULT OF WEAR. THE WEAR OCCURRED AT AN ACCELERATED RATE AS COMPARED TO THE EXPECTED PERFORMANCE BASED ON PREVIOUS ENGINEERING TESTS AND THE SERVICE HISTORY ON ETS. THE PROBABLE CAUSE OF THE ACCELERATED WEAR WAS A MICROSCOPIC SCRATCH ON THE WIPER WHICH HAD OCCURRED DURING MANUFACTURE OF THE TRANSDUCER TASK CLOSED CAUSE * PROBABLE CAUSE: A MICROSCOPIC SCRATCH ON THE POTENTIOMETER WIPER CONTACT SURFACE CAUSED ACCELERATED WEAR OF THE RESISTIVE ELEMENT WITH THE RESULTING SHORTED TURNS TASK II. CORRECTIVE ACTION * NO CORRECTIVE ACTION IS REQUIRED. THE FAILURE IS THE DIRECT RESULT OF THE TRANSDUCER DESIGN AND THE LIMITATIONS OF THE MANUFACTURING ENVIRONMENT PREVIOUS FAILURES OF TRANSDUCERS ON ETS HAD RESULTED IN A COMPLETE REVIEW AND APPRAISAL OF THE TRANSDUCER, AS DOCUMENTED ON CAPS E-082R. AS A RESULT OF THE CAPS, NUMEROUS CHANGES, IMPROVEMENTS, CONTROLS, AND INSPECTIONS WERE PUT IN THE MANUFACTURING PROCESSES. THE LMMSS PROCUREMENT QUALITY REPRESENTATIVE FOR GULTON HAS PERFORMED A NO-NOTICE INSPECTION OF THE MANUFACTURING FACILITY AND FOUND THAT ALL OF THE CORRECTIVE ACTIONS WHICH PROTECT THE WIPER DURING MANUFACTURE, DEVELOPED AS PART OF E-082R, ARE STILL BEING ADHERED TO. REFERENCE: MEMO FROM MR. RAY BRYANT, DATED NOVEMBER 6, 1995 TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES *THIS IS AN EXPLAINED CLOSURE OF THE CAPS THERE ARE NO CONSTRAINTS FOR THE SHORTED TURNS ON THE RESISTIVE ELEMENT OF THE LH2 TRANSDUCERS. THE LAUNCH COMMIT CRITERIA PROTECTS SAFETY BY REQUIRING THREE FUNCTIONAL PRESSURE TRANSDUCERS AT T-10 SECONDS. IN ADDITION, THE PRESSURIZATION SYSTEM IS TOLERANT TO ONE "HARD" FAILURE IN FLIGHT ALWAYS AND PROBABLY TWO, DEPENDING ON OCCURRENCE TIME AND FAILURE MODE REFERENCE: CAPS E-082(R). SINCE THE RETURN TO FLIGHT FOLLOWING STS-51L, 184 UNITS FUNCTIONED A T-10 SECONDS WITHOUT ANY SHORTED TURNS IN FLIGHT. ADDITIONALLY, THE DETANKING ULLAGE PRESSURES CONTINOUSLY MONITORED AND THIS TYPE OF ANOMALY WOULD BE DETECTED PRIOR TO THE NEXT TANKING NOTE: THIS IS ALSO THE DEFERRAL RATIONALE TASK CLOSED TASK IV. CAPS CLOSURE SUMMARY * THE FAILURE OF THE PRESSURE TRANSDUCER DURING THE QUALIFICATION TEST DUE TO SHORTED TURNS IS AN EXPECTED FAILURE MODE FOR POTENTIOMETER TYPE DEVICES. THE DIFFERENCE BETWEEN THE EXPECTED PERFORMANCE OF THE TRANSDUCER AND THE FAILURE IS THAT THE FAILURE OCCURRED WITH FAR LESS OPERATING TIME AND FEWER PRESSURE CYCLES THAN THE NORMAL. THE FAILURE WAS ACCELERATED BY A MICROSCOPIC SCRATCH ON THE POTENTIOMETER WIPER THAT IS AN INHERENT RISK IN THE MANUFACTURING PROCESS. REVIEW OF THE MANUFACTURER'S FACILITY FOUND THAT THE PREVIOUSLY ESTABLISHED PRACTICES WHICH REDUCE THE NUMBER OF OCCURRENCES OF DAMAGE TO THE TRANSDUCER COMPONENTS ARE STILL IN FORCE. NO NEW CORRECTIVE ACTION IS REQUIRED TASK CLOSED |
| MSFC Response/Concurrence MSFC DEFERRAL CONCURRENCE THIS REPORT HAS BEEN DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 08126 REV. F PARAGRAPH 3.3.10.1, ITEM I WHICH STATES "THE PROBLEM IS APPLICABLE TO THE FLIGHT(S) (SYSTEM IS INSTALLED OR USED ON THE FLIGHT); HOWEVER, SSP MANAGEMENT AGREES THAT SUFFICIENT SUBSTANTIATING EVIDENCE EXISTS THAT THE HARDWARE/SOFTWARE IN QUESTION CAN BE FLOWN SAFELY." ___JEFFERY L. RATLEY 10/19/95___ ___M. PESSIN 10/19/95__________ DESIGN DATE CHIEF ENGR DATE J. RATLEY M. PESSIN ___ALEX ADAMS 10/19/95_________ ___PARKER N. COUNTS 10/19/95___ S&MA DATE PROJECT MGR DATE (FOR) M. SMILES P. COUNTS |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A16677 | IFA# -- | Contractor RPT# E-161 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-089 | Asmnt Part Name LH2 ULLAGE PRESSURE | Asmnt Serial/Lot# 1700 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD EIC - EI-CONTAM | FAIL MODE EG - SIG HI OR LO |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |