WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A12096 | In-Flight Anomaly Number -- | Contractor Report Number E-123-2 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LOX PRESSURE TRANSDUCER FAILED DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1R | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LOX PRESSURE TRND | PART# PD740098-079 | SER/LOT# 2231 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LOX PRESSURE TRND | PART# PD7400098-079 | SER/LOT# 2231 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode MT - P/T HI OR LO | Cause ETT - EI-TEST-EQUP |
| System ELECTRICAL | Defect XN - NA | Material C - EEE | Work Contact J. ADAMS | Fail Date 03/10/1989 |
| Received at MSFC 03/15/1989 | Date Isolated -- | FMEA Reference 3.2.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EE - RANDOM | Time Cycle LMTD LIFE |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 05/07/1992 | CN RSLV SBMT 05/02/1989 | Defer Date -- | Add Date 03/16/1989 | R/C Codes 3 - F/TE -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer A. JACKMAN | S & MA R. JACKSON | Project M. PESSIN | Project MGR J. SMELSER |
| Approval |
| Design A. JACKMAN | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project J.SMELSER | Project MGR J. SMELSER |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 05/30/1989 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description LOX PRESSURE TRANSDUCER FAILED THE VENDOR ATP DURING THE HIGH RESOLUTION CALIBRATION TEST (ATP NUMBER 3061000081). THE UNIT DEVELOPED A LARGE OUTPUT VOLTAGE ERROR ON THE PRESSURE RISE. APPROXIMATELY AT 18 PSIG THE UNIT DEVELOPED A LARGE OUTPUT ERROR AND ITS FULL SCALE ERROR AT ATMOSPHERIC PRESSURE WAS 17% HIGH PREVIOUS CAPS: E-082, E-091, E-101, E-106, E-110, E-111, E-113, E-115, E-119, E-120, E-121, E-122 AND MSFC REPORT NO. A12029 |
| Contractor Investigation/Resolution 4/3/89 - THIS PROBLEM REPORT HAS BEEN DEFERRED FOR STS-30 BASED ON THE FOLLOWING RATIONALE: THE LOX PRESSURE TRANSDUCER IS CRIT 1R. THERE ARE FOUR UNITS INSTALLED WHILE THREE ARE REQUIRED TO BE FUNCTIONAL IF ONE UNIT FAILS TO OPERATE THE BACK-UP UNIT COULD BE SWITCHED TO UNTIL T-10 SECONDS ALL EFFECTIVITIES CLEARED, SINCE THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING; ALL INSTALLED COMPONENTS HAVE SUCCESSFULLY PASSED ACCEPTANCE TESTING THE ABOVE DEFERRAL RATIONALE HAS BEEN APPROVED BY THE ET PROJECT MANAGER, MR. J. SMELSER _______SIGNED 4/21/89______________________ CAUSE: TEST EQUIPMENT MALFUNCTION R/C: TEST EQUIPMENT HAS BEEN MODIFIED TO PREVENT APPLYING EXCESSIVE PRESSURE TO THE PRESSURE TRANSDUCER AND TO RECORD THE PRESSURE DURING TESTING GENERAL PRESSURE TRANSDUCER S/N 2231 FAILED DURING VENDOR ACCEPTANCE TESTING AND WAS DOCUMENTED ON MARS T-34394. THE FAILURE WAS VIRTUALLY IDENTIFICAL TO THAT DESCRIBED IN PR A12096 EXCEPT THAT IT OCCURRED ON PRESSURE RISE AT APPROXIMATELY 18 PSIG TASK I FAILURE INVESTIGATION THE TRANSDUCER DOCUMENTED ON MARS T-35394 DOES NOT WARRANT A FORMAL FAILURE ANALYSIS. THE FAILURE IS IDENTICAL TO THAT ON MARS T-35919 FAILURE ANALYSIS T-35919 FOUND THAT THE TRANSDUCER FAILED DUE TO A MALFUNCTION IN THE TEST EQUIPMENT UTILIZED IN THE VENDOR ATP. HIGH PRESSURE, FAR EXCEEDING THE 45 PSI PROOF PRESSURE, WAS APPLIED TO THE TRANSDUCER. PHYSICAL DISTORTION OF THE PRESSURE PORT ANEROID CAPSULES WAS MEASURED. THE SECOND FAILURE, MARS T-34394, COMING AS IT DID AT THE SAME POINT IN THE VENDOR ATP, BACKS THE FAILURE ANALYSIS RESULTS. THE AUTOMATED TEST EQUIPMENT WAS UNABLE TO DISCRIMINATE BETWEEN A TEST EQUIPMENT MALFUNCTION, RESULTING IN DAMAGE TO A TRANSDUCER, AND TRANSDUCER FAILURE TASK CLOSED TASK II CORRECTIVE ACTION THE CAUSE OF THE TEST EQUIPMENT MALFUNCTION IS UNDER INVESTIGATION BY GULTON SERVONICS' PERSONNEL CLOSURE STATEMENT GULTON SERVONICS HAS BEEN UNABLE AS YET TO IDENTIFY THE ROOT CAUSE OF THE TEST EQUIPMENT MALFUNCTION. IN LIEU OF CORRECTING THE CAUSE, SEVERAL MEASURES WERE TAKEN TO PREVENT DAMAGE TO THE TRANSDUCERS UNDER TEST. THE GAS PRESSURE SUPPLY TO THE TEST EQUIPMENT IS NOW LIMITED BY A PRESSURE REGULATOR TO THE PROOF PRESSURE RATING OF THE TRANSDUCER. A POWER LINE VOLTAGE TRANSIENT SUPPRESSOR WAS PLACED BETWEEN THE TEST EQUIPMENT AND THE AC POWER SOURCE. A STRIP CHART RECORDER WAS DIRECTLY CONNECTED TO THE TEST EQUIPMENT PRESSURE SENSOR, THUS BYPASSING THE COMPUTER IN THE DATA ACQUISITION LOOP. IN THE EVENT OF FUTURE TEST EQUIPMENT MALFUNCTIONS WHICH RESULT IN A HIGHER THAN INTENDED PRESSURE BEING APPLIED TO A TRANSDUCER, THE CHART RECORDER WILL PROVIDE A RECORD OF THE EVENT. THE CHART WILL BE APPENDED TO THE ATP RESULTS OF EACH TRANSDUCER. EFFORTS TO DETERMINE THE ROOT CAUSE OF THE TEST EQUIPMENT MALFUNCTIONS CONTINUE. SHOULD IT PROVE POSSIBLE, AT A LATER DATE, TO IDENTIFY THE TEST EQUIPMENT PROBLEMS, FURTHER CHANGES TO THE AUTOMATED TEST EQUIPMENT WILL BE MADE TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED TRANSDUCERS HAVE SUCCESSFULLY PASSED THE ACCEPTANCE TEST TASK CLOSED TSK IV CAPS CLOSURE SUMMARY THE VENDOR'S TEST EQUIPMENT MALFUNCTIONED AND DAMAGED A PRESSURE TRANSDUCER BY APPLYING EXCESSIVE PRESSURE. THE TEST EQUIPMENT FAILED TO RECORD THE PRESSURE EVENT. THE TEST EQUIPMENT HAS BEEN MODIFIED TO CORRECT BOTH PROBLEMS TASK CLOSED THIS PROBLEM REPORT IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A12096 | IFA# -- | Contractor RPT# E-123-2 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-079 | Asmnt Part Name LOX PRES TRANSDUCER | Asmnt Serial/Lot# 2231 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETT - EI-TEST-EQUP | FAIL MODE MT - P/T HI OR LO |
| Asmnt FMEA 3.2.1.1 | Asmnt FM 1 | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |