WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A12934 | In-Flight Anomaly Number -- | Contractor Report Number S-075 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title UNUSUAL ALIGNMENT - OV 102 TO ET 35 |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE STRUCTURAL ASSY | PART# 80911031780 | SER/LOT# ET-40 | MANUFACTURER MMC |
| Test/Operation L - FLD | Prevailing Condtion N - INSPECTION | F / U UC | Fail Mode MU - MECH TOLRNCE | Cause MPT - MFG-PRC-EQUP |
| System STRUCTURAL | Defect MD - M SIZE | Material S - STRUCT | Work Contact D. WESTPHAL | Fail Date 05/04/1990 |
| Received at MSFC 05/11/1990 | Date Isolated 05/04/1990 | FMEA Reference N/A | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom MU - MECH TOLRNCE | Time Cycle -- |
| Effectivity Text ET35, ET37, ET39 AND ET40 THRU ET60; CLOSED, 12/11/90 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 05/25/1990 | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary - MOST PROBABLE CAUSE WAS THE INTERCHANGE OF THE BALL FITTING HAT SECTION BETWEEN THE (3) UNITS OF THE ALIGNMENT TRUSS T12A7393 |
| Last MSFC Update 02/09/1995 | CN RSLV SBMT 09/19/1990 | Defer Date -- | Add Date 05/16/1990 | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design O. MOON | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design O. MOON | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 12/11/1990 | Status C - CLOSED | F/A Completion 09/01/1990 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID DC&R S-90-006 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CLOSURE RATIONALE SUBMITTED, 9/19/90 |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description PROBLEM DESCRIPTION: AS A RESULT OF UNUSUAL ALIGNMENT OF THE OV 102 (COLUMBIA) WITH ET-35 DURING STACKING ACTIVITIES, A SUSPECT CONDITION WAS REVEALED WHICH COULD AFFECT OTHER ETS RELATIVE TO THE BIPOD (FORWARD) ATTACH POINTS AS IT RELATES TO THE AFT ORBITER ATTACHING HARDWARE ON THE ET. FURTHER INVESTIGATIONS INCLUDED A RE-VERIFICATION OF THE ORBITER ATTACH POINTS ON ET-40 WHICH WAS THE NEXT ET SCHEDULED FOR SHIPMENT TO KSC. IT WAS DETERMINED THAT THE ORBITER CROSS BEAM ON THE E02 (-Y SIDE) WAS .125"FWD OF E03 (+Y SIDE), WHICH VIOLATES THE ICD OF +/-.090. THE E03 (+Y SIDE) BALL FITTING WAS CONFIRMED TO BE WITHIN .001" OF EB3 (UPPER SRB ATTACH FITTING). THIS CAPS IS ISSUED TO INVESTIGATE THESE OCCURRENCES AND TO IMPLEMENT CORRECTIVE ACTIONS AS REQUIRED NOTE: THIS IS A DISCRETIONARY CAPS (REFERENCE PARAGRAPH 1.6.2.3C OF MMC-ET-RA03) AND DOES NOT SPECIFICALLY RELATE TO ANY CIL ITEM |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence OTHER ITEMS CONTRIBUTING TO THE TOLERANCE VARIATION IN THE ALIGNMENT PROCEDURE INCLUDE: - MANUFACTURING PROCESS - INITIAL TOOL SET UP ALIGNED E02 & E03 INDEPENDENT OF EO1 - MANUFACTURING TOLERANCES PLUS TOOL TOLERANCES EXCEEDED ENGINEERING FOR E02 AND E03 - TOOLING - ALIGNMENT OF SCOPE MOUNT ON T12A7393 TOOL - OPTICS MOUNT ON T12A7393 TOOL - OPTICS ACCURACY - OPTICS TRANSIT SQUARE ALIGNMENT GENERAL: AFTER SOME DIFFICULTY IN MATING ET-35 WITH OV-102 COLUMBIA ORBITER, IT WAS OBSERVED THAT ONE THREAD PROTRUDED FROM THE ADJUSTABLE (+Y) END OF THE BIPOD CLEVIS WHICH IS THE MINIMUM ALLOWED BY OMRSD. THIS UNUSUAL CIRCUMSTANCE PROMPTED AN INVESTIGATION WHICH INCLUDED OPTICAL AND CALCULATED DIMENSIONS RELATIVE TO THE POSITION OF THE ORBITER IN RELATIONSHIP TO THE CENTER LINE OF THE ET. THE DATA INDICATED THAT THE ORBITER WAS 1.47" IN THE +Y DIRECTION AT THE FORWARD BIPOD ATTACH POINT WHICH IS .400" MORE THAN THE ICD REQUIREMENT. FURTHER OPTICAL MEASUREMENTS WERE MADE ON THE ORBITER CROSS BEAM ON ET-35 AND IT WAS REPORTED THAT THE EO-2 FITTING WAS LOCATED .200" FORWARD OF THE E03 THE ICD REQUIREMENT IS +/- .090" TO FURTHER UNDERSTAND THE CONDITION EXPERIENCED ON ET-35, A DECISION WAS MADE TO RE-VERIFY THE AFFECTED DIMENSIONS ON ET-40 PRIOR TO SHIPMENT TO KSC. MEASUREMENTS WERE MADE ON EO-2 AND EO-3 (ORBITER ATTACH POINTS) IN RELATIONSHIP TO EB-3 AND EB-4 (UPPER SRB FITTINGS). THE UPPER SRB FITTINGS ARE IN PLANE WITH THE 2058 RING FRAME AND THE ORBITER ATTACH POINTS (EO-2 RELATIVE TO EO-3), BY ICD REQUIREMENT, SHOULD BE WITHIN +/- .090". ONCE THIS DIMENSION IS ESTABLISHED, THE CROSS BEAM MID-POINT (BETWEEN EO-2 AND EO-3) IS DETERMINED AND OPTICAL ALIGNMENTS AND CHECKS ARE MADE TO DETERMINE THE POSITION OF EO-1 BIPOD YOKE ATTACH POINT. IT WAS DETERMINED THAT AN OUT-OF-TOLERANCE CONDITION EXISTED AT POSITION EO-2 ON ET-40 TASK I: PROBLEM/FAILURE INVESTIGATION 1. MANUFACTURING ENGINEERING AND TOOL DESIGN EVALUATE THE AFT ET/ORBITER INTERFACE STRUCTURE ASSEMBLY/ALIGNMENT PROCESSES TO DETERMINE POSSIBLE CONTRIBUTORS TO THE ET-40 NONCONFORMANCE COMPLETED: 5/31/90 CLOSURE STATEMENT A POTENTIAL PRIME CONTRIBUTION TO THE OUT-OF-TOLERANCE CONDITION IS THE POSSIBLE INTERCHANGING OF HAT SECTIONS ON THE T12A7393 TOOL. HAT SECTIONS DID NOT HAVE CONTROLLED INTER-CHANGEABILITY BETWEEN THE THREE UNITS OF THE T12A7393 UNTIL FEBRUARY, 1986. OTHER DATA IS BEING ACCUMULATED UNDER TASK 8 OF THIS CAPS. REF. MEMO 3614-90-111 2. MANUFACTURING ENGINEERING AND TOOL DESIGN ANALYZE THE T12A7021 ASSEMBLY TOOL TO DETERMINE WHETHER THE TOOL'S STIFFNESS/TOLERANCES WERE ADEQUATE TO ENSURE INSTALLATION/ALIGNMENT OF THE AFT INTERFACE HARDWARE WITHIN DRAWING REQUIREMENTS COMPLETED: 5/31/90 CLOSURE STATEMENT ALL DEFLECTIONS AND LOCATION DIFFERENCES INDICATE THAT TOOL DEFLECTION DID NOT CAUSE THE OUT-OF-PLANE CONDITION OF EO2 AND EO3 FOUND ON ET-40 REF. ATTACH. III TO MEMO 3614-90-111 3. ENGINEERING PUBLISH DATA RELATIVE TO ENGINEERING REQUIREMENTS AND TOLERANCE VARIATIONS AFFECTING THE EO1 ICD REQUIREMENTS AND MANUFACTURING TOLERANCE AFFECTS (SIC) ON THESE ICD DIMENSIONS COMPLETED: 5/9/90 CLOSURE STATEMENT: A CAD STUDY WAS PERFORMED ON THE EO-1 WORST CASE TOLERANCE. USING WORST CASE DRAWING TOLERANCES AND WORST CASE TOOLING TOLERANCES, DATA INDICATES THAT POSITIVE THREAD EXPOSURE ON THE BIPOD CLEVIS CAN BE ACHIEVED IN WORST CASE CONDITIONS. REFERENCE MEMO 3511-90-005 4. RELIABILITY ASSURANCE REVIEW BUILD DATA WHICH WOULD AFFECT ALIGNMENT ON ET-40 TO DETERMINE IF ANY ABNORMAL CONDITIONS (MRBS, DRS, ETC.) EXISTS WHICH WOULD CONTRIBUTE TO THE OUT-OF-TOLERANCE CONDITION AT EO-1 AND EO-2 COMPLETE: 5/7/90 CLOSURE STATEMENT: THE FOLLOWING BUILD AND ALIGNMENT DATA WAS REVIEWED TO DETERMINE IF AN EVENT OCCURRED WHICH WOULD CONTRIBUTE TO THE ORBITER CROSS BEAM MIS-ALIGNMENT ON ET-40 1. 80900209002-999 VERTICAL ALIGNMENT -- CELL A 2. 80914151910-M009 LH2 FWD DOME MECH. ASSY 3. 80911051124-010 FTG. INSTL. ET/SRB 4. 80911051109 BI-POD FTG. INSTL 5. 80911071790 STRUCTURE ASSY ET/ORBITER ACT 6. 80911009190 BI-POD FIT CHECK ALIGNMENT VERIFICATION NO MARS OR DRS WERE PROCESSED WHICH WOULD CONTRIBUTE TO THE OUT-OF-SPEC CONDITION OF ET-40 5. RELIABILITY ASSURANCE ISSUE DC&R TO RE-VALIDATE ICD DIMENSIONS ON ETS AS IDENTIFIED ON DC&R S-90-006 COMPLETED: 5/14/90 CLOSURE STATEMENT: DC&R WAS ISSUED TO INSPECT ET-41 THROUGH ET-55 AND ET-57 THROUGH ET-60 TO VERIFY THE RELATIONSHIP OF EO-3 TO THE 2058 RING FRAME. EO-2 RELATIONSHIP TO EO-3 AND RELATIONSHIP OF EO-1 TO EO-2 AND EO-3 NOTE: ET-40 AND ET-56 WERE CHECKED AT MAF BY O.D. ET-MGT.082 ET-37 AND ET-39 WERE CHECKED BY KSC TPS #5525A-274 6. MANUFACTURING ENGINEERING AND QUALITY ENGINEERING PROVIDE RATIONALE FOR ACCEPTING ALL ETS ASSEMBLED USING THE NEW EO1/EO2/EO3 ALIGNMENT FIXTURE, T12A7428, BASED ON THE DESIGN, RESOLUTION OF DISCREPANCIES AND SUBSEQUENT DESIGN CHANGES ECD: CANCELLED DUE TO PROGRAM DECISION TO REVERIFY ALL POST DD250 ETS AND ET-56 THROUGH ET-60 BY DC&R AT MAF OR TPS AT KSC 7. MANUFACTURING ENGINEERING AND STRUCTURES DESIGN REVIEW ALL ET STRUCTURAL ALIGNMENT (EO1-EO5, EB1-EB8) INTERFACE DESIGN REQUIREMENTS (ICDS), ENGINEERING DRAWING REQUIREMENTS AND MANUFACTURING BUILD PROCESSES FOR PROPER FLOW DOWN OF REQUIREMENTS TO BUILD. THIS SHOULD INCLUDE, BUT NOT BE LIMITED TO, SUCH ITEMS AS, (1) CONSISTENCY OF REQUIREMENTS, (2) TOLERANCE STUDY, (3) MANUFACTURING PROCESS, AND (4) MANUFACTURING BUILD PROCESS ADEQUACY. PROVIDE A FLOW-DOWN MATRIX THAT DISPLAYS THE REQUIREMENTS AND CONCLUSIONS OF THE REVIEW COMPLETED: 9/1/90 CLOSURE STATEMENT: A REVIEW OF ALL STRUCTURAL ALIGNMENT INTERFACE DESIGN REQUIREMENTS, ENGINEERING DRAWING REQUIREMENTS, AND MANUFACTURING ALIGNMENT PROCESSES WERE EVALUATED. ALSO A TOLERANCE STUDY WAS PERFORMED. THIS STUDY HAS SHOWN THAT ENGINEERING REQUIREMENTS MEETS ICD REQUIREMENTS AND THAT THE MANUFACTURING BUILD TOLERANCES MEET THE ENGINEERING REQUIREMENTS WITH ONE EXCEPTION. THE BUILD TOLERANCES EXCEEDS THE ENGINEERING REQUIREMENTS FOR THE X-X ALIGNMENT OF EO2 AND EO3 BY 0.002 AND 0.003 RESPECTIVELY. THESE TOLERANCES HAVE BEEN ADJUSTED TO MEET ENGINEERING REQUIREMENTS. REFERENCE MEMO 3614-90-142, ATTACHED 8. MANUFACTURING ENGINEERING DEVELOP A STATISTICAL APPROACH FOR ANALYZING THE BUILD TOLERANCE (TOOLING, OPTICS, ETC.) STACK-UPS AND EVALUATE THE AS-BUILT DATA FROM THE DC&R RE-VERIFICATION MEASUREMENTS TO DEVELOP A PROBABILITY ASSESSMENT. THIS TASK IS BEING PERFORMED TO PROVIDE SUPPORTING RATIONALE FOR THE PROBABLE CAUSE IDENTIFIED IN ITEMS 1 AND 2 COMPLETED: 9/1/90 CLOSURE STATEMENT: A STATISTICAL ANALYSIS WAS PERFORMED USING DATA GATHERED FROM THE BUILD PROCESS. ALL ASPECTS INCLUDING REQUIREMENTS, PROCESSES, TOOLING AND HISTORICAL DATA HAVE BEEN REVIEWED. AREAS WERE FOUND THAT ARE PRESENTLY MARGINAL. TO ENHANCE THE ALIGNMENT PROCESS CORRECTIVE ACTIONS HAVE BEEN IMPLEMENTED. ALSO A COMPUTERIZED DATA SYSTEM IS BEING IMPLEMENTED WHICH WILL ENHANCE THE STATISTICAL ANALYSIS. REFERENCE MEMO 3614-90-157, ATTACHED TASK II CORRECTIVE ACTIONS: - AS A RESULT OF TASK I. ITEM 8 THE FOLLOWING CORRECTIVE ACTIONS HAVE BEEN IMPLEMENTED: - IMPROVED MANUFACTURING PROCESS - IMPROVED INITIAL SET UP OF ALIGNMENT TOOL - IMPROVED METHOD FOR LOCATION OF BIPOD AT NOMINAL - RECORDING OF BUILD INFORMATION - IMPLEMENTED LAMINATED SHIM AT THRUST STRUT TO BALL FITTINGS - ADJUSTED VERTICAL SHIM THICKNESS WITH STRUT INSTALLED - TIGHTENED BUILD TOLERANCES FOR X-X ALIGNMENT FOR EO2 AND E03 - IMPROVED AND REWORKED TOOLING - SCALE ON BIPOD FIXTURE - REVERIFIED TOOLING TO ICT - IMPLEMENT ALIGNMENT TOOL T12A7428 IN PLACE OF T12A7021 - INSTALLED TOOL STABILIZER STRUTS - REPLACE OPTICS MEASUREMENT MOUNTS ECD: 1-2-91 - IMPROVED OPTICS ACCURACY - REPLACE OPTICS SQUARE SET-UP WITH DIRECT OPTICAL LINE - IMPLEMENT STATISTICAL ANALYSIS AND TRACKING CHARTS, ECD: 12/1/90 NOTE: ALL CORRECTIVE ACTIONS ARE COMPLETED. THE TWO ITEMS WITH ECD'S ARE PROCESS ENHANCEMENTS AND DO NOT REQUIRE IMPLEMENTATION PRIOR TO CAPS CLOSURE TASK III CLEARANCE OF EFFECTIVITIES: NO CONSTRAINTS TO FLIGHT. THE ACCEPTABILITY OF THE POSITIONS OF E02/E03 RELATIVE TO EO1 IS VERIFIED DURING ORBITER/ET MATE IN THE KSC VAB FOR ALL ETS. THE VERIFICATIONS REQUIRED BY THIS CAPS WILL ASSURE A SUCCESSFUL ORBITER MATE FOR ALL ETS TASK IV CAPS CLOSURE SUMMARY FOLLOWING THE IDENTIFICATION OF THE ET-35 ALIGNMENT CONCERN AND THE SUBSEQUENT DETERMINATION OF THE OUT-OF-TOLERANCE CONDITION ON ET-40, SEVERAL INVESTIGATIONS WERE CONDUCTED TO DETERMINE THE CAUSE OF THE EO1, EO2, EO3 ALIGNMENT PROBLEM AND ASSURE THAT THE OTHER ICD STRUCTURAL ALIGNMENT REQUIREMENTS WERE ACHIEVED THROUGH THE CAPS INVESTIGATION, THE ET/ORBITER INTERFACE STRUCTURAL ASSEMBLY/ALIGNMENT PROCESS, THE ALIGNMENT TOOLS, ENGINEERING BUILD TOLERANCE VARIATIONS, THE BUILD DATA, AND A REQUIREMENTS FLOW DOWN (ICD, DRAWING AND BUILD TOLERANCES) WERE EVALUATED DURING THE INITIAL INVESTIGATION THE INTERCHANGEABILITY OF THE HAT SECTIONS ON TOOL T12A7393 WAS IDENTIFIED AS A POTENTIAL PRIME CONTRIBUTOR TO THE ALIGNMENT OUT-OF-TOLERANCE CONDITION FOR ET-35 THROUGH ET-42. THE HAT SECTION ON THE THREE UNITS OF T12A7393 ALIGNMENT TRUSS WERE NOT FUNCTIONALLY CO-ORDINATED UNTIL ET-43. HAT SECTIONS INTERCHANGED BETWEEN UNITS OF THE T12A7393 COULD HAVE CAUSED MISALIGNMENT OF THE BALL FITTINGS UP TO 0.250 INCH. SUBSEQUENT INVESTIGATIONS HAVE NOT BEEN ABLE TO ASCERTAIN WHICH UNITS OF THE HAT SECTIONS WERE USED WITH THE OUT OF TOLERANCE ET-35, ET-37, AND ET-40; HOWEVER, THE HAT SECTIONS WERE USED INTERCHANGEABLY DURING THE PERIOD AND ARE THE MOST PROBABLE CAUSE FOR THE OUT OF TOLERANCE CONDITION. THE DEFLECTION AND ASSOCIATED LOCATION DIFFERENCES INDICATE THAT THE TOOL (T12A7021) DID NOT CAUSE THE OUT-OF-PLANE CONDITION. A CAD STUDY WAS PERFORMED ON EO-1 WORST CASE TOLERANCES. USING WORST CASE DRAWING TOLERANCES AND WORST CASE TOOLING TOLERANCES THE DATA INDICATED THAT THE POSITIVE THREAD EXPOSURE ON THE BIPOD CLEVIS CAN BE ACHIEVED IN WORST CASE CONDITION. THE BUILD DATA REVIEW INDICATED THAT NO MARS OR DRS WERE PROCESSED THAT COULD CONTRIBUTE TO THE OUT-OF-SPEC. CONDITION. THE FLOW DOWN TOLERANCE STUDY HAS SHOWN THAT THE ENGINEERING REQUIREMENTS MEETS THE ICD AND THE MANUFACTURING BUILD TOLERANCES MEETS THE ENGINEERING WITH ONE EXCEPTION. THE EXCEPTION BEING THE BUILD TOLERANCES EXCEEDED THE ENGINEERING REQUIREMENTS FOR THE X-X ALIGNMENT OF EO2 AND EO3 BY 0.002 AND 0.003 RESPECTIVELY THROUGHOUT THE STUDIES, A VARIABILITY IN LOCATION OF THE BALL FITTINGS HAS BEEN SHOWN THAT CANNOT BE ATTRIBUTED SOLELY TO THE INTERCHANGE OF THE HAT SECTIONS. THIS VARIABILITY AND RESULTING EXCURSION OF THE BIPOD DURING ORBITER MATE IS A RESULT OF CONTRIBUTIONS FROM THE MANY VARIABLES ENCOMPASSING THE TOTAL ORBITER INTERFACE ALIGNMENT PROCESS REFERENCE CAPS-075 ET/ORBITER ALIGNMENT PRESENTATION, ATTACHED IN ORDER TO ENHANCE THE ALIGNMENT PROCESS, IMPROVEMENTS TO THE MANUFACTURING PROCESS INSTRUCTION, TOOLING AND OPTICS ACCURACY WERE REQUIRED. THE MANUFACTURING PROCESS INSTRUCTIONS WERE IMPROVED BY MODIFYING; THE INITIAL SET UP OF THE ALIGNMENT TOOL, METHOD FOR LOCATION OF BIPOD AT NOMINAL AND BY TIGHTENING THE BUILD TOLERANCES FOR X-X ALIGNMENT OF EO2 AND EO3. THE TOOLING HAS BEEN IMPROVED BY MODIFYING THE SCALES ON THE BIPOD FIXTURE, REVERIFYING THE TOOLS TO THE ICT AND BY IMPLEMENTING ALIGNMENT TOOL T12A7428 IN PLACE OF T12A7021 THE OPTICS ACCURACY HAS BEEN IMPROVED BY REPLACING THE OPTICS SQUARE WITH DIRECT OPTICAL LINE OF SIGHT. FURTHER ENHANCEMENT TO THE OPTICS ACCURACY WILL BE ACHIEVED BY REPLACING THE SPHERICAL MOUNTS WITH "V" MOUNTS BY ET-61. IN ADDITION TO THE ABOVE, MANUFACTURING ENGINEERING WILL IMPLEMENT STATISTICAL ANALYSIS AND TRACKING CHARTS BY 12-1-90 ET 59 AND 60 WILL BE ALIGNED WITH ALL OF THE ENHANCEMENT IN PLACE (EXCEPT FOR OPTICS MOUNTS). THESE ETS WILL BE REVERIFIED BY DC&R S-90-006. THE ACCEPTANCE OF THE REVERIFICATION RESULTS AND VERIFICATION BY ALIGNMENT CHECK TOOL INDICATES THAT THE ALIGNMENT PROCESS IS UNDER CONTROL. ALSO THE ALIGNMENT CHECK TOOL USED FOR REVERIFICATION PER DC&R WILL BE USED UP TO ET-63 ALL PREVIOUSLY BUILT ETS I.E. ET-35, 37, 39 AND 40 THROUGH 60 SHALL BE REVERIFIED TO ASSURE ET/ORBITER ALIGNMENT MEET THE ENGINEERING REQUIREMENTS |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A12934 | IFA# -- | Contractor RPT# S-075 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 80911031780 | Asmnt Part Name STRUCTURAL ASSY | Asmnt Serial/Lot# ET-40 |
| HCRIT CD -- | FCRIT CD 3 | CAUSE CD MPT - MFG-PRC-EQUP | FAIL MODE MU - MECH TOLRNCE |
| Asmnt FMEA N/A | Asmnt FM N/A | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |