WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A12210 | In-Flight Anomaly Number -- | Contractor Report Number E-125-1 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LOX PRESSURE TRANSDUCER FAILED WITH OPEN CIRCUIT DURING ATP |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT 1R | Sys_Lvl N | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE LOX PRESSURE TRN | PART# PD7400098-079 | SER/LOT# 2237 | MANUFACTURER GULTON |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE LOX PRESSURE TRN | PART# PD7400098-079 | SER/LOT# 2237 | MANUFACTURER GULTON |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause ETT - EI-TEST-EQUP |
| System ELECTRICAL | Defect ES - ELSTRS | Material C - EEE | Work Contact J. ADAMS | Fail Date 04/28/1989 |
| Received at MSFC 05/01/1989 | Date Isolated -- | FMEA Reference 3.2.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location GULTON | Symptom EL - SHORT | Time Cycle N/A |
| Effectivity Text -- |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary THE TRANSDUCER WAS DAMAGED BY IMPROPERLY CONNECTING IT TO THE VENDOR ATP VIBRATION TEST STATION. THE TEST EQUIPMENT ELECTRICAL CONNECTIONS HAVE BEEN MODIFIED TO PREVENT A RECURRENCE |
| Last MSFC Update 08/03/1989 | CN RSLV SBMT 06/29/1989 | Defer Date -- | Add Date 05/02/1989 | R/C Codes 3 - F/TE -- -- |
| Assignee |
| Design A. JACKMAN | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. BRIDWELL |
| Approval |
| Design A. JACKMAN | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 07/14/1989 | Status C - CLOSED | F/A Completion 05/31/1980 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description DURING SETUP OF THE VIBRATION PORTION OF THE VENDOR ATP, AN OPEN CIRCUIT CONDITION WAS DETECTED BETWEEN THE "WIPER" AND THE RETURN SIDE OF THE POTENTIOMETER REF. MARS T-34396, CAPS E-082, E-091, E-106, E-110, E-111, E-112, E-115, E-119, E-120, E-121, E-122, E-123, AND E-124 |
| Contractor Investigation/Resolution 5/1/89 - THIS PROBLEM REPORT HAS BEEM DEFERRED FOR STS-30 BASED ON THE FOLLOWING RATIONALE THE LOX PRESSURE TRANSDUCER IS CRIT 1R. THERE ARE FOUR UNITS INSTALLED WHILE THREE ARE REQUIRED TO BE FUNCTIONAL IF ONE UNIT FAILS TO OPERATE THE BACK-UP UNIT COULD BE SWITCHED TO UNTIL T-10 SECONDS ALL EFFECTIVITIES CLEARED, SINCE THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING. ALL INSTALLED COMPONENTS HAVE SUCCESSFULLY PASSED ACCEPTANCE TESTING THE ABOVE DEFERRAL MEETS THE DEFERRAL REQUIREMENTS OF NSTS 07700 VOLUME XI, ITEM C, WHICH STATES "THE PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE AND IS CLEARLY SCREENED BY ACCEPTANCE TEST, PREFLIGHT CHECKOUT, OR SPECIAL TEST." THE ABOVE DEFERRAL RATIONALE HAS BEEN APPROVED BY THE ET PROJECT MANAGER, MR. J. SMELSER ______MR. J. SMELSER (SIGNED 5/3/89)________________________ CAUSE: THE TRANSDUCER RESISTIVE ELEMENT WAS BURNED OUT DUE TO IMPROPER CONNECTION TO THE VENDOR ATP TEST EQUIPMENT R/C: THE VENDOR TEST EQUIPMENT HAVE BEEN MODIFIED GENERAL THE TRANSDUCER HAD SUCCESSFULLY COMPLETED THE INSULATION RESISTANCE, ROOM TEMPERATURE CALIBRATION, AND PROOF PRESSURE SEGMENTS OF THE VENDOR ATP-3061-0000-81. DURING SET-UP FOR THE VIBRATION TEST, PER PARAGRAPH 5.4, THE DEFECT WAS DISCOVERED. THE FAILURE IS SIMILAR TO THOSE WHICH HAVE RESULTED WHEN THE 5 VOLT POWER SUPPLY HAS INADVERTENTLY BEEN APPLIED ACROSS THE WIPER TO "RETURN" LEADS OF THE TRANSDUCER TASK I FAILURE INVESTIGATION FAILURE ANALYSES ARE TO BE PERFORMED ON THE TRANSDUCERS AT MAF COMPLETED: 5/31/89 CLOSURE STATEMENT FAILURE ANALYSIS OF THE TRANSDUCER FOUND THAT THE RESISTIVE ELEMENT HAD BEEN BURNED OUT BY THE APPLICATION OF EXCESSIVE CURRENT. THE TRANSDUCER HAD BEEN INCORRECTLY CONNECTED TO THE TEST EQUIPMENT, RESULTING IN THE HIGH CURRENT. REFERENCE MARS T34396 AND MARS T34397 TASK CLOSED TASK II CORRECTIVE ACTION THE VENDOR TEST EQUIPMENT, THE VIBRATION TEST STATION, WAS MODIFIED BY THE ADDITION OF A JUNCTION BOX TO PREVENT IMPROPER CONNECTION OF THE TRANSDUCERS REFERENCE MARS T34396 AND MARS T34397 TASK CLOSED TASK III CLEARANCE OF EFFECTIVITIES ALL ET'S CLEARED. THE FAILURE OCCURRED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED TRANSDUCERS HAVE SUCCESSFULLY PASSED THE ACCEPTANCE TEST TASK CLOSED TASK IV CAPS CLOSURE SUMMARY THE TRANSDUCER WAS DAMAGED BY IMPROPERLY CONNECTING IT TO THE VENDOR ATP VIBRATION TEST STATION. THE TEST EQUIPMENT ELECTRICAL CONNECTIONS HAVE BEEN MODIFIED TO PREVENT A RECURRENCE TASK CLOSED THIS PROBLEM REPORT IS CONSIDERED CLOSED |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A12210 | IFA# -- | Contractor RPT# E-125-1 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-079 | Asmnt Part Name LOX PRES TRANSDUCER | Asmnt Serial/Lot# 2237 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETW - EI-TEST-WORK | FAIL MODE EG - SIG HI OR LO |
| Asmnt FMEA 3.2.1.1 | Asmnt FM 1 | FMEA CSE N/A | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |