| REVIEW ITEM DISPOSITION (RID) |
| --- |
| 1. Review Type ENG Technical Review | 2. RFA No. | 3. Review Date June 22, 2001 |
| 4. Title: ISO/WD 14620-3 Space systems – Safety requirements – Part 3: Flight safety systems |
| Action: Paragraph 6.1.5 (c) – This paragraph should be deleted. It is not a requirement and it is not clear what is meant by “upper Earth atmosphere”. Paragraph 6.1.11 – Need to define what is meant by “national …authority”. Paragraph 6.1.15 – Need to define the phrase “externally controlled FTS”. This could be taken to imply that a flight termination system can be internally controlled or autonomous. I suggest adding a requirement that all FTS be controlled (commanded) from the ground. Paragraph 6.1.17 – This requirement is too specific for a high-level international standard (the response time …shall be between 4 and 25 milliseconds). Paragraph 6.4.4 – This should specify whether or not software can be used as one of the inhibits. Paragraph 8.2.3 – The TDTS should not be required to store data if it is part of an expendable on-board system. |
| 6. Originator: James Andary | Organization: 730 | Telephone: 6-2269 |
| 7. Response: |
| 8. Response By: | Organization: | Telephone: | Date Prepared: |
| 9. Originator Contacted: | Yes | No | Date: |
| 10: Disposition: | Deferred | Closed |  |
| 11: Comments: |  |
|  | Chairperson | Date |  |

450-Forms-02 (05/00)
Original