U.S. Department of Treasury

Fleet AFV Program Report for Fiscal Year 2001

November 20, 2002

This U.S. Department of Treasury Fleet AFV Program Report for Fiscal Year 2001 presents the Department’s data on the number of alternative fuel vehicles (AFVs) acquired in fiscal year (FY) 2001, and its planned acquisitions and projections for FY 2002 and FY 2003. The report has been developed in accordance with the Energy Policy Act of 1992 (EPAct) (42 U.S.C. 13211-13219) as amended by the Energy Conservation Reauthorization Act of 1998 (Public Law 105-388) (ECRA), and Executive Order 13149 (signed by the President in April 2000).  The Department acquired 420 covered vehicles in FY 2001. The EPAct mandates that the Department acquire at least 315 AFVs to comply with the 75 percent AFV acquisition requirement.  Treasury acquired 70 AFVs. Our plans indicate an improved level of compliance for FY 2002 and FY 2003 with projected acquisitions of 150 and 175 AFVs respectively.

# Legislative Requirements

The Energy Policy Act of 1992 (EPAct) requires that 75 percent of all covered light-duty vehicles acquired for Federal fleets in FY 2001 and beyond must be AFVs (where the fleets have 20 or more vehicles, are capable of being centrally fueled, and are operated in a metropolitan statistical area with a population of more than 250,000 based on the 1980 census). Certain emergency, law enforcement, and national defense vehicles are exempt from these requirements. EPAct also sets a goal of using replacement fuels to displace at least 30 percent of the projected consumption of motor fuel in the United States annually by the year 2010. The Energy Conservation and Reauthorization Act of 1998 amended EPAct to allow one alternative fuel vehicle acquisition credit for every 450 gallons of pure biodiesel fuel consumed in vehicles over 8,500 pounds gross vehicle weight rating. “Biodiesel credits” may fulfill up to 50 percent of an agency’s EPAct requirements. The head of each Federal agency must also prepare and submit a report to Congress outlining the agency’s AFV acquisitions and future plans by November 13th each year. Executive Order 13149 directs Federal agencies operating a fleet of 20 or more vehicles within the United States to reduce their annual petroleum consumption by at least 20 percent by the end of FY 2005 (compared to FY 1999 levels) by using alternative fuels in AFVs more than 50 percent of the time, improving the average fuel economy of new light-duty petroleum-fueled vehicle acquisitions by one mpg by FY 2002 and 3 mpg by FY 2005, and using other fleet efficiency measures.

# Treasury Approach to Compliance with EPAct and E.O. 13149

Due to its varied and diverse missions, the Treasury Department’s fleet is decentralized.  Each bureau operates, maintains, acquires, and funds its vehicle program. Overall, 90% of Treasury's fleet is used for law enforcement, leaving less than ten percent of the Department's fleet as covered under the Act.  This includes almost all Treasury owned vehicles as well as a portion of those leased from GSA.

To achieve compliance with the legislative mandates of EPAct and E.O. 13149, Treasury will attempt to acquire 75 percent of new covered light-duty vehicles as AFVs, and use alternative fuel in these vehicles a majority of the time, where the vehicles and alternative fuels are readily available and do not adversely affect mission accomplishment. The decision to take advantage of a new surcharge program that will add $10 monthly to the cost of every vehicle leased through the General Services Administration (GSA) to help cover the higher incremental cost of many AFV models (compared to conventional vehicles) will rest with each bureau and factor in alternative fuel availability, vehicle fund availability and mission needs.

Treasury will also endeavor to acquire light duty vehicles with a higher fuel economy of one mpg in FY 2002 and 3 mpg in FY 2005, consistent with mission suitability.  Treasury has investigated the possibility of establishing its own refueling facilities, however the great majority of the Treasury fleet neither starts from nor returns to a common location, thereby making centralized fueling impractical.

# Treasury Fleet Compliance for FY 2001

Figure 1 is a graphical depiction of AFV acquisitions by Treasury’s covered fleet in fiscal year 2001 and projections for FY 2002 and FY 2003. Treasury acquired 263 covered light-duty vehicles (LDVs) in fiscal year 2001, of which 70 were AFVs.  Treasury gained no credits for biodiesel fuel use or for acquiring dedicated light, medium, and heavy-duty AFVs.

Figure 1.  Summary of Treasury’s FY 2001 AFV Acquisitions

Additional vehicles commercially leased or purchased by Treasury were not “covered” vehicles.  The 2,271 law enforcement light-duty vehicles acquired in FY 2001 were not counted for compliance, and included both normal fleet replenishment and replacements for those lost in the collapse of the World Trade Center buildings.

# Special Projects of the Treasury Department Fleet Related to AFV and Infrastructure Acquisitions

# No special projects are currently underway.

# Alternative Fuel Use by Treasury Fleets in FY 2001

Table 2 presents alternative fuel use data for the Treasury’s fleets in fiscal year 2001. The majority of covered vehicles acquired by Treasury and other Federal fleets are leased from GSA, and the leasing contract folds in the maintenance and fuel costs for the vehicles. This is accomplished by the use of a GSA credit card that the fleets use to purchase alternative fuel. However, since product code standards are not uniform among suppliers of alternative fuels (e.g., ethanol or E-85), it is impossible for credit vendors to accurately track the purchase of alternative fuels with this credit card. The exception is natural gas, which is on-site at the Federal Law Enforcement Training Center, allowing the bureau to provide an accurate accounting of fuel used.

### Table 2. Treasury Fuel Use in FY 2001

| Fuel Type | Quantity | Unit |
| --- | --- | --- |
| Biodiesel – B100 |  | Gallons |
| CNG | 1,854 | Gallons @ 3,600 psi, 70oF |
| CNG |  | Hundred cu. ft. |
| Diesel | 111,396 | Gallons |
| E-85 | 83,003 | Gallons* |
| Gasoline | 699,226 | Gallons** |
| Methanol |  | Gallons |
| Propane |  | Gallons |

* 	Estimate based on incomplete data

**	Estimated after deducting for USSS extra vehicles for the Winter Olympics

# Treasury’s Fleet AFV Acquisitions for FY 2001 and FY 2002

The Treasury Department supports the goals of the EPAct and EO13149 and has encouraged its bureaus to comply with their requirements to the maximum extent possible, including their exempt vehicles.  There are several significant challenges inherent in meeting these goals, however:

- Insufficient availability of AFV’s suitable for the intended mission,  whether from GSA, a commercial lease, or directly from the manufacturer;

- GSA is the first choice for covered vehicles.  If the required AFV’s are not available, commercial leasing costs are a significant impediment even if the required vehicles are available;

- The additional incremental cost of the vehicles; which can be significant and must be covered from appropriated funds;

- The Treasury fleets neither start from the same location nor return to the same location each day, making them dependent on commercial facilities for refueling.  Only the vehicles on the Federal Law Enforcement Training Center campuses (both outside of MSA’s) and some USSS high-speed training vehicles (which are not licensed and never leave the campus) are capable of being centrally fueled;

- Where fuel may be available from a public utility or municipal government, each one has its own payment system or billing process, and a separate agreement must be established with each one.  Different fueling systems also exist for CNG and the vehicles must use compatible sites or carry adapters;

- Lack of easy availability of alternative fuels and the added time to drive to and return from a fueling site; and

- Resale value, as all Department-owned vehicles are replaced using exchange/sale procedures to help reduce the need for appropriated funds when replacing the vehicle.

# Petroleum Savings

It is difficult, if not impossible, to project petroleum savings for FY 2002 and FY 2003 based upon the estimated AFV availability and acquisitions, improvements in fuel economy, and fleet efficiency. FY 1999 baseline is being reported as the baseline year for petroleum usage, with a total of 853,529 gallons. Usage in 2001 was 810,623 gallons, a decrease of 5.15% from FY 1999.   Potential petroleum savings for FY 2002 and FY 2003 are projected as 85,000and 95,000 gallons respectively.

# Summary

As detailed in this report, Treasury acquired, to the extent possible, AFVs in accordance with the EPAct for FY 2001 and projects an improved level of compliance in FY 2002. The Treasury Department will continue to implement its strategy for complying with the requirements of Executive Order 13149, with the goal of at least a 20 percent reduction in the fleet’s annual petroleum consumption in FY 2005.  This will be done by:

- Encouraging the bureaus to acquire the most fuel-efficient vehicle suited for the task;

- Urging that the number of miles driven by the bureaus be reduced by:

  - Consolidating trips;

  - Using taxis or public transportation  to the maximum extent possible;

  - Where possible, meeting electronically rather than face-to-face; and

- Reviewing bureau acquisitions and GSA vehicle assignments for areas of improvement.

Appendix

|  | Department of the Treasury |  | AFV Acquisition Report for FY 2001 |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Acquisitions |  |  |  |  |
|  |  | Converted | Leased | Purchased | Total | Total Stock |
| 1 | Total # of vehicles acquired | xxxxxx | 420 | 2271 | 2691 | 19706 |
| 2 | Exempt as law-enforcement or national-security vehicles | xxxxxx |  | 2271 | 2271 | 16449 |
| 3 | Exempt due to geographic placement | xxxxxx |  |  | 0 | 150 |
| 4 | EPAct "covered fleet" vehicles (line 1 - (line 2 + line 3) (No double-counting of vehicles in lines 2 and 3.) | xxxxxx | 420 | 0 | 420 |  |
| 5 | E85 flex-fuel vehicles |  | 49 |  | 49 | 176 |
| 6 | Dedicated ethanol vehicles |  |  |  | 0 |  |
| 7 | M85 flex-fuel vehicles |  |  |  | 0 |  |
| 8 | Dedicated methanol vehicles |  |  |  | 0 |  |
| 9 | CNG dual-fuel vehicles |  | 1 |  | 1 | 4 |
| 10 | CNG dedicated vehicles |  |  |  | 0 | 2 |
| 11 | LNG dual-fuel vehicles |  |  |  | 0 |  |
| 12 | LNG dedicated vehicles |  |  |  | 0 |  |
| 13 | Propane/LPG dual-fuel vehicles |  |  |  | 0 |  |
| 14 | Propane/LPG dedicated vehicles |  |  |  | 0 |  |
| 15 | Dimethyl ether dedicated vehicles |  |  |  | 0 |  |
| 16 | Electric vehicles (dedicated) -- ZEV |  |  |  | 0 |  |
| 17 | Hydrogen dedicated vehicles -- ZEV |  |  |  | 0 |  |
| 18 | Credits claimed from medium-duty vehicle acquisitions (report separately) |  |  |  | 0 |  |
| 19 | Credits claimed from heavy-duty vehicle acquisitions (report separately) |  |  |  | 0 |  |
| 20 | Credits claimed from ZEV (hydrogen and electric) vehicle acquisitions |  |  |  | 0 |  |
| 21 | Total AFVs and credits (sum of lines 5-20) | 0 | 50 | 0 | 50 | 182 |
| 22 | AFV percentage of EPAct covered fleet acquisitions (line 21 ÷ line 4 × 100) |  | 12% | 0% | 12% | 0 |
|  | Submitting official: Date: |  |  |  |  |  |
| ________________________ | Address: Phone: |  |  |  |  |  |
| ____ __________________________ | e-mail: |  |  |  |  |  |