SOIL SURVEY FEATURES

| SOIL DELINEATIONS AND LABELS |  |
| --- | --- |
| Limit of soil survey (label) and/or denied access area | Label |

STANDARD LANDFORM AND

MISCELLANEOUS SURFACE

FEATURES

| Bedrock escarpment |  |
| --- | --- |
| Non-bedrock escarpment |  |
| Gully |  |
| Levee |  |
| Short steep slope |  |
| Blowout |  |
| Borrow pit |  |
| Clay spot |  |
| Closed depression |  |
| Gravel pit |  |
| Gravely spot |  |
| Landfill |  |
| Lava flow |  |
| Marsh or swamp |  |
| Mine or quarry |  |
| Miscellaneous water |  |
| Perennial water |  |
| Rock outcrop |  |
| Saline spot |  |
| Sandy spot |  |
| Severely eroded spot |  |
| Sinkhole |  |
| Slide or slip |  |
| Sodic spot |  |
| Spoil area |  |
| Stony spot |  |
| Very stony spot |  |
| Wet spot |  |

AD HOC FEATURES

| SFP | 1 |  |
| --- | --- | --- |
|  | 2 |  |
|  | 3 |  |
| DUR | 4 |  |
|  | 5 |  |
| FUM | 6 |  |
|  | 7 |  |
|  | 8 |  |
|  | 9 |  |
|  | 10 |  |
|  | 11 |  |
|  | 12 |  |
| BOM | 13 |  |
|  | 14 |  |
|  | 15 |  |
|  | 16 |  |
|  | 17 |  |
|  | 18 |  |
|  | 19 |  |
| BCH | 20 |  |
|  | 21 |  |
|  | 22 |  |
|  | 23 |  |
| ALD | 24 |  |
|  | 25 |  |
| SAS | 26 |  |
| TYP | 27 |  |
|  | 28 |  |
|  | 29 |  |
| SWA | 30 |  |
|  | 31 |  |
|  | 32 |  |
|  | 33 |  |
| SER | 34 |  |
| COB | 35 |  |
|  | 36 |  |
|  | 37 |  |
|  | 38 |  |
|  | 39 |  |
| TER | 40 |  |
| SDL | 41 |  |
| DET | 42 |  |
| KIP | 43 |  |
|  | 44 |  |

# CULTURAL FEATURES

(Optional)

| National, state or providence |  |
| --- | --- |
| County or parish |  |
| County or parish |  |
| Reservation (national or state forest or park) |  |
| Field sheet matchline and neatline |  |
| Public Land Survey System Section Boundary |  |
| Public Land Survey System Section Corner Tics. |  |

# TRANSPORTATION

| Divided road Normally not shown |  |
| --- | --- |
| Other road Normally not shown |  |
| Trail Normally not shown |  |

ROAD EMBLEMS

| Interstate |  |
| --- | --- |
| Federal |  |
| State |  |
| County, farm or ranch |  |

# LOCATED OBJECTS

| Airport, airfield |  |
| --- | --- |
| Cemetery |  |
| Church |  |
| Farmstead, house (omit in urban areas) |  |
| Lighthouse |  |
| Located object (Label) |  |
| Lookout tower |  |
| Oil and/or natural gas well |  |
| Other Religion (label) |  |
| School |  |
| Soil sample site (compiled only not published) |  |
| Tank (label) |  |
| Windmill |  |

# HYDROGRAPHIC FEATURES

(Optional)

Strike though features not used

| Drainage end (indicates direction of flow) |  |
| --- | --- |
| Perennial stream |  |
| Intermittent stream |  |
| Unclassified stream |  |
| Perennial drainage or irrigation ditch |  |
| Intermittent drainage or irrigation ditch |  |
| Unclassified drainage or irrigation ditch |  |
| Flood pool line |  |
| Spring |  |
| Well, artesian |  |
| Well, irrigation |  |

OTHER FEATURES TO INCLUDE

State Coordinate Tics

Geographic Coordinate Tics

Small and medium dams

SPECIAL SYMBOLS FOR SOIL SURVEY AND SSURGO

LABEL	NAME________	DESCRIPTION______________________________________________

BLO	Blowout	A small saucer-, cup-, or trough-shaped hollow or depression formed by wind erosion on a preexisting sand deposit.  Typically _____to _____acres.

BPI	Borrow pit	An open excavation from which soil and underlying material have been removed usually for construction purposes.  Typically ___2__to ___5__acres.

CLA	Clay spot	A spot where the surface layer is silty clay or clay in areas where the surface layer of the named soils in the surrounding map unit is sandy loam, loam, silt loam, or coarser.

DEP	Depression, closed	A shallow, saucer-shaped area that is slightly lower on the landscape than the surrounding area and is without a natural outlet for surface drainage.  Typically _____to _____acres.

ESB	Escarpment, bedrock	A relatively continuous and steep slope or cliff produced by erosion or faulting, which breaks the general continuity of more gently sloping land surfaces.   Exposed material is hard or soft bedrock.

ESO	Escarpment, other	A relatively continuous and steep slope or cliff that generally is produced by erosion but can be produced by faulting, which breaks the continuity of more gently sloping land surfaces.  Exposed earthy material is nonsoil or very shallow soil.

GPI	Gravel pit	An open excavation from which soil and underlying material have been removed and used, without crushing, as a source of sand or gravel.  Typically _____to _____acres.

GRA	Gravelly spot	A spot where the surface layer has more than 35 percent, by volume, rock fragments that are mostly less than 3 inches in diameter in an area of surrounding soil with less than 15 percent fragments.  Typically _____to _____acres.

GUL	Gully	A small channel with steep sides cut by running water and through which water ordinarily runs only after a rain or after ice or snow melts.   It generally is an obstacle to wheeled vehicles and is too deep to be obliterated by ordinary tillage.

LDF	Landfill	An area of accumulated waste products of human habitation that can be above or below natural ground level.  Typically __2___to __5___acres.

LAV	Lava flow	A solidified body of rock formed through lateral, surficial outpouring of molten lava from a vent or fissure.   Often lobate in shape.  Typically _____to _____acres.

LVS	Levee	An embankment that confines or controls water, especially one built along the banks of a river to prevent overflow on lowlands.

MAR	Marsh or swamp	A water-saturated, very poorly drained area, intermittently or permanently covered by water.   Marsh areas are dominantly vegetated by sedges, cattails, and rushes.   Swamps are dominantly vegetated by trees or shrubs.   Not used in map units where poorly drained or very poorly drained soils are the named components.  Typically _____to _____acres.

MPI	Mine or quarry	An open excavation from which soil and underlying material are removed and bedrock is exposed.   Also denotes surface openings to underground mines.  Typically _____to _____acres.

MIS	Miscellaneous water	Small, man-made water area that is used for industrial, sanitary, or mining applications and contains water most of the year.  Typically _____to _____acres.

WAT	Perennial water	Small, natural or man-made lake, pond, or pit that contains water most of the year.  Typically _____to _____acres.

ROC	Rock outcrop	An exposure of bedrock at the surface of the earth.   Not used where the named soils of the surrounding map unit are shallow over bedrock or where "bedrock" is a named component of the map unit.  Typically _____to _____acres.

SAL	Saline spot	An area where the surface layer has an electrical conductivity of 8 mmhos cm-1 more than the surface layer of the named soils in the surrounding map unit, which have an EC of 2 mmhos cm-1 or less.  Typically _____to _____acres.

SAN	Sandy spot	A spot where the surface layer is loamy fine sand or coarser in areas where the surface layer of the named soils of the surrounding map unit is very fine sandy loam or finer.

ERO	Severely eroded spot	An area where on the average 75 percent or more of the original surface layer has been lost because of accelerated erosion.  Not used in map units with component phases that are named severely eroded, very severely eroded, or gullied.

SLP	Short, steep slope	Narrow soil area that has slopes that are at least two slope classes steeper than the slope class of the surrounding map unit.

SNK	Sinkhole	A closed depression formed either by solution of the surficial rock or by collapse of underlying caves.  Typically _____to _____acres.

SLI	Slide or slip	A prominent landform scar or ridge caused by fairly recent mass movement or descent of earthy material resulting from failure of earth or rock under shear stress along one or several surfaces.  Typically _____to _____acres.

SOD	Sodic spot	An area where the surface layer has a sodium adsorption ratio that is at least 10 more than the surface layer of the named soils in the surrounding map unit, which have a sodium adsorption ratio of 5 or less.  Typically _____to _____acres.

SPO	Spoil area	A pile of earthy materials, either smoothed or uneven, resulting from human activity.  Typically _____to _____acres.

STN	Stony spot	A spot where 0.01 to 0.1 percent of the surface is covered with rock fragments that are greater than 10 inches in diameter in areas where the surrounding soil has no surface stones.  Typically _____to _____acres.

STV	Very stony spot	A spot where 0.1 to 3 percent of the surface is covered with rock fragments that are greater than 10 inches in diameter in areas where less than 0.01 percent of the surface of the surrounding soil is covered with stones.  Typically _____to _____acres.

WET	Wet spot	A somewhat poorly drained to very poorly drained area that is at least two drainage classes wetter than the named soils in the surrounding map unit.  Typically _____to _____acres.

AD HOC SYMBOLS

For

Pacific Southwest MLRA Region 2

04/01

LABEL	NAME________	DESCRIPTION____________________________________________________

BCH  20	Beaches	A gently sloping zone, typically with a concave profile, of unconsolidated material extending landward from the low-water line to the place where there is a definite change in material or physiographic form (such as a cliff)

BOM   13	Bomb crater	A bowl shaped hole in the ground between 10 to 25 feet in diameter and between 7 and 15 feet deep caused by aerial bombs or naval guns.  Typically .05 to .10 acres.

COB   35	Cobbly spot	Surface layer has more than 35 percent, by volume, of rock fragments 3 to 10 inches in diameter in areas where less than 0.01 percent of the surface of the surrounding soil is covered with cobbles.  Typically 0 to 5 acres.

DET   42	Detrimental deposits	Areas of spreading or deposits of cement dust, cement, or other types of materials that, when on the surface, inhibit the growth of plants, and make classification of the underlying soil impractical.  Typically 0 to 5 acres.

DUR   4	Duripan	The duripan is a subsurface horizon that is cemented by illuvial silica to the degree that is less than 50 percent of the volume of air-dry fragments that slake in water or during prolonged soaking in acid (HCL). Typically 0 to 5 acres.

FUM   6	Fumarole	A volcanic vent emitting steam or gases, or any other localized expression of geothermal dynamics. Typically 3 to .6 acres.

KIP   43	Kipuka	An island in the midst of a lava flow that escaped burial by the flowing lava because the lava was diverted around it.  Typically .5 to 1.0 acres.

SAS   26	Saline sodic spot	Surface layer with a sodium adsorption ration that is 10 or more and an electrical conductivity of 8 decisiemens more than the surface layer of the named soils in the surrounding map unit, which has a sodium adsorption ratio of 5 or less and which has and EC of 4 decisiemens/meter or less.  Typically 0 to 5 acres.

SDL  41	Sandy loam surface	A spot where the surface layer is sandy loam in areas where the surface layer of the named soils of the surrounding map unit is loamy fine sand or coarser.  Typically 0 to 5 acres.

SWA   30	Seasonal water table	A water table which has been altered by seepage from irrigation.  Not used where the major components have the same characteristics.  Typically 0 to 5 acres.

SER   34	Serpentine outcrop	An exposure of serpentinitic bedrock at the surface of the earth. Not used where the named soils of the surrounding map unit are shallow over bedrock.  Typically 0 to 5 acres.

SFP   1	Short, flat slope	Narrow soil area that has slopes that are at leas 2 slope classes less than the slope class of the surrounding map unit. Typically 0 to 5 acres.

TER   40	Terrace remnant	A fan remnant or stream terrace that remains or is left standing above the general land surface after erosion has reduced the surrounding area.  Typically 0 to 5 acres.

TYP   27	Series Type Location	Location of the soil series typical pedon.

ALD   24	Alluvial Deposit	Deposits of alluvial material too small to be delineated

surrounded by non-alluvial areas