WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A13534 | In-Flight Anomaly Number -- | Contractor Report Number E-143 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TRANSDUCER FAILED INSULATION RESISTANCE IN-PROCESS CHECK |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl N | Misc Codes A (1) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE GH2 ULL PRES TRNSDCR | PART# PD7400098-089 | SER/LOT# 2302 | MANUFACTURER GULTON SERV |
| Test/Operation L - FLD | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EL - SHORT | Cause U - UNKNOWN |
| System ELECTRICAL | Defect EP - ELVAL | Material B - CIRCBD | Work Contact J. ADAMS | Fail Date 02/21/1991 |
| Received at MSFC 02/25/1991 | Date Isolated 02/22/1991 | FMEA Reference 3.4.1.2 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EL - SHORT | Time Cycle -- |
| Effectivity Text PROBLEM CLOSED 04/23/91 |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 03/07/1991 | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary CAUSE UNKNOWN - AMONG THE POSSIBLE CAUSES ARE: HANDLING DAMAGE PRIOR TO OR DURING INSTALLATION OF THE TRANSDUCER; AND WORKMANSHIP ERROR DURING MANUFACTURE OF THE TRANSDUCER |
| Last MSFC Update 01/11/1995 | CN RSLV SBMT 03/26/1991 | Defer Date -- | Add Date 02/26/1991 | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| Approval |
| Design R. MOYE | Chief Engineer M. PESSIN | S & MA R. JACKSON | Project -- | Project MGR G. LADNER |
| PAC Assignee T. HESTER | PAC Review Complete TH | MSFC Closure Date 04/23/1991 | Status C - CLOSED | F/A Completion 03/21/1991 |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID MARS; T-116883 & T-116884 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary CLOSED AT CONTRACTOR, 3/18/91. REVISED BY CONTRACTOR, 3/26/91 |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description THE LH2 ULLAGE PRESSURE TRANSDUCER FAILED AN IN-PROCESS CHECK OF INSULATION RESISTANCE THE PRESSURE TRANSDUCER FAILED THE INSULATION RESISTANCE TEST STEP OF THE WIRE HARNESS SPLICE TEST TP-7J01-FT. THE UNIT HAD AN INSULATION RESISTANCE OF APPROXIMATELY 3 MEGOHMS AT 50VDC. THE REQUIREMENT IS A MINIMUM OF 20 MEGOHMS AT 50 VDC NOTE: THE TRANSDUCERS ARE LIMITED LIFE CONTROLLED |
| Contractor Investigation/Resolution |
| MSFC Response/Concurrence TASK I. FAILURE INVESTIGATION A FAILURE ANALYSIS WILL BE PERFORMED ON THE TRANSDUCER AND DOCUMENTED ON THE COMPONENT LEVEL MARS, T-116884 ECD: MARCH 7, 1991 COMPLETE: MARCH 12, 1991 CLOSURE STATEMENT FAILURE ANALYSIS TRACED THE LOW INSULATION RESISTANCE TO THE INTERNAL MECHANISM OF THE TRANSDUCER. THE RESISTIVE ELEMENT OF THE POTENTIOMETER HAD LOW RESISTANCE TO THE ANODIZED ALUMINUM MOUNTING BLOCK NEAR THE LEAD WIRE ATTACHMENT. THE TRANSDUCER HAD NOT BEEN IMPROPERLY TESTED AT MAF; NO MORE THAN THE ALLOWED 50 VDC HAD BEEN USED IN MEGOHMMETER TESTING THERE WAS A SMALL DENT ON THE FACE OF THE FLAIRED TUBE FITTING WHICH INDICATED A MINOR IMPACT HAD OCCURRED. THERE WAS INSUFFICIENT INFORMATION AVAILABLE TO IDENTIFY THE CAUSE OF FAILURE. AMONG THE POSSIBLE CAUSES WERE HANDLING DAMAGE DURING INSTALLATION ON THE ET AND/OR A WORKMANSHIP PROBLEM DURING MANUFACTURE OF THE TRANSDUCER (REF. FAILURE ANALYSIS T-116884) TASK CLOSED TASK II. CORRECTIVE ACTION NO CORRECTIVE ACTION IS REQUIRED. THIS IS THE FIRST OCCURRENCE OF A RESISTIVE ELEMENT INSULATION RESISTANCE FAILURE IN THE PD7400098 SERIES A TOTAL OF 832 TRANSDUCERS HAVE BEEN DELIVERED TO MAF. THERE ARE ADEQUATE TESTS IN THE ET BUILD CYCLE AND AT KSC TO ASSURE PERFORMANCE TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES THIS IS AN EXPLAINED CLOSURE OF THE CAPS ALL ETS CLEARED. THE TRANSDUCER FAILED THE FIRST OF FOUR TESTS OF INSULATION RESISTANCE PERFORMED AT MAF. ALL DELIVERED ETS HAVE PASSED THE INSULATION RESISTANCE TESTS. IN THE EVENT A TRANSDUCER IS REPLACED AT KSC, THE INSULATION RESISTANCE IS TESTED FOLLOWING INSTALLATION THE INSULATION RESISTANCE TESTS AT MAF ARE AS FOLLOWS: TP-FJ07-FT PERFORMED AT THE TIME OF SPLICING THE TRANSDUCER TO THE ET WIRING TP-7C07-FA PERFORMED FOLLOWING COMPLETION OF ELECTRICAL COMPONENT INSTALLATIONS IN THE FINAL ASSEMBLY AREA TP-6C104/204-AT PERFORMED DURING FINAL ACCEPTANCE TESTING IN BUILDING 420 TP-6D101-AT PERFORMED AS THE LAST ELECTRICAL TEST IN BUILDING 420 THE TEST AT KSC IS PERFORMED AT THE TIME OF SPLICING THE LH2 TRANSDUCER TO THE ET WIRING. IT IS REQUIRED BY OMRSD FILE IV, APPENDIX "C", "LINE REPLACEABLE UNIT RETEST REQUIREMENTS", TCN000.170, "LH2 TRANSDUCER IR CHECK" TASK CLOSED TASK IV. CLOSURE SUMMARY THIS IS AN EXPLAINED CLOSURE OF THE CAPS THE ROOT CAUSE OF THE FAILURE COULD NOT BE DETERMINED. AMONG THE POSSIBLE CAUSES ARE HANDLING DAMAGE PRIOR TO/DURING INSTALLATION AND WORKMANSHIP ERRORS DURING MANUFACTURE OF THE TRANSDUCER. THIS IS THE FIRST OCCURRENCE OF AN INSULATION RESISTANCE FAILURE IN THE PD7400098 TRANSDUCER SERIES DUE TO A FAILURE IN THE POTENTIOMETER RESISTIVE ELEMENT. A TOTAL OF 832 TRANSDUCERS OF THIS SERIES HAVE BEEN DELIVERED TO MAF. THERE SUFFICIENT TESTS IN THE ET BUILD CYCLE TO ASSURE PERFORMANCE OF THE VEHICLE. NO CORRECTIVE ACTION IS REQUIRED TASK CLOSED 02/26/91: DEFERRAL RATIONALE THIS PROBLEM REPORT IS DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 07700, VOLUME XI, PARAGRAPH 3.4.1, ITEM C AND NSTS 08126, REV. D, PARAGRAPH 3.3.10.1, ITEM D WHICH STATES, "THE PROBLEM CONDITION IS CLEARLY SCREENED BY PREFLIGHT CHECKOUT OR SPECIAL TESTS (I.E., FAILURE MODE SHOULD NOT OCCUR FOLLOWING THE TEST)." ***APPROVED BY ET PROJECT MANAGER, G. LADNER ON 02/26/91*** 4/23/91 - CLOSED IN MSFC PRACA DATABASE |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A13534 | IFA# -- | Contractor RPT# E-143 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400098-089 | Asmnt Part Name GH2 ULL PRES TRNSDCR | Asmnt Serial/Lot# 2302 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD U - UNKNOWN | FAIL MODE EL - SHORT |
| Asmnt FMEA 3.4.1.2 | Asmnt FM 2 | FMEA CSE AA | FMEA SCSE N/A |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |