SPECIAL SPECIFICATION

SECTION 10612

CLEAN ROOM METAL WALL SYSTEMS

Page

PART 1 - GENERAL

1.01  Summary 	2

1.02  Quality Assurance 	2

1.03  Submittals.	2

1.04  Delivery, Storage and Handling 	3

PART 2 - PRODUCTS

2.01  General 	4

2.02  Materials.	4

PART 3 - EXECUTION

3.01  Preparatory Work.	6

3.02  Installation.	6

3.03  Cleaning 	6

SPECIAL SPECIFICATION

SECTION 10612

CLEAN ROOM METAL WALL SYSTEMS

PART 1 - GENERAL

1.01   	SUMMARY

A.  	Section includes materials, equipment and services necessary to fabricate and erect the clean room metal wall systems.

B.  	Clean room metal wall systems shall include studless wall panel system, 1/2-inch batten clean room panel system, doors, door frames and door hardware, electrical cutouts and electrical boxes and wireways, return air grilles, glazing and glazing strips, all trim members for both systems and all gasketing and sealants necessary to maintain the light, air and sound requirements and clean facility integrity of the installation.

1.02   	QUALITY ASSURANCE

A.  	Manufacturer's Representative:  Install under the direct supervision of material manufacturer's technical representative.

B.  	Qualifications of Installer:  Manufacturer or an installer previously approved, trained and authorized by the manufacturer.

C.  	Comply with recommendations of manufacturers of materials included in Work.

1.03   	SUBMITTALS

A.  	Submit in accordance with the provisions of Section 01300.

B.  	Shop Drawings:  Indicate floor plans, elevations (showing panel joint locations), sizes and details of all components, door frames, trim, connections, anchor spacing, cut-out details, wall furring system, material finishes and method of installation.  Catalog cuts not acceptable.

C.  	Product Data:  Data shall indicate manufacturer's name, product names and sufficient literature and data to establish product's conformance with the requirements of this Section.

D.  	Samples:

1.  	Include a one foot by one foot sample of each type of panel unit and one sample of each component.

2.  	Palette of coating colors.

E.  Certificate:  Certify that proposed materials meet or exceed specified requirements.

F. 	 	Maintenance Data:  Submit data indicating material manufacturer's maintenance recommendations.

1.04   	DELIVERY, STORAGE AND HANDLING

A.  	Delivery:

1.  	Do not deliver material to project site sooner than 30 days prior to installation.

2.  	Deliver materials in manufacturer's original unopened and undamaged containers and packages.

B.  	Storage:

1.  	Store materials in a clean, dry area, under cover, on raised platforms, and in original containers or packages.

2.  	Store materials in accordance with manufacturer's recommendations.

C.  	Handling:  Handle materials in such a manner to prevent damage.

D.  	Protect materials from:

1.  	Dirt, oil and other contaminants.

2.  	Extreme temperatures.

3.  	Moisture, including condensation.

E.  	Follow other recommendations of material manufacturers.

PART 2 - PRODUCTS

2.01   	GENERAL

A.  	Material specified herein is manufactured by Plascore, Inc.  Materials conforming to the requirements specified herein manufactured by an approved equal will be considered.

2.02   	MATERIALS

A. 	Studless wall system (2 inch) shall consist of aluminum honeycomb core faced on both sides with 0.032 inch aluminum sheets.  Adhesive to be thermoset modified epoxy, non-outgassing.

B.  	Batten wall system shall consist of 1/2-inch standard clean room panel of aluminum honeycomb core faced on both sides with 0.032 inch aluminum sheets.  Adhesive to be thermoset modified epoxy, non-outgassing.

C.  	Accessories:

1. 		Studless Wall System:  Provide all accessories such as, but not limited to, standard head and floor tracks, battens, H-splices, splice plates, corner tubes, gaskets, glazing frames, return air grilles and electrical components, all as required for a complete installation.

2.  	Batten Wall System:  Provide all accessories such as, but not limited to, trim members, inside and outside corner members, battens and caps, gaskets, glazing frames, shims, all as required for a complete installation.

3.  	Metal Furring Channels:  Galvanized, 20 gauge minimum, face width 1-3/8 inch x 7/8 inch depth.

D.  	Doors, Frames and Hardware:  Provide manufacturer's standard materials.  Doors and frames to be integrally sealed.  Hardware specified in Section 08710.

E.  	Glazing specified in Section 08800.  Provide Santoprene thermoplastic rubber glazing gasket.

F.  	Finishes:

1.  	Clean Room Wall Panel Systems:  Finish panels with a roll-coated conductive epoxy.  Color to be selected by A/E.

2. 		Aluminum tracks, trim, closures, doors and door frames, grilles and other exposed aluminum surfaces to be given a fluoropolymer paint coating (PVDF Kynar 500) conforming to AAMA 605.2.  Color to be selected by A/E.

PART 3 - EXECUTION

3.01    	PREPARATORY WORK

A.  	Prior to commencing work, thoroughly examine all underlying and adjoining work, surfaces and conditions upon which work is in any way dependent for perfect results.

B.  	Report all conditions which affect work.

C.  	No "waiver of responsibility" for incomplete, inadequate or defective underlying and adjoining work, surfaces and conditions will be considered, unless notice of unsatisfactory conditions has been filed and agreed to in writing before work begins.

D.  	Commencement of work constitutes acceptance of surfaces.

E.  	Machine door frames to receive finish hardware.

3.02   	INSTALLATION

A.  	Install clean room metal wall systems in accordance with reviewed shop drawings and manufacturer's recommendations.

B.  	Assemble all components into a rigid structure with tight straight line joints.

C.  	Completed installation free of exposed fasteners.

3.03   	CLEANING

A. Thoroughly clean components in accordance with manufacturer's recommendations.

B.  	Touch-up scratches with manufacturer's touch-up paint in a manner acceptable to the SDR.

END OF SECTION