D19H & D20 Test Preparation Goals and Options

More voltage tap channels (priority=1):

| Option | Plus | Minus |
| --- | --- | --- |
| No change: | No hassle, no risk. | Lose info on failure location. |
| Add wires: | No risk to present system. | More heat load, difficult. |
| Replace “1.8K direct wires” with bronze: | Less heat load to 1.8K reservoir. | Some new technology risk. |
| Replace all V-tap wires with bronze. | Min. heat-load to both reservoirs; Improved hook-up convenience. | Maximum new technology risk. |

Diagnostic Wiring Requirements:

Need more wires, but less heat-load (goal: < 10W to 4.3K,  < 1W to 1.8K).

Helium-gas sealable @ 300K.

Helium II sealable @ 1.8K.

Flexible and strong enough to pull in new wires as the old wires are removed.

Rugged enough to last many years without maintenance.

Sufficient kind and # of wires to meet future magnet requirements.

Insulation (relative to ground): 1 KV (air regions); 7KV (helium regions).

Heater wires large enough to deliver 80% of stored voltage to 3 ohms at 300K.

Spare wires (10%).

Modular enough to permit partial replacement of damaged modules in the future.

Easy magnet disconnect.

Easy cryostat removal

Maximum Cryostat Diagnostics:

| Location | 4-wire | 2-wire | Total Wires |
| --- | --- | --- | --- |
| Vacuum | T5/6/7, JT-Heater2 | 0 | (16)4 |
| LL1 | T1/2/3/4, LL11 | 0 | (20)4 |
| LL2 | T10/11, LL21 | 0 | 12 |
| LL3 | T22/23/24/25/26/28/29, LL31, 2-Heaters2 | 0 | 40 |
| LL4 | T9, LL41, [LL4S1]3, [GaLo]3, [GaHi]3 | 0 | 20 |
| Magnet | T30-39 (Mag, 5 splices, 4 pole gauges) | [2-microphone] | 44 |
| Total | 37 x 4 | 2 x 2 | 116+ (36) |

LHe sensors require 75 mA dc.

Requires 25 Wdc: 100 ohm heaters require 50 V @ 0.5A, 1K ohm heaters require 160 V @ 0.16A.

[xxx] = optional back-up (can be borrowed).

(xx) = old feed thru.

Maximum Diagnostic Wire Requirements:

Magnet

Voltage

Tap

Cryostat

Monitor

Strain

| Gauge | Heater Supply | Heater Monitor |
| --- | --- | --- |
| Present |

47

26 Ga. Cu

128 + (36)

26 Ga. Cu

Shared

(Cryo)

Shared

(Vtap)

Shared

| (Vtap) |
| --- |
| LBQF1 | 7 | 128 (32 x 4) | 0 | (2x2)x4 = 16 | 2x2 = 4 |
| LBQF2 | 69 | 128 (32 x 4) | 22 x 4 = 88 | (4x2)x2 = 16 | 4x2 = 8 |
| D20 | 72 | 152 (38 x 4) |

16x4 = 64

| (8 pole4 + 8 end-cell) | (4x2)x2 = 16 | 2x2 = 4 |
| --- | --- | --- |
| Proposed |

1001

32 Ga. P-Cu

1922 + (36)

32 Ga. P-Cu

Shared

(Cryo)

16

26 Ga. Cu3

Shared

(Vtap)

10 bundles of 5 twisted-pairs/bundle, individually potted within its own Teflon tube.

6 bundles of 16 twisted-pairs/bundle, individually potted within its own Teflon tube (PG3-8).

4.3K intercept provided.

The 8 inner pole gauges exit at the return-end and are not counted in this summary.

Magnet Diagnostic Amplifier Requirements:

Diagnostic Goals:

Locate quench origins.

Verify proper heater operation.

Locate fast motions: coil, axial position, & azimuthal angle.

Measure splice voltages.

| Magnet | Voltage | Derivative | Imbal. | Iheater | Vheater | Totals |
| --- | --- | --- | --- | --- | --- | --- |
| Range | (See below) | 100-500V/s | 50mV | 100A | 500V | n.a. |
| LBQF1 |

4 coils (250V)

Vmag (500V)

2-leads (2V).

4 coils

1 seg/coil

= 4

T-B

1-2

3-4

Ih6,7

|  | Vh6,7 |
| --- | --- |

11 volts.

4 deriv.

3 imbal.

Total=18

LBQF2

4 coils (250V)

Vmag (500V)

2-leads (2V).

4coils

17 segs/coil

<= 68

T-B

1-2

| 3-4 | Ih1,2,3,4 | Vh1,2,3,4 |
| --- | --- | --- |

15 volts.

68 deriv.

3 imbal.

Total=86

D20

8 coils (250V)

Vmag (500V)

2 leads (2V)

8 splice (10mmV).

4 coils

15 segs/coil

= 60

T-B, 1-2, 3-4.

1i-o, 2i-o,

3i-o, 4i-o.

| Q-A (13). | Ih1,2,3,4 | Vh1,2,3,4 |
| --- | --- | --- |

19 volts.

60 deriv.

20 imbal.

8 microV.

Total=107

DiagnosticWiring Implementation

Polyimide-insulated, 32 Ga. P-Cu, twisted-pair wires.

Multiple wires within Teflon tubing (voltage isolation & sealing ease).

Soft epoxy potted-in-tubing (warm-flexible internal helium seal).

2-Way vacuum potting, with labeled/prestripped wires & extension tubes.

3” long, greased 1.8K helium plug .

Swaged-RTV 300K helium plug.

Terminal strip patching, lead-ins to magnet extension-cords, 1.5” centers.

Strain-reliefs for module ends.

Mylar-sheet pin protectors under and between T-strips.

7’ umbilical extension cords plug into male pin connectors on the magnet.

Low-voltage warm interface:  standard 32-pin Amphenol (6).

Low-voltage magnet interface:  100 pin Hypertronics (1).

High-voltage warm interface:  50 pin Hypertronics (2).

High-voltage magnet interface:  50 pin Hypertronics (4, skipping rows).

4-Pin heater supply connector with patching T-strip on magnet.

Magnet connectors: inward-facing pins, out-facing solder terminals.

D20 Voltage-Tap and Quench-Heater Penetration-Wiring Specifications

| Feature | V-Monitor | Heater |
| --- | --- | --- |
| # of wires/bundle: | 10 | 4 |
| # of bundles: | 10 | 1 |
| Wire size: | #32, twisted, solid (P-Cu). | #18 Cu |
| Insulation: | Teflon protected polyimide. | Same |
| Warm connections: | Shielded terminal-strip array. | Same |
| Cold connections: | Circum. terminal-strip array. | Same |
| Connector labels: |

Section ID [Loc# from pole]

(D2C7, Q4A2, Q1B5, D1D8).

Section ID

| (D2C, Q4A) |
| --- |
| dB/dt noise: | Individually twisted bundles. | Same |
| Electro-static noise: | Shielded (cryostat to amplifier). | Same |
| 300K helium seal: | Swaged RTV epoxied tubes. | Same |
| 1.8K helium seal: | RTV sealed/Teflon plug. | Same |
| 300K heat-intercept: | Cold-vapor counter-flow. | Spiral |
| 4.3K heat-intercept: | 3” insul. coincident with He-II seal. | Spiral |

Voltage-Tap Wiring Panel Layout

Features:

Array layout via terminal-strips (for easy re-wiring).

Far-apart taps (higher voltage) are generally farther apart.

Array element labels are the 1-100 as on the SHV patch-panel.

Easy labeling alternative: compatible with any magnet less than (or equivalent to) a 2-layer quad, or a 4-layer dipole.

Voltage isolation = 7KV (warm air).

Cover to protect fragile wiring/pins.

Quench-Heater Wiring Panel Layout

Features:

Two independent power supplies

Two 2-wire I-supply sets (#18-stranded, Cu).

Two 8-wire V-monitor sets (#32-solid, P-Cu).

Series/parallel connection capability at cold end.

Easy interface to present Quench-Heater PS.

Labeling scheme consistent with V-Tap scheme, permitting easy ID of heater location.

Terminal-strip hook-up flexibility.

Hardware Layout

Plumbing Changes:

| Old | New | Reason |
| --- | --- | --- |
| 2” Elbow to lift-plate: | 2” Tee + 1”RL | Diag. wires access. |
| Hi-V tree: | P-gage R-L | Better usage. |
| 10psi R-V tree (El+Tee+El) |

Turned upside-down.

Tee+El.

No H2O danger.

Fewer joints.

20psi R-V tree (Tee+Tee+Tee)

Turned upside-down.

Tee+Tee

No H2O danger.

| Fewer joints. |
| --- |
| 25psi lift-plate riser | Shorten | Reduce moment. |

LHe Displacer Requirements:

| Requirement | Implication |
| --- | --- |
| LHe displacement: | Leak-free containers. |
| Substantial reduction in LHe volume: | Close or nested cylinders, as long as practical. |
| Low heat-capacitance: | Substantially empty. |
| No explosion danger: | Small energy containment capability. |
| Competitive with LHe costs: | 3-4 $/liter. |
| Rugged, durable, reusable: | Tough, abuse-tolerant skin/housing. |
| No danger to refrigerator: | No dust generation. |
| No danger to magnet wiring: |

Relatively easy insertion.

| Light weight. |
| --- |
| Repairable: | Resealable. |
| Minimal pump/purge contamination: | Minimal virtual leaks. |

LHe Displacer Solutions:

| Feature | Stacked-Cylinder Vacuum Logs |
| --- | --- |

Hollow Sphere

| Filled-Logs | Hollow Sphere Insert | Vacuum Insert |
| --- | --- | --- |
| Cylinder shapes: | Hex-packed tubing. | Welded aluminum skins. |

Two.

Concentric.

Two, SS.

| Concentric. |
| --- |
| Low-cost skin: | Multiple 2” Conduits. | Rolled, thin wall skin. | Same | Same, but thicker. |
| Low heat capacitance: | Empty | Predominantly filled with hollow balls. | Same | Vacuum |
| Rugged: | Metal tubes. | Vacuum-potted, reinforced epoxy. | Same | Vacuum |
| Low-cost filler: | Empty | Silica/epoxy/hollow ball composite. | Same | Vacuum |
| Leak-free ends: | Spring-loaded, teflon lift-plate. | Epoxy-sealed welds. | Same | Flange |
| Small stored energy: | Pressure-relief valves. |

Epoxy-sealed hollow balls.

| Thin-wall pres. relief. | Same | None |
| --- | --- | --- |

LHe Displacer Solutions:

Stacked-Cylinder Vacuum Logs

Hollow Sphere

Filled-Logs

Hollow Sphere

| Filled-Insert | Vacuum -Insert |
| --- | --- |

Warm Diagnostic Wiring Requirements:

Signal Type

Bundles

(#)

Wires (1)

(#/bundle)

Source

(2,3)

Destn.

Remarks

(4,5,6,7,8,9)

High

| Volts | 10 |
| --- | --- |

10

| H.V. Teflon | Lower/small V-tap box |
| --- | --- |

SHV-out panel

(SV35)

Twisted within bundles.

E.S shielded.

| 1 KV (bundle-bundle). |
| --- |
| Heater | 2 |

10

| 4-16 Ga. | Upper/large diag. box |
| --- | --- |

Heater patch-panel

(SV-60)

!6 Ga: (2 twisted pair).

Twist with twisted 10-wire.

E-S shielded.

Low

| Volts | 6 | 32 | Upper/large diag. box |
| --- | --- | --- | --- |

Ctrl-Rm

(S03, S04)

16 twisted pair.

E.S shielded.

Sensor wire size: 24-28 Ga. (to keep things small and flexible (for easy shielding and assembly).

Cryostat ends: female connector that safely mates to the cryostat’s male (continuous shield).

Protect cryostat connection: against water, dirt, and bumping.

Bundles: Twist as tight as practical within bundles.  Twist bundles lightly within E.S shield.

H.V. Bundles: Protect adequately for 2 KV between bundles, and any bundle to E.S. shield.

E.S. shield:  Cryostat end should be flexible for two feet or more.

Heater- Supply wires: 2-twisted pairs/bundle (16 Ga or larger).

Heater Bundle: Bundle by twisting the twisted 2-pair with the twisted 10-wire.

Electrostatic shields: Flexible at the cryostat; continuous to destination.

Signal Transport Specifications:

| Requirements | Implementation |
| --- | --- |
| Sex convention: |

Signal source = male;    power source = female.

Amplifier output is male only.

Hypertronics block/column numbering convention:

Left to right facing the source (M/J17 at bottom).

Pin 17 reserved for shield.

Diagnostic wiring convention:

Excitation currents before voltages.

Signal before reference; Plus before minus.

| Excitation pins are 1(+) & 2(-) + 4*N (N=0,1,2..). |
| --- |
| 32-pin amp.breakout: | Add new channels as LEMO cable water-falls. |
| Signal “OR-ing” minimization: | Distribute locally processed signals (like Imag, Imbal, Ref) thru a local breakout panel. |
| 4-Pin/2-pin diagnostic flexibility: | No changes or additions needed. |
| Patching cables (6ft): |

70 2-pin/Lemo

25 2-pin/2-pin Amphenol.

25 Lemo/Lemo.

10 Lemo/BNC (single, reference gnded).

10 Lemo/BNC (dual/differrential).

Patching boxes:

Add three Lemos to every available box.

Make & label one as inverting.

Label owner and provide secure repository.

Lemo wiring convention:

Lecroy: sig. = bulkhd male, ref. = bulkhd female.

Reference color = black

Magnet Transport/Restraint Requirements:

| Requirements | Implementation |
| --- | --- |
| Axial displacement (low friction): | Eight, 6” iron wheels on roller bearings. |
| Tranverse displacement (low friction): | Multi-tons (borrowed). |
| Height & vertical angle adjustment: | “Out-rigger” jacks on cart corners. |
| Axial insertion (low friction): | Cam-follower “roller-skis”. |
| Capable of bridging any insertion gaps: | Roller-skis are 48 inches (1st to last roller). |
| Roller peak-pressure reduction: |

Crowned roller-wheels (30”)

| Spring mounted skis.. |
| --- |
| Cart/cryo transition roller safety: | Double roller density at middle of each ski. |
| Parallel skis: | Adjusted when mounted. |
| Seismic constraints: | Welded/slotted barrier bar-stops. |
| Cryo/vac sealing-flange protection: | Teflon bumpers on cart’s rail-extension. |
| Insertion/removal systemt: | Insertion screws;eye-bolt with come-along. |

# Text boxes

300K

4.3K

1.8K

Potted, twisted bundles

Heater wires

Teflon Plug

1.8 K Seal

A

B

C

1

D

2

3

4

5

6

7

8

9

10

TOP

A

B

C

1

D

2

3

4

5

6

7

8

9

10

BOT

A

B

C

D

TOP

V

I

V

I

BOT

Power Supply

Power Supply

Hi-V

Terminal Strips

Lo-V

Terminal

Strips

Lo-V

Heater

Box

P

10 psi R-V’s

20 psi R-V’s

Hi Volts

Box

LL3

LL2

LL1

Cryostat Wall

Cryostat Wall

Cryostat Layouts

Magnet

Displacer

Magnet

Teflon

Epoxy

Sealing details

Vacuum