MSFC PRACA : 2003-02-12 07:54

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A01003 | In-Flight Anomaly Number -- | Contractor Report Number S-035 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title WELD ROD TYPE CO-MINGLED |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (2) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER A |
| HARDWARE NCA | NOMENCLATURE WELD WIRE - WELD ROD | PART# VARIOUS | SER/LOT# N/A | MANUFACTURER VARIOUS |
| Test/Operation X - ALE | Prevailing Condtion -- | F / U UC | Fail Mode -- | Cause -- |
| System STRUCTURAL | Defect MT - TYPE W | Material -- | Work Contact J. FINCHER | Fail Date 11/26/1979 |
| Received at MSFC 01/30/1980 | Date Isolated -- | FMEA Reference 1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom -- | Time Cycle -- |
| Effectivity Text ET AND SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 10/07/1987 | CN RSLV SBMT 10/14/1980 | Defer Date -- | Add Date -- | R/C Codes 2 - MFG -- -- |
| Assignee |
| Design E. BRYAN | Chief Engineer -- | S & MA D. NEWMAN | Project M. PESSIN | Project MGR -- |
| Approval |
| Design J. NICHOLS | Chief Engineer -- | S & MA C. NEWMAN | Project J. ODOM | Project MGR -- |
| PAC Assignee C. NEWTON | PAC Review Complete CN | MSFC Closure Date 10/30/1980 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: MSFC ALERT NO. MSFC-A-79-04 1. THE ALERT REF'ED THE FINDING OF CO-MINGLED INCO 718 WELD ROD WITH INCO 62, INCO 82 OR A SERIES 600 ROD WHICH CAUSED A STRUCTURAL FAILURE ON A SPACE SHUTTLE ENGINE. SUBSEQUENT MSFC DIRECTION HAS EXTENDED THIS ALERT TO ENCOMPASS ALL FUSION WELDING 2. NASA/MSFC LETTER SA32/702-80 IDENTIFIED THAT A LOT OF INCO-718 WELD WIRE AT ARROWHEAD PRODUCTS WAS FOUND TO BE CO-MINGLED BY 15% WITH HAYNES 188 |
| Contractor Investigation/Resolution 1. CAUSE - CONTROLS UNTILIZED BY SOME MANUFACTURERES OR SUPPLIERS OF WELD ROD & WELD WIRE DURING VAIROUS PROCESS STEPS MAY INCREASE THE POTENTIAL FOR CO-MINGLING OF VARIOUS TYPES OF FILLER WIRE 2. RESOLUTION - IMPLEMENTED THE FOLLOWING POSITIVE CONTROLS WHICH ASSURE CORRECT FILLER WIRE TYPE HAS BEEN UTILIZED FOR EACH FUSION WELD ON THE ET. A) REVERIFY ALL 2319 ALUMINUM WELD WIRE/WELD ROD & DOCUMENT. (MAF) B) REQUIRE SAMPLING BEFORE & AFTER WELDING, IF WELD WIRE FROM SPOOLS (MAF) C) IMPLEMENT DC&R ACTIONS AS PERMANENT CHANGE TO EXISTING PROCESS CONTROLS. (REF OD ET/MFG-163) D) STRUCTURAL ENG'RG & QUAL ENG'RG DISPSOTION ALL PRODUCTION WELDS ALREADY COMPLETED. (REF MEMO 80M0-0832, -0620). E) REQUIRE SUPPLIERS PERFORMING FUSION WELDS TO VERIFY FILLER WIRE TYPE PRIOR TO USE & AFTER USE FOR SPOOLS. F) MSFC-STD-655, (STD- WELD FILLER METAL CONTROL OF) CHANGE PROPOSAL TO BE IMPLEMENTED TO INCLUDE SUPPLIER PRODUCT ASSURANCE REQMNT. (ETM-64-119) G) STRUCTURAL ENG'RG PERFORMED AN ANALY OF FACTOR OF SAFETY ON CRIT WELDS & DISPOSITONED SUBJECT WELDS. (REF DC&R P-80-02-ET-6 & MEMO 3723-80-071) H) AUTOMATED METHOD ESTABLISHED TO ACCOMPLISH VERIFICATION OF 2319 FILLER WIRE TYPE AS AN INLINE OPERATION. (REF RFF-7-8-80). I) INVESTIGATED IMPACT IF HAYNESS 188 WERE USED IN LIEU OF THE REQUIRED INCONEL 718. BASED UPON PROOF LOAD TESTS & MARGINS OF SAFETY, THE ENGR'NG ANALY DOES NOT REFLECT ANY STRENGTH DEFICIEN- CIES. (REF MEMO 3512-80-124). EFFECTIVITY - ET-1 & SUBS. 10/30/80 - CLOSURE DISTRIBUTED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A01003 | IFA# -- | Contractor RPT# S-035 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# -- | Asmnt Part Name -- | Asmnt Serial/Lot# -- |
| HCRIT CD -- | FCRIT CD -- | CAUSE CD -- | FAIL MODE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |