MSFC PRACA : 2003-02-12 08:41

MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A16646 | In-Flight Anomaly Number -- | Contractor Report Number E-160 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LOX LEVEL SENSOR FAILURE |
| EICN# -- | ELEMENT ET | Contractor LMMSS | FSCM# -- | FCRIT 1R |
| HCRIT -- | Sys_Lvl -- | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE LRU | NOMENCLATURE -- | PART# -- | SER/LOT# -- | MANUFACTURER -- |
| HARDWARE NCA | NOMENCLATURE LEVEL SENSOR | PART# 74L4-1 & 74L4-2 | SER/LOT# NOTED | MANUFACTURER B. F. GOODRI |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EQ - OUTPUT ERROR | Cause MTP - MFG-TST-INST |
| System ELECTRICAL | Defect CN - CONTAM | Material A - CIRC T | Work Contact JOHN ADAMS | Fail Date 09/26/1995 |
| Received at MSFC 09/26/1995 | Date Isolated 09/25/1995 | FMEA Reference 3.6.1.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location BFG AERO | Symptom EJN - ISOLATION | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date 03/26/1996 | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 01/24/2001 | CN RSLV SBMT 12/28/1995 | Defer Date 09/26/1995 | Add Date 09/26/1995 | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design J. RATLEY | Chief Engineer M. PESSIN | S & MA M. SMILES | Project -- | Project MGR P. COUNTS |
| Approval |
| Design J. RATLEY | Chief Engineer M. PESSIN | S & MA J. GREEN | Project -- | Project MGR C. SUMNER |
| PAC Assignee J. NELSON | PAC Review Complete JMN | MSFC Closure Date 01/25/1996 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID N-902 - N-904 |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description ITEM 1) A 74L4-1 LO2 LEVEL SENSOR (S/N 1701) FAILED THE SUPPLIER ACCEPTANCE TEST (ATP). THE SENSOR FAILED THE INSULATION RESISTANCE TEST FOLLOWING THE THERMAL SHOCK PORTION OF THE ATP ITEMS 2, 3, AND 4) 74L4-2 LH2 LEVEL SENSORS, S/N 2332, 2335, AND 2338 RESPECTIVELY, FAILED THE SUPPLIES ACCEPTANCE TEST (ATP) THE SENSOR FAILED THE INSULATION RESISTANCE TEST FOLLOWING THE THERMAL SHOCK PORTION OF THE ATP CRITICALITY: THE 74L4-1 LOX LEVEL SENSOR IS CRIT. 3 IN ALL POSITIONS ON THE ET FOR LOW INSULATION RESISTANCE. HOWEVER, THE 74L4-1 SENSOR IS VIRTUALLY IDENTICAL TO THE 74L4-2 LH2 LEVEL SENSOR. THE 74L4-2 LEVEL SENSOR IS CRIT. 1R; FMEA ITEM CODE 3.6.1.1; "FAILS WITH FALSE WET SIGNAL." NOTE: THE SENSORS ARE LIMITED LIFE CONTROLLED * REVISION "C" CLOSES ALL TASKS. SEE ASTERISKS |
| Contractor Investigation/Resolution GENERAL: 1) THE 74L4-1 LOX LEVEL SENSOR WAS UNDERGOING THE ACCEPTANCE TEST AT THE SUPPLIER, B. F. GOODRICH AEROSPACE, MILITARY FUEL AND INTEGRATED SYSTEMS DIVISION, IN VERGENNES, VERMONT. THE TESTING IS CONTROLLED BY ACCEPTANCE TEST PLAN-946, REVISION S. THE SENSOR FAILED PARAGRAPH 6.5.3 WHICH REQUIRED THE INSULATION RESISTANCE TO BE EQUAL TO OR GREATER THAN 500 MEGOHMS WITH 500 VOLTS DC APPLIED. THE ACTUAL VALUE OF THE INSULATION RESISTANCE WAS AS LOW AS 150 MEGOHMS AND VARIED WITH THE PASSAGE OF TIME. THE FAILURE OCCURRED SEPTEMBER 25, 1995, AND WAS DOCUMENTED ON NCD N-902 2,3,4) THREE 74L4-2 LH2 LEVEL SENSORS WERE UNDERGOING THE ACCEPTANCE TEST AT THE SUPPLIER, B.F. GOODRICH, MILITARY FUEL AND INTEGRATED SYSTEMS DIVISION, IN VERGENNES, VERMONT. THE TESTING IS CONTROLLED BY ACCEPTANCE TEST PLAN-945, REVISION O. THE SENSORS FAILED PARAGRAPH 6.5.3 WHICH REQUIRES THE INSULATION RESISTANCE TO BE EQUAL TO OR GREATER THAN 500 MEGOHMS WITH 500 VOLTS DC APPLIED THE ACTUAL VALUES OF THE INSULATION RESISTANCE OF THE LH2 SENSORS WERE: 85 MEGOHMS FOR S/N 2332; 9 MEGOHMS FOR S/N 2335; AND 3 MEGOHMS FOR S/N 2338. THE FAILURES OCCURRED OCTOBER 23, 1995, AND WERE DOCUMENTED ON NCD N-904 THE LEVEL SENSOR UTILIZES THE DECREASE IN THE ELECTRICAL RESISTANCE OF A METAL WHEN COOLED TO DETECT THE PRESENCE OF A CRYOGENIC FLUID THE SENSOR USES A GOLD FLASHED PLATINUM WIRE, .0005 INCH IN DIAMETER, AS THE SENSING ELEMENT. THE LEVEL SENSOR SIGNAL CONDITIONER, WHICH IS MOUNTED IN THE ORBITER, PROVIDES A CONSTANT CURRENT TO THE SENSING ELEMENT WHICH CAUSES IT TO RISE IN TEMPERATURE. THE TEMPERATURE AND RESISTANCE OF THE ELEMENT DECREASE RADICALLY WHEN IMMERSED IN A CRYOGENIC LIQUID. THE SIGNAL CONDITIONER DETECTS THE DECEASE IN RESISTANCE AND CONVERTS IT TO A "WET" OUTPUT SIGNAL THE SIGNAL CONDITIONER IS ALSO DESIGNED TO GIVE A "WET" SIGNAL IN THE EVENT OF LOW INSULATION RESISTANCE IN THE LEVEL SENSOR THE SENSOR HAS AN ALUMINUM CASE WHICH IS PRODUCED BY INVESTMENT CASTING. VERY FEW OF THE INTERNAL SURFACES, AND NONE OF THE EXTERNAL SURFACES, ARE FINISH MACHINED FOR DIMENSIONAL CONTROL. THE INTERNAL SURFACES OF THE CASE AND THE COVER ARE PAINTED WITH A SPRAYED-ON, BAKED, TEFLON PAINT. THE PAINT PREVENTS WETTING OF THE CASE, I.E., RETENTION OF CRYOGENIC FLUIDS, AND ALSO PROVIDES SOME ELECTRICAL INSULATION BETWEEN THE CASE AND THE SENSOR ELEMENT THE ELEMENT IS SUPPORTED BY A CERAMIC SUBSTRATE. THE SUBSTRATE HAS FIRED-ON GOLD CIRCUIT PATHS WHICH PROVIDE A MEANS TO TERMINATE THE ELEMENT WIRE BY WELDING. THE SENSOR OUTPUT WIRES ARE ATTACHED TO THE SUBSTRATE BY STEEL TERMINALS HELD IN PLACE WITH RIVETS AND SPRING WASHERS TASK I. FAILURE INVESTIGATION A. THE FAILED 74L4-1 SENSOR, S/N 1701, WAS DOCUMENTED ON NCD N-902 THE NCD WILL BE DISPOSITIONED FOR FAILURE ANALYSIS TO BE PERFORMED AT THE SUPPLIER RESPONSIBILITY: R. RAMSEY/3830 - M. COMBS/3830 J. ADAMS/3741 - D. WESTPHAL/3740 COMPLETE: DECEMBER 19, 1995 * CLOSURE STATEMENT FAILURE ANALYSIS WAS IN PROGRESS ON THE SENSOR WHEN THE FAILURES LISTED BELOW IN I.B. OCCURRED. THE SUPPLIER PERSONNEL THEN VOLUNTEERED THE INFORMATION THAT THIS FAILURE HAD ALSO OCCURRED WHEN THE SENSOR WAS WET. FAILURE ANALYSIS HAD DETECTED NO ANOMALOUS CONDITIONS. THE SENSOR WAS REASSEMBLED TO THE DRAWING REQUIREMENTS AND IT PASSED THE ATP WHEN RETESTED. THIS RESULT CONFIRMED MOISTURE AS THE MOST LIKELY CAUSE OF THE FAILURE B. THE FAILED 74L4-2 SENSORS, S/N'S 2332, 2335, AND 2338 WERE DOCUMENTED ON NCD-904. THE NCD WILL BE DISPOSITIONED FOR FAILURE ANALYSIS TO BE PERFORMED AT THE SUPPLIER RESPONSIBILITY: R. RAMSEY/3830 - M. COMBS/3830 J. ADAMS/3741 - D. WESTPHAL/3740 COMPLETED: NOVEMBER 3, 1995 CLOSURE STATEMENT IMMEDIATELY FOLLOWING THE INSULATION RESISTANCE (IR) TEST FAILURES, THE SUPPLIER PERSONNEL OBSERVED THAT THE SENSORS WERE WET INVESTIGATION FOUND THAT THE METHODS FOR DRYING THE SENSORS FOLLOWING THE CRYOGENIC IMMERSION TESTS PRIOR TO IR TESTING WERE INEFFECTIVE. ALL THREE SENSORS PASSED THE IR TESTING AFTER DRYING THIS TYPE OF FAILURE HAD NOT OCCURRED BEFORE BECAUSE THE TEST PERSONNEL HAD ALWAYS CHOSEN TO STOP TESTING FOR THE DAY FOLLOWING THE CRYOGENIC TESTS. THE SENSORS WERE LEFT IN THE OPEN AIR ON THE WORK BENCH OVERNIGHT. THIS RESULTED IN THE SENSORS BEING COMPLETELY DRY WHEN THE IR TEST STARTED. A REVISION TO THE ATP IS BEING DEVELOPED, SEE I.C. BELOW C. THE SUPPLIER IS REVISING THE ATPS FOR BOTH THE 74L4-1 AND THE 74L4-2 SENSORS TO PROPERLY CONTROL THE DRYING PRIOR TO PERFORMING THE IR TEST. THE CHANGES WILL REQUIRE DOCUMENTATION ACCOUNTABILITY SHEET (DAS) APPROVAL RESPONSIBILITY: R. RAMSEY/3830 - M. COMBS/3830 L. COLON/4120 - Z. KIRKLAND/4100 COMPLETE: DECEMBER 5, 1995 * CLOSURE STATEMENT THE ATPS WERE REVISED. SEE TASK II CAUSE * 1) THE PROBABLE CAUSE OF THE FAILURE OF THE 74L4-1 SENSOR WAS INCORRECT WORK INSTRUCTIONS IN THE ATP. THE TEST INSTRUCTIONS LEFT THE SENSOR WET WITH WATER WHEN THE INSULATION RESISTANCE TEST WAS PERFORMED 2,3,4) THE ROOT CAUSE OF THE FAILURE OF THE 74L4-2 SENSORS WAS INCORRECT WORK INSTRUCTIONS IN THE ATP. THE TEST INSTRUCTIONS LEFT THE SENSORS WET WITH WATER WHEN THE INSULATION RESISTANCE TEST WAS PERFORMED TASK II. CORRECTIVE ACTION * THE SUPPLIER ACCEPTANCE TEST PLANS FOR BOTH THE 74L4-1 AND 74L4-2 SENSORS WERE REVISED TO REQUIRE DRYING THE SENSORS IN OPEN AIR OVERNIGHT PRIOR TO BEGINNING THE INSULATION RESISTANCE TESTS REFERENCE: 1) FOR THE 74L4-1, DOCUMENTATION ACCOUNTABILITY SHEET (DAS) AYE-188, ATP-946 REVISION T; AND 2) FOR THE 74L4-2, DAS AYP-186, ATP-945 REVISION R TASK CLOSED TASK III. CLEARANCE OF EFFECTIVITIES *THIS IS AN EXPLAINED CLOSURE OF THE CAPS ALL ETS CLEARED. THE SENSORS FAILED DURING VENDOR ACCEPTANCE TESTING AND ALL INSTALLED SENSORS HAVE PASSED THE VENDOR TESTS. THERE ARE TESTS OF SENSOR INSULATION RESISTANCE AFTER INSTALLATION ON THE ET NOTE: THIS IS ALSO THE DEFERRAL RATIONALE TASK IV. CAPS CLOSURE SUMMARY * THE SUPPLIER ATP FAILURES OF THE INSULATION RESISTANCE CHARACTERISTIC WERE THE RESULT OF INADEQUATE WORK INSTRUCTIONS FOR SENSOR DRYING FOLLOWING A CRYOGENIC TEST SEGMENT. THE ATPS FOR BOTH SENSOR TYPES WERE REVISED TO PREVENT A RECURRENCE TASK CLOSED |
| MSFC Response/Concurrence THIS REPORT HAS BEEN DEFERRED FOR THE NEXT SIX MONTHS PER NSTS 08126 REV. F PARAGRAPH 3.3.10.1, ITEM D WHICH STATES "THE PROBLEM CONDITION IS CLEARLY SCREENED BY PREFLIGHT CHECKOUT OR SPECIAL TESTS (I.E., FAILURE MODE SHOULD NOT OCCUR FOLLOWING THE TEST)." JEFFERY L. RATLEY 9/26/95 M. PESSIN 9/26/95 -------------------------- ----------------------- DESIGN DATE DESIGN DATE J. RATLEY M. PESSIN ALEX ADAMS 9/27/95 P. COUNTS 9/26/95 -------------------------- ----------------------- S&MA DATE PROJECT MGR DATE M. SMILES P. COUNTS |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A16646 | IFA# -- | Contractor RPT# E-160 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-1 | Asmnt Part Name LEVEL SENSOR | Asmnt Serial/Lot# AS NOTED |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD MTP - MFG-TST-INST | FAIL MODE EQ - OUTPUT ERROR |
| Asmnt FMEA 3.6.1.1 | Asmnt FM 1 | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |