POLAR Spacecraft Status As of: Tues 19 Jun 07, 12:00 EST

(Changes from last week in bold border)

| Subsystem/ Component | NOAA-12D AM 16:59=AN STIP data only No IPD processing | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC&LAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- | --- |
| LAUNCHED | 05/14/91 | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 Recursive SCT | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU-1 | B-BUS XSU-1: TOAR444 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO | NO |
| ADACS | Nominal Mode Autonomous swap to YGC 30 Aug, commanded back to nominal 31 Aug RGmode=Monitor Gyro chans=XYZ | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI BU random enables daily bias+6.5 mS | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase Enabled | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 1 | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 3A, 4, 5B Safestate 5B 4b low pressure | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON 137.50 MHZ | #1 ON As of 19 June 07 | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #2 ON 137.9125 MHZ |
| BTX | #1 136.77 MHZ | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 1 – HRPT; 2,3 - Playback | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 – Playback & MCM usage 3 low power unused | 3 – HRPT TOAR424 low power 2 & 1 Playback STX-1 Power drop STX-4 no modulation | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, eclipse states and sun angle) | ArrayOff -60 since 5/23/07 Full Sun Sun Angle 16 uptrend to 20 in early Jan 07 Shunt degraded SA CANT=37 degs PSSS trigger =18.5 | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 SA CANT=37 degs | Array Off -40 Since 7/16/02 Eclipse all year Sun Angle 34 Steady trend SA CANT=22 degs Transitioning to full sun S/C in Sept 07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend SA CANT=37 degs | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 SA CANT=22 BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal HRPT and APT data only | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 |  | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 |  | Nominal | Nominal | Nominal | Nominal |
| AMSU-B |  | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | ON/Inop Turned On 4/30/05 for power balance Filter Wheel OFF | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 |
| MSU | ON/Inop Turn off 6/11/06 23:15 for power balance during eclipse season |  |  |  |  |
| SSU |  |  |  |  |  |
| DCS RFI investigation | Nominal | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR |  | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP |  | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | ON/Nominal Autonomous reset 8 Jun, back to nominal 10 June Turned on 8/30/04 Elec-CH-HVPS=4 Prot-CH-HVPS=0 TED level=3 | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 15:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 16:00z | Nominal Elec-CH-HVPS=1 27 June 17:00z Prot-CH-HVPS=0 |
| SBUV |  |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept Grating motor investigation | Nominal Anode mode since 6 July 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | Nominal TCE’s back to nominal configuration following 7/25/04 UVtrip. | TCE26 & 15H Telem invalid TOAR 432 TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

NOAA-12:	There were relatively no changes to the rest of the NOAA-12 health situation during the past week.

NOAA-15:	There were relatively no changes to the NOAA-15 health situation during the past week.  The VTX was turned on 19 June 2007.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload subsystems during the past week and the rest of the spacecraft subsystems were also nominal during this time.

NOAA-16 will be in full sunlight beginning in mid-August.  This is the first time ever it will not be eclipsing.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload subsystems during the past week and the rest of the spacecraft subsystems except the STX-4 were also nominal during this time.

On Jday 170 at 00:13z, Polar Ops crew members were not able to achieve Bit Sync or Frame Sync lock when attempting to play-down LAC data on STX4 from DTR3B on NOAA-17.  The crew tried a second attempt during this contact, but still could not get a lock.  At the 01:38z contact, the Polar Ops crew recovered 100% of the DTR3B via STX2 and receieved verbal recognition from Wallops CDA that there was no modulation from STX4.  On the ensuing contact at 03:17z, crews tried to play-down LAC data from both DTR3A and DTR3B, but again could not get Bit Sync or Frame Sync lock.  At 05:08z, crews manaully stopped the Stored Command Table (SCT) from dictating STX4 to play-down LAC data off of DTR4A.  Contacts at 06:47z & 08:29z were used by the crews  to recover all data that was supposed to be played down via STX4.

At ~12:00z, the Polar Ops AET notified engineering that it was experiencing problems with STX4.  Upon examining STX4's telemetry, he power and temperature were at nominal levels and were behaving as expected (see Figures 1 & 2).  Engineering requested that crews leave on STX4 during the 13:56z pass in order for Wallops CDA (WCDA) to measure the RF signal strength of all the S-band transmitters on NOAA-17.

During the 15:34z pass,  STX4 was configured for both AIP and HRPT play-downs, however no modulation was seen.  WCDA confirmed there was no modulation.

No modulation was received from STX4 again on the 17:16z pass, where playbacks of GAC and LAC playbacks from DDR2A and DDR2B respectively.  The GAC playback was also performed simultaneously (and successfully) on STX1 to help eliminate the XSU as a source of the problem and to verify the functionality of STX1.

At 20:30z, loads were sent to NOAA-17 that removed STX4 from the SCT.  Fairbanks CDA reported a RF signal strength of -51 dBm for STX4 and there was carrier lock during this contact.  Another play-down of HRPT data, however no modulation was received and there was no Bit Sync or Frame Sync lock.

At 23:50z, STX4 will be turned on and configured for TIP Bi-phase data.  STX4 will be on and in this configuration until the next contact at 01:16z., from that point on STX4 will be off until further notice.  Thanks to the crews no data was lost during this anomaly.  The investigation is on-going.

NOAA-18:	There were relatively no changes to the NOAA-18 health situation during the past week.  The performance of the payload except for the AMSU-A1 was nominal.

The AMSU-A1 reflector 2 position at earth scene 30 (P1P30RF2) was flagging yellow low.  It appears that the reflector 2 motor is undershooting its expected position for earth scene 30 over the southern hemisphere, and is drawing more current at this time.  There are also signs of this effect for the cold target position.  No effects were noted for earth scenes 1, 15, or 20.

Figures 3-6 are 12 hour history plots from days 134, 158 and 162, and history plot which covers days 157-159, respectively.  The attached plots contain BSINORBA (which is -1 at the southern extreme of the orbit and +1 at the northern extreme of the orbit), the reflector 2 motor current, position data for earth scene 30, and position data for the reflector 2 cold calibration target.  For day 134 the reflector positions show a shift in value in the southern half of the orbit, but the motor current remains steady.  Day 158 shows the minima in the position data getting stronger, especially for the cold cal position, and the beginning of bumps in the motor current over the South Pole.  The 162 data shows the effects grew even stronger.  ABE plots for day 164 were not available at the time these plots were made, but 3100 plots are consistent with these plots.  Investigations continue.

The NOAA-18 HIRS was in a ‘quiet’ period again so the HIRS test was run on 15 June 2007.

MetOp A:	No changes reported on the NOAA instruments on MetOp.