UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C. 20460

OFFICE OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

October 17, 2007

MEMORANDUM

SUBJECT:	Product Chemistry Chapter for the Triclosan Reregistration Eligibility Decision (RED) Document

DP Barcode: 335401		Reregistration Case No.:  2340

FROM:	Srinivas Gowda, Microbiologist/Chemist

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

TO:			Mark Hartman, Branch Chief

Diane Isbell, Team Leader

Heather Garvie, Chemical Review Manager

Regulatory Management Branch II

Antimicrobials Division (7510P)

Timothy McMahon, Risk Assessor

THRU:	Siroos Mostaghimi, Team Leader, Team one

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

Norman Cook, Branch Chief

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

Chemical Name				PC Code     CAS#	     Common Name

5-Chloro-2-(2,4-dichlorophenoxy)phenol	54901	        3380-34-5    Triclosan

Attached is the Product Chemistry Chapter for the Triclosan RED Document.

TRICLOSAN

REREGISTRATION ELIGIBILITY DECISION

PRODUCT CHEMISTY CHAPTER

PC Code:  54901; Case No. 2340

REGULATORY HISTORY

5-Chloro-2-(2,4-dichlorophenoxy)phenol (Triclosan) was first registered with the EPA on June 19, 1969.  Presently, there are 20 active products, no inert products, and 4 pending products under PC Code 054901, which are listed in Table 1 under Appendix.  This chemical is a diphenyl ether derivative primarily used in cosmetics, toilet soaps, and antiseptics.  It is also used as a bacteriostat and fungistat in plastics, polymers, textile and implantable medical devices to give these materials "antibacterial properties."

CHEMICAL IDENTIFICATION

Figure 1.  Molecular Structure of Triclosan

Common Name:		Triclosan

Chemical Name:		5-Chloro-2-(2,4-dichlorophenoxy)phenol

Other Name(s):		2,4,4’-Trichloro-2’-hydroxydiphenyl ether

Phenol, 5-chloro-2-(2,4-dichlorophenoxy)-

5-Chloro-2-(2,4-dichlorophenoxy)phenol

Irgasan DP-300R

Irgaguard B1000

VIV-20

CAS Registry Number:	3380-34-5

OPP Chemical Code:	54901

Case Number:		2340

Empirical Formula:		C12H7Cl302

Molecular Weight:		289.541

Technical Grade

Manufacturers:		Ciba Specialty Chemicals Corp

Harmet International/Vivimed Labs Limited

End Use

Manufacturers:	Aeris Technologies Ltd.

Ciba Specialty Chemicals Corp.

Huntsman International, LLC

Microban Products Company

Rohm and Haas Company

Sanitized Inc.

S.C. Johnson & Son Inc.

Thomson Research Associates

Troy Chemical Corp.

Vikon Chemical Co.

Vivimed Labs Limited

Percent Active Ingredient

In Technical Grade Product:	>99.0% (Ciba) and 99.9% (Harmet/Vivimed)

Formulation Types

Registered:			Technical Grade Active Ingredient:

Technical Chemical

Manufacturing Product:

Formulation Intermediate

End Use Products:

Ready-to-Use

Pelleted/Tableted

Emulsifiable Concentrate

Soluble Concentrate

Impregnated Materials

Chemical Properties:	Triclosan is a white crystalline powder with a faint odor and melting point of 56.5°C (133.7°F).  Triclosan is solid and, therefore, has no boiling point.  Triclosan has a log Kow of 4.8 at 25oC and a low vapor pressure of 5.2E-6 mm Hg at 25˚C and 2.2E-6 mm Hg at 20˚C.  Triclosan is soluble in water at 0.012 g/l (12 ppm) at 20˚C.  Triclosan is readily soluble in alkaline solutions and many organic solvents.  It has a bulk density of 1.55 x 103 kg/m3 at 22˚C.

PRODUCT CHEMISTRY DATA REQUIREMENTS FOR REREGISTRATION OF TRICLOSAN:

Product chemistry data requirements and results are summarized in Tables 2 and 3 under, “APPENDIX”.

FINDINGS/CONCLUSIONS:

All product chemistry data requirements have been fulfilled for the active ingredient triclosan.  See Tables 2 and 3 under, “APPENDIX”.  RASSB has no objections to the reregistration of triclosan with respect to product chemistry data requirements.

APPENDIX:

Table 1.  Registered Active Products of Triclosan

| EPA Reg. No. | Percent Active Ingredient | Registrant |
| --- | --- | --- |
| 2829-139 | 99% | Rohm & Hass Company |
| 2829-145 | 10% | Rohm & Hass Company |
| 3090-165 | 10% | Sanitized Inc. |
| 3090-215 | 99% | Sanitized Inc |
| 3090-219 | 7.5% | Sanitized Inc. |
| 4822-429 | 0.06% | S.C. Johnson & Son Inc. |
| 5383-127 | 99% | Troy Chemical Corp. |
| 6390-25 | 2% | Vikon Chemical Company, Inc. |
| 10466-24 | 1.6% | Thomson Research Associates |
| 10466-27 | 3% | Thomson Research Associates |
| 10466-38 | 99% | Thomson Research Associates |
| 10466-42 | 1% | Thomson Research Associates |
| 42182-1 | 99% | Microban Products Company |
| 70404-2 | 99% | Ciba Specialty Chemicals Corporation |
| 70404-5 | 99% | Ciba Specialty Chemicals Corporation |
| 73951-1 | 99.9% | Vivimed Labs Limited |
| 82523-1 | 0.69% | Aeris Technologies LTD |
| 83884-7 | 10% | Huntsman International, LLC |
| 83884-9 | 99% | Huntsman International, LLC |
| 83884-10 | 99% | Huntsman International, LLC |

Table 2: Manufacturing and Impurity Data for Triclosan

Product Identity, Composition, and Analysis

| Old Guideline No. | New Guideline No. | Requirement | Use Pattern2 | MRID | Status1 | Details or Deficiency |
| --- | --- | --- | --- | --- | --- | --- |
| 61-1 | 830.1550 | Product identity and composition | 3,4,7 | 42027901 45358501 | A | Refer to Chemical Identification on page 2 |
| 61-2a | 830.1600 | Description of materials used to produce the product | 3,4,7 | 42027901 45358502 | A | CBI |
| 61-2a | 830.1620 | Description of production process | 3,4,7 | 42027901 45358502 45487201 | A | CBI |
| 61-2a | 830.1650 | Description of formulation process | 3,4,7 | 42027901 45358502 45487201 | A | CBI |
| 61-2b | 830.1670 | Discussion of formation of impurities | 3,4,7 | 42027901 42027902 43277802 45358503 45358504 | A | CBI |
| 62-1 | 830.1700 | Preliminary analysis | 3,4,7 | 42027902 45358504 | A | CBI |
| 62-2 | 830.1750 | Certified limits | 3,4,7 | 42027901 43277802 43533901 45358503 45358505 | A | CBI |
| 62-3 | 830.1800 | Enforcement analytical method | 3,4,7 | 42027902 45358506 | A | Reverse Phase HPLC Method Gas Chromatography |
| 64-1 | 830.1900 | Submittal of samples | 3,4,7 |  | N/A |  |

1A = Acceptable; N/A = Not Applicable.

2Use Pattern:

(3) Commercial, institutional and industrial premises and equipment

(4) Residential and public access premises

(7) Materials preservatives

Table 3: Physical and Chemical Properties for Triclosan

| Old Guideline No. | New Guideline No. | Requirement | Use Pattern2 | MRID | Status1 | Results or Deficiency |
| --- | --- | --- | --- | --- | --- | --- |
| 63-2 | 830.6302 | Color | 3,4,7 | 42027902 45358502 | A | White Crystals |
| 63-3 | 830.6303 | Physical state | 3,4,7 | 42027902 45358502 | A | Crystalline Powder |
| 63-4 | 830.6304 | Odor | 3,4,7 | 42027902 | A | Faint Odor |
| 63-5 | 830.7200 | Melting Point | 3,4,7 | 42027904 | A | 56.5˚C |
| 63-6 | 830.7220 | Boiling Point | 3,4,7 |  | N/A |  |
| 63-7 | 830.7300 | Density, Bulk Density, or Specific Gravity | 3,4,7 | 42027904 | A | 1.55 x 103 kg/m3 at 22˚C |
| 63-8 | 830.7840 | Water solubility: column elusion method; shake flask method. Fat Solubility: | 3,4,7 | 42027904 | A A | 0.012 g/l at 20˚C > 65g/100g fat at 37°C |
| 63-8 | 830-xxxx | Solubility in organic solvents | 3,4,7 |  | N/A | Readily soluble (Source: TOXNET) |
| 63-9 | 830.7950 | Vapor Pressure | 3,4,7 | 42027904 | A | 5.2E-6 mm Hg at 25˚C 2.2E-6 mm Hg at 20˚C |
| 63-10 | 830.7370 | Dissociation constants in water | 3,4,7 | 42027904 | A | pKa=8.14 at 20°C |
| 63-11 | 830.7550 | Partition coefficient (n-octanol / water), shake flask method. | 3,4,7 | 42027902 42027904 | A | Log Po/w = 4.8 at 25˚C |
| 63-12 | 830.7000 | pH | 3,4,7 |  | N/A |  |
| 63-13 | 830.6313 | Stability to normal and elevated temperatures. Stability to metals Stability to metal ions | 3,4,7 | 42027902 43022601 43277801 | A A A | No thermal effect. Stable when exposed to Metals. Triclosan exposed to zinc and zinc ions showed the same decrease in % a.i. as control. Triclosan exposed to iron ions showed a greater decrease in % a.i. than the control. |
| 63-17 | 830.6317 | Storage stability | 3,4,7 | 45358502 |  | No deterioration after 12 months storage |

1 A = Acceptable; N/A = Not applicable.

2Use Pattern:

(3) Commercial, institutional and industrial premises and equipment

(4) Residential and public access premises

(7) Materials preservatives

BIBLIOGRAPHY

MRID  				           Citation

42027901	LoMenzo, J. (1991) Irgasan DP 300: Product Identity and Composition. Unpublished study prepared by Ciba-Geigy Corp.

42027902	Basingthwaite, J. (1983) Irgasan DP 300: Batch Analysis and Analytical Methodology. Unpublished study prepared by Ciba-Geigy Ag.

42027904	Vogel, A. (1990) Irgasan 300 DP: Report on Melting Point/Melting Range. Unpublished study prepared by Ciba-Geigy Ltd.

43022601	Morrissey, M. (1993) Stability Determination of Irgasan DP 300 in the Presence of Metal: Final Report: Lab Project Number: HWI 6117-246. Unpublished study prepared by Hazleton Wisconsin, Inc.

43277801	Morrissey, M. (1994) Stability Determination of Irgasan DP300 Exposed to Metal Ions: Final Report: Lab Project Number: HWI 6117-261. Unpublished study prepared by Hazleton Wisconsin, Inc.

43277802	Schatowitz, B. (1990) Additional Data Required by the US EPA for the Results of the Analysis of Irgasan DP300 for Dioxins/Furans: Lab Project Number: 102290. Unpublished study prepared by Ciba-Geigy Ltd.

43533901	Schatowitz, B. (1995) Additional Data Required by the U.S. EPA for the Product Analysis of Irgasan DP 300: Lab Project Number: 11995. Unpublished study prepared by Ciba Research Services.

45358501	Harvey, W. (2001) Product Identity and Composition: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 3 p. {OPPTS 830.1550}

45358502 	Harvey, W. (2001) Description of Production Process: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 64 p. {OPPTS 830.1620}

45358503	Harvey, W. (2001) Discussion of Formation of Impurities: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 18 p. {OPPTS 830.1670}

45358504 	Harvey, W. (2001) Preliminary Analysis: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 19 p. {OPPTS 830.1700}

45358505 	Harvey, W. (2001) Certified Limits: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 21 p. {OPPTS 830.1750}

BIBLIOGRAPHY

MRID  				           Citation

45358506 	Harvey, W. (2001) Enforcement Analytic Method: Triclosan. Unpublished study prepared by Vivimed Labs LTD. 5 p. {OPPTS 830.1800}

45472801 	Harvey, W. (2001) Summary of Physical/Chemical Properties: Triclosan. Unpublished study prepared by Har-Met International, Inc. 4 p.

Sign-off Date       :  10/17/07

DP Barcode No.   :  D33540l