UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

WASHINGTON, D.C. 20460

OFFICE OF

PREVENTION, PESTICIDES AND

TOXIC SUBSTANCES

February 22, 2008

MEMORANDUM

SUBJECT:		Preliminary Ecological Hazard and Environmental Risk Assessment Science Chapter for the Triclosan Reregistration Eligibility Decision (RED) Document

DP Barcode:  341569		Reregistration Case No.:  2340

FROM:		Genevieve Angle, Biologist

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

TO:			Mark Hartman, Branch Chief

Diane Isbell, Team Leader

Regulatory Management Branch II

Antimicrobials Division (7510P)

Timothy McMahon, Risk Assessor

THRU:		Siroos Mostaghimi, Team Leader, Team 1

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

Norman Cook, Branch Chief

Risk Assessment and Science Support Branch (RASSB)

Antimicrobials Division (7510P)

Chemical Name	PC Code	CAS#		Common Names

5-Chloro-2-	54901		3380-34-5	Triclosan

(2,4-dichlorophenoxy)phenol

Attached is the Ecological Hazard and Environmental Risk Assessment Science Chapter for the Triclosan RED Document.

ECOLOGICAL HAZARD AND ENVIRONMENTAL

RISK ASSESSMENT CHAPTER

Triclosan

### PC Code: 054901

### CASE No.: 2340

02/22/08

Genevieve Angle - Biologist

Antimicrobials Division

Office of Pesticide Programs

U.S. Environmental Protection Agency

1200 Pennsylvania Avenue, NW

Washington, DC 20460

Table of Contents

Page

Executive Summary ……………………………………………………………………………… 5

1.  Ecological Toxicity Data . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .6

A.  Toxicity to Terrestrial Animals . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .6

1.  Birds, Acute  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 6

2.  Birds, Subacute. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8

3.  Mammals, Acute and Chronic . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9

B.  Toxicity to Aquatic Animals . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9

1.  Freshwater Fish, Acute . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9

2.  Freshwater Invertebrates, Acute . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .10

3.  Estuarine and Marine Organisms, Acute . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .11

4.  Aquatic Organisms, Chronic . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .12

C.  Toxicity to Plants . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . ..12

II.  Risk Assessment and Risk Characterization . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  . . ..13

A.  Environmental Fate Assessment Summary . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .. . . . .14

B.  Environmental Exposure And Qualitative Environmental Risk Assessment… . .. . . . . ..15

C.  Endangered Species Considerations . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  . . . . . . . . . . .17

III.  Confirmatory Data Required. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .. . . . . . . . . ..18

IV.  Label Hazard Statements for Terrestrial and Aquatic Organisms. . . . . . . . . . .  . . . . . . . . .. 19

V.  References . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  . . . . . . . . . . 20

LIST OF TABLES

Page

Table 1 – Acute Oral Toxicity of Triclosan to Birds. …. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .8

Table 2 – Subacute Oral Toxicity of Triclosan to Birds. . . . . . …. . . . . . . . . . . . . . . . . . . . . . . 9

Table 3 – Acute Toxicity of Triclosan to Freshwater Fish. . . . . . . . . . . . …. . . . . . . . . . . . . . . 10

Table 4 – Acute Toxicity of Triclosan to Freshwater Invertebrates. . . . . . …. . . . . . . . . . . . . . 11

Table 5 – Chronic Toxicity of Triclosan to Freshwater Organisms. . . . …. . . . . . . . . . . . . . . . 12

Table 6 – Toxicity of Triclosan to Aquatic Plants. . . . . . . . . . . . …. . . . . . . . . . . . . . . . . . . . ..13

Ecological Hazard and Environment Risk Assessment

### For Triclosan

Executive Summary:

Only a small portion of the uses of triclosan are regulated by the U.S. EPA and therefore covered in this document.  Triclosan is currently registered by the EPA as a bacteriostat, fungicide/fungistat and mold/mildewcide for materials preservation, residential and public access premises and commercial, institutional and industrial premises and equipment.   Its materials preservation uses include: adhesives, fabrics, vinyl, latex, plastics, polyethylene, polyurethane, synthetic polymers, styrene, floor wax emulsions, rope, textiles, caulking compounds, sealants, coatings, polypropylene, rubber, inks, cellulosic materials, slurries, films and latex paints.  The residential and public access premises uses include: brooms, mulch, floors, shower curtains, awnings, tents, mattresses, toothbrushes, toilet bowls, urinals, garbage cans, refuse container liners, insulation, concrete mixtures, grouts, air filter materials, upholstery fabrics, human wastes and rugs/carpets.  The commercial, institutional and industrial premises and equipment uses include: conveyor belts, fire hoses, dye bath vats and ice making equipment.

An ecological risk assessment is not typically conducted for the types of uses registered for triclosan.  However, since triclosan has been detected in natural waters, EPA has performed a qualitative environmental risk assessment using monitoring levels of triclosan found in waterways and toxicity values from the tables in section I to develop risk quotients (RQs) and compare them to levels of concern (LOCs) for triclosan.  LOCs were not exceeded for fish but were exceeded for aquatic plants.  There were no acceptable acute toxicity studies for freshwater invertebrates or estuarine and marine organisms nor were there any acceptable chronic toxicity studies available for aquatic organisms.  Therefore, risk to these species could not be assessed.

Data Gaps:

- Freshwater invertebrate acute study (850.1010);

- As outlined in the environmental fate chapter for triclosan, the registrant is required to provide a scientific rationale, including appropriate modeling (e.g., surface water modeling), that addresses and quantifies the amounts of triclosan and triclosan transformation products (e.g., triclosan methyl) occuring in various environmental compartments (e.g., surface waters, biosolids, soil, fish, shellfish) from triclosan antimicrobial pesticide uses;

- Relative to the above requirement, if the registrant is not able to provide a satisfactory scientific rationale that determines the quantities of triclosan and triclosan transformation products in various environmental compartments, then EPA will assume that the present levels of triclosan and triclosan transformation products detected in such compartments occurs because of registered antimicrobial use patterns.  In this case, OPP will require the environmental fate data outlined in the triclosan environmental fate chapter; and

- Depending on the results of the environmental fate studies, which may be required (see triclosan environmental fate chapter), additional acute and chronic nontarget organism studies may be required.  These include the following studies:

a. Estuarine/marine fish acute study (850.1075) [Technical Grade Active 	Ingredient (TGAI)];

b. Estuarine/marine shrimp acute study (850.1035) (TGAI);

c. Estuarine/marine mollusk acute study (850.1025) (TGAI);

d. Fish early life-stage (freshwater) study (850.1400) (TGAI);

e. Aquatic invertebrate (freshwater) life-cycle study (850.1300) (TGAI);

f. Fish life-cycle study (850.1500);

g. Fish bioconcentration study – BCF (850.1730) (TGAI);

h. Acute sediment toxicity to freshwater invertebrates (850.1735) (TGAI); 			i. Acute sediment toxicity to estuarine invertebrates (850.1740) (TGAI); 			and

j. Additional plant toxicity testing:  an additional algal toxicity test 					(850.5400) with the freshwater green alga, Selenastrum capricornutum; 				and studies on the rooted freshwater macrophyte rice (Oryza sativa) – 				850.4225 and 850.4250 (2 tests on seedling emergence and vegetative 				vigor).

Label Hazard Statements/Use Recommendations:

Triclosan labels must state:

“This pesticide is toxic to fish and aquatic invertebrates.”

"Do not discharge effluent containing this product into lakes, streams, ponds, estuaries, oceans, or other waters unless in accordance with the requirements of a National Pollutant Discharge Elimination System (NPDES) permit and the permitting authorities are notified in writing prior to discharge.  Do not discharge effluent containing this product to sewer systems without previously notifying the local sewage treatment plant authority.  For guidance contact your State Water Board or Regional Office of the EPA."

I.	Ecological Toxicity Data

The toxicity endpoints presented below are based on the results of ecotoxicity studies submitted to EPA to meet the Agency’s data requirements for the uses of triclosan.

A.	Toxicity to Terrestrial Animals

(1)	Birds, Acute

In order to establish the toxicity of triclosan to avian species, the Agency requires an acute oral toxicity study using the technical grade active ingredient (TGAI).  The preferred-test species is either mallard duck (a waterfowl) or bobwhite quail (an upland game bird).  The results of three acute oral toxicity studies, submitted for triclosan, are provided in the following table (Table 1).

# Table 1.  Acute Oral Toxicity of Triclosan to Birds

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (mg/kg) | Toxicity Category | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- | --- |
| Mallard duck (Anas platyrhynchos) | Triclosan 99.7% | LD50 = >2150 NOAEL = 2150 | Relatively nontoxic | Yes (core) - 14-day test duration - 19 weeks of age | 430226-03 |
| Bobwhite quail (Colinus virginianus) | Triclosan 99.7% | LD50 = 825 NOAEL = <147 | Slightly toxic | Yes (core) - 14-day test duration - 21 weeks of age | 430226-02 |
| Bobwhite quail (Colinus virginianus) | Triclosan 3.89% | LD50 = >2000 NOAEL = N.R. | Relatively nontoxic | Yes (core for formulated product) | 410089-10 |

These three acceptable acute oral toxicity studies indicate that triclosan is slightly toxic to relatively nontoxic to birds on an acute oral basis. The guideline requirement OPPTS 850.2100/(71-1) is satisfied.

(2)	Birds, Subacute

A subacute dietary study using the TGAI may be required on a case-by-case basis depending on the results of lower-tier ecological studies and pertinent environmental fate characteristics in order to establish the toxicity of a chemical to avian species.  This testing was required for triclosan.  The preferred-test species is either the mallard duck or bobwhite quail.  The results of two subacute dietary toxicity studies, submitted for triclosan, are provided in the following table (Table 2).

# Table 2.  Subacute Oral Toxicity of Triclosan to Birds

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (ppm) | Toxicity Category | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- | --- |
| Bobwhite quail (Colinus virginianus) | Triclosan 99.7% | LC50 (diet) = >5000 NOAEC = 1250 | Relatively nontoxic | Yes (core) - 8-day test duration - 13 days of age | 430226-04 |
| Bobwhite quail (Colinus virginianus) | Triclosan 3.89% | LC50 (diet) = >5000 NOAEC = N.R. | Relatively nontoxic | Yes (core for formulated product) - 8-day test duration - 7-10 days of age | 410089-11 |

The results of these two acceptable studies indicate that triclosan is relatively nontoxic to avian species through subacute dietary exposure. These studies fulfill guideline requirement OPPTS 850.2100/ (71-2a – Bobwhite quail/71-2b – Mallard duck).

(3)	Mammals, Acute and Chronic Toxicity

Wild mammal testing is not required by the Agency.  In most cases, rat toxicity values obtained from studies conducted to support data requirements for human health risk assessments substitute for wild mammal testing.  Refer to the human toxicology chapter of this RED for mammalian toxicity data.  Also, refer to the toxicology chapter for information on triclosan’s potential as an endocrine disruptor.

B.	Toxicity to Aquatic Animals

The Agency requested that aquatic toxicity studies be conducted with triclosan since, under typical use conditions, it may be introduced into the aquatic environment.

(1)	Freshwater Fish, Acute

In order to establish the acute toxicity of triclosan to freshwater fish, the Agency requires freshwater fish toxicity studies using the TGAI.  The preferred test species are rainbow trout (a coldwater fish) and bluegill sunfish (a warmwater fish).  The results of 5 freshwater fish acute studies submitted for triclosan are presented in Table 3.

# Table 3.  Acute Toxicity of Triclosan to Freshwater Fish

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (mg/L) | Toxicity Category | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- | --- |
| Rainbow Trout (Oncorhynchus mykiss) | Triclosan 99.3% | LC50 = 0.288 NOAEC = 0.100 | Highly toxic | Yes (core) - 96-hr test duration - static test system | 439693-01 |
| Fathead minnow (Pimephales promelas) | Triclosan 99.7% | LC50 = 0.26 LOEC = 0.18 NOAEC = 0.10 | Highly toxic | No (supplemental) - 96-hr test duration - static test system - nominal concentrations not verified | 430460-01 |
| Bluegill sunfish (Lepomis macrochirus) | Triclosan 3.89% | LC50 = 37.2 NOAEC = N.R. | Slightly toxic | Yes (core for formulated product) - 96-hr test duration - static test system | 410089-13 |
| Rainbow Trout (Oncorhynchus mykiss) | Triclosan 3.89% | LC50 = 23.4 NOAEC = N.R. | Slightly toxic | Yes (core for formulated product) - 96-hr test duration - static test system | 410089-12 |

Freshwater acute toxicity tests indicate that triclosan is highly toxic to slightly toxic to fish on an acute basis.  These studies fulfill guideline requirement OPPTS 850.1075 (72-1a&b).  Because acute toxicity to fish is <1.0 mg/L, the environmental hazard section of triclosan labels must state: “This pesticide is toxic to fish.”

(2)	Freshwater Invertebrates, Acute

The Agency requires a freshwater aquatic invertebrate study using the TGAI to establish the acute toxicity to freshwater invertebrates.  The preferred test species is Daphnia magna.  The results of three studies submitted for triclosan are provided in the following table (Table 4).  Note that in a search of the available data on triclosan, the U.S. EPA’s Office of Water found an EC50 as low as 0.13 mg/L for the Cladoceran Ceriodaphnia dubia (U.S. EPA, 2007).

Table 4.  Acute Toxicity of Triclosan to Freshwater Invertebrates

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (mg/L) | Toxicity Category | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- | --- |
| Waterflea (Daphnia magna) | Triclosan 99.7% | EC50 = 0.39 NOAEC = 0.10 (a.i.) | Highly toxic | No (supplemental) - 48-hr test duration - static test system - nominal concentrations not verified | 430460-02 |
| Waterflea (Daphnia magna) | Triclosan 3.89% | LC50 = 0.42 NOAEC = N.R. | Highly toxic | No (supplemental) - 48-hr test duration - static test system - lack of pH and DO measurements and formulated product used | 410089-14 |

The results of these studies indicate that triclosan is highly toxic to freshwater invertebrates.  These studies do not fulfill guideline requirement OPPTS 850.1010 (72.2a).  Because the acute aquatic invertebrate toxicity values are < 1.0 mg/L, the environmental hazard section of triclosan labels must state:  “This pesticide is toxic to aquatic invertebrates.”

(3)	Estuarine and Marine Organisms, Acute

Acute toxicity testing with estuarine and marine organisms using the TGAI is required when the end-use product is intended for direct application to the marine/estuarine environment or effluent containing the active ingredient is expected to reach this environment.  The preferred fish test species is the sheepshead minnow.  The preferred invertebrate test species are mysid shrimp and eastern oysters.  At this time this testing is not required for triclosan, but is dependent upon the results of environmental fate data which may be required.  (See triclosan environmental fate chapter and comments above on potential data requirements).  No studies have been submitted to fulfill these data requirements (OPPTS 850.1075/(72-3a), OPPTS 850.1035/(72-3c) and OPPTS 850.1025/(72-3b)).

(4)	Aquatic Organisms, Chronic

Chronic toxicity testing (fish early life stage and aquatic invertebrate life cycle) is required for pesticides when certain conditions of use and environmental fate apply.  The preferred freshwater fish test species is the fathead minnow.  The preferred freshwater invertebrate is Daphnia magna.  At this time this testing is not required for triclosan, but is dependent upon the results of environmental fate data which may be required.  (See triclosan environmental fate chapter and comments above on potential data requirements).

The results of one toxicity study submitted for triclosan is presented in Table 5.  Note that in a search of the available data on triclosan, the U.S. EPA’s Office of Water found a NOEC as low as 0.006 mg/L for the Cladoceran Ceriodaphnia dubia (U.S. EPA, 2007).

#### Table 5.  Chronic Toxicity of Triclosan to Freshwater Organisms

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (mg/L) | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- |
| Waterflea (Daphnia magna) | Triclosan % purity unknown | LOEC = <0.1388 NOAEC = N.R. | No (supplemental) - 21-day test duration - static renewal test system - growth not measured as a chronic endpoint - % a.i. not given - raw data missing - concentration analysis insufficient | 437407-01 |

No fathead minnow study has been submitted. The study on the waterflea does not fulfill the guideline requirement for a chronic aquatic invertebrate study (OPPTS 850.1300).

- Toxicity to Plants

Non-target plant phytotoxicity testing is required for pesticides when certain conditions of use and environmental fate apply.  At this time this testing is not required for triclosan, but is dependent upon the results of environmental fate data which may be required.  (See triclosan environmental fate chapter and comments above on potential data requirements).  However, testing has been conducted with triclosan on several aquatic plant species.  Testing is normally conducted with one species of aquatic vascular plant (Lemna gibba) and four species of algae:  (1) freshwater green alga, Selenastrum capricornutum, (2) marine diatom, Skeletonema costatum, (3) freshwater diatom, Navicula pelliculosa, and (4)  bluegreen cyanobacteria, Anabaena flos-aquae.  The rooted aquatic macrophyte rice (Oryza sativa) is also tested in seedling emergence and vegetative vigor tests.

Four studies that evaluate the toxicity of triclosan to freshwater aquatic plants have been submitted. Results of these studies are presented in Table 6.  Note that in a search of the available data on triclosan, the U.S. EPA’s Office of Water found an EC50 as low as 0.0007 mg/L for the green alga Scenedesmus subspicatus and an EC25 as low as 0.00067 mg/L for the blue-green alga Anabaena flos-aquae (U.S. EPA, 2007).

Table 6.  Toxicity of Triclosan to Aquatic Plants

| Species | Chemical, % Active Ingredient (a.i.) Tested | Endpoint (mg/L) | Satisfies Guidelines/ Comments | Reference (MRID No.) |
| --- | --- | --- | --- | --- |
| Marine Diatom (Skeletonema costatum) | Triclosan 99.5% | EC50 = >0.066 NOEC = 0.0126 | Yes (core) - 96-hour test duration - static test system | 444228-01 |
| Freshwater Diatom (Navicula pelliculosa) | Triclosan 99.5% | EC50 = 0.016 NOEC = 0.005 | Yes (core) - 96-hour test duration - static test system | 444228-01 |
| Bluegreen Cyanobacteria (Anabaena flos-aquae) | Triclosan 99.5% | EC50 = 0.0012 NOEC = N.R. | Yes (core) - 96-hour test duration - static test system | 444228-01 |
| Duckweed (Lemna gibba) | Triclosan 99.5% | EC50 = >0.0625 NOEC = 0.0125 | Yes (core) - 7-day test duration - static test system | 444228-01 |

The guideline requirement for an algal toxicity test (850.5400, 123-2) is partially fulfilled.  One additional algal toxicity test under 850.5400 is outstanding: a test with the freshwater green alga, Selenastrum capricornutum.  The other non-target aquatic plant toxicity requirement, floating freshwater aquatic macrophyte duckweed (Lemna gibba) – guideline 850.4400 - is satisfied.  Studies on the rooted freshwater macrophyte rice (Oryza sativa) – 850.4225 and 850.4250 (2 tests on seedling emergence and vegetative vigor) -- have not been submitted.

II.	Risk Assessment and Characterization

The triclosan uses that EPA regulates are classified as “indoor” uses.  An ecological risk assessment is not typically conducted for the types of uses registered for triclosan.  However, since triclosan has been detected in natural waters (see triclosan environmental fate chapter), EPA has performed a qualitative environmental risk assessment using monitoring levels of triclosan found in waterways and toxicity values from the tables in section I to develop risk quotients (RQs) and compare them to levels of concern (LOCs) for triclosan.

A.        Environmental Fate Assessment Summary

Triclosan [5-chloro-2-(2,4-dichlorophenoxy)phenol] is a white crystalline powder with low solubility in water (12 ppm).  Triclosan is hydrolytically stable under abiotic and buffered conditions over the pH 4-9 range based on data from a preliminary test at 50°C.  Photolytically, Triclosan degrades rapidly under continuous irradiation from artificial light at 25°C in a pH 7 aqueous solution, with a calculated aqueous photolytic half-life of 41 minutes.  One major transformation product has been identified, DCP (2,4-dichlorophenol), which was a maximum of 93.8-96.6% of the applied at 240 minutes post-treatment.

In soil, triclosan is expected to be immobile based on an estimated Koc of 9,200.  Triclosan is not expected to volatilize from soil (moist or dry) or water surfaces based on an estimated Henry’s Law constant of 1.5 x 10-7 atm-m3/mole.  Triclosan exists partially in the dissociated form in the environment based on a pKa of 7.9, and anions do not generally adsorb more strongly to organic carbon and clay than their neutral counterparts.  In aquatic environments, triclosan is expected to adsorb to suspended solids and sediments and may bioaccumulate (Kow 4.76), posing a concern for aquatic organisms.  There is a low to moderate potential for bioconcentration in aquatic organisms based on a BCF range of 2.7 to 90.

Hydrolysis is not expected to be an important environmental fate process due to the stability of triclosan in the presence of strong acids and bases.  However, triclosan is susceptible to degradation via aqueous photolysis, with a half-life of <1 hour under abiotic conditions, and up to 10 days in lake water.  An atmospheric half-life of 8 hours has also been estimated based on the reaction of triclosan with photochemically produced hydroxyl radicals.  Additionally, triclosan may be susceptible to biodegradation based on the presence of methyl-triclosan following wastewater treatment.

Of the published literature studies on the occurrence of triclosan in waste water treatment plants, treatment plant efficiency, and open water measurements of triclosan, the majority suggest that aerobic biodegradation is one of the major and most efficient biodegradation pathways (70-80%) through which triclosan and its by-products are removed from the aquatic environment, with actual efficiencies ranging from 53-99% (Kanda et al., 2003) in activated sludge plants, and trickle down filtration ranging from 58-86% (McAvoy et al., 2002).  Another pathway of removing triclosan from water in wastewater treatment plants is through the sorption of triclosan and associated by-products to particles and sludge (10-15%) because of the chemical’s medium to high hydrophobicity.  Benchtop fate testing of triclosan found that 1.5-4.5% was sorbed to activated sludge and 81-92% was biodegraded (Federle et al., 2002).

###### B.	Environmental Exposure and Qualitative Environmental Risk Assessment

Risk assessment integrates the results of the exposure and ecotoxicity data to evaluate the likelihood of adverse ecological effects. One method of integrating the results of exposure and ecotoxicity data is called the quotient method.  For this method, risk quotients (RQs) are calculated by dividing exposure estimates by ecotoxicity values, both acute and chronic:

RQ = EXPOSURE/TOXICITY

RQs are then compared to levels of concern (LOCs).  These LOCs are criteria used by OPP to indicate potential risk to nontarget organisms and the need to consider regulatory action.  The criteria indicate that a pesticide used as directed has the potential to cause adverse effects on nontarget organisms.  LOCs currently address the following risk presumption categories: (1) acute - the potential for acute risk is high, regulatory action may be warranted in addition to restricted use classification; (2) acute restricted use - the potential for acute risk is high, but this may be mitigated through restricted use classification; (3) acute endangered species - the potential for acute risk to endangered species is high, and regulatory action may be warranted, and (4) chronic risk - the potential for chronic risk is high, and regulatory action may be warranted, (5) non-endangered plant risk – potential for effects in non-target plants, and (6) endangered plant risk – potential for effects in endangered plants.   Currently, EFED does not perform assessments for chronic risk to plants, acute or chronic risks to nontarget insects, or chronic risk from granular/bait formulations to birds or mammals.

The ecotoxicity test values (measurement endpoints) used in the acute and chronic risk quotients are derived from required studies.  Examples of ecotoxicity values derived from short-term laboratory studies that assess acute effects are: (1) LC50 (fish and birds), (2) LD50 (birds and mammals), (3) EC50 (aquatic plants and aquatic invertebrates) and (4) EC25 (terrestrial plants).  Examples of toxicity test effect levels derived from the results of long-term laboratory studies that assess chronic effects are: (1) LOAEC (birds, fish, and aquatic invertebrates), and (2) NOAEC (birds, fish and aquatic invertebrates). For birds and mammals, the NOAEC generally is used as the ecotoxicity test value in assessing chronic effects, although other values may be used when justified. However, the NOAEC is used if the measurement endpoint is production of offspring or survival.

Risk presumptions, along with the corresponding RQs and LOCs are tabulated below.

Risk Presumptions for Terrestrial Animals

| Risk Presumption | RQ | LOC |
| --- | --- | --- |

Birds and Wild Mammals

| Acute Risk | EEC1/LC50 or LD50/sqft2 or LD50/day3 | 0.5 |
| --- | --- | --- |
| Acute Restricted Use | EEC/LC50 or LD50/sqft or LD50/day (or LD50 < 50 mg/kg) | 0.2 |
| Acute Endangered Species | EEC/LC50 or LD50/sqft or LD50/day | 0.1 |
| Chronic Risk | EEC/NOAEC | 1 |

1  abbreviation for Estimated Environmental Concentration (ppm) on avian/mammalian food items

2    mg/ft2             	3  mg of toxicant consumed/day

LD50 * wt. of bird             	LD50 * wt. of bird

Risk Presumptions for Aquatic Animals

| Risk Presumption | RQ | LOC |
| --- | --- | --- |
| Acute Risk | EEC1/LC50 or EC50 | 0.5 |
| Acute Restricted Use | EEC/LC50 or EC50 | 0.1 |
| Acute Endangered Species | EEC/LC50 or EC50 | 0.05 |
| Chronic Risk | EEC/MATC2 or NOAEC | 1 |

1  EEC = (ppm or ppb) in water

2  MATC = maximum allowable toxicant concentration

| Risk Presumptions for Plants |  |  |
| --- | --- | --- |
| Risk Presumption | RQ | LOC |

| Terrestrial and Semi-Aquatic Plants |
| --- |
| Acute Risk | EEC/EC25 | 1 |
| Acute Endangered Species | EEC/EC05 or NOAEC | 1 |

| Aquatic Plants |
| --- |
| Acute Risk | EEC1/EC50 | 1 |
| Acute Endangered Species | EEC/EC05 or NOAEC | 1 |

- EEC = (ppb/ppm) in water

Triclosan was found in approximately 36 US streams (Klopin et al., 2002), where effluent from activated sludge waste water treatment plants, trickle down filtration, and sewage overflow are thought to contribute to the occurrence of triclosan in open water. For this study, the U.S. Geological Survey surveyed a network of 139 streams across 30 states during 1999 and 2000.  The selection of sampling sites was biased toward streams susceptible to contamination (i.e. downstream of intense urbanization and livestock production). The median concentration of triclosan was 40 ng/L and the maximum concentration detected was 280 ng/L (Klopin et al., 2002).  Discharge into U.S. surface waters has resulted in other researchers finding triclosan from the low ng/L levels to a maximum of 2.3 µg/L (U.S. EPA, 2007).

From the toxicity tables in section I above, the highest toxicity in an acceptable fish study was achieved in a study on the rainbow trout (Oncorhynchus mykiss).  The LC50 value obtained in this study was 0.288 mg/L (MRID 439693-01).  There were no acceptable acute toxicity studies for freshwater invertebrates or estuarine and marine organisms nor were there any acceptable chronic toxicity studies available for aquatic organisms.  Therefore, risk to these species cannot be assessed.  The highest toxicity in an acceptable aquatic plant toxicity study was achieved in a study on the bluegreen cyanobacteria (Anabaena flos-aquae).  The EC50 value obtained in this study was 0.0012 mg/L and no NOEC was reported (MRID 444228-01).

For aquatic animals the LOC ranges from 0.05 for endangered species to 1 for chronic risks.  Comparing the maximum concentration of triclosan found in U.S. surface waters (2.3 µg/L or 0.0023 mg/L) to the highest toxicity found in a fish acute study (0.288 mg/L), an RQ of 0.008 is obtained.  This is less than all LOCs for aquatic animals and therefore the potential for triclosan to cause adverse effects on fish is not high.

For aquatic plants the LOC is 1.  Comparing the maximum concentration of triclosan found in US streams (2.3 µg/L or 0.0023 mg/L) to the highest toxicity found in aquatic plants (0.0012 mg/L), an RQ of 1.92 is obtained.  This is higher than the LOC and therefore the potential for acute risk to aquatic plants from triclosan exists.

- Endangered Species Considerations

Section 7 of the Endangered Species Act, 16 U.S.C. Section 1536(a)(2), requires all federal agencies to consult with the National Marine Fisheries Service (NMFS) for marine and anadromous listed species, or the United States Fish and Wildlife Services (FWS) for listed wildlife and freshwater organisms, if they are proposing an "action" that may affect listed species or their designated habitat.  Each federal agency is required under the Act to insure that any action they authorize, fund, or carry out is not likely to jeopardize the continued existence of a listed species or result in the destruction or adverse modification of designated critical habitat.  To jeopardize the continued existence of a listed species means "to engage in an action that reasonably would be expected, directly or indirectly, to reduce appreciably the likelihood of both the survival and recovery of a listed species in the wild by reducing the reproduction, numbers, or distribution of the species.  "50 C.F.R. 402.02”.

To facilitate compliance with the requirements of the Endangered Species Act subsection (a)(2) the Environmental Protection Agency, Office of Pesticide Programs has established procedures to evaluate whether a proposed registration action may directly or indirectly reduce appreciably the likelihood of both the survival and recovery of a listed species in the wild by reducing the reproduction, numbers, or distribution of any listed species (U.S. EPA 2004).  After the Agency’s screening-level risk assessment is performed, if any of the Agency’s Listed Species LOC Criteria are exceeded for either direct or indirect effects, a determination is made to identify if any listed or candidate species may co-occur in the area of the proposed pesticide use.  If determined that listed or candidate species may be present in the proposed use areas, further biological assessment is undertaken.  The extent to which listed species may be at risk then determines the need for the development of a more comprehensive consultation package as required by the Endangered Species Act.

For certain use categories, the Agency assumes there will be minimal environmental exposure, and only a minimal toxicity data set is required (Overview of the Ecological Risk Assessment Process in the Office of Pesticide Programs U.S. Environmental Protection Agency - Endangered and Threatened Species Effects Determinations, 1/23/04, Appendix A, Section IIB, pg.81).  Chemicals in these categories therefore do not undergo a full screening-level risk assessment.

This preliminary analysis indicates that there is a potential for triclosan use to overlap with listed species and that a more refined assessment is warranted, to include direct, indirect and habitat effects.  The more refined assessment should involve clear delineation of the action area associated with proposed use of triclosan and best available information on the temporal and spatial co-location of listed species with respect to the action area.  This analysis has not been conducted for this assessment.  An endangered species effect determination will not be made at this time.

- Confirmatory Data Required:

- Freshwater invertebrate acute study (850.1010);

- As outlined in the environmental fate chapter for triclosan, the registrant is required to provide a scientific rationale, including appropriate modeling (e.g., surface water modeling), that addresses and quantifies the amounts of triclosan and triclosan transformation products (e.g., triclosan methyl) occuring in various environmental compartments (e.g., surface waters, biosolids, soil, fish, shellfish) from triclosan antimicrobial pesticide uses;

- Relative to the above requirement, if the registrant is not able to provide a satisfactory scientific rationale that determines the quantities of triclosan and triclosan transformation products in various environmental compartments, then EPA will assume that the present levels of triclosan and triclosan transformation products detected in such compartments occurs because of registered antimicrobial use patterns.  In this case, OPP will require the environmental fate data outlined in the triclosan environmental fate chapter; and

- Depending on the results of the environmental fate studies, which may be required (see triclosan environmental fate chapter), additional acute and chronic nontarget organism studies may be required.  These include the following studies:

a. Estuarine/marine fish acute study (850.1075) [Technical Grade Active 	Ingredient (TGAI)];

b. Estuarine/marine shrimp acute study (850.1035) (TGAI);

c. Estuarine/marine mollusk acute study (850.1025) (TGAI);

d. Fish early life-stage (freshwater) study (850.1400) (TGAI);

e. Aquatic invertebrate (freshwater) life-cycle study (850.1300) (TGAI);

f. Fish life-cycle study (850.1500);

g. Fish bioconcentration study – BCF (850.1730) (TGAI);

h. Acute sediment toxicity to freshwater invertebrates (850.1735) (TGAI);

i. Acute sediment toxicity to estuarine invertebrates (850.1740) (TGAI); 			and

j. Additional plant toxicity testing:  an additional algal toxicity test 					(850.5400) with the freshwater green alga, Selenastrum capricornutum; 				and studies on the rooted freshwater macrophyte rice (Oryza sativa) – 				850.4225 and 850.4250 (2 tests on seedling emergence and vegetative 				vigor).

IV.	 Label Hazard Statements for Terrestrial and Aquatic Organisms:

Triclosan labels must state:

“This pesticide is toxic to fish and aquatic invertebrates.”

"Do not discharge effluent containing this product into lakes, streams, ponds, estuaries, oceans, or other waters unless in accordance with the requirements of a National Pollutant Discharge Elimination System (NPDES) permit and the permitting authorities are notified in writing prior to discharge.  Do not discharge effluent containing this product to sewer systems without previously notifying the local sewage treatment plant authority.  For guidance contact your State Water Board or Regional Office of the EPA."

V.  REFERENCES

41008910.  Terrell, Y.  1985.  Acute Oral Toxicity Study of Issue Plus II; ID No. 88-472; Prepared by American Standards Biosciences Corp. for Diversey Wyandotte Corporation, Wyandotte, Michigan.

41008911.  Terrell, Y.  1988.  Avian Dietary Quaily (Litmus Test) of Issue Plus in Bobwhite Quail; Project No. 88-471; Prepared by American Standard Biosciences Corp. for Diversey Wyandotte Corporation, Wyandotte, Michigan.

41008912.  Terrell, Y.  1988.  The Acute Toxicity Bioassay of Issue Plus on Rainbow Trout; Project No. 88-474; Prepared by American Standard Biosciences Corp. for Diversey Wyandotte Corporation, Wyandotte, Michigan.

41008913.  Terrell, Y.  1988.  The Acute Toxicity Bioassay of Issue Plus on Bluegill Sunfish; Project No. 88-473; Prepared by American Standard Biosciences Corp. for Diversey Wyandotte Corporation, Wyandotte, Michigan.

41008914.  Terrell, Y.  1988.  Acute Toxicity of Issue Plus on Daphnia magna; Project No. 88-475; Prepared by American Standard Biosciences Corp. for Diversey Wyandotte Corporation, Wyandotte, Michigan.

42322101.  Boettcher, J.  1990.  Report on the Acute Toxicity (96h) of FAT 80, 023/Q to Zebrafish.  Test No. G 069 04.  Prepared by Ciba-Geigy, Ltd., D&C Product Ecotoxicology, Basel, Switzerland.  Submitted by Ciba-Giegy Corporation, Greensboro, North Carolina.

42322102.  Wuethrich, V.  1990.  48-Hour Acute Toxicity of FAT 80, 023/Q to Daphnia magna (OECD-Immobilization Test).  Project No. 262923.  Prepared by RCC Umweltchemie AG, Itingen, Switzerland.  Submitted by Ciba-Giegy Corporation, Greensboro, North Carolina.

43022602.  Pedersen, C.A. and B.R. Helsten.  1993.  Triclosan (IRGASAN DP300(): 14-Day Acute Oral LD50 Study in Bobwhite Quail.  Study performed by Bio-Life Associates, Ltd., Neillsville, Wisconsin.  Laboratory Project No. 102-024-03.  Submitted by CIBA-GEIGY Corporation, Greensboro, North Carolina.

43022603.  Pedersen, C.A. and B.R. Helsten.  1993.  Triclosan (IRGASAN DP300(): 14-Day Acute Oral LD50 Study in Mallard Ducks.  Study performed by Bio-Life Associates, Ltd., Neillsville, Wisconsin.  Laboratory Project No. 102-023-04.  Submitted by CIBA-GEIGY Corporation, Greensboro, North Carolina.

43022604.  Pedersen, C.A. and B.R. Helsten.  1993.  Triclosan (IRGASAN DP300(): 8-Day Acute Dietary LC50 Study in Bobwhite Quail.  Study performed by Bio-Life Associates, Ltd., Neillsville, Wisconsin.  Laboratory Project No. 102-022-01.  Submitted by CIBA-GEIGY Corporation, Greensboro, North Carolina.

43046001.  Bowman, J.H.  1990.  Acute Toxicity of D1063.01 (Triclosan: Irgasan DP300) to Fathead Minnow (Pimephales promelas).  Laboratory Project ID No. 38655.  Prepared by Analytical Bio-Chemistry Laboratories, Inc, Columbia, Missouri.  Submitted jointly by Proctor and Gamble Company and Ciba-Geigy Corp.

43046002.  Forbis, A.D. and J.G. Muckerman.  1990.  Acute Toxicity of D1063.01 (Triclosan: Irgasan DP300) to Daphnia magna.  Laboratory Project ID No. 38656.  Prepared by Analytical Bio-Chemistry Laboratories, Inc, Columbia, Missouri.  Submitted jointly by Proctor and Gamble Company and Ciba-Geigy Corp.

43740701.  Wuethrich, V.  1990.  Influence of FAT 80023/Q (Irgasan DP300) on Reproduction of Daphnia magna.  Project No. 262934.  Prepared by RCC Umweltchemie AG, Itingen, Switzerland.  Submitted by Ciba-Giegy AG, Basel, Switzerland.

43969301.  Sword, M.C.  1996.  Static Acute Toxicity of Triclosan to Rainbow Trout.  Study performed by ABC Laboratories, Inc., Columbia, Missouri.  Laboratory Report No. 42997.  Sponsored by CIBA Chemical Division, Greensboro, North Carolina.

44422801.  Staveley, J.P. and T.L. Williams.  1997.  Effects of Triclosan on the Growth and Reproduction of Aquatic Plants.  Study performed by Carolina Ecotox, Inc., Durham, North Carolina.  Laboratory Report ID: 21-02-1.  Sponsored by Ciba-Geigy Corporation, Greensboro, North Carolina.

Federle, T.W., Kaiser, S.K., and Nuck, B.A. 2002. Fate and Effects of Triclosan in Activated Sludge.  Environmental Toxicology and Chemistry/SETAC.  21(7): 1330-7.

Kanda, R., Griffin, P., and James, H.A., et al. 2003. Pharmaceutical and Personal Care Products in Sewage Treatment Works.  Journal of Environmental Monitoring.  5(5): 823-30.

Klopin, D.W., Furlong, E.T., Meyer, M.T., et al. 2002. Pharmaceuticals, Hormones, and Other Organic Wastewater Contaminants in U.S. Streams, 1999-2000: A National Reconnaissance. Environmental Science and Technology. 36(6): 1202-11.

McAvoy, D.C., Schatowitz, B., Martin, J., et al. 2002. Measurement Of Triclosan In Wastewater Treatment Systems. Environmental Toxicology and Chemistry. 21 (7): 1323-9.

U.S. Environmental Protection Agency, Office of Water.  Summary of Available Aquatic Toxicity Data for Aquatic Life Water Quality Criteria Development for Triclosan.  Draft: August 16, 2007.

# Footnotes

The Agency is making this statement because triclosan and triclosan transformation products are being detected in various environmental components (see triclosan environmental fate chapter).