National Climatic Data Center

DATA DOCUMENTATION

FOR

DATA SET 6117 (DSI-6117)

# CRN Raw Data

July 29, 2003

National Climatic Data Center

151 Patton Ave.

Asheville, NC  28801-5001  USA

Table of Contents

Topic                                                 Page Number

1.  Abstract................................................... 3

2.  Element Names and Definitions: ............................ 3

3.  Start Date................................................ 14

4.  Stop Date................................................. 14

5.  Coverage.................................................. 14

6.  How to order data......................................... 14

7.  Archiving Data Center. ................................... 14

8.  Technical Contact......................................... 14

9.  Known Uncorrected Problems................................ 14

10. Quality Statement......................................... 14

11. Essential Companion Data Sets............................. 15

12. References................................................ 15

1.   Abstract:  The U.S. Climate Reference Network (USCRN) is a network of climate stations now being deployed as part of a National Oceanic and Atmospheric Administration (NOAA) initiative. Its primary goal is to provide future long-term homogeneous observations of temperature and precipitation that can be coupled to long-term historical observations for the detection and attribution of present and future climate change. Data from the USCRN will be used in operational climate monitoring activities and for placing current climate anomalies into an historical perspective.

When fully implemented, the CRN will provide observations from approximately 250 locations.  Each location will be carefully selected to capture the representative climate regions of the nation.  A communications network will link each location to the National Climatic Data Center (NCDC), where the observations will be quality controlled, archived, and made readily available with their metadata to a worldwide clientele.

The primary CRN measurement parameters are air temperature and precipitation accumulation.  Measurement of these two parameters is essential for the climate record, and is required at all CRN field sites. Secondary measurement parameters are wind speed, solar radiation, and ground surface (skin) temperature. Secondary parameters contribute to improving the confidence in the observational measurements, and provide insight into the reliability and performance of the primary sensors.

Every CRN instrument site is being equipped with a standard set of automated sensors, a data logger, and a satellite communications transmitter attached to a typical 3 meter (10 feet) instrument tower.  The Atmospheric Turbulence and Diffusion Division (ATDD) of NOAA's Air Resources Laboratory assembles, calibrates installs and, presently, maintains the sites.  The specific system capabilities and modes of operation have been documented in the CRN Functional Requirements Document (FRD).  Further information is contained in other documents such as the Site Information Handbook, Instrument Manuals, and Metadata Management and are available from NCDC’s CRN website.

The CRN Program addresses the full spectrum of data management functions, such as measuring and recording climate related surface environmental parameters, data processing and quality control, timely access to data and documentation, data analysis, extensive documentation, long-term life cycle maintenance, and long-term stewardship (archive).  This document is limited to describing specific data management processes involved in data ingest, data processing, data quality control and data archive. It also provides information on how to read the raw, unprocessed CRN data.

2.   Element Names and Definitions:

The USCRN data flow begins with the sensors in the field and ends with the access and archive of this data after it has been processed.  Every USCRN instrument site is being equipped with a standard set of automated sensors, a data logger, and a satellite communications transmitter attached to a typical 3 meter (10 feet) instrument tower.  There are three temperature probes recording data independently and three measurements of precipitation data from a three-wire Geonor gauge. Other measured parameters are wind speed, solar radiation, and ground surface (skin) temperature.  (Candidate parameters for future addition include relative humidity, soil moisture, and soil temperature.)  Precipitation data, recorded every fifteen minutes, temperature data, and the other hourly observations are collected in a data logger attached to the tower. These data are transmitted within a few minutes after each hour via a GOES satellite transmitter for further delivery to NCDC.  The data management overview is described in this section, beginning with the acquisition of the data.

At the field sites, a suite of automated instrument sense meteorological parameters.  These sensors are sampled frequently as a function of the response time of the instrument.  Temperature data, for example, are polled from all three sensors every two seconds. A processing unit, or data logger, creates five-minute averages of the polled values. The twelve five-minute averages are averaged to produce hourly values. Precipitation data are recoded for each of three wires on the rain gauges every fifteen minutes.  (Specifics of data acquisition for temperature, precipitation, and for all the other parameters are available on the CRN website).  The total processing time for the data logger is about 0.6 seconds. The data stream is sent to a communications device, or data buffer, and transmitted via GOES (see Figure1-1). The message usually takes about 7 seconds to transmit.

Figure 1-1.  Data Acquisition Data Stream

A 20-second transmit window for GOES is open, starting at the top of the hour. A second 20-second window follows the first.  If however, the processing of the data is not completed before the opening of the second window, the data are held in the Transmitter Buffer for later transmission.  One reason for failure to transmit is a failure to get a lock on the GPS synchronization.  The data logger clock is reset every 6 hours to enable synchronization.

If the data have not transmitted for whatever reason, all the data that have not been transmitted are later transmitted, in what is called "data catch up mode."  Approximately 30 days of data can be stored and transmitted in catch-up mode.

The data stream leaving the data logger has 80 values, each six-characters long, 4 digits, one decimal point, and a (+ or -) sign indicator, making a 480-character length record.  The transmit buffer put together the current record and the record from the previous 2 hours, making a record of 1440 characters. The GOES transmission adds a 38 character leader to the data message.

Data are initially sensed by instruments in the field and processed into meteorological values by the Data Logger, then transmitted to NCDC.  The USCRN dataflow is schematically shown in Figure 1-2.  Data flows from the Field Sites, through the Communications Network, to NCDC, then made available to the User Community.

Figure 1-2.  USCRN Data Management Activities

The Data Management activities described in this document are in the NCDC square of the Figure 1-2.  They include the processes of data ingest, processing, quality control, archive and access.

The processes that affect the data stream, that is, any source code, script files, or other procedures that affect the way the data is processed are Configuration Items.  Changes to Configuration Items are under Configuration Management.  The Configuration Management Plan and the Configuration Management Procedures, documented elsewhere, describe the approval process and procedures for changes to Configuration Items.

Once approved, the Data Operations Division handles implementing changes to the software within the appropriate branch.   The processes for data Ingest, Processing, automated Quality Control, and Archive are maintained by the Data Processing Branch of NCDC and are described in the CRN Ingest document (see Appendix A).  The Data Access Branch maintains the processes for data display and web Access.  Programming is done with accepted standards - C++, Perl, Java, etc. and documented to industry standards.  Following approval, changes to the software are initiated by through Change Request forms, sent to the Network Monitoring Lead and are logged through emails.  The appropriate branch of the Data Operations Division implements the change following the generic process described in the Change Request document and sketched in the change request flow diagram (see Figure 1-3).

Figure 1-3.  CRN Change Request Flow Diagram

Once the software changes are tested and implemented, the Network Monitoring Team Lead ensures that the closure to the change request is filed in the email folder, and registers appropriate metadata documentation with the Data Archive Branch.

Data Ingest

After the data stream are acquired at the Field Site and transmitted over the communications network, they are ingested at NCDC.  The Data Ingest Process described here begins with acquiring the data from GOES and ends with creating a Raw Data Archive.

## Ingest from Transmissions

Data are transmitted over the communications network to the GOES Wallops Virginia facility The Data Ingest allow for multiple access pathways from GOES to NCDC (see figure 2-1) including a direct readout from GOES and NOAA port channel from the National Weather Service Telecommunications Gateway (NWSTG).

Figure 2-1.  Ingest Pathways

The primary data ingest pathway is the GOES Local Read Out Ground Station (LRGS). Through this path, data from the GOES communication are available for ingest at NCDC approximately 5 minutes past each hour.

A data ingest script file process samples two communications ports, primarily, the GOES and secondarily, NOAAPORT. The process, which runs continuously 24 hours a day, 7 days a week is run on a microcomputer called Humboldt.  In the event that no data are received from either pathway, a script will automatically be executed which will attempt to retrieve data from alternative avenues, such as from the Reston US Geological Survey (see Figure 2-2).

Figure 2-2.  Data Ingest

As Humboldt receives incoming data streams, it initiates another process that writes a Raw Data Archive on a mass storage device.  This archive is an exact replica of the data as ingested, before any sort of data processing or manipulation has occurred.  The Raw Data Archive conforms to best practices of NCDC NARA standards, that is, with back-up off-site storage, media migration, and so forth.  The Active Archive Branch of NCDC maintains the Dataset documentation for the Raw Data Archive.

## Ingest from PDAs

If for some reason data transmission failed, or the data transmitted did not successfully make it through the communications network to the NCDC archives, a Personal Digital Assistant (PDA) can be used to download data from the data logger.  Data is retained at each site in the memory of the data logger for approximately five to six months.

A process is run during data ingest to generate time of receipt statistics.  At the end of every calendar month, ATDD personnel monitor the Data Availability statistics. Stations that have had less than 97% data availability for the month are flagged and stations missing any data in the previous 4 months are examined.  An analysis is performed to determine if there is a possibility data may reside on the data logger at the site that can be used to supplement the data received and archived at NCDC.  If the analysis indicates there is any possibility data can be retrieved, the site host/contact is notified and a PDA (along with instructions, batteries, return shipping label, etc.) is shipped via overnight mail to the site.  (Note: 5 sites currently have laptop PCs with data logger software that allows the retrieval of data onto the laptop, which can then be emailed to ATDD).

When a PDA is returned to ATDD, the data on the PDA is downloaded to the ATDD FTP site into the directory:      ftp://ftp.atdd.noaa.gov/pub/crn/palm

The data files on the FTP site have a naming convention of: XXXXXXXX_YYYYMMDD, where:

XXXXXXXX	- GOES ID of the station (6 to 8 characters, as required)

YYYY		- Year of last piece of data in file

MM		- Month of last piece of data in file

DD		- Day of month of last piece of data in file

At NCDC a cron job checks the ATDD FTP directory on a routine basis, and if it finds a new file in the directory the file is downloaded to NCDC.  An auto-generated email is sent from NCDC to ATDD to indicate that a file has been successfully retrieved at NCDC.

If any files from the ATDD FTP site are processed at NCDC, a message is generated by NCDC that has the following columns:

GOES ID

Year:Mo

#Obs Expected

#Obs Before Recovery

#Obs Recovered

% Recovered

% Complete

# Data Processing

## Data Ingest Processing

Data Ingest Processing involves breaking the raw data file into individual

#### Figure 3-1.  Data Ingest Process

records and writing direct access files.  As the Raw Data Archive File is being written, a Data Load script is simultaneously run on Humboldt.  The script checks the record length, and breaks the data stream, consisting of three observations, into three individual records (see Figure 3-1).  The process anticipates the record length for each station.  The data stream is an ASCII flat file with three observations per record, the present hour, and the two previous hours. Most stations have 80 six-character values and some header information.  There can be a variation in the record length if a station is configured with one or with 3 wires on the Geonor rain gauge, or if a station records more secondary parameters.  Stations with a 3-wire Geonor have longer record lengths (1718 characters) than stations with a 1-wire Geonor (1130 characters.)  If the record length is unacceptable, the record is discarded.  If it is as expected, the data stream is broken into three individual records.

The data stream now contains one record of 80 values, with the values in order as follows:

- Year

- Julian Date

- Time, 24 hour format with midnight equal to 2400

- Latitude

- Longitude

- Temperature #1 hourly average

- Temperature #1 standard deviation

- Temperature #2 hourly average

- Temperature #2 standard deviation

- Temperature #3 hourly average

- Temperature #3 standard deviation

- CS500 probe Temperature hourly average

- CS500 probe Temperature standard deviation

- CS500 probe RH hourly average

- CS500 probe RH standard deviation

- Temperature #1 hour minimum

- Temperature #1 hour minimum time of occurrence

- Temperature #2 hour minimum

- Temperature #2 hour minimum time of occurrence

- Temperature #3 hour minimum

- Temperature #3 hour minimum time of occurrence

- Temperature #1 hour maximum

- Temperature #1 hour maximum time of occurrence

- Temperature #2 hour maximum

- Temperature #2 hour maximum time of occurrence

- Temperature #3 hour maximum

- Temperature #3 hour maximum time of occurrence

- Average Temperature for sensor 1 for minutes 55 to 59

- Average Temperature for sensor 2 for minutes 55 to 59

- Average Temperature for sensor 3 for minutes 55 to 59

- Precipitation for 0 to 15 minutes of hour VW #1

- Precipitation for 16 to 30 minutes of hour VW #1

- Precipitation for 31 to 45 minutes of hour VW #1

- Precipitation for 46 to 60 minutes of hour VW #1

- Precipitation total for hour VW #1

- Wind Speed average for hour

- Wind Speed standard deviation

- Solar Radiation

- Solar Radiation standard deviation

- Surface Temperature

- Surface Temperature standard deviation

- Hour rain gage frequency average for VW #1

- Hour rain gage frequency minimum for VW #1

- Hour rain gage frequency maximum for VW #1

- Fan speed output for aspirated shield #1 East

- Fan speed output for aspirated shield #2 South

- Fan speed output for aspirated shield #3 West

- Battery voltage for fan and GOES transmitter battery

- Battery voltage for fan and GOES transmitter battery under full load

- Battery voltage for CR23X data logger

- Time in minutes during the past hour that the enclosure door was open

- CR23X program version number

- mm depth at end of 1st 15 minutes for VW #1

- mm depth at end of 2nd 15 minutes for VW #1

- mm depth at end of 3rd 15 minutes for VW #1

- mm depth at end of 4th 15 minutes for VW #1

- Rainfall for VW #2 1st 15 minutes in mm

- Rainfall for VW #2 2nd 15 minutes in mm

- Rainfall for VW #2 3rd 15 minutes in mm

- Rainfall for VW #2 4th 15 minutes in mm

- Rainfall total for hour for VW #2

- mm depth at end of 1st 15 minutes for VW #2

- mm depth at end of 2nd 15 minutes for VW #2

- mm depth at end of 3rd 15 minutes for VW #2

- mm depth at end of 4th 15 minutes for VW #2

- Hour rain gage frequency average for VW #2

- Hour rain gage frequency minimum for VW #2

- Hour rain gage frequency maximum for VW #2

- Rainfall for VW #3 1st 15 minutes in mm

- Rainfall for VW #3 2nd 15 minutes in mm

- Rainfall for VW #3 3rd 15 minutes in mm

- Rainfall for VW #3 4th 15 minutes in mm

- Rainfall total for hour for VW #3

- mm depth at end of 1st 15 minutes for VW #3

- mm depth at end of 2nd 15 minutes for VW #3

- mm depth at end of 3rd 15 minutes for VW #3

- mm depth at end of 4th 15 minutes for VW #3

- Hour rain gage frequency average for VW #3

- Hour rain gage frequency minimum for VW #3

- Hour rain gage frequency maximum for VW #3

Note all temperature measurements are in degrees Celsius.  All wind speed measurements are in meters per second. All voltages are in volts.

More detailed information about the USCRN Limits and Ranges can be found in Appendix A.

Next, a Fortran common block is defined.  Knowing the order of the elements in the data stream, the position of signs and decimal points, a check is performed to ensure that expected characters appear in the expected places.  If the data are garbled, the record is rejected.  Otherwise, the record is accepted. Lastly, a script is run on Humboldt to Write Direct Access Files.

## Data Processing

More data processing occurs after the Humboldt writes the Direct Access Files. Further processing includes automatic procedures to eliminated duplicates, processes to produce data message files, processes to perform automatic quality control checks, and to load data into Oracle Data Tables for on-line access (See Figure 3-2).  These processes are outline in the next two sections.

Using direct access files enables easy data access and availability and allows for easy elimination of duplicate observations. As the files are being written, a process checks for and discards duplicate records, (remember, every record could be ingested three times).

.

Figure 3-2.  Data Process

After discarding duplicate messages, every hour the script DATA MSG is run to identify what data were not received for the hour.  A file is produced and sent via email to the Network Monitoring Team.  A sample excerpt from the file follows:

DATA MSG FOR LATEST HOUR

GMT HOUR 09 not found for station Barrow 4 ENE, NOAA (CMDL Observatory) on Sun Jun 15 05:55:01 EDT 2003

LAST KEY IN crn200306.00F0B0 IS 1413H035

GMT HOUR 09 not found for station Fairbanks 11 NE, NOAA / NESDIS (FCDAS) on Sun Jun 15 05:55:01 EDT 2003

LAST KEY IN crn200306.0102CE IS 1418H313

NO DATA RECEIVED FOR 0184DA John Day 35 WNW, John Day Fossil Beds Nat. Mon for Jun 2003

The process CRN INV produces inventories of the data, showing time periods of missing data.  It is produced daily and monthly. These reports are available by automated email once daily for the previous day, and once monthly for the previous month.  Summary reports on Data Inventory can also be produced on demand for any range of stations, for any range of time periods. This command is available on the restricted access CRN Website (http://www.ncdc.noaa.gov/oa/climate/uscrn/).

# Data Archive

Both raw and processed data are stored in archives.  Unprocessed data, the Raw Data, are written to a mass storage device during data ingest (see Figure 2-2). The Raw Data Archive is registered in the NESDIS data catalog as TD# 6117. Processed or flagged data are written to a mass storage device following quality control (see figure 3-2).  The Flagged Data Archive is registered in the NESDIS data catalogue as TD# 3286. Documentation for both archives resides with the Archive Branch of the Data Operations Division.

TD# 3286 adheres to full compatibility with NCDC element-structured databases. Archival CRN data files will adhere to full compatibility with NCDC element-structured data bases. Hourly, daily, and monthly data will be compatible with

- TD3280 - Hourly (requiring WBAN numbers),

- TD3200 - Daily (requiring coop numbers) and

- TD3220 – Monthly (requiring coop numbers).

The dataset documentation for TD# 3286 includes a description of the data stream, elements recorded, and units of measurement (go to on-line documentation and select 3286 here: http://www4.ncdc.noaa.gov/ol/documentlibrary/datasets.html.)   One page summaries on each of the sensors, which explain how each parameter (temp, precip, solar etc) is measured, is also included with the dataset documentation and can be found on the CRN web site (see

http://www.ncdc.noaa.gov/servlets/crninstrdoc#SENSORS)

The Archive is done within NARA standards using approved storage media and equipment. Mitigation plans include an automated migration from data on the mass store to higher capacity media.  Physical off-site storage with routine back-up procedures exist.   NCDC is developing Continuity of Operations Plan.   With the implementation of the Comprehensive Large Array Stewardship System (CLASS) NCDC will have a mirror site in Washington DC.

3.   Start Date: 20011001

4.   Stop Date: Ongoing.

5.   Coverage: Areal Coverage USA

a. Southernmost Latitude:   25o S. Latitude

b. Northernmost Latitude:   50o N. Latitude

c. Westernmost Longitude: -125o W. Longitude

d. Easternmost Longitude:  -65o E. Longitude

6.   How to Order Data:

Ask NCDC’s Climate Services about the cost of obtaining this data set.

Phone: 828-271-4800

FAX: 828-271-4876

E-mail: NCDC.Orders@noaa.gov

7.   Archiving Data Center:

National Climatic Data Center

Federal Building

151 Patton Avenue

Asheville, NC  28801-5001

Phone: (828) 271-4800.

8.   Technical Contact:

National Climatic Data Center

Federal Building

151 Patton Avenue

Asheville, NC  28801-5001

Phone: (828) 271-4800.

9.   Known Uncorrected Problems: None.

10.  Quality Statement: The process CRN-QC performs automated quality control on the Direct Access Files. Briefly, these processes include the following checks.

- Modular 1 performs sensor limit checks

- Modular 2 performs standard deviation checks

- Modular 3 performs inter-comparison checks

Next, the CRN2DB script loads data and flags into the Oracle data base Table Files, one for the data and one for the flags.

Hourly, a QA/AC message shows data that have failed some quality control check (see Appendix F for a sample).  Script files produce Data Flag Summary reports from the Flag Table. These reports are produced daily, weekly, and monthly.  The various data quality flags are displayed in the Monthly Flag Summary report.

Summary reports on Data Flags can also be produced on demand for any range of stations, for any range of time periods. This command is available on the restricted access Website (http://www.ncdc.noaa.gov/oa/climate/uscrn/) for CRN Data Access Module.

In addition, CRN data are included in with separate systems run by the Data Processing Branch of the Data Operations Division.  Specifically, CRN temperature data are used in TEMPVAL, an automated quality control process used for validating data from the Cooperative Station Network.

11.  Essential Companion Datasets: None.

12.  References: No information provided with original documentation.

Appendix A

El Flg Ch  ID         Description                                Units             Range Limits

| 1 |  | 37 | Full ID |  |  | Min Max | Max |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2 |  | 6 | Year | 4-digit year |  | 2000 | 2020 |
| 3 |  | 6 | jday | Julian Date - Day of the year from 1 - 366 |  | +001.0 | +366.0 |
| 4 |  | 6 | time | Hour and Minute of observation hour | hours, minutes | +0001. | +2400. |
| 5 |  | 6 | lat | Latitude of the CRN site | Degrees, tenths | CRN MSL | CRN MSL |
| 6 |  | 6 | lon | Longitude of the CRN site | Degrees, tenths | CRN MSL | CRN MSL |
| 7 8 | 7 | 6 6 | temp1avg temp1sd | 60 minute average of temp sensor # 1 Standard deviation of temp sensor # 1 | Degrees C | -60.00 0.0000 | +60.00 3.0000 |
| 9 10 | 9 | 6 6 | temp2avg temp2sd | 60 minute average of temp sensor # 2 Standard deviation of temp sensor # 2 | Degrees C | -60.00 0.0000 | +60.00 3.0000 |
| 11 12 | 11 | 6 6 | temp3avg temp3sd | 60 minute average of temp sensor # 3 Standard deviation of temp sensor # 3 | Degrees C | -60.00 0.0000 | +60.00 3.0000 |
| 13 14 | 13 | 6 6 | cs500tavg cs500tsd | 60 minute average of RH temp sensor Standard deviation of RH temp sensor | Degrees C | -60.00 0.0000 | +60.00 3.0000 |
| 15 16 | 15 | 6 6 | cs500rhav Cs500rhsd | 60 minute average of RH sensor Standard deviation of RH sensor | Percent | +00.00 0.0000 | +100.0 30.000 |
| 17 | 17 | 6 | tmp1min | Minimum temp recorded by temp sensor #1 | Degrees C | -60.00 | +60.00 |
| 18 | 18 | 6 | tmp1ntime | Minute of the hour the min temp occurrred | hours, minutes | +0000. | +2359. |
| 19 | 19 | 6 | tmp2min | Minimum temp recorded by temp sensor #2 | Degrees C | -60.00 | +60.00 |
| 20 | 20 | 6 | tmp2time | Minute of the hour the min temp occurrred | hours, minutes | +0000. | +2359. |
| 21 | 21 | 6 | tmp3min | Minimum temp recorded by temp sensor #3 | Degrees C | -60.00 | +60.00 |
| 22 | 22 | 6 | tmp3time | Minute of the hour the min temp occurrred | hours, minutes | +0000. | +2359. |
| 23 | 23 | 6 | tmp1max | Maximum temp recorded by temp sensor #1 | Degrees C | -60.00 | +60.00 |
| 24 | 24 | 6 | tmp1time | Minute of the hour the max temp occurrred | hours, minutes | +0000. | +2359. |
| 25 | 25 | 6 | tmp2max | Maximum temp recorded by temp sensor #2 | Degrees C | -60.00 | +60.00 |
| 26 | 26 | 6 | tmp2time | Minute of the hour the max temp occurrred | hours, minutes | +0000. | +2359. |
| 27 | 27 | 6 | tmp3max | Maximum temp recorded by temp sensor #3 | Degrees C | -60.00 | +60.00 |
| 28 | 28 | 6 | tmp3time | Minute of the hour the max temp occurrred | hours, minutes | +0000. | +2359. |
| 29 | 51 | 6 | avt1_5559 | Average Temp of Sensor #1 for minutes 55 - 59 | Degrees C | -60.00 | +60.00 |
| 30 | 52 | 6 | avt2_5559 | Average Temp of Sensor #2 for minutes 55 - 59 | Degrees C | -60.00 | +60.00 |
| 31 | 53 | 6 | avt3_5559 | Average Temp of Sensor #3 for minutes 55 - 59 | Degrees C | -60.00 | +60.00 |
| 32 | 29 | 6 | pcp0-15 | Amount of precip recorded during 1st 15 minutes VW#1 | millimeters | +0.000 | +600.0 |
| 33 | 30 | 6 | pcp16-30 | Amount of precip recorded during 2nd 15 minutes VW#1 | millimeters | +0.000 | +600.0 |
| 34 | 31 | 6 | pcp31-45 | Amount of precip recorded during 3rd 15 minutes VW#1 | millimeters | +0.000 | +600.0 |
| 35 | 32 | 6 | pcp46-60 | Amount of precip recorded during 4th 15 minutes VW#1 | millimeters | +0.000 | +600.0 |
| 36 | 33 | 6 | pcphtot | Amount of precip recorded for the hour VW#1 | millimeters | +0.000 | +600.0 |
| 37 38 | 34 | 6 6 | avgwspd awspdsd | Average wind speed recorded for the hour Average wind speed standard deviation | Meters/sec | +00.00 0.0000 | +60.00 20.000 |
| 39 40 | 36 | 6 6 | solrad solradsd | Amount of solar radiation recorded during past hour Solar radiation standard deviation | Watts/sq meter | +0000. 0.0000 | +1500. 550.00 |
| 41 42 | 38 | 6 6 | sfctmp sfctmpsd | Temperature of the ground surface Surface temp standard deviation | Degrees C | -60.00 0.0000 | +90.00 6.0000 |
| 43 | 40 | 6 | pcpgavfreq | Average frequency of WRG vibrating wire | Hertz | +0000. | +3000. |
| 44 | 41 | 6 | pcpgfreqmn | Minimum frequency of WRG vibrating wire | Hertz | +0000. | +1000. |
| 45 | 42 | 6 | pcpgfreqmx | Maximun frequency of WRG vibrating wire | Hertz | +0000. | +3000. |
| 46 | 43 | 6 | fanspd1e | The fan speed of the aspirated shield #1 East | Revs/sec | +90.00 | +125.0 |
| 47 | 44 | 6 | fanspd2s | The fan speed of the aspirated shield #2 South | Revs/sec | +90.00 | +125.0 |
| 48 | 45 | 6 | fanspd3w | The fan speed of the aspirated shield #3 West | Revs/sec | +90.00 | +125.0 |
| 49 | 46 | 6 | battvol | Battery voltage of fan & GOES transmitter | Volts | +12.00 | +14.50 |
| 50 | 47 | 6 | battvol_fl | Battery voltage of fan & GOES transmitter, full load | Volts | +11.00 | +14.50 |
| 51 | 48 | 6 | battvol_dl | Battery voltage of CR23X datalogger | Volts | +10.00 | +14.50 |
| 52 | 49 | 6 | opndoor_tm | # of minutes datalogger door open past hour | hours, minutes | +0001. | +2359. |
| 53 | 50 | 6 | cr23xver |  |  |  |  |
|  | 54 | 6 | pcp2_0015 |  |  |  |  |
|  | 55 | 6 | pcp2_1630 |  |  |  |  |
|  | 56 | 6 | pcp2_3145 |  |  |  |  |
|  | 57 | 6 | pcp2_4660 |  |  |  |  |
|  | 58 | 6 | pcp2htot |  |  |  |  |
| 54 | 59 | 6 | gdp1st15_1 | Gage Depth Reading 1st 15 minutes VW#1 | millimeters | -2.000 | +600.0 |
| 55 | 60 | 6 | gdp2nd15_2 | Gage Depth Reading 2nd 15 minutes VW#1 | millimeters | -2.000 | +600.0 |
| 56 | 61 | 6 | gdp3rd15_3 | Gage Depth Reading 3rd 15 minutes VW#1 | millimeters | -2.000 | +600.0 |
| 57 | 62 | 6 | gdp4th15_4 | Gage Depth Reading 4th 15 minutes VW#1 | millimeters | -2.000 | +600.0 |
| 58 | 63 | 6 | pcp1st15_2 | Precipitation 1st 15 minutes for VW#2 | millimeters | +0.000 | +600.0 |
| 59 | 64 | 6 | pcp2nd15_2 | Precipitation 2nd 15 minutes for VW#2 | millimeters | +0.000 | +600.0 |
| 60 | 65 | 6 | pcp3rd15_2 | Precipitation 3rd 15 minutes for VW#2 | millimeters | +0.000 | +600.0 |
| 61 | 66 | 6 | pcp4th15_2 | Precipitation 4th 15 minutes for VW#2 | millimeters | +0.000 | +600.0 |
| 62 | 67 | 6 | pcphrtot_2 | Precipitation hour total for VW#2 | millimeters | +0.000 | +600.0 |
| 63 | 68 | 6 | gdp1st15_2 | Gage Depth Reading 1st 15 minutes VW#2 | millimeters | -2.000 | +600.0 |
| 64 | 69 | 6 | gdp2nd15_2 | Gage Depth Reading 2nd 15 minutes VW#2 | millimeters | -2.000 | +600.0 |
| 65 | 70 | 6 | gdp3rd15_2 | Gage Depth Reading 3rd 15 minutes VW#2 | millimeters | -2.000 | +600.0 |
| 66 | 71 | 6 | gdp4th15_2 | Gage Depth Reading 4th 15 minutes VW#2 | millimeters | -2.000 | +600.0 |
| 67 | 72 | 6 | pcpgavfq_2 | Gage Hour Freq Average for VW#2 | Hertz | +0000. | +3000. |
| 68 | 73 | 6 | pcpgmnfq_2 | Gage Hour Freq Minimum for VW#2 | Hertz | +0000. | +1000. |
| 69 | 74 | 6 | pcpgmxfq_2 | Gage Hour Freq Maximum for VW#2 | Hertz | +0000. | +3000. |
| 70 | 75 | 6 | pcp1st15_3 | Precipitation 1st 15 minutes for VW#3 | millimeters | +0.000 | +600.0 |
| 71 | 76 | 6 | pcp2nd15_3 | Precipitation 2nd 15 minutes for VW#3 | millimeters | +0.000 | +600.0 |
| 72 | 77 | 6 | pcp3rd15_3 | Precipitation 3rd 15 minutes for VW#3 | millimeters | +0.000 | +600.0 |
| 73 | 78 | 6 | pcp4th15_3 | Precipitation 4th 15 minutes for VW#3 | millimeters | +0.000 | +600.0 |
| 74 | 79 | 6 | pcphrtot_3 | Precipitation hour total for VW#3 | millimeters | +0.000 | +600.0 |
| 75 | 80 | 6 | gdp1st15_3 | Gage Depth Reading 1st 15 minute VW#3 | millimeters | -2.000 | +600.0 |
| 76 | 81 | 6 | gdp2nd15_3 | Gage Depth Reading 2nd 15 minute VW#3 | millimeters | -2.000 | +600.0 |
| 77 | 82 | 6 | gdp3rd15_3 | Gage Depth Reading 3rd 15 minute VW#3 | millimeters | -2.000 | +600.0 |
| 78 | 83 | 6 | gdp4th15_3 | Gage Depth Reading 4th 15 minute VW#3 | millimeters | -2.000 | +600.0 |
| 79 | 84 | 6 | pcpgavfq_3 | Gage Hour Freq Avg for VW#3 | Hertz | +0000. | +3000. |
| 80 | 85 | 6 | pcpgmnfq_3 | Gage Hour Freq Minimum for VW#3 | Hertz | +0000. | +1000. |
| 81 | 86 | 6 | pcpgmxfq_3 | Gage Hour Freq Maximum for VW#3 | Hertz | +0000. | +3000. |
|  |  | T | Transmit | * means that this element will be transmitted via the NOAAport in SHEF format |  |  |  |
|  |  |  |  | a means that the average of these elements will be transmitted via the NOAAport in SHEF format |  |  |  |

# Text boxes

offline

online

Raw-Data Archive

Flagged-Data Archive

Maintenance Provider

Maintenance Notification

Quality Control

Processing

Ingest

Access

User Community

Internet

Processing Unit

Communications Device

Instrument Suite

Field Sites

Communications Network

NCDC