# DAG Concept Element 11

(Terminal Arrival: Self Spacing for Merging and In-trail Separation)

# Overview Description

January 31, 2002

# NAS2-98005

# Technical Research in Advanced Air Transportation Technologies

Final

Overview Description

# DAG Concept Element 11

# (Terminal Arrival: Self Spacing for Merging and In-trail Separation)

CDRL Item 5b

# Prepared under

# RTO – 62

# AATT Operational Concept for ATM – Year 2002 Update

#### January 31, 2002

#### Prepared For:  NASA Ames Research Center

#### Moffett Field, CA 94035-1000

#### Prepared By:  Titan Systems Corporation – SRC Division

#### Billerica, MA 01821-4134

# DAG CE.11 – Terminal Arrival: Self Spacing for Merging and In-trail Separation

###### Overview Description

Concept Element 11 (CE-11) is focused on bringing greater flight efficiency and runway throughput to busy terminal areas and runways through flight crew (FC) use of flight management system (FMS) and cockpit display of traffic information (CDTI) technology. The general idea is that by implementing a distributed control system via integrating FMS and CDTI avionics with the air traffic management (ATM) system would enable the flight crew (FC) to provide tighter control of the merging and spacing processes. The excess spacing buffers that exist between consecutive aircraft during approach could be reduced. This spacing buffer reduction could increase runway throughput. In addition, by enabling the aircraft to fly more direct or efficient routes within the terminal airspace, additional flight efficiencies could be realized.

This concept is based on the general hypothesis that by enabling distributed approach control conducted by the individual participating FCs would provide greater flight efficiency and other benefits and would be more cost effective than providing the air traffic service provider (ATSP) with more automation tools to pursue the same benefits. Future research experiments are to be conducted to prove or disprove this hypothesis.

#### Concept Overview

In visual meteorological conditions (VMC), aircraft are often able to maintain closer spacing during the terminal approach phase of flight, thereby increasing the capacity of the terminal area and the runway acceptance rate.  In the current system, the FC’s are often requested to accept responsibility for visual self-separation once they acknowledge they can see the immediately leading aircraft.  In this situation, the FC is responsible for determining and then maintaining a safe separation from the immediate Lead aircraft, and is therefore not subject to the ATSP’s minimum separation requirements. CE-11 addresses providing similar spacing during instrument meteorological conditions (IMC) via use of the CDTI.

Figure 1 is a bubble chart of the different aspects of CE-11. It shows the conceptual sequential roles of the ATSP and FC (that is, properly Equipped Aircraft) in using both ground system and flight deck technology to improve the approach phase of flight, beginning outside of the TRACON and ending at the final approach fix (FAF). Note that the ATSP continues to have extensive involvement in this concept in defining and managing the traffic approach scenario and in conducting the ATSP procedures that enable this concept to work.

Figure 1. Sequential Stages of the CE-11 Processes

Self-separation will enable the FC’s of equipped aircraft to merge autonomously with another arrival stream and/or maintain in-trail separation relative to a designated Lead aircraft under IMC as they would under VMC, thus potentially increasing arrival throughput.  In this investigation, self-merging and spacing applies to aircraft that are subject to spacing requirements during arrival, extending from the terminal area feeder fix (FF) or TRACON boundary to FAF.

Anticipated procedures for self merging and spacing involve the ATSP transferring responsibility for in-trail separation to FCs of properly equipped aircraft, while retaining responsibility for separating these aircraft from crossing and non-equipped traffic.  Once the FC receives clearance to merge and maintain spacing relative to a designated Lead aircraft, the FC establishes and maintains a relative position of their aircraft with frequent monitoring and speed/course adjustments.

Under some conditions, information such as required time of arrival (RTA) at the FAF may be provided by an appropriate ATSP-based DST, thereby enabling accurate inter-arrival spacing that accounts for differing final approach speeds or wake vortex avoidance.  Similarly, RTAs may be used at each traffic stream merge point so that aircraft FMS guidance generates trajectories that are smoothly merged by meeting the associated RTAs.

Self-merging and spacing will make use of data link capabilities to provide traffic position information. The CDTI and/or advanced flight director/heads up display (HUD) will provide guidance technology as the source of spatial and temporal situation awareness to the FC.  Cues within the traffic display will provide information to the FC to enable either manual merging followed by station keeping or monitoring of automatic 4D trajectory management by the FMS.

#### BIBLIOGRAPHY

- Sorensen, John, Detailed Description for CE-11, Terminal Arrival: Self-Spacing for Merging and In-trail Separation, Seagull Technology Inc., November 2000.

- Anon., “Concept Definition for Distributed Air/Ground Traffic Management (DAG-TM) Version 1.0,” NASA AATT Project Internal Document, September 1999.

- Anon., “DAG-TM Concept Element 11 Research Plan,” NASA AATT Project Internal Document, March 15, 2000.

- Sorensen, J., Hollister, W., Burgess, M., and Davis, D., “TCAS-Cockpit Display of Traffic Information (CDTI) Investigation,” DOT/FAA/RD-91, Federal Aviation Administration, Washington, DC, April 1991.

- Love, W. D., et al, “A Concept for Reducing Oceanic Separation Minima Through the Use of a TCAS-Derived CDTI,” NASA CR-172258, Washington, D.C., January 1984.

- Chappell, S. L., et al, “Pilots’ Use of a Traffic Alert and Collision Avoidance System (TCAS II) in Simulated Air Carrier Operations,” NASA TM-100094, NASA Ames Research Center, Moffett Field, CA, 1989.

- Sorensen, J. A., and Goka, T., “Analysis of In-Trail Following Dynamics of CDTI-Equipped Aircraft,” J. of Guidance, Control, and Dynamics, Vol. 6, No. 3, May-June 1983.

- Goka, T., “Enhanced TCAS II/CDTI Traffic Sensor Digital Simulation Model and Program Description,” NASA CR 172445, Langley Research Center, Hampton, VA, October 1984.

- Connelly, M. E., “Simulation Studies of Airborne Traffic Situation Display Applications,” MIT ESL-R-751, Cambridge, MA, May 1977.

- Williams, D. H., “Time-Based Self-Spacing Techniques Using Cockpit Display of Traffic Information During Approach to Landing in a Terminal Area Vectoring Environment,” NASA TM-84601, Langley Research Center, Hampton, VA, 1983.

- Williams, D. H., and Wells, D. C., “Jet Transport Operations Using Cockpit Display of Traffic Information During Instrument Meteorological Conditions,” NASA TP-2567, Langley Research Center, Hampton, VA, May 1986.

- Hart, S. G., and Wempe, T. E., “Cockpit Displays of Traffic Information: Airline Pilots’ Opinions about Content, Symbology, and Format,” NASA TM 78601, Ames Research Center, Moffett Field, CA, August 1979.

- Palmer, E. A., et al, “Perception of Horizontal Aircraft Separation on a Cockpit Display of Traffic Information,” Human Factors, Vol. 22, No. 5, October 1980.

- Abbott, T. S., “A Compensatory Algorithm for the Slow-Down Effect on Constant-Time-Separation Approaches,” NASA TP 2386, Langley Research Center, VA, 1985.

- Abbott, T. S., “Simulation of a Cockpit-Display Concept for Executing a Wake-Vortex Avoidance Procedure,” NASA TP-2300, 1984.

- Abbott, T. S., “A Cockpit-Display Concept for Executing a Multiple Glide-Slope Approach for Wake-Vortex Avoidance,” NASA TP-2386, 1985.

- Swedish, W. J., “Evaluation of the Potential for Reduced Longitudinal Spacing on Final Approach,” Rep. No. FAA-EM-79-7, August 1979.

- Cieplak, J. J., “Operational Trials of the In-Trail Climb Procedure: Interim Results,” Mitre Paper 97W0000121, 1995.

- RTCA, “Guidance for Initial Implementation of Cockpit Display of Traffic Information, Document No. RTCA/DO-243, 1998.

- RTCA, “Operations Concepts for Cockpit Display of Traffic Information (CDTI) Applications,” Draft 1, RTCA Paper No. 186-98, September 1998.

- RTCA, “Development and Implementation Planning Guide for Automatic Dependent Surveillance Broadcast (ADS-B) Applications,” Paper No. 114-99/SC186-135, August 1999.

- Safe Flight 21 Steering Group, “Safe Flight 21 Master Plan, Version 2.0,” March 2000.

- Olmos, B. O., Mundra, A., et al, “Evaluation of Near-Term Applications for ADS-B/CDTI Implementation,” 98WAC-73, World Aviation Congress Conference, September 1998.

- Olmos, B. O., “Wilmington (ILN) ’99 OpEval: Overview,” April 2000.

- Stone, R., “Paired Approach Concept; Increasing IFR Capacity to Closely Spaced Parallel Runways,” United Airlines white paper, October 1998.

- Waller, M. C., and Scanlon, C. H., “A Simulation Study of Instrument Meteorological Condition Approaches to Dual Parallel Runways Spaced 3400 and 2500 Feet Apart Using Flight-Deck-Centered Technology, NASA TM-1999-208743, Langley Research Center, Hampton, VA, March 1999.

- Hammer, J., “Study of the Geometry of a Dependent Approach Procedure to Closely Spaced Parallel Runways,” 18th Digital Avionics Systems Conference, St. Louis, MO, October 1999.

- Carpenter, B. D., and Kuchar, J. K., “A Probability-Base Alerting Logic for Aircraft on Parallel Approach,” NASA CR 201685, Langley Research Center, Hampton, VA, April 1997.

- Delzell, S., Johnson, W. W., and Liao, M. “Pilots’ Spatial Mental Models for Memory of Heading and Altitude,” 17th Digital Avionics Systems Conference, Bellevue, WA, 1998.

- NASA AVOSS reference.

- Anon., “Point-in-Space Ghosting Technology,” Scientific Consulting & Automated Technological Services (SCATS) viewgraph presentation, DAG TM Workshop, NASA Ames Research Center, May 2000.