HQ 958629

FEBRUARY 21, 1996

CLA-2  RR:TC:MM   958629 JAS

CATEGORY:   Classification

TARIFF NO.:   8428.90.00, 8464.20.00, 8479.89.95

Port Director of Customs

110 South 4th. St.

Minneapolis, MN  55401

RE:   PRD 3501-94-100323; Machines for Producing Insulated Glass

Windows,

Glass Working Machines, Window Making Production Line;

Loading, Loading

Machine. Heading  8428, Machine for Removing Metal From

Glass; Metal                        Grinding Machine,  Heading

8460; Washing and Drying Machine, Inlet and Outlet

Station, Functional  Unit, Section XVI, Note 4

Dear Port Director:

This is our decision on Protest 3501-94-100323, filed

against your classification under the Harmonized Tariff Schedule

of the United States (HTSUS), of certain machines made in Austria

for a production system used to manufacture insulating glass for

windows, doors, etc.  The entry under protest was liquidated on

May 20, 1994, and this protest  timely filed on August 17, 1994.

FACTS:

The machines covered by this protest are ten (10)

individual components which, together with other machines not the

subject of this protest, make up the Type LV 38/25 PSL Insulating

Glass Production Line.

The model RTV-11/25AV is a positioning machine or outlet

transport station that inserts glass sheets into the model AKL-25V stripper, which is a machine that grinds  the edges  of the

glass sheets;  the model RTV-22/25WEV inlet transport machine

moves glass sheets into the model VHW-25V8 washing and drying

machine, and the model RTV-38 outlet transport station removes

the glass from washer/dryer; the model RTV 32WE inlet transport

unit transports glass sheets to a coating machine whose specific

function is unspecified; the model RSV-38/25B is a frame mounting

machine that assembles butyl coated spacer frames onto the glass

sheets; the model PSL-35/25V assembles glass panes together with

the necessary spacer frames;  the model

- 2 -

FPL-25/25 flat press machine presses the glass panes and spacer

frames together into an airtight unit; finally, the model RTV-32/25 transport and storing machine removes glass sheets from one

machine in the production line and stores them for processing in

another machine in the line.

The merchandise was incorrectly entered under subheading

8474.80.00, HTSUS, as other machinery for working earth, stone,

or other mineral substances in solid form.  Customs reclassified

the model RTV-11/25AV and the model AKL-25V in liquidation under

heading 8460, as metal finishing machines, and the remaining

models under heading 8479, as machines not elsewhere specified or

included in Chapter 84.  Protestant maintains these machines were

incorrectly entered under provisions of heading 8474 as sorting,

screening and washing machinery.  Protestant's claim is that the

machines, when interconnected, are for cold working glass, and

are, therefore, classifiable in a subheading of heading 8464, and

that heading 8464 is a more specific provision than heading 8460.

The provisions under consideration are as follows:

8428                 Other lifting, handling, loading or

unloading machinery...:

8428.90.00                           Other machinery...1.2

percent

*              *              *              *

8460                  Machine tools for

...grinding...polishing or otherwise finishing

metal...:

Other grinding

machines...:

8460.29.00                           Other...4.4 percent

*              *              *              *

8464                  Machine tools for...cold working

glass:

8464.20                            Grinding or polishing

machines:

8464.20.00 (now 20.50)                 Other...2.6 percent

8464.90                             Other:

8464.90.00 (now 90.50)                 Other...2.6 percent

- 3 -

*              *              *              *

8479                  Machines and mechanical appliances

having individual

functions, not specified or included elsewhere in [Chapter

84]:

8479.89                             Other:

8479.89.90 (now 89.95)                 Other...3.2 percent

ISSUE:

Whether the ten (10) machines are classifiable individually,

or together, as a machine tool for working glass.

LAW AND ANALYSIS:

Merchandise is classifiable under the Harmonized Tariff

Schedule of the United States (HTSUS) in accordance with the

General Rules of Interpretation (GRIs).  GRI 1 states in part

that for legal purposes, classification shall be determined

according to the terms of the headings and any relative section

or chapter notes, and provided the headings or notes do not

require otherwise, according to GRIs 2 through 6.  Section XVI,

Note 4, provides, in part, that where a machine consists of

individual components intended to contribute together to a

clearly defined function covered by one of the headings in

chapter 84 or chapter 85, then the whole is considered to be

classified in the heading appropriate to that function.

The Harmonized Commodity Description And Coding System

Explanatory Notes (ENs) constitute the official interpretation of

the Harmonized System.  While not legally binding, and therefore

not dispositive, the ENs provide a commentary on the scope of

each heading of the Harmonized System and are thus useful in

ascertaining the classification of merchandise under the System.

Customs believes the ENs should always be consulted.  See T.D.

89-80, 54 Fed. Reg. 35127, 35128 (Aug. 23, 1989).

As to protestant's claim under heading 8464, relevant ENs at

p. 1283 state under (II) MACHINE-TOOLS FOR COLD WORKING GLASS,

that machines of heading 84.64 are used for cold-working as

opposed to hot-working glass, and include, in addition to certain

sawing, cutting, slitting, grinding, drilling and turning

machines, other machines for truing, polishing and engraving

glass.  In our opinion, the entire ten components do not form a

single production line for making insulated glass windows, doors,

etc., and, for this reason, they cannot be classified as a

functional unit under either under subheading 8464.20.50 or

subheading 8464.90.50.  However, the model AKL-25V stripper, or

grinding machine, comports with the description in the cited ENs.

The literature indicates the model RTV-11/25AV outlet transport

section positions the

- 4 -

glass sheet so that it can be moved into the model AKL-25

striping machine.  These two machines are a functional unit under

Section XVI, Note 4, that together perform a grinding function

appropriate to machines of heading 8464.

The model RTV-22/25WEV transports glass sheets to the inlet

portion of the model VHW-25V8, washing and drying machine.  The

cleaned and dried glass is then unloaded by the model RTV-38

outlet transport station.  These three machines contribute

together to perform a washing and drying function.  However,

washing and drying machines are not specifically described in

heading 8479.  Because that heading does not describe a machine

or machines by specific function, these three machines cannot be

classified in heading 8479 by virtue of Section XVI, Note 4.

Both the RTV-22/25WEV and the RTV-38 perform a loading or

unloading function appropriate to machines of heading 8428, while

the model VHW-25V8 remains a washing/drying machine classifiable

in appropriate provisions of heading 8479.

The model RTV-32WE inlet transport station transports glass

sheets to a coating machine.  Because the coating machine is not

a part of this protest, the two cannot be classified as a

functional unit. The model RTV-32WE performs a function

appropriate to machines of heading 8428.

Neither the model RSV-38/25B frame mounting machine, the

model PSL-35/25W assembly machine, nor the model FPL-25/25 flat

press machine, as described, cold works glass, so that none can

be classified under heading 8464.  These machines perform an

assembling function appropriate to machines of heading 8479.

However, as previously stated, because these machines are not

regarded as a functional unit under Section XVI, Note 4, each is

provided for separately in heading 8479.

Finally, the model RTV-32/25 performs a transport function

appropriate to machines of heading 8428.

HOLDING:

Under the authority of GRI 1, the model RTV-11/25AV and the

model AKL-25 are provided for in heading 8464.  They are a

functional unit classifiable in subheading 8464.20.00, HTSUS.

Under the authority of GRI 1, the models RTV-22/25WEV and

the RTV-38 are provided for in heading 8428.  Each is separately

classifiable in subheading 8428.90.00, HTSUS.  The model VHW-25V8

is provided for in heading 8479.  It is classifiable in

subheading 8479.89.90 (now 95).  The model RTV-32WE and the model

RTV-32/25 are provided for in heading 8428.  Each is separately

classifiable in subheading 8428.90.00, HTSUS.  The models RSV-38/25B, PSL-35/25V and FPL-25/25 are provided for in heading

8479.  Each is separately classifiable in subheading 8479.89.90

(now 95).

- 5 -

The merchandise should be reclassified as indicated above,

and the protest  ALLOWED in part and DENIED in part, as

appropriate.  In accordance with Section 3A(11)(b) of Customs

Directive 099 3550-065, dated August 4, 1993, Subject: Revised

Protest Directive, you should mail this decision, together with

the Customs Form 19, to the protestant no later than 60 days from

the date of this letter.  Any reliquidation of the entry or

entries in accordance with the decision must be accomplished

prior to mailing the decision.  Sixty days from the date of the

decision the Office of Regulations and

Rulings will take steps to make the decision available to Customs

personnel via the Customs Rulings Module in ACS and to the public

via the Diskette Subscription Service, the Freedom of Information

Act and other public access channels.

Sincerely,

John Durant, Director

Tariff Classification

Appeals Division