STT Fake Data Generator

S.L.Linn 12 Jan 2002

Overview

A Fake data generator was implemented for use with DFEC board in the test stand located in FCH3. The board uses a 53MHz clock from a data pump, which is transmitted to the board through a LVDS cable into the link2 connection. The outputs are sent to the two G-link transmitters in slot 4. The fiber cables are routed to MCH2. The SMT data uses the top transmitter in 16 bit mode. Track data uses the L3_OUT bus, which feeds the bottom G-link transmitter in 20 bit mode.  The event is repeated every 1 sec. In MCH2 the cables are grey(CFT) and orange(SMT). The stttest.bit file was downloaded to the 4th slot in the FCH3 test stand via the JTAG interface. In the future, I will implement the download using a compact flash card.

A fake event was taken from the L2STT Monte Carlo, where a 50 GeV muon was simulated at phi=82.5 degrees.

CFT Data

The track hits CFT sector=17/fiber doublet=22, and the L2 trigger produces the following output stream.

...

F0 0000

F0 0000

B5 0301

B0 1110

B0 01A2

B0 FFFF

B0 0000

B0 0000

B0 0114

B0 3C02

B0 A201

BA 735B

F0 0000

F0 0000

...

where bits [0:19] are reversed in the transmitted data and F00000 are filler words. Bits [17:23] are G-link controls.

SMT Data

SMT data is delayed by ~5us with respect to the CFT data. The SMT data consists of 7 hits to form a cluster with centroid at (6.7101, 0.883403, 2.22355) cm. The hits are in Crate=0,HDI=5, and Chip=4 with

hit	chan	data

1	2	8

2	3	11

3	4	29

4	5	11

5	6	15

6	7	11

7	8	11

The HDI corresponding to bits [0:7] is given the index 4, however, the cluster in HDI index 5 is repeated.

This produces the following data stream

...

F0 C0C0 - fill

F0 C0C0 - fill

B0 0505 - seq

B0 0504 - hdi

B0 8484 - chip

B0 0000 - zero

B0 0202 – chan 1

B0 0808 – data 1

B0 0303 – chan 2

B0 0B0B – data 2

B0 0404 – chan 3

B0 1D0D – data 3

B0 0505 – chan 4

B0 0B0B – data 4

B0 0606 – chan 5

B0 0F0F – data 5

B0 0707 – chan 6

B0 0B0B – data 6

B0 0808 – chan 7

B0 0B0B – data 7

B0 C0C0 - fill

B0 C0C0 - fill

F0 C0C0 - fill

F0 C0C0 - fill

F0 C0C0 - fill

...

where bits [0:19] are reversed in the transmitted data and F0C0C0 are filler words.

VHDL

The design is a block diagram called stttest.bde. This entity has two inputs: clock and reset signals. The two outputs are quad_out(SMT) and l3_out(CFT). Stttest connects four processes which are finite state machines:

L1.vhd – generates a pulse every 10 seconds

Delta.vhd – delays the l1acc signal by ~5us

Cft.vhd – stores and outputs cft data

Smt.vhd – stores and outputs smt data

The top level testbench is called tb.vhd. It is configured and executed by

Tb_beh_cfg.vhd and tb_beh.do for functional simulations, and

Tb_tim_cfg.vhd and tb_tim.do for timing simulations.

# Synthesis

From the Design Flow Manager -> synthesis options-> Run Mode: ->choose GUI and Top Level Unit: choose stttest from the pulldown menu.

Choose synthesis and FPGA Express will start and open a window.

The left window will have a file structure stttest->WORK->all-design-files.vhd.

Choose stttest and then SYNTHESIS->update.

From the pull-down menu choose stttest as the top level design

A box will open. Set clock frequency to 53 MHz and uncheck [ ]skip constraints.

From pull down menus choose: Vendor(Xilinx), Device(V600BG560), Speed(-5) and Family(VIRTEX). OK.

A chip will be created in the right window called stttest.

Choose the chip. From the high level menu choose SYNTHESIS->edit constraints->ports->Use I/O Reg->true

Global Bufer-> BUFGP for clocks

Close

Choose chip

SYNTHESIS->Optimize chip

SYNTHESIS->Export Netlist

Exit

## Implementation

From the Flow Manager -> implement options->GUI

Brouse to find the Netlist file c:/My_Designs/stttest/synthesis/stttest.edf. OK.

Choose implement. A box will open saying that the synthesis is not up to date… and choose NO.

A window will open with a box for the constraints file. Choose custom and brouse to find the configuration file c:/My_Designs/stttest/src/u5_pins.cfg

Design->options->

Implementation: edit options->optimize and map -> Pack I/O Reg -> Inp and Out. OK.

Set part if necessary.

Simulation: edit options->sim data options->Active VHDL

Configuration -> JTAG

edit options->readback  [X} Enable readback

OK. OK.

Design->Implement

Exit.

### Data Formats